## Slide 1
Tips for Staying Afloat in
The Reference System Alphabet Soup NAD83? NAVD88? IGS08? ITRF14? NGVD29? NAD27? WGS84? NATRF22?
Which epoch... ellipsoid... geoid model?
Nic Kinsman
Alaska Regional Geodetic Advisor
National Organization for the Advancement of Acronyms
nicole.kinsman@noaa.gov
Anchorage, Alaska
202-306-5736

## Slide 2: Overview of Topics
Introduction to the National Geodetic Survey (NGS)
Terms, definitions, & common reference frames
Useful tools
Best practices for documentation of reference frames (metadata)
Tips & resources for transformations
Practical guidance for working with geopositonal data in Alaska
AKPA 1996

## Slide 3: NATIONAL GEODETIC SURVEY (NGS)
Introduction to the

## Slide 4
NGS is part of NOAA NOS
Mission:
To provide science-based solutions through collaborative partnerships to address evolving economic, environmental, and social pressures on our ocean and coasts.

## Slide 5
NGS provides the framework for all positioning activities in the Nation.
The foundational elements:
latitude, longitude, elevation,
shoreline position
+ changes over time
= informed decision making for:
mapping and charting, navigation,
flood risk determination,
transportation, land use and
ecosystem management
NGS MISSION:
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.

## Slide 6
Meaningful coordinates
Flood Planning
Navigation
Aviation
Engineering
Mapping
Disaster Response
Surveying
The NSRS is a common reference system for positioning geospatial data
Defining locations relative to geodetic control = absolute positional accuracy

## Slide 7: NGS Regional Advisor Program

## Slide 9: NGS Programs
Modernizing the NSRS
OPUS
GPS Satellite Orbits
CORS
GRAV-D
Height Modernization
ECO
Airport Surveys
VDatum
Geodetic Advisor Program
Emergency Response Imagery
Coastal Mapping
NGS Products and Services

## Slide 10
Network of designated GNSS receivers across the United States managed by NOAA’s National Geodetic Survey.
The CORS network facilitates position activities that are tied to the National Spatial Reference System (NSRS), there are presently 108 active CORS in Alaska.
Users can access authoritative NSRS positioning tools via NGS Online Positioning User Service (OPUS).
AB36
Manley Hot Spring
CORS Network
Notes: The CORS network is a multi-purpose cooperative endeavor involving government, academic, and private organizations. The sites are independently owned and operated. Each agency shares their data with NGS, and NGS in turn analyzes and distributes the data free of charge. As of August 2015, the CORS network almost 2,000 stations, contributed by over 200 different organizations, and the network continues to expand.
Like with any dual use infrastructure, different stakeholders have different priorities. As active geodetic control has emerged as the new infrastructure for precise positioning activities, the scientific community has been primarily at the helm of the GNSS network development in Alaska. Surveyors and the GIS community are increasingly dependent on data being made freely available by scientific agencies with similar, but not identical priorities.
Examples of how priorities might be different:
- Scientific community seeks network densification over tectonically active/complex regions
- Surveying community largely desires densification around population centers, and other corridors such as roads and pipelines
- Surveying community desires real-time or near-real time data, and many scientific applications do not require consistent telemetry
Direct Uses:
Geodesy and Seismology (tectonic motion)
Surveying
Scientific field measurements
Space weather
Atmospheric water vapor
GPS reflectometry (snow depth, water levels, soil moisture)
In-direct Uses:
Remote sensing (imagery, elevation)
Mapping

## Slide 11
>15 min of L1/L2 GPS data >>> www.ngs.noaa.gov/OPUS
Processed automatically on NGS computers
Solution via email - in minutes
Fast, easy, consistent access to NSRS
Online Positioning User Service (OPUS S/RS)

## Slide 12: TERMS, DEFINITIONS and common reference frames
Overview of

## Slide 13: GPS vs. GNSS (space, control, and user segments)
Global Positioning System
Global Navigation Satellite System
GPS
GLONASS
Galileo
BeiDou

## Slide 14
Geodetic Control =
The Gateway to the NSRS
Passive
Marks
Active
(CORS)

## Slide 15
Data Sheets vs. Shared Solutions Integrated Database (IDB) OPUS Database

## Slide 16: Datums & Reference Frames
XYZ vs. LLH
aka P(L,L,H)
= lat.
= long.
= ht.
Sally
Jane
?
A reference standard for measuring elevations

## Slide 17: The Practicality of Datums
Meades Ranch,
Kansas
Rimouski, Quebec
We are aware
We can measure
We care
And the MODERNIZATION 

## Slide 18: Common Reference Systems
International Terrestrial Reference Frame (ITRF##)
National Spatial Reference System (NAD27 & NGVD29, NAD83 & NAVD88, …)
World Geodetic System (…, WGS72, WGS84)

## Slide 19: Reference Ellipsoids
Defined by:
  Size/shape
  Origin
  Orientation
  Scale
Clarke 1866 – in NAD 27
GRS80 – in NAD83
WGS84 – in WGS84
Note: GRS80 and WGS84 are VERY similar, but not exactly the same in shape.

## Slide 20: Migrating Ellipsoids
2.2 meters
NAD 83
Origin
ITRF 00 ≈ WGS84
Origin
Earth’s
Surface
h83
h00
NAD83 (~static) is no longer geocentric
GRS80
WGS84
Geocentric!
1-2 cm/yr
in US

## Slide 21: GNSS: What TYPE OF POSITIONAL DATA?
Autonomous GNSS:
  All native GNSS data are collected with reference to IGS
  Data may be transformed to a different reference frame
Augmented GNSS (NDGPS, RTK, RTNs):
  Datum will correspond to that of your control [e.g. NAD83(2011)]
Heights are relative to the ellipsoid 
Reference Ellipsoid

## Slide 23: ‘Societally-Relevant’ Elevations
Old source:
We got a ‘geoid’ by connecting observations at tide gauges to get a surface which most closely ‘fits’ the national mean sea level in a least squares sense.
New source:
We can measure gravity to map an equipotential surface that is a best fit to the global mean sea level.
But… for a geoid that can be combined with the ellipsoid to obtain heights that correspond to a regional/national vertical datum we make adjustments.
Geoid12A
Geoids are vertical ‘translation’ surfaces that approximate an idealized global sea surface

## Slide 24
Breaking down orthometric heights
http://neverwildenough.blogspot.com/2013/12/cartography-and-visualisation-i.html
aka ‘Elevations’
Not exact

## Slide 25: Evolution of the Gravimetric Geoid
EGM08
GRACE
GOCE
USGG2012
GEOID12A/B
2012
2008
2014
2015
2016
xGeoid14B
xGeoid15B
xGeoid16B
+
GRAV-D
GOCO05S
NGA
ArcticGP
Notes: NGA Arctic Gravity Grid (2017)

## Slide 26: NSRS Modernization
Active
Control
+
Geoid
Passive
Control
NAD83/NAVD88  NATRF2022*/NAPGD2022
Fixed  Semi-dynamic
GPS/GNSS = official gateway to precise positioning
(Geometric) (Geopotential)
*one of 4 RFs

## Slide 27: DOCUMENTATION OF DATUMS (metadata)
Best practices for

## Slide 28: Use Complete Nomenclature
NAD83

## Slide 29: Use Complete Nomenclature
NAD83(2011) epoch 2010.00
Reference System
&
Year Established
Tells us:
mathematical framework
general application
Authority
Tells us:
data in refinement
location
geoid model
Realization
or
Adjustment
Reference date
Tells us:
position of control
periodization length

## Slide 30: Relationship between the MANY ‘flavors’ of nad83 and GNSS-derived NAVD88 HEIGHTS
All hybrid geoid models from NGS are intended for use with NAD83, but for the most consistent results, ensure that the geoid model used matches the correct ‘flavor’ of NAD83
Alaska: For NAD83(1986) use Geoid06
For NAD83(2007), NAD83(CORS96) use Geoid09
For NAD83(2011) use Geoid 12A/B
NAD83
(2007)
NAD83
(2011)
NAD83
(1986)
NAD83
(1997)
NAD83
(2011)
Birth: NAD83(1986) Differential leveling only
1st adjustment NAD83(1997) GNSS/HARN and more leveling also: NAD83(HARN)
NAD83(CORS96) GNSS/CORS (2007.00 epoch in AK)
2nd adjustment NAD83(2007) GNSS/CORS
3rd adjustment NAD83(2011) CORS
Note: for Alaska these are the only three hybrid geoid models that exist
Adjustments to the National Spatial Reference System (NSRS)

## Slide 31: Use Complete Nomenclature
MLLW

## Slide 32: Use Complete Nomenclature
MLLW(9452210; NTDE 1960-78)
Datum
NOAA Tide Station
National Tidal Datum Epoch
(or Modified 5-year Procedure dates)

## Slide 33: Guiding Principals:
Consider your data’s absolute & relative accuracies (CONTROL)
Consider the needs of future users
Epoch of datum and epoch of collection are different
Some notes:
EPSG codes are not always complete – use caution
Be careful with transformations

## Slide 34: TRANSFORMATIONS
Tips and resources for

## Slide 35
TRANFORMATION FLAVORS
Ellipsoid shifts are 3-D so planer shifting tools are only an approximation when going between NAD83 and ITRF08/WGS84
  Options:
    2 parameter 2 shifts
    3 parameter 3 shifts
    5 parameter 3 shifts, axis scale, flattening
    7 parameter 3 shifts, 3 rotations, scale
    10 parameter everything above + rotation origin
    14 parameter 3 shifts, 3 rotations, scale + time
    Surface fitting grid transformations (e.g. NADCON) n/a
A CAUTION for DATUM TRANSFORMATIONS IN GIS
Few handle 3-D geometric datum shifts at this time!!
Example:
NAD83  WGS84
Data will be shifted horizontally, but the z values are the same (= ‘Franken-Datums’)

## Slide 36
when in doubt… check.

## Slide 37: Vertical Datum Transformations
Here Be Dragons
NOME, 4th of JULY, 2012
Sea of VERTCON
& VDATUM
Alaska

## Slide 38
TOOLS FOR VERTICAL DATUM CONVERSION
OUTSIDE:
VERTCON = NGVD29  NAVD88
VDatum = NAVD88 (and others) to Local Tidal
          NAD 83 (NSRS2007/CORS96) transformation grids
          “VDatum was originally was designed to accommodate 28 transformations spanning the three major classes of vertical datums: orthometric, ellipsoidal, and tidal. A geoid model was used to convert between orthometric and ellipsoidal datums, a topography of the sea surface was computed to relate orthometric and tidal datums, and tidal modeling was used to compute the tidal datums.”
ALASKA:
?

## Slide 39: “Rosetta” Benchmarks
Where do you find these for NGVD29?
      Airport construction diagrams
      Land survey plats (BLM often)
      FEMA FIS documentation
Where do you find these for Local Tidal datums?
      CO-OPS tidal BM sheets
      OPUS Shared DB
DATUM A
DATUM B
Two Published Elevations

## Slide 40: HTDP

## Slide 41: USEFUL TOOLS
Some other

## Slide 42: NGS Tools: OPUS
https://www.ngs.noaa.gov/OPUS/

## Slide 43
SHARE YOUR OPUS SOLUTIONS
A call to arms.
- Support geoid model and 2022 transformation tool development
- provide a status update on the 'health' of all marks of public interest
- support the development of VDATUM and other tidal to geodetic transformation tools in Alaska
- Extended occupations (24-48 hours in duration) compliment long-term CORS records and improve models used within tools such as HTDP
http://europa.ngs.noaa.gov/GPSonBM/
New! Contact Nic for Sample Data

## Slide 44
https://www.ngs.noaa.gov/marks/descriptions

## Slide 45: OPUS Shared DB - Maps
https://www.ngs.noaa.gov/OPUS/showMarks.jsp
https://beta.ngs.noaa.gov/opusmap/

## Slide 46: CORS Maps
https://beta.ngs.noaa.gov/corsmap/
https://www.ngs.noaa.gov/CORS_Map/

## Slide 47
https://beta.ngs.noaa.gov/gtkweb/

## Slide 48: Space Weather
http://www.swpc.noaa.gov/

## Slide 49: RINEX Cheats
https://igscb.jpl.nasa.gov/components/formats.html
http://www.gage.es/sites/default/files/gLAB/HTML/SBAS_Navigation_Rinex_v3.01.html

## Slide 50: Practical Guidance for Alaska
The reality up north:

## Slide 51
ARP
mark
rotate NRP to face true north
antenna height
JGE, 2015
For antenna calibrations, photos, ARP and NRP diagrams, see geodesy.noaa.gov/ANTCAL/
antenna type & hgt are important for accurate results
each type has unique biases
Notes: Antennas are the one area where OPUS users can force errors into their solutions.
Must be on approved list (e.g. calibrated).
Dual-frequency geodetic quality.
Phase center locations different, & that affects orthometric height.
Align North Reference Point to true north. Examples of NRP: face plate (as antenna above, antenna cable connector (for separate antenna/receiver), and north arrow on antenna.
ARP height measured vertically, NOT slant.
ANTENNA TYPE: GNSS antennas aren’t like survey telescopes, which have a point (reticule) where all measurements take place. The “phase center” measuring points of an antenna will wander as each satellite’s azimuth and elevation changes. These variations are unique for each model of antenna. OPUS mixes data from across long distances and from different antenna types (rover + CORS) so this is a source of error. However, the GNSS community has measured these phase center variations for many antenna types, a process known as “calibration” which measures the variations with respect to an antenna’s reference point, or ARP. You tell OPUS where the ARP is, and it will do the rest.
ANTENNA HEIGHT:
The height of the antenna is measure vertically (not slant height) up from the from the mark, to the Antenna Reference Point which is almost always the center of the bottom-most, permanently attached piece of the antenna. Some antennas have a short removable pipe or extension to them, these are NOT part of the antenna, and must be considered part of the tripod height.
If in doubt you can find photos and diagrams of each antenna (that we have calibrated) at the URL shown.
So if you leave the antenna height as “0” this will be the height OPUS returns, of the antenna’s ARP.
Image posted as http://geodesy.noaa.gov/sitemsgs/OPUS/about/images/ant_hgt_BBBK23.png

## Slide 52: OPUS Static vs. Rapid Static
 | Static | Rapid Static
Input (dual-frequency GPS) | 2-48 hours | 15 minutes-2 hours
Output | normal, extended, XML sharing, projects | normal, extended, XML
Accuracy (95%confidence) | 1-2 cm horizontal 3-6 cm ellipsoidal height | 1-2 cm horizontal 4-8 cm ellipsoidal height
Network Geometry | 3 CORS, preferably within 1000 km of rover | 3-9 CORS, surrounding & within 250 km of rover
Availability | global | 90% of CONUS (subject to geometry, above)

## Slide 53: OPUS AVAILIBILITY DELAYS

## Slide 55
Check your CORS!

## Slide 56: SOME GENERAL ‘MSL’ ADVICE FOR ALASKA
  Any time you encounter an elevation or height (3 feet for example) be sure to ask “3 feet above WHAT?”
  If the answer is height above ‘Mean Sea Level’, is it:
    The National Standard Sea Level (NAVD88)
    An older national vertical datum based on sea level (NGVD29)
    Local Mean Sea Level (based on tide gauge)
    Local Mean Sea Level (based on something else)
        If it is Local Mean Sea Level, when was it calculated and by whom?

## Slide 57: Educational Videos
http://www.ngs.noaa.gov/corbin/class_description/NGS_Video_Library.shtml
NGS has partnered with The COMET Program to develop educational videos.
View videos on COMET YouTube channel: https://www.youtube.com/playlist?list=PLsyDl_aqUTdGmAeHGgFucHkTfWDOwElOB
Notes: There are currently seven videos, 2 to 5 minutes long.
Series on Geodetic Datums
What are Geodetic Datums? (4:30)
How Were Geodetic Datums Established? (3:11)
What is the Status of Today’s Geodetic Datums? (4:48)
What’s Next for Geodetic Datums? (4:41)
Other videos:
Precision and Accuracy in Geodetic Surveying (2:25)
Two 'Right' Feet? Understanding the Difference Between U.S. Survey Feet and International Feet (2:39)
Geospatial Infrastructure for Coastal Communities: Informing Adaptation to Sea Level Rise (4:06)
More videos coming:
Common GNSS Error Sources
Coastal Elevation Data
VDATUM
What is a bench mark (passive control)?
What is a CORS (active control)?

## Slide 58: NGS Monthly Webinar Series
http://www.ngs.noaa.gov/web/science_edu/webinar_series/
Presentations related to NGS programs, projects, products and services.
Second Thursday of every month,
2:00-3:00 p.m. East Coast time.
Webinar series Web-pages:
view previously recorded webinars,
register for upcoming webinars, and
subscribe for monthly notifications.
Contact: NGS.Webinar@noaa.gov

## Slide 59
Thank You!
Please contact me: nicole.kinsman@noaa.gov Cell: 202-306-5736