## Slide 1
U. S. Datums: Where We’ve Been,
Where We’re Going
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
Louisiana Society of Professional Surveyors – District 2
2017 Fall Technical Session
Thibodaux, Louisiana
October 27, 2017

## Slide 2: Presentation Outline
- National Geodetic Survey.
- Horizontal / Geometric Datums.
- Vertical Datums.
- GRAV-D and what it’s about.
- New Reference Frames & Preparing for them.
- Update on NGS Products.
- Questions.

## Slide 3: U.S. Department of Commerce National Oceanic & Atmospheric Administration National Geodetic Survey
Mission: To define, maintain & provide access to the
National Spatial Reference System (NSRS)
to meet our Nation’s economic, social & environmental needs
National Spatial Reference System
* Latitude * Scale
* Longitude * Gravity
* Height * Orientation
& their variations in time
Notes: - NSRS benefit to the nation = $2.5B/year
est. 300K precision GPS users worldwide (2008); ¼ in US
- Very exciting to us at NGS to see how it has evolved over the years – now cm-accuracy capability / tracking with time

## Slide 4: NGS MISSION - The NSRS
Define - National Coordinate Sys. (NSRS)
Maintain - the NSRS
Provide Access
Notes: Define: explain how NSRS was developed through the passive network, status of passive network, and how NSRS now based on CORS network.
Maintain: determination of CORS positions and the changes to those positions, datum (ref. frame) updates (ex. NAD (2011), updated hybrid geoid models, programs and tools for transformations, inverses, on-line vertical leveling adjustments, Geodetic Tool kit.
Access: provide access to the NSRS through CORS static data, control mark datasheets, and the suite of OPUS products.

## Slide 5: Federal Users of the NSRS
Notes: Many of these users also sit on the Federal Geodetic Control Subcommittee, so there is a feedback loop between the providers of geodetic control (NGS) and the users of that control.

## Slide 6: GEODETIC DATUMS
  VERTICAL
  1 D (Orthometric Height) (e.g. NGVD 29, NAVD 88, Tidal)
  HORIZONTAL
  2 D (Latitude and Longitude) (e.g. NAD 27, NAD 83 (1986))
  GEOMETRIC
  3 D (Latitude, Longitude and Ellipsoid Height)
  Fixed and Stable - Coordinates seldom change
  (e.g. NAD 83 (1994), NAD 83 (2007), NAD83 (2011))
  also
  4 D (Latitude, Longitude, Ellipsoid Height, Velocities) Coordinates change with time
  (e.g. ITRF00, ITRF05, ITRF08)

## Slide 7
The National Geodetic Survey 10 year plan
Mission, Vision and Strategy
2013 – 2023
http://www.ngs.noaa.gov/INFO/NGS10yearplan.pdf
Official NGS policy as of Jan 9, 2008
  (updated in 2013)
  Modernized agency
  Attention to accuracy
  Attention to time-changes
  Improved products and services
  Integration with other fed missions
2022 Targets:
  Replace NAD 83 and NAVD 88
  Cm-accuracy access to all coordinates
  Customer-focused agency
  Global scientific leadership

## Slide 8: U.S. Horizontal Datums

## Slide 9
Datums - Horizontal
Horizontal
North American Datum Of 1927
- Used early triangulation surveys (first called US Std Datum).
- Based at Meades Ranch, KS & used Clarke 1866 spheroid.
North American Datum of 1983 (1986)
- Used 250,000 points (triangulation, Doppler, a few GPS pts).
- Based at geocentric location using Geodetic Ref. Sys. 1980.
Updates*
NAD83 (1990’s) – State HARN / FBN surveys.
NAD83 (late 90’s – early 2000’s) – Efforts to establish ellipsoid heights.
NAD83 (2007) – Remove regional distortions, better with align CORS.
NAD83 (2011) – Adjustment to realign CORS / passive control.
* Not a new datums

## Slide 10: National Spatial Reference System(NSRS) Improvements in the Horizontal Datums
TIME NETWORK LOCAL
NETWORK SPAN ACCURACY ACCURACY
NAD 27 1927-1986 10 meter (1 part in 100,000)
NAD83(86) 1986-1990 1 meter (1 part in 100,000)
NAD83(199x)* 1990-2007 0.1 meter B-order (1 part in 1 million)
HARN A-order (1 part in 10 million)
NAD83(2007) 2007 - 2011 0.01 meter 0.01 meter
(CORS)
NAD83(2011) 2011 - 2022 0.01 meter 0.01 meter
(CORS)

## Slide 12: NGS Published CORS

## Slide 13
NAD83 is NON-geocentric & hence inconsistent w/GNSS
Difficult to maintain consistency between CORS & passive networks
NAD 83 does not track/report passive mark motion
Lack of monumentation stability / permanency
Necessary for agreement with future ubiquitous positioning capability
Why Replace NAD83?

## Slide 14: North American Datum 1983 (NAD83) Shortcomings
Inconsistency of NAD83 vs.
- International Terrestrial Reference Frame
[ITRF08]
- World Geodetic System 1984
[WGS84 (G1762)]
CORS & passive network inconsistency / challenges
vs.
NAD83
ITRF08/WGS84

## Slide 15: Future Geometric (3-D) Reference Frame
Replace NAD83 with new geometric reference frame – by 2022
CORS-based, accessed via GNSS observations
Coordinates & velocities in ITRF & new US reference frame
Passive control tied to new reference frame (not a component)
Transformation tools will relate NAD83 to new US
reference frame ( NADCON / GEOCON / GEOCON11 / ….. )

## Slide 16
New geometric datum minus NAD 83 (horizontal)

## Slide 17
New geometric datum minus NAD 83 (ellipsoid height)

## Slide 18: U.S. Vertical Datums

## Slide 19
VERTICAL CONTROL USED FOR NGVD 1929 DATUM

## Slide 21
Notes: Many of these users also sit on the Federal Geodetic Control Subcommittee, so there is a feedback loop between the providers of geodetic control (NGS) and the users of that control.

## Slide 22
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Weren’t adopted in Canada
  Were determined by leveling from a single point, allowing cross-country error build up
Why isn’t NAVD 88 good enough anymore?

## Slide 24
Long term fix: Re-level some/all of NAVD 88
  81,500 km of 1st order leveling at least
  625,000 km of mixed 1st and 2nd order leveling
Re-leveling NAVD 88 estimated to cost between
  $200 Million and $2 Billion
Time factor in that amount of leveling
Still would have problems related to passive control
Can NAVD 88 be fixed?
Notes: Re-leveling NAVD 88 won’t fix:
Sparseness of the bench marks
Continued subsidence or uplift of bench marks
Destruction of bench marks
Canada’s decision not to adopt NAVD 88
Whatever errors caused a continent-wide 1 meter build up in the leveling the first time around

## Slide 25: NEW VERTICAL DATUM (Rationale)
  A move away from differentially leveled passive control as the defining mechanism of the reference surface
  To be consistent with the shift in the geometric reference frame/ellipsoid (2022)
  Improvement in our technical abilities in reference surface realization (geopotential gravimetric reference surface - 1cm accuracy of the geoid (GNSS/GRAV-D))
  Goal - ability to establish 2cm orthometric height anywhere in U.S. using a minimum of 15 min. of GNSS data.
  The new geopotential reference surface will be aligned with the geometric reference frame/ellipsoid (i.e., no hybrid geoid)

## Slide 26
Best long term fix:
Replace NAVD 88 with a 1cm vertically accurate geopotential reference frame (surface)……..but how?
First, let’s talk a little bit about geoids.
Can NAVD 88 be fixed?

## Slide 27: Definitions: GEOIDS vs GEOID HEIGHTS
GEOID - “The equipotential surface of the Earth’s gravity field which best fits, in the least squares sense, (global) mean sea level.”*
Can’t see the surface or measure it directly.
Can be modeled from gravity data as they are mathematically related.
Note that the geoid is a vertical datum surface
A geoid height is the height from an ellipsoidal datum to a geoid.
Hence, geoid height models are directly tied to the geoid and ellipsoid that define them (i.e., geoid height models are not interchangeable).
*Definition from the Geodetic Glossary, September 1986
Notes: -What does equipotential surface mean?
-If we could see or measure the geoid, this could be our vertical datum.
-It may be in the future, and we must plan for a transition.
-For now, we are dependent on leveling observations on the surface to create our datum.
-The leveling datum may or may not be a true equipotential surface (i.e., NAVD 88 =/ true geoid).
-use the geoid height models to transform between the ellipsoidal and vertical datums.

## Slide 28
  Why do we need Geoid Models?
The geoid surface is mathematically related to gravity
Understanding the gravity field is important because it:
  impacts survey measurements
  dictates the direction water flows
  improves development of natural resources (iron ore, oil, water, etc.)
Geoid models allow us to relate different kinds of heights
GRACE Satellite Gravity
Notes: Why do we care about geoid models?

## Slide 29: Measuring and relating different kinds of heights
Ellipsoid heights
  Inherent to GNSS measurements
  Need accurate ellipsoid height control
  Better field procedures = better heights
Orthometric heights
  Measure by leveling surveys
  Most accurate but most expensive
  Difficult to maintain over time, esp. on national scale
Geoid heights
  Derived from model developed from gravity observations
  Can provide relationship between e.h. and o.h.
Notes: Ellipsoid height - height of ground referenced to the ellipsoid
Orthometric height – distance of the ground from geoid (along plumb line)
Geoid height – distance between ellipsoid and geoid (perpendicular to ellipsoid)

## Slide 30: The ellipsoid, the geoid, and you
Earth surface
Ellipsoid
Geoid
Orthometric height, H
Geoid height, NG
Ellipsoid height, h
Deflection of the vertical
Mean sea level
Note: Geoid height is negative everywhere in the coterminous US
h = H + NG
You are here

## Slide 31
GPSBM1999: 6,169 total 0 Canada STDEV 9.2 cm (2σ) GPSBM2003: 14,185 total 579 Canada STDEV 4.8 cm (2σ) GPSBM2009: 18,291 total 576 Canada STDEV 2.8 cm (2σ)
GPS Bench Marks used for Geoid 12B (23,961)
Notes: GPSBM for G12A = 23,961 used.
These are the control data used to make GEOID99, GEOID03 and GEOID09 (GPS on bench marks: GPSBM’s).
Improvements in Distribution are primarily due to obtaining data in Canada.
The bulk of the increase comes in one state: Minnesota (603 => 4161).
Note the inequitable distribution.
You could practically grid the GPSBM’s in South Carolina or Minnesota and get a good result.
Other places are not so fortunate…
Also note that this shows distribution but not quality of the points.
Some regions (e.g., Texas) have systematic quality problems (due to subsidence) that impact the GPSBM’s and the derived hybrid geoids.
Current techniques rely on creating models of the systematic effects at multiple wavelengths. If the spatial density doesn’t support the shorter wavelength models, then the quality of predictions will commensurately be reduced.
Note that a hyper-dense survey isn’t necessary to achieve optimal results. Later discussion on Minnesota will emphasize this.

## Slide 32
LA GPSBM Marks for Geoid 12B (194)

## Slide 33: Which Geoid for Which NAD 83?
NAD 83(2011) --- Geoid12B
NAD 83(2007) --- Geoid09
NAD 83(19xx) --- Geoid03
--- Geoid99
--- Geoid96

## Slide 34: Current and Best NGS Geoid: USGG2012
GRACE + 2 yrs of GOCE + other satellite data
+ World Gravity Model (EGM2008)
+ Estimated Gravity from Topography
+ Around Two Million Surface Gravity Points
But even this isn’t good enough for a 1-2 cm accuracy vertical reference surface

## Slide 35
Replace the Vertical Datum of the USA by 2022 (at today’s funding)
GRAV-D is:
  An airborne gravity survey of the entire country and its holdings
  A 2022 gravimetric geoid accurate to 1 cm
  Long-term monitoring of geoid change over time
  Partnership surveys
Working to launch a collaborative effort with the USGS for simultaneous magnetic measurement
Acting Manager: Monica Youngman
Monica.Youngman@noaa.gov
Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
Gravity and Heights are
inseparably connected
Notes: GRAV-D is the NGS project designed to replace NAVD88 with a vertical datum based upon a gravimetric geoid accurate to 1 cm. Heights above this datum will be accessed via GNSS measurements. Three thrusts of project. Launch USGS collaboration for simultaneous mag measurement.

## Slide 36
Building a Gravity Field
Long Wavelengths
(≥ 250 km)
GRACE/GOCE/Satellite Altimetry
Intermediate Wavelengths
(500 km to 20 km)
Airborne Measurement
Surface Measurement and
Predicted Gravity from Topography
Short Wavelengths
(< 100 km)
+
+
Notes: Give example of how short wavelength information is like low altitude aerial photos (1/2” pixel accuracy) in that it provides very accurate and detailed information. The long wavelength gravity can be likened to the old LANDSAT imagery (3 meter pixel accuracy) in that it was good over large areas, but didn’t give much detail for local areas. The intermediate wavelength gravity data gives us a connection between the two (the short and long), allowing the NGS gravity team to use all available gravity information in working toward the production of a 1 cm accurate gravitational surface.

## Slide 37: Data Collection Scope
Entire U.S. and territories
  Total Square Kilometers: 15.6 million
  ~200 km buffer around territory or shelf break if possible
  Initial target area for 2022 deadline
Notes: Project Scope:
Scope of the project: cover roughly 15.6 million square kilometers – contiguous united states, Alaska, Hawaii, Guam, and American Samoa
In order to blend with satellite altimetry data the airborne survey is done to the continental shelf where possible or ~ 200 km beyond the shoreline or border, whichever is further
Deadline of 2022 for datum rollout, which means a target of 2021 to finish the airborne survey
Priority areas were defined as Alaska and coastal areas
Challenges:
Fixed annual budget and time  design of surveys had to fit within an annual budget of $3.5 million and meet the deadline
This was a major factor in setting altitude and line spacing

## Slide 38: GRAV-D Status 3-31-17: 59%

## Slide 39: Survey and Block Plans
Data lines spaced 10 km apart
Cross lines spaced 60-80 km apart
Flight altitude 20,000 ft
Nominal speed 220-250 kts
Notes: Block layout based on aircraft, adjust size of block if needed

## Slide 40
Field Quality Control Processing
  GPS/IMU combined solution using differential positioning
  Gravity processing with Issac (internal software)
Final Processing
  GPS/IMU combined solution using Precise Point Positioning (PPP)
  Gravity processing with Newton (internal software)
  Quality evaluated and data minimally trimmed
  Processed data and documentation released
Data Processing
Notes: Data Processing
In the field a differential GPS-IMU solution is used to evaluate daily whether flights need to be reflown because precise ephemeris are not available
Final processing is done using Precise Point Positioning (PPP) – an analysis was done comparing differential and PPP, there was either no effect or small improvements in the gravity solutions from PPP
Gravity processing done using in-house software, Newton, which applies the absolute gravity tie, removes drift, and applies a vertical acceleration, Eotvos, and offlevel corrections and then is filtered three times with a time-domain frequency filter
End of line trimming
Data documentation produced and package released on the website
This plot is an example of part of the output. We aim for +/- 5 mGals from EGM08 – as you can see in this plot there is a significant section that deviates from that. However, part of the goal of the airborne campaign is to improve upon EGM08, so while it is a good guide, it cannot be the final determination. This line, for example, if you compare to an adjacent line it looks like this.

## Slide 41
Lake Michigan
Green = EGM08, Blue = Airborne
Notes: These are two lines over Lake Michigan where the airborne data (blue) shows significant deviations from EGM08 (Green). However, the x-axis is latitude and you can see that the deviations are supported independently by both lines. This type of visual analysis is extremely useful day-to-day in the field as we determine which lines need to be reflown. In the final processing we also do line to line cross correlation to evaluate overall line agreement.

## Slide 42: Online Data Portal http://www.ngs.noaa.gov/GRAV-D/data_products.shtml
Interactive Google Map:
  Up-to-date info on all blocks
  27 blocks released (Was 20 in Jan. 2014)
  Clicking a block pops up basic info and a link to the block’s page if data is available

## Slide 43: Experimental Geoids
Combining most recent satellite, airborne, and terrestrial gravity data to test methods for 2022
Published annually
  Updated with airborne gravity data
  Available on the website
Testing methods
  Blending techniques
  Density
  Terrestrial data improvements
http://beta.ngs.noaa.gov/GEOID/xGEOID/

## Slide 44
“Action speaks louder than words but not nearly as often.” ― Mark Twain
Prove that our goal with GRAV-D is possible:
“...the gravimetric geoid used in defining the future vertical datum of the United States should have an absolute accuracy of 1 centimeter at any place and at any time.”
-- The NGS 10 year plan (2008-2018)
Notes: The above quote refers to one of many ambitious goals in the NGS 10 year plan. While admirable, its achievability remains an open question. In order to begin addressing the actual achievable accuracy of a gravimetric geoid model, NGS will engage in a variety of testing methods prior to the 2022 date when the gravimetric geoid will serve as the reference surface for a new vertical datum. The first such testing method took place in the summer of 2011 and is known as the Geoid Slope Validation Survey of 2011, or GSVS11. As its name implies, this survey tested the accuracy of differential geoid undulations between points ("geoid slopes") from NGS's gravimetric geoid models. The baseline for comparison will be independently computed geoid slopes from two methods, GPS and leveling as well as Deflections of the Vertical.

## Slide 45: Validating Geoid Accuracy
NGS plans up to 3 surveys to validate the accuracy of the gravimetric geoid model
  GSVS11
    2011; Low/Flat/Simple: Texas; Done; Success!
  GSVS14
    2014; High/Flat/Complicated: Iowa; Field work Complete
  GSVS17
    2017?; High/Rugged: Colorado? Wyoming?
COLORADO

## Slide 46: Geoid Slope Validation Survey
325 km
218 points
1.5 km apart
Austin
Rockport
Observe geoid shape (slope) using multiple independent terrestrial survey methods
  GPS + Leveling
  Deflections of the Vertical
Compare observed slopes (from terrestrial surveys) to modeled slopes (from gravimetry or satellites)
  With / Without new GRAV-D airborne gravity
Notes: But will this method produce a sufficiently accurate geoid?
This summer, we conducted an experiment to determine the accuracy of our geoid. We selected a line that extended 325 km from downtown Austin, Texas (North end) to Rockport, Texas (South end). There were 218 official survey points along the line, with an average spacing of 1.5 km between them. We compared the slope of the geoid along the line determined with GPS + leveling with deflections of the vertical as measured by the ETH Zurich DIADEM zenith camera. We also compared the observed geoid slope with slopes calculated from various geoid models to evaluate the their quality. As for NGS models, we tested geoids that both included and didn’t include new GRAV-D airborne gravity.

## Slide 47: Surveys Performed
GPS: 20 identical units, 10/day leapfrog, 40 hrs ea.
Leveling: 1st order, class II, digital barcode leveling
Gravity: FG-5 and A-10 anchors, 4 L/R in 2 teams
DoV: ETH Zurich DIADEM GPS & camera system
LIDAR: Riegl Q680i-D, 2 pt/m2 spacing, 0.5 km width
Imagery: Applanix 439 RGB DualCam, 5000’ AGL
Other: RTN, short-session GPS, extra gravity marks around Austin, gravity gradients

## Slide 48
GPS
DoV
Leveling
Gravity
LIDAR/
Imagery
Notes: These are just a small sampling of the field crews in action. Not shown are the RTN, FG-5, short-session GPS, relative gravity and mark setting crews.

## Slide 49: GSVS11 Results
Chart: Predicted Errors of various geoid models over GSVS11 after removal of GPS/Leveling error budget
| 0.4 - 15 | 15 - 30 | 30 - 46 | 46 - 63 | 63 - 81 | 81 - 101 | 101 - 122 | 122 - 145 | 145 - 172 | 172 - 204 | 204 - 247 | 247 - 325
USGG2009 | 0.87101 | 1.0601 | 1.364 | 1.665 | 1.8562 | 2.2611 | 2.5576 | 2.6428 | 2.8322 | 2.8066 | 2.4464 | 1.4332
EGM2008 | 0.87101 | 1.1721 | 1.5813 | 1.8794 | 1.9635 | 2.0475 | 2.1311 | 2.4299 | 2.6195 | 2.5918 | 2.774 | 1.9324
xEGM-G | 0.87101 | 1.2821 | 1.6884 | 2.091 | 2.491 | 2.7861 | 2.9768 | 2.9588 | 2.7261 | 2.1534 | 1.9962 | 2.618
xEGM-GA | 0.75409 | 0.82689 | 0.90587 | 0.98594 | 0.94092 | 1.021 | 1.1006 | 0.9134 | 0.67938 | 0.56322 | 0.80921 | 1.5634
xUSGG-GA-R-K480 | 0.75409 | 0.94538 | 1.025 | 1.1055 | 1.0655 | 1.1456 | 1.2253 | 0.9134 | 0.14682 | 0.29532 | 0.62034 | 1.1551
“1 cm geoid”
Geoids
without
GRAV-D
Geoids with
GRAV-D
xUSGG2011
Notes: This slide is a companion to the previous one, but the h-H errors have been removed, in an RMS sense, from the total h-H-N errors, leaving gravimetric geoid model errors only.
As seen previously, the geoids based on airborne gravity data are the best performers, and the very slight degradation using new high resolution software at short wavelengths is noticeably offset by the significant improvement at medium wavelengths.
In fact, as a general statement, it could be said that adding airborne gravity data to the gravimetric geoid model has yielded about 1 cm differential geoid undulation accuracy across all distances (orange and red bars), in the region of GSVS11, and that this can be further improved by continued improvement to the high resolution modeling software.

## Slide 50: GSVS – 2014 (Iowa)
Minimal Trees (GPS)
No major bridges/water crossings (Leveling)
Along roads (ease of access)
Mostly cloud-free nights
Under GRAV-D coverage (or will be)
With at least some existent bench marks/NAVD 88 level lines
A "significant enough" geoid slope to be interesting
For GSVS11, we wanted "low and flat" topography. For GSVS14 we'll want to step this up to "high and flat" or possibly "medium high, more-or-less flat and gravimetrically complex"
Denison, IA
Cedar Rapids, IA
Central Iowa
330 km
205 points

## Slide 51: GSVS17 Colorado
The third (and likely final) GSVS has taken place along US160, from Durango to Walsenburg, in southern Colorado.
High elevation and rugged topography. “Worst case” for geoid modeling.
Variation from 6,000’ (MSL) to 11,000’, over two passes.
12

## Slide 52
Estimated change in orthometric heights from NAVD 88 to NAPGD2022
NAPGD2022: North American Geopotential Datum of 2022
NAPGD2022 approximated using xGEOID16B

## Slide 54
Extent of 2022 gravimetric geoid model used for new geopotential reference frame

## Slide 55: New Reference Frames for U.S.

## Slide 57
Notes: https://www.youtube.com/playlist?list=PLsyDl_aqUTdFY6eKURmiCBBk-mP4R10Dx

## Slide 58: Details: Blueprint documents
Blueprint for 2022, Part 1: Geometric Coordinates
  A.K.A. NOAA Technical Report NOS NGS 62 (April 2017 release)
  Time-dependency
  Four terrestrial reference frames
  Intra-frame velocity models
Blueprint for 2022, Part 2: Geopotential Coordinates
  A.K.A. NOAA Technical Report NOS NGS 64 (September 2017 release)
  Time-dependency
  One geopotential datum
    Interrelated global geopotential model, regional geoid grids, regional DoV grids, regional surface gravity grids

## Slide 59: Scientific Decisions
Blueprint for 2022, Part 1: Geometric
  Four plate-fixed Terrestrial Reference Frames
    - And what “plate fixed” means
  Mathematical equation between IGS and TRFs
    - Plate Rotation Model for each plate
    - Coordinates at survey epoch
  Intra-frame velocity model
    - To compare coordinates surveyed at different epochs

## Slide 60: Names (Geometric)
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 61: Four Frames/Plates in 2022
Tectonic plates modeled by NGS
July 12, 2017
2017 Esri User Conference
13

## Slide 62: Euler Pole
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.
Euler's fixed point theorem states: any motion of a rigid body on the surface of a sphere may be represented as a rotation about an appropriately chosen rotation pole (“Euler Pole”)

## Slide 63: Non-Eulerian motions in the TRFs
Non-Eulerian motions at CORS
Note the obvious impact of the plate boundary in western CONUS
Note the non-zero nature of all vectors even in “stable North America”
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 64: Intra-frame velocities
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748
This is the velocity of the
point in ITRF. Includes all
movements, but the
dominant one is the
rotation of the N.A. Plate.
This is the velocity of the
point in NATRF2022.
Rotation of plate removed.
It is not constant because
the point still suffers small
“intra-frame” velocities.
Such IFVs will be captured
in a model by NGS.

## Slide 65: Scientific Decisions
Blueprint for 2022, Part 2: Geopotential
  Replace leveling based datums with a gravimetric geoid model
  Global 3-D Geopotential Model (GGM)
    - Will contain all GRAV-D data
    - Able to yield any physical value on/above surface
  Special high-resolution geoid, DoV and surface gravity products consistent with GGM
    - Not global: NA/Pacific, American Samoa, Guam/CNMI
  Time-Dependencies
    - Geoid monitoring service
    Heights will be determined using GNSS technology and the high resolution geoid

## Slide 66: Names (Vertical)
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 67
GEOID2022 (et al) over the North America/Pacific/Caribbean/Central America/Greenland region will range from 0 to 90 latitude and from 170 to 350 longitude.
GEOID2022 (et al) over Guam/CNMI:
11-22 latitude, 143-148 longitude
GEOID2022 (et al) over American Samoa:
-16 to -10 latitude, 186-193 longitude

## Slide 68: Preparing for New Reference Frames

## Slide 69: How to Plan for 2022
Move to newest realizations
  NAD 83(2011) epoch 2010.00
  GEOID12B (hybrid geoid)
Move to NAVD 88
  understand the accuracy of VERTCON in your area
Utilize passive marks that are up to date
  Stay aware of what marks are included in datum updates
  Use OPUS & Hgt. Mod procedures to update mark positions
Use OPUS for GPSBMs
  Help improve future geoid models & relationship with new datum
NGS Outreach Efforts
  Participate in NGS webinars, Geospatial summits, contact NGS Regional Advisor, etc.

## Slide 70: Metadata is Critical
Your positional metadata should include:
  datum
  epoch
  source / methods
These will facilitate transforming from current to new datum
Maintaining your original survey data will provide more accurate results
Notes: Metadata related to how someone establishes control is important. Important for today’s positions, but especially as we moving toward and into the coming new datums in 2022.

## Slide 71: GPS on Bench Marks
http://www.ngs.noaa.gov/heightmod/GPSonBM.shtml
2014 prioritized bench marks (needing GPS observations) by GEOID12A estimated accuracy, vertical order, stability, and distance from road
2017
Collaborating with NSPS for another Surveyors Week Campaign
NGS is making new maps of priority marks
NGS is making new associated materials to be ready in Feb. 2015
Becoming year-round campaign
Notes: Talk about the GPSBM efforts and how these OPUS – Share solutions are being used to help improve the hybrid geoid models.

## Slide 72: What is “GPS on Bench Marks (GPSBM)?
Collecting GPS observations on a bench mark that has an NGS published orthometric height from leveling. This will provide updated (accurate) information for:
Latitude, longitude, and ellipsoid height
* GPSBM submittals are made through the OPUS – Share service.

## Slide 73: Benefits of GPS on BM (Users)
- Improve coming hybrid geoid model
- Improve transformation tool for new geopotential datum (vertical) in 2022
- Maintenance of ground mark network

## Slide 74: OPUS Share Service
Notes: Metadata related to how someone establishes control is important. Important for today’s positions, but especially as we moving toward and into the coming new datums in 2022.

## Slide 75
Notes: Many of these users also sit on the Federal Geodetic Control Subcommittee, so there is a feedback loop between the providers of geodetic control (NGS) and the users of that control.

## Slide 76
Notes: Subscriber service, webinar series, videos, NSRS Newsletter

## Slide 77
  Four-part series
The first part, covering the NGS Ten Year Plan, OPUS-DB, OPUS-Projects, and Foundation CORS appeared in the January 2015 issue.
Find this article at:
http://www.amerisurv.com/content/view/13361/153/

## Slide 78: Update on NGS Products

## Slide 79: NADCON - Historical Overview
1989 : NAD 83(1986) released
  1990: NADCON v1.0 released: NAD27 <--> NAD83 (86)
  1990-1997: NADCON v2.1 NAD27 <--> NAD83 (HARN)
  DOS based program, PC based
  1997-2005: NADCON v2.1 NAD27 <--> NAD83 (HARN / FBN)
          Only 19 states had significant shifts from HARN to FBN
          Program expanded to handle FBN changes
          Program still DOS / PC based
  2004: NADCON v4.2 SAME TRANSFORMATIONS
          Efforts made to improve NADCON, JAVA based / Windows driven menus
          Program expanded to handle FBN changes

## Slide 80: Historical Overview Cont.
  2007: GEOCON v1.0 NAD83 (HARN / FBN) <--> NAD83 (2007)
          Transformations from last NAD83, pre-2007 epoch
          Program expanded to provide ability of on-line computations
          Program built for transformations to be relative to “national” adjustment
  2011: GEOCON11 v1.0 NAD83 (2007) <--> NAD83 (2011)
          GEOCON expanded to go with latest NAD83 adjustment
          Program expanded to provide ability of on-line computations
  2012: GEOCON & 11 v1.0 SAME TRANSFORMATIONS
          Program improvements / bug fixes
  2012: GEOCON v2.0 SAME TRANSFORMATIONS
          One combined “GEOCON” program
          HARN & FBN Adjustment results accounted for on state by state basis
          2007 & 2011 Nationwide

## Slide 81: Historical Overview: Problems
Multiple DOS based programs
Lack of documentation
Inconsistent decision making
  Accuracy reporting
  State vs nationwide grids
  Skipping over transformations
“Missteps” made by NGS…
    Too many to list, can read in the report.

## Slide 82: What is NADCON v5.0?
How?
Fresh pull of IDB
New suite of analysis tools
New grids from scratch
No realizations skipped
Make available through Geodetic Toolkit
Transformations and error estimates for any point within a regional boundary, provided through biquadratic interpolation off of a grid
Lat/lon in arcseconds
Ellipsoidal height in meters

## Slide 83: NADCON 5 in the Geodetic Toolkit
CURRENTLY
IN
BETA

## Slide 84
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
X, Y, Z
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83

## Slide 85
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 86
It will “hold” everything.
  GNSS, leveling, gravity, DoV, etc.
  CORS and surveys
  Equipment descriptions & histories, site logs, etc.
  Models
  Guidelines & strategies
It’s a tool, not just an archive of results.
  Searches and filters.
  Statistics
  Plots
  Reports
  - Database will enable ability to track position changes over time
New NGS Database

## Slide 87
It’s common for projects to collect several types of data, e.g. gravity&GNSS, leveling&GNSS, static&kinematic GNSS. They’re related so let’s not treat them as separate.
OPUS-for-everything is a working name for a proposed web app to consolidate and process all data from a project.
“Feeding” the database.

## Slide 88
Improved view and features for session / marks table.
Changes to how OPUS Projects defines sessions.
Ability to Add / Delete CORS
Better baseline processing.
Adjustments using NGS software ADJUST.
Auto creation of B-file & G-file.
OPUS-Projects – new Bluebooking features

## Slide 89
? ? QUESTIONS ? ?