# Harbor Beach, Lake Huron

Host organization: Sensient Flavors Inc.

Contact: Plant Manager: James A. Tenbusch

Tel: 989-479-3034

Fax: 989-479-3320

Email: jim.tenbusch@sensient-tech.com

Address: 79 State St.

Harbor Beach, MI 48441-1255

Direction: From the intersection of State St. (Hwy M142) and North Huron Ave (Hwy M25), go east on State St. through the gate at the industrial area, then past the white building to the second set of gates.  The gauge house is through those gates on the north side of the peninsula.  Permission to access the area is required and can be given from the guard shack found north of the State St. and North Huron Ave intersection.  The guard shack is on the right about 1 block north on North Huron Ave.

Notes:

- Tide gauge house looks in good shape and clean both inside and out.

- Plenty of room for a 5-½ ft shelf for equipment along with another 3-½ ft on lower shelf.

- No concrete pillar can be installed due to ground fill.

- GPS antenna can be installed on the brick wall of the gauge house – the brick wall goes down to the foundation (foundation looks in a very good condition.)

- Antenna cable will be no longer than 50ft.

- If we do not use the wireless Internet we can share the existing phone line, or to have another phone line installed.

- The plant manager is willing to let NOAA use their computer room for the equipment along with providing us with a network connection. Additional phone line installation is required if we need one.

- Needs to send a letter to the Manager for his and company’s approval.

- If we use the wireless network/serial units we may have to buy a repeater – there is a building between the water gauge house and the plant’s building housing computer room. This middle building is a little bit higher than we want. A network communication test will help us to decide on this repeater issue.

- Needs batteries and power inverter.