## Slide 1
Modernizing the National Spatial Reference System
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
BLUF
What?
Why?
How?

## Slide 3: Bottom Line, Up Front
If you do geospatial work in the USA…
and you work in the National Spatial Reference System..
every product you’ve ever made…
  every survey…
  every map…
  every lidar point cloud…
  every image…
  every DEM…
  WILL have the wrong coordinates on it in 4 years.
  Let’s talk about what this means, why it is happening, and how it will affect things going forward

## Slide 4: What…
…is NGS?
…is the NSRS?
…is not the NSRS?

## Slide 5: National Geodetic Survey
U.S. Government/Executive Branch
  Department of Commerce
    National Oceanic and Atmospheric Administration
      National Ocean Service
        National Geodetic Survey
The government’s oldest scientific agency
  Survey of the Coast (1807)
  Coast Survey (1836)
  Coast and Geodetic Survey (1878)
  National Geodetic Survey (1970)

## Slide 6: NGS mission
To define, maintain, and provide access to the National Spatial Reference System to meet our nation’s economic, social, and environmental needs
Notes: Our mission statement is widely available on various NGS web pages. But how did we get here?

## Slide 7: The National Spatial Reference System (NSRS)
Coordinate system
  Latitude, Longitude, Height, etc
  Projected coordinates too:
    UTM
    State Plane
    U.S. National Grid
Federal civilian agencies – mandated
  Lots of other users too

## Slide 9: NGS and the NSRS – legal context
OMB A-16:
  Requires all federal civilian geospatial agencies to use geodetic control
  Puts DOC/NOAA (=NGS) in charge of that control
  NGS has defined that control as the NSRS
  FGCS has issued requirements via FRNs to use the most recent components of the NSRS
    1989: NAD 83
    1993: NAVD 88
    2009: ASVD02, NMVD03, GUVD04
    2011: VIVD09
    2012: PRVD02

## Slide 10: NGS and the NSRS – legal context
FGCS requirements do not apply to:
  Military/Intelligence federal agencies
  State and local governments
  Private individuals and companies
But these groups often do adopt all or part of the NSRS to be compatible with most federal geospatial data
  Could lead to mixing NSRS and non-NSRS information.
    Fine, but has to be done right.

## Slide 11: So what is and is not the NSRS?
If NGS (or its predecessors*) did not make it, it is not in the NSRS**
* Survey of the Coast (1807-1836)
Coast Survey (1836-1878)
Coast and Geodetic Survey (1878-1970)
** The term “NSRS” was adopted in 1994, but today is used to encompasses all historic datums of NGS and its predecessors, though the FGCS regularly adopts the latest components

## Slide 12: These are part of the NSRS
Hor Datums / Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations / Conversions
USSD | NGVD 29 | IGLD55 | GEOID90 | NADCON
NAD 27 | NAVD 88 | IGLD85 | GEOID93 | VERTCON
NAD 83 | PRVD02 |  | ALASKA94 | 
 | ASVD02 |  | GEOID96 | SPCS 27
 | NMVD03 |  | GEOID99 | SPCS 83
 | GUVD04 |  | GEOID03 | 
 | VIVD09 |  | GEOID06 | 
 |  |  | GEOID09 | 
 |  |  | GEOID12(A,B) | 
These are select entries, not a complete list

## Slide 13: These are not part of the NSRS
Hor Datums / Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations / Conversions
WGS 84 | IHRS |  | OSU91A | CORPSCON
ITRF |  |  | EGM96 | Appendix B.6 of DMA TR 8350.2 (WGS 84)
IGS |  |  | EGM2008 | Oregon Coordinate Reference System
 |  |  |  | The Kansas Regional Coordinate System
These are select entries, not a complete list

## Slide 14: Mixing NSRS and non-NSRS?
Just do it right
Right:
  The Oregon CRS has a mathematically defined relationship to the NSRS
Wrong:
  “WGS 84 is the same as NAD 83”
  “WGS 84 is the same as the ITRF”
  “Sub-meter accuracy is possible using WGS 84”
    Such statements gloss over critical facts about history, accuracy and application

## Slide 15: Accuracy
Consider your users’ accuracy needs
  3 Meters?
    Then WGS 84 is NAD 83
    Global 14 parameter transformations will suffice
  3 Decimeters?
    Then NAD 83(2011) is NAD 83(NSRS2007)
      But NAD 83(1986) is not the same as NAD 83(HARN)
    NADCON will suffice as a transformation
  3 Centimeters?
    Every detail matters

## Slide 16: Why…
…is NGS modernizing the NSRS?

## Slide 17: Drivers of change
The current NSRS has issues:
  Non-geocentricity of ellipsoid
  Outdated geoid as the zero height surface
  Does not account for time change
    These first 3 are larger than available positioning accuracy today and can not be “hidden in the noise”
  Significant dependence upon passive marks
More details available in Appendix A of the proceedings of the 2010 Geospatial Summit:
  https://www.ngs.noaa.gov/library/pdfs/SP_NOS_NGS_10.pdf

## Slide 18: NAD 83’s non-geocentricity
~2.2 m
NAD 83 origin
IGS14 origin
Earth’s Surface
hNAD83
hIGS14
fNAD83 – fIGS14
lNAD83 – lIGS14
hNAD83 – hIGS14
all vary
smoothly by latitude
and longitude
same
GRS-80
ellipsoid

## Slide 19: Effect upon latitude/longitude

## Slide 20: Non-Geocentricity: Latitude

## Slide 21: Non-Geocentricity: Longitude

## Slide 22: Non-Geocentricity: Ellipsoid Height

## Slide 23: Outdated geoid
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface:

## Slide 24
Watch the grid!
Time Changes - Horizontal

## Slide 25: Time-Dependency
The IGS14 frame is not beholden to any tectonic plate
  Thus the four plates with U.S. populations will have time-dependent latitudes/longitudes:
    North America: 1-3 cm / year (CONUS, Alaska)
    Pacific: 7-8 cm / year (Hawaii, AS)
    Caribbean: 1-2 cm / year (PR, USVI)
    Mariana: 1-4 cm / year (Guam, CNMI)

## Slide 26: Change to lat/lon every year

## Slide 27: Time Changes - Vertical
Crust uplifts and subsides
  Wide variety of spatial and temporal scales
  GIA is uplifting much of the North half of CONUS
  Agricultural water withdrawal subsides the crust (see left)
  Etc

## Slide 28: Passive Control
The NSRS suffers from use of passive control marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
PID: EZ0840

## Slide 29: How…
…will NGS modernize the NSRS?
…will this affect me?

## Slide 30
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
Sep 2017
Geopotential:
Nov 2017
Working in the
modernized NSRS:
May 2019

## Slide 31: “Modernizing the NSRS” means…
Replacing NAD 83
Replacing NAVD 88
Re-inventing Bluebooking
Improving the Geodetic Toolkit
Better Surveying Methodologies
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 32
Latitude, Longitude
& Ellipsoid Heights

## Slide 33: Replacing the NAD 83’s
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 34: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Fixed: NAD 83 isn’t geocentric
Fixed: NAD 83 doesn’t rotate properly with its plates
Method: Define each of the 4 new frames equal to IGS14 @ 2020
  Define each frame’s movement by a plate rotation only
  Put another way: “The frame rotates so your coordinates don’t have to”

## Slide 35
Time “t ” when
all four TRFs and
IGS14 are identical.
(2020.0)
0
MATRF2022
MATRF2022
Rotation of Mariana Plate
t=t + Dt
(“the future”)
0
t=t - Dt
(“the past”)
0
CATRF2022
CATRF2022
NATRF2022
PATRF2022
NATRF2022
PATRF2022
Rotation of Caribbean Plate
IGS14 frame through time
IGS14 frame
IGS14 frame
Rotation of Pacific Plate
Rotation of North American Plate
The relation of five global reference
frames through time.
Rotations are not to scale

## Slide 36
What does it mean to provide time-dependent coordinates in 5 frames?

## Slide 37: BSMK (North Dakota)

## Slide 38: BSMK (North Dakota)
NATRF2022 Latitude is CONSTANT over time
As per NGS policy decision circa 2018:
t0 = 2020.0

## Slide 39: BSMK (North Dakota)
NATRF2022 Longitude is constant over time

## Slide 40: BSMK (North Dakota)
No matter WHAT frame, the ellipsoid height is dropping over time

## Slide 41: PIN1 (S. California)

## Slide 42: PIN1 (S. California)
Latitude in NATRF2022 and PATRF2022 change over time

## Slide 43: PIN1 (S. California)
Longitude in NATRF2022 and PATRF2022 change over time

## Slide 44: PIN1 (S. California)
No matter WHAT frame, the ellipsoid height is rising over time

## Slide 45: CORS Velocities – IGS08

## Slide 46: CORS Velocities – NATRF2022

## Slide 47: CORS Velocities – PATRF2022

## Slide 48: CORS Velocities – NAD 83(2011)

## Slide 49
Orthometric Heights
(“Sea Level Heights”) and other
gravity-related quantities

## Slide 50: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 51: Geopotential Basics
Why isn’t this a vertical datum?
  Because it contains more than heights
    And therefore NGS wants to be accurate in its name

## Slide 52: Expected changes to orthometric heights

## Slide 53: Expected changes to orthometric heights

## Slide 54: Definitional Relationship
Time-dependent ellipsoid heights
come from time-dependent
CORS coordinates which serve as control for your time-dependent GNSS survey.
They will be modeled in the IFVM
Time-dependent geoid undulations
are modeled in the dynamic component of GEOID2022 (“DGEOID2022”), which will come from the geoid monitoring service, or GeMS.

## Slide 55: Geoid Monitoring Service
Goal: Track all changes to the geoid which would prevent 1 cm accuracy
Three major aspects:
  Secular Shape: Hudson Bay
  Episodic Shape: Massive Earthquakes
  Geoid relation to Sea level: Global Sea Level Change

## Slide 56: Secular Mass Movement
Notes: There are two manifestations of the growing mass in the deep mantle under Hudson Bay:
Geometric – a GPS receiver will see the crust uplifting as the increase in mantle mass pushes the crust up in a displacement.
Geopotential – a gravimeter on the surface will sense the growing mass as an increase in the acceleration of gravity, BUT this will be slightly tempered by a reduction in gravity as well (because the gravimeter on the surface is getting farther from the Earth’s center). Still, the gain (from mass increase) is larger than the loss (from geometric movement) for a net gain. Because the net gain in gravity is not caused purely by being at a new crustal height, this translates into an increase in geoid undulations, or a “swelling” of the geoid in this region.
This is different than a purely geometric change caused by a compression of the crust. In that case, no significant mass is entering or leaving the region so, while GPS might sense a subsidence and a surface gravimeter might sense a slight increase as it moves closer to the Earth’s center, the geoid would not actually change.

## Slide 57: High resolution products
GEOID2022
  Official converter of *TRF2022 ellipsoid heights into NAPGD2022 orthometric heights
DEFLEC2022
  Surface deflections of the vertical in N/S and E/W
GRAV2022
  Surface acceleration of gravity
DEM2022
  Official DEM used in creation of all above products
All will be 1 x 1 arcminute grids
All will cover three finite regions of the globe
All will have a static and dynamic component
  Dynamic surface gravity and DEM not expected to be ready by 2022

## Slide 58: The three gridded regions
“North American region”
¼ of the Earth
“Guam/CNMI region”
“American Samoa region”

## Slide 59
Converting NAD 83 and NAVD 88
geospatial data into
NATRF2022/PATRF2022/
CATRF2022/MATRF2022
and NAPGD2022

## Slide 60: Two options: NCAT and VDatum
Currently semi-independent programs
Being merged behind the scenes when calling identical routines, such as “NADCON 5.0”
  NCAT will remain “purely geodetic”
  VDatum will be “NCAT plus tidal datums”
Both will get “VERTCON 3.0” in late 2018
Both will run in 3 modes:
  Web services, Browser interactive, Downloadable

## Slide 61: NGS Coordinate Conversion and Transformation Tool (NCAT)
Now with
NADCON 5!
www.ngs.noaa.gov/NCAT/

## Slide 62: VDatum
vdatum.noaa.gov

## Slide 63: Thank you!

## Slide 64: Questions? FYI: ASPRS/ILMF will hold a panel session on modernizing the NSRS Denver, January 28-30