## Slide 1
NGS Update: 2022 Datums and Related Products
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
NSRS 2022 Overview Workshop
Florida Dept. of Environmental Protection
Tallahassee, FL
December 5, 2019

## Slide 2: U.S. Department of Commerce National Oceanic & Atmospheric Administration National Geodetic Survey
Mission: To define, maintain & provide access to the
National Spatial Reference System (NSRS)
to meet our Nation’s economic, social & environmental needs
National Spatial Reference System
* Latitude * Scale
* Longitude * Gravity
* Height * Orientation
& their variations in time
Notes: - NSRS benefit to the nation = $2.5B/year
est. 300K precision GPS users worldwide (2008); ¼ in US
- Very exciting to us at NGS to see how it has evolved over the years – now cm-accuracy capability / tracking with time

## Slide 3: New U.S. Geometric Datums in 2022

## Slide 4: National Spatial Reference System(NSRS) Improvements in the Horizontal Datums
TIME NETWORK METHOD
NETWORK SPAN ACCURACY OF REFERENCE
NAD 27 1927-1986 10 meter
NAD83(86) 1986-1990 1 meter
NAD83(199x)* 1990-2007 0.1 meter
HARN
NAD83(2007) 2007 - 2011 0.01 meter
(CORS)
NAD83(2011) 2011 - 2022 0.01 meter
(CORS)
TRAVERSE & TRIANGULATION -
GROUND MARKS USED FOR REFERENCING THE NSRS.
GPS BECOMES MEANS OF POSITIONING – STILL GRND MARKS.
GPS – CORS STATIONS ARE MEANS OF REFERENCE FOR THE NSRS.
TERRESTRIAL BASED
REFERENCE SYSTEM
FOR NSRS
TERRESTRIAL BASED REFERENCED
SYSTEM FOR NSRS
SPACE BASED
REFERENCE SYSTEM
FOR NSRS

## Slide 5
NSRS Reference Basis
Old Method - Ground
Marks (Terrestrial)

## Slide 6
NSRS Reference Basis
New Method - GNSS Stations
(CORS)

## Slide 7: NSRS “Geometric Constraints” CORS
* Stations shown for
concept purposes only.

## Slide 8
Datum based on best known information about the earth’s size and shape from the early 1980’s (≈40 years old), and the terrestrial survey data of the time.
NAD83 is NON-geocentric & hence inconsistent w/GNSS .
Why Replace NAD83?
NAD83 is now ≈2.2 m. off from currently know mass center of earth
Replacement is necessary for agreement with current / future capabilities of GNSS positioning.

## Slide 10: Future Geometric (3-D) Reference Frame
Blueprint for 2022: Part 1 – Geometric Datum
Replace NAD83 with new geometric reference frame – by 2022.
CORS-based, accessed via GNSS observations.
Coordinates & velocities in ITRF (IGS) & new US reference frame.
      (coordinates in time) (stable coordinates)
  Transformation tools will relate NAD83 to new US reference frame (NCAT with 2022 transformation).

## Slide 11: Datum Names
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 12: Four Frames/Plates in 2022
Tectonic plates modeled by NGS
July 12, 2017
2017 Esri User Conference
13

## Slide 13
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.
NSRS Plate Rotation Modeling
EULER Pole
13

## Slide 14: CORS Velocities – IGS08
Crustal motion to be removed by Intra Frame Velocity Models for each TRF.
Notes: These velocities were arrived at by taking IGS08 velocities and removing the 3 parameter Euler Pole rotation of the North American plate as currently known (ITRF08 plate motion model).
These residual velocities will then be modeled into the IFVM for NATRF2022

## Slide 15
New geometric datum minus NAD 83 (horizontal)
For Florida = 0.8 > 1.02 m (2.6 > 3.3 ft.)
NATRF2022

## Slide 16
NATRF2022
For Florida = -1.39 > -1.62 m (-4.5 > -5.3 ft.)

## Slide 17: Geometric Position Epochs

## Slide 18
NGS OPUS SOLUTION REPORT
Geometric Position Epochs

## Slide 19: New U.S. Vertical Datum in 2022

## Slide 20
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Were determined by leveling from a single point, allowing cross-country error build up
Why isn’t NAVD 88 good enough anymore?
* NAVD 88 is a terrestrial based vertical datum that changes as the land changes.

## Slide 22
Long term fix: Re-level some/all of NAVD 88
  81,500 km of 1st order leveling at least
  625,000 km of mixed 1st and 2nd order leveling
Re-leveling NAVD 88 estimated to cost between
  $200 Million and $2 Billion
Time factor in that amount of leveling
Still would have problems related to passive control
Can NAVD 88 be fixed?
Notes: Re-leveling NAVD 88 won’t fix:
Sparseness of the bench marks
Continued subsidence or uplift of bench marks
Destruction of bench marks
Canada’s decision not to adopt NAVD 88
Whatever errors caused a continent-wide 1 meter build up in the leveling the first time around

## Slide 24: NEW VERTICAL DATUM (Rationale)
  A move away from differentially leveled passive control as the defining mechanism of the reference surface
  To be consistent with the shift in the geometric reference frame/ellipsoid (2022)
  Improvement in our technical abilities in reference surface realization (geopotential gravimetric reference surface - 1cm accuracy of the geoid (GNSS/GRAV-D))
  Goal - ability to establish 2cm orthometric height anywhere in U.S. using a minimum of 15 min. of GNSS data.
  The new geopotential reference surface will be aligned with the geometric reference frame/ellipsoid (i.e., no hybrid geoid)

## Slide 25: Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
  The New:
  The North American-Pacific
  Geopotential Datum of 2022
  (NAPGD2022)
  - Will include:
  GEOID2022
  DEFLEC2022
  GRAV2022
  DEM2022

## Slide 26
Building a Gravity Field
Long Wavelengths
(≥ 250 km)
GRACE/GOCE/Satellite Altimetry
Intermediate Wavelengths
(500 km to 20 km)
Airborne Measurement
Surface Measurement and
Predicted Gravity from Topography
Short Wavelengths
(< 100 km)
+
+
Notes: Give example of how short wavelength information is like low altitude aerial photos (1/2” pixel accuracy) in that it provides very accurate and detailed information. The long wavelength gravity can be likened to the old LANDSAT imagery (3 meter pixel accuracy) in that it was good over large areas, but didn’t give much detail for local areas. The intermediate wavelength gravity data gives us a connection between the two (the short and long), allowing the NGS gravity team to use all available gravity information in working toward the production of a 1 cm accurate gravitational surface.

## Slide 27
Replace the Vertical Datum of the USA by 2022 (at today’s funding)
GRAV-D is:
  An airborne gravity survey of the entire country and its holdings
  A 2022 gravimetric geoid accurate to 1 cm
  Long-term monitoring of geoid change over time
  Partnership surveys
Working to launch a collaborative effort with the USGS for simultaneous magnetic measurement
Acting Manager: Jeffery Johnson
Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
Gravity and Heights are
inseparably connected
Notes: GRAV-D is the NGS project designed to replace NAVD88 with a vertical datum based upon a gravimetric geoid accurate to 1 cm. Heights above this datum will be accessed via GNSS measurements. Three thrusts of project. Launch USGS collaboration for simultaneous mag measurement.

## Slide 28: Survey and Block Plans
Data lines spaced 10 km apart.
Cross lines spaced 60-80 km apart.
Flight lines run 100-150 km offshore.
Flight altitude 20,000 ft.
Nominal speed 220-250 knots.
Notes: Block layout based on aircraft, adjust size of block if needed

## Slide 29: GRAV-D Status - Over 79% Complete (Oct. 2019)

## Slide 30: Geoid Monitoring Service (GeMS)
Goal: Track all changes to the geoid which would prevent 1 cm accuracy
Aspects included:
  Shape, Secular: e.g. Hudson Bay
  Shape, Episodic: e.g. Massive Earthquakes
  W0, Secular: Global Sea Level Change (see next slides)
Examples of things excluded:
  Size, Secular: Mass quantity of Earth is effectively static
  Shape, Periodic: Seasonal glacier cycle

## Slide 31
Extent of 2022 gravimetric geoid model used for NAPGD2022

## Slide 32: Expected changes to orthometric heights – NAVD88 to NAPGD2022
For Florida = 0.1 > -0.3 m (4 > -11 in.)

## Slide 35: How to Plan for 2022
Move to newest realizations
  NAD 83(2011) epoch 2010.00
  GEOID12B (hybrid geoid)
Move to NAVD 88
  understand the accuracy of VERTCON in your area
Utilize passive marks that are up to date
  Stay aware of what marks are included in datum updates
  Use OPUS & Hgt. Mod procedures to update mark positions
Metadata
  Document positions in current datums to know what you have in the future.
NGS Outreach Efforts
  Participate in NGS webinars, Geospatial summits, contact NGS Regional Advisor, etc.
GEOID 18 (hybrid geoid)

## Slide 36: NGS Products Update Coordinate Conversion and Transformation Tool – NCAT using NADCON v5.0

## Slide 37: NGS Products Update - NCAT

## Slide 38: NGS Products Update - NCAT

## Slide 39
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022
NADCON
GEOCON
GEOCON 11

## Slide 40
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022
NCAT (NADCON 5)

## Slide 41: NGS GPS on BM Project (2022 Transformation Model)

## Slide 42: GPSonBM Lives On
The 2022 Transformation Tool Campaign
NGS’ GPSonBM program is now requesting data to build the models that NCAT and VDatum will use to transform data from existing datums to the new datums in 2022.
NCAT
VDatum

## Slide 43: 2022 Transformation Tool Campaign Goals
NGS will make a national scale, mapping grade transformation tool with the data we have in the NGS Database or Shared through OPUS
To produce transformation results with an reasonable amount of uncertainty, NGS has a goal of GPSonBM data at 10 km spacing
We must interpolate over areas with data gaps
Uncertainties in the transformed coordinates will grow larger as the distance from a GPSonBM data point increases
Opportunity exists to densify local areas with data at up to 2 km spacing to increase accuracy and better resolve complex areas with topographic relief

## Slide 44: Search, Measure, Bookmarks, Export Selected Lists, more…

## Slide 47
New Mark Recovery Webpage
Submitting recovery information will let NGS and others know if the mark is still usable and pictures will make it easier to find.
www.ngs.noaa.gov/surveys/mark-recovery

## Slide 48
Share GPS observations through OPUS
Upload 4+hour GPS observation file
Provide antenna type, antenna height, and email address
Select “Yes, Share”
Identify the Mark by PID
Write a “To Reach” description
Attach 2 photos: Close up & Horizon
Respond to confirmation email

## Slide 49
ARP
mark
rotate NRP to face true north
antenna height
JGE, 2015
For antenna calibrations, photos, ARP and NRP diagrams, see geodesy.noaa.gov/ANTCAL/
Antenna Type & Antenna Height are crucial for accurate results
Each Antenna Type has unique biases

## Slide 50
? ? QUESTIONS ? ?
Denis.Riordan@noaa.gov