## Slide 1: State Plane 2022 Where Things Stand and the Road Ahead
December 9, 2021
Michael L. Dennis, PhD, RLS, PE
SPCS2022 Project Manager

## Slide 2
SURVEYORS
projected
coordinate systems
REAL GEODESISTS
…don’t use projected
coordinate systems

## Slide 3: The stuff of geodesist nightmares…

## Slide 4: A “flat Earth” for the future
State Plane Coordinate System of 2022 (SPCS2022)
Referenced to 2022 Terrestrial Reference Frames
Same reference ellipsoid as SPCS 83 (GRS 80)
Same 3 projection types as SPCS 83 and 27:
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 5: Previous NGS State Plane webinars
State Plane Coordinate System (May 5, 2021, at Geospatial Summit)
State Plane 2022: The Shape of Things to Come (June 11, 2020)
Be a Part of the Change: A Guide to Customizing State Plane for 2022 (October 10, 2019)
The State Plane Coordinate System of 2022: Making It Your Way (May 6, 2019, at Geospatial Summit)
State Plane Coordinate System Update (March 7, 2019)
Building a State Plane Coordinate System for the Future (April 12, 2018)
The State Plane Coordinate System: History, Policy, Future Directions (March 8, 2018)

## Slide 6: Poll Question
Which of the previous seven State Plane webinars have you attended?
418 of 604 attendees responded

## Slide 7: Poll Question
Are you associated with any of the following SPCS2022 stakeholder groups in your state? (select all that apply)
427 of 604 attendees responded

## Slide 8: Getting acquainted with SPCS2022
Distortion design philosophy
  Linear distortion minimized at topographic surface (not at ellipsoid surface)
  Purpose: to reduce difference between projected “grid” and actual “ground” distances
Other things:
  Zone “layers”
  Low distortion projections (LDPs)
  Status and performance of zone designs
  The timing of it all…

## Slide 9: SPCS2022 “layers” and designs
Max of up to 3 zone “layers” allowed
  One must be statewide zone
  Most states will have total of 2 layers
NGS designs:
  Statewide zone for every state
  Multiple zones not designed by stakeholders
Many states made requests and proposals
  Requests for zones designed by NGS
  Proposals for zones designed by stakeholders

## Slide 10
State Plane Coordinate System of 2022 (968 zones in 56 states and territories)

## Slide 12: Status of zone layout and designs
Designs by NGS
  159 zones (including 54 statewide)
  Range from 1 to 22 zones per state (max in Alaska)
  Plus 3 “special use zones” (in more than one state)
Designs by state stakeholders
  806 zones in 28 states
  Range from 1 to 88 zones per layer (max in Ohio)
Total = 968 zones for 56 states and territories
  Number may decrease, but will not increase

## Slide 15
Map projection linear distortion
Ellipsoid surface (~“sea level”)
Topographic surface
Grid (“map”) distance
Projection surface
Horizontal ground distance
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
Grid distance < ground distance
Map projection designed to minimize linear distortion on ellipsoid (at “sea level”)

## Slide 16
Map projection linear distortion
Projection surface
Map projection designed to minimize linear distortion at ground surface
Topographic surface
This design approach is used for SPCS2022 (minimizes distortion with respect to topography)
Ellipsoid surface (~“sea level”)
Grid distance ≈ ground distance

## Slide 17: Linear distortion performance
Cause of distortion can be split into 2 types:
  Distortion due to Earth curvature
  Distortion due to change in ellipsoid height
Both types contribute to total distortion
  Curvature: increases with square of zone width
  Height: increases linearly with change in height
Distortion may be low outside zone boundary
  Can use a zone beyond its bounding polygon
  It’s OK to “color outside the lines”

## Slide 18: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio
20 ppm | 2 cm/km | 0.1 ft/mile | 1:50,000
50 ppm | 5 cm/km | 0.3 ft/mile | 1:20,000
100 ppm | 10 cm/km | 0.5 ft/mile | 1:10,000
400 ppm | 40 cm/km | 2.1 ft/mile | 1:2,500

## Slide 19: SPCS2022 zones designed by NGS
Linear distortion design criterion
  e.g., ±20, ±50, ±100, ±400 ppm, etc.
Criterion must satisfy at least all of following:
  90% of population
  75% of all cities and towns (by location only)
  50% of entire zone area
Limitations for designs by NGS
  Minimum design criterion ±50 ppm (1:20,000)
  May be less if existing zone small
Low distortion projections (LDPs)
  Must be designed by others for distortion < ±50 ppm

## Slide 20: Low distortion projections (LDPs)
What is an LDP?
  Projection “grid” and “ground” distance nearly same
  For SPCS2022, distortion < ±50 ppm (±0.3 ft/mile)
  Common criterion is ±20 ppm (±0.1 ft/mile)
SPCS2022 includes LDPs
  Designed by stakeholders
  Coverage can be complete or partial (discontinuous)
Minimum zone width
  50 km (31 miles) if height range <= 250 m
  10 km (6 miles) if height range > 250 m

## Slide 21
49 zones
Distortion increment 400 ppm (1:2,500 = 2.11 ft/mile)
Percent area within:
±20 ppm = 7%
±50 ppm = 18%
±100 ppm = 36%
±400 ppm = 88%

## Slide 22
49 zones
Distortion increment 100 ppm (1:10,000 = 0.53 ft/mile)
Percent area within:
±20 ppm = 7%
±50 ppm = 18%
±100 ppm = 36%
±400 ppm = 88%

## Slide 23
106 zones
Distortion increment 100 ppm (1:10,000 = 0.53 ft/mile)

## Slide 24
107 zones
Distortion increment 100 ppm (1:10,000 = 0.53 ft/mile)

## Slide 25
106 zones
Distortion increment 100 ppm (1:10,000 = 0.53 ft/mile)
Percent area within:
±20 ppm = 6%
±50 ppm = 17%
±100 ppm = 41%
±400 ppm = 91%

## Slide 26
49 zones
Distortion increment 100 ppm (1:10,000 = 0.53 ft/mile)
Percent area within:
±20 ppm = 7%
±50 ppm = 18%
±100 ppm = 36%
±400 ppm = 88%

## Slide 27
49 zones
Distortion increment 50 ppm (1:20,000 = 0.26 ft/mile)
Percent area within:
±20 ppm = 7%
±50 ppm = 18%
±100 ppm = 36%
±400 ppm = 88%

## Slide 28
65 zones in 16 states
Distortion increment 50 ppm (1:20,000 = 0.26 ft/mile)
Percent area within:
±20 ppm = 26%
±50 ppm = 53%
±100 ppm = 79%
±400 ppm = 99.8%

## Slide 29
581 zones in 19 states
Distortion increment 50 ppm (1:20,000 = 0.26 ft/mile)
Percent area within:
±20 ppm = 84%
±50 ppm = 95%
±100 ppm = 98%
±400 ppm = 100%

## Slide 30
646 zones in 35 states
Distortion increment 50 ppm (1:20,000 = 0.26 ft/mile)
Percent area within:
±20 ppm = 54%
±50 ppm = 73%
±100 ppm = 89%
±400 ppm = 99.9%

## Slide 31
660 zones
Distortion increment 50 ppm (1:20,000 = 0.26 ft/mile)
Percent area within:
±20 ppm = 50%
±50 ppm = 69%
±100 ppm = 85%
±400 ppm = 99.7%

## Slide 32
660 zones
Distortion increment 20 ppm (1:50,000 = 0.11 ft/mile)
Percent area within:
±20 ppm = 50%
±50 ppm = 69%
±100 ppm = 85%
±400 ppm = 99.7%

## Slide 33
187 zones in 10 states
Distortion increment 20 ppm (1:50,000 = 0.11 ft/mile)
Percent area within:
±20 ppm = 73%
±50 ppm = 88%
±100 ppm = 97%
±400 ppm = 100%

## Slide 34
660 zones
Distortion increment 20 ppm (1:50,000 = 0.11 ft/mile)
Percent area within:
±20 ppm = 50%
±50 ppm = 69%
±100 ppm = 85%
±400 ppm = 99.7%

## Slide 35
846 zones
Distortion increment 20 ppm (1:50,000 = 0.11 ft/mile)
Percent area within:
±20 ppm = 58%
±50 ppm = 76%
±100 ppm = 89%
±400 ppm = 99.9%

## Slide 36
846 zones
Distortion increment 50 ppm (1:20,000 = 0.26 ft/mile)
Percent area within:
±20 ppm = 58%
±50 ppm = 76%
±100 ppm = 89%
±400 ppm = 99.9%

## Slide 37
Distortion increment 50 ppm (1:20,000 = 0.26 ft/mile)
106 zones
Percent area within:
±20 ppm = 6%
±50 ppm = 17%
±100 ppm = 41%
±400 ppm = 91%

## Slide 38
Percent land area within:
±20 ppm = 0.2%
±50 ppm = 0.5%
±100 ppm = 1%
±400 ppm = 4%
±1000 ppm = 11%
±5000 ppm = 82%

## Slide 39
Percent land area within:
±20 ppm = 0.2%
±50 ppm = 0.5%
±100 ppm = 1%
±400 ppm = 4%
±1000 ppm = 11%
±5000 ppm = 82%

## Slide 40
Percent land area within:
±20 ppm = 17%
±50 ppm = 38%
±100 ppm = 69%
±400 ppm = 99.8%

## Slide 41
Percent land area within:
±20 ppm = 17%
±50 ppm = 38%
±100 ppm = 69%
±400 ppm = 99.8%

## Slide 42
Percent land area within:
±20 ppm = 4%
±50 ppm = 11%
±100 ppm = 36%
±400 ppm = 99.1%

## Slide 43
Percent land area within:
±20 ppm = 17%
±50 ppm = 38%
±100 ppm = 69%
±400 ppm = 99.8%

## Slide 44
Percent land area within:
±20 ppm = 17%
±50 ppm = 38%
±100 ppm = 69%
±400 ppm = 99.8%

## Slide 45
Percent land area within:
±20 ppm = 49%
±50 ppm = 74%
±100 ppm = 88%
±400 ppm = 99.9%

## Slide 46
Percent land area within:
±20 ppm = 47%
±50 ppm = 73%
±100 ppm = 88%
±400 ppm = 99.9%

## Slide 47: Poll Question
Most states will have more than one SPCS2022 “layer.” Which layer do you expect to use most often in your work?
427 of 604 attendees responded

## Slide 48: About the timing of it all…
Finalize all designs in 2022
Other things in 2022
  Provide machine-readable definitions
  SPCS2022 report
  Modify NGS algorithms (e.g., 1-parallel Lambert)
Release with rollout of modernized NSRS
  Final definitions available in 2022
  But will not release before new “datums”
  Likely after 2025…

## Slide 49: Likely after 2025?
Seriously?

## Slide 50: But I want to use SPCS2022 now!

## Slide 51: But I want to use SPCS2022 now!
Some want to use designs with NAD 83
  Same reference ellipsoid
  Near identical performance
Can reference to NAD 83, however:
  Will not become part of SPCS 83
  Will not be supported in NGS products & services
If you use designs with NAD 83:
  Change grid origins by large amount
  Will help avoid confusion with SPCS2022 version

## Slide 52: Poll Question
Do you want to use the SPCS2022 zone designs with NAD 83, before the new reference frames (“datums”) are released?
434 of 604 attendees responded

## Slide 53: What to expect for SPCS2022
Coordinates will change by at least 10,000 m
  Latitude and longitude change about 1-2 m
  Rest of change due to projection definition
Less difference between “grid” and “ground”
More than one zone layer in most states
  Zones will be similar to SPCS 83 in some states
  Zones will be very different in most states
Every state will have a statewide zone layer

## Slide 54: SPCS2022 summary
Minimize distortion at topo surface, not ellipsoid
Up to 3 zone “layers” allowed
  Some layers very similar to existing SPCS 83
  Some layers very different
Total of 968 zones (likely will decrease somewhat):
  54 statewide zones
  911 zones that cover part of a state
  3 special use zones
Will be implemented along with Modernized NSRS
  Earlier usage with NAD 83 will not be supported by NGS
  Can change/add/remove zones after modernized NSRS

## Slide 55
geodesy.noaa.gov
Questions?

## Slide 56: Poll Question
What is your profession?
266 registrants responded