## Slide 1
An Introduction to Geoid Slope Validation Surveys - What they are, and Why they Matter
NGS Webinar, July 12 2018
Derek van Westrum, Ph.D.
NGS Observations and Analysis Division
derek.vanwestrum@noaa.gov
NOAA’s National Geodetic Survey
geodesy.noaa.gov

## Slide 2: Outline
NGS, its history and mission
Height
  Historical methods (Old Way)
  Equipotential surfaces and the geoid
  Modern height determinations (New Way)
  The new Geopotential Reference System (NAPGD2022)
GRAV-D operations (Making this Happen)
Geoid Slope Validation Surveys (Making Sure it Works)
  Texas, Iowa, and Colorado

## Slide 3: NGS Mission Statement
To define, maintain, and provide access to the National Spatial Reference System (NSRS) to meet our nation’s economic, social, and environmental needs.
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, and orientation throughout the United States, for all federal agencies.
Emergency Response Imagery, Flood zones
Levee Safety Program
Topographic Maps and interior water data for the nation
Nautical charts, among many other geospatial applications
Aeronautical Data Quality Assurance
NSRS gravity data for the geospatial mission of NGA

## Slide 4
The National Geodetic Survey Ten-Year Plan
Support the users of the National Spatial Reference System.
Modernize and improve the National Spatial Reference System.
Expand the National Spatial Reference System stakeholder base through partnerships, education, and outreach.
Develop and enable a workforce with a supportive environment.
Improve organizational and administrative functionality.
Notes: The NGS “State Geodetic Advisor” program has engaged a long-standing cost-sharing partnership between NGS and various states. On many levels it is a success... However, the program has been a patchwork success and does not serve the nation equitably. Recognizing this imbalance… NGS determined to transition to a regional advisor program. The regional program will consist of a smaller cadre of advisors, all well-trained and dynamic educators capable of serving multi-state regions, and the new program will be run all at the cost to NGS alone.
NGS Ten-Year Strategic Plan, 2013
The NGS Ten-Year Plan was adopted at the beginning of 2013, including four major goals and an enterprise goal:
Goal 1: Support the Users of the National Spatial Reference System.
Goal 2: Modernize and Improve the National Spatial Reference System.
Goal 3: Expand the National Spatial Reference System Stakeholder Base through Partnerships, Education and Outreach.
Goal 4: Develop and Enable a Workforce with a Supportive Environment.
Enterprise Goal: Improve Organizational and Administrative Functionality.

## Slide 5: National Geodetic Survey Ten-Year Strategic Plan
  By 2022, reduce all definitional & access-related errors in geometric reference frame to 1 cm when using 15 min of GNSS data
  “Replace NAD83”
  (NAD83 = North American Datum 1983)
  By 2022, reduce all definitional & access-related errors in orthometric heights in geopotential datum to 2 cm when using 15 min of GNSS data
  “Replace NAVD88”
  (NAVD88 = North American Vertical Datum 1988)
https://geodesy.noaa.gov/web/about_ngs/info/tenyearfinal.shtml

## Slide 6: Current NSRS
NAD83
  North American Datum of 1983
  Horizontal reference system: Latitude and Longitude
  Replaces NAD27
NAVD88
  North American Vertical Datum of 1988
  Replaces NGVD29
  (I’ll say more about it, but mainly: its replacement is the focus of this talk…)
Meades Ranch Triangulation Station (NAD27)

## Slide 7: Height
It’s just the distance1 up2 from somewhere3, right?
Measured how?
Exactly which direction is that?
Where?
We’ll kinda go in reverse order…

## Slide 8: “Old Man and The Sea (Level)”
The National Geodetic Survey, our Nation's first civilian scientific agency, was established by President Thomas Jefferson in 1807 as the Survey of the Coast. Its mission was, and still is, to survey the U.S. coastline and create nautical charts of the coast to help increase maritime safety. As the nation grew westward surveys of the U.S. interior began. In 1878 the agency was given a new name, the U.S. Coast and Geodetic Survey (USC&GS), which it maintained until 1970.
So, you basically went down to the seashore with a ruler, and kept track of much you went up as you went inland…

## Slide 9: Leveling
“Simply” keep track of accumulated height differences.
“First order” accuracy: 0.7mm/√km
Need gravity (or model) at each benchmark

## Slide 11: “Old Man and The Sea (Level) cont.”
“…a leveling network on the North American Continent, ranging from Alaska, through Canada, across the United States, affixed to a single origin point on the continent:
Tide Station & Location = Pointe-au-Pere, Rimouski, Quebec, Canada
PID = TY5255
GSD* Designation = 54L071
Bench Mark = 1250 G
Height above LMSL ≡ 6.271m
  Massive leveling and gravity campaign across the country in the 1980s yielded measurements at >500,000 benchmarks
NAVD88, the current vertical datum is still based on sea level

## Slide 12: Problems with NAVD88
It is only realized at the benchmarks it occupies. “New” points, or local survey control, must be leveled to an existing benchmark
Benchmarks change (height, especially) or disappear with time:
  Hydrology – subsidence from ground water usage (10s of meters in California!)
  Cryospheric – glacial isostatic adjustment (post-glacial rebound)
  Earthquakes, volcanoes
  Pesky vandals…

## Slide 13: Problems with NAVD88 cont.
It has an annoying “tilt” with respect to “sea level”*
Sea level isn’t level (dynamic topography)
Sea level isn’t constant with time…
*by which, I mean the “geoid”…

## Slide 14: So, we need new datums!
New Datums (horizontal and vertical) are coming in 2022:
http://www.geodesy.noaa.gov/datums/newdatums/index.shtm
Replacing NAD83 with a geocentric reference fame. GNSS based
Replacing NAVD88 with a gravity based geoid, NAPGD2022. The GRAV-D project combines satellite, airborne, and terrestrial gravity measurements…

## Slide 15: Back to Basics
How do we best measure and describe the shape of the Earth?
Through a series of successive models:
Most everyone not paying attention (~forever): the earth is flat
Eratosthenes (~200 BC) used wells to show the
Earth is a sphere, and calculated its radius to ~10%.
Cassini (1666) noticed Jupiter appears elliptical, and Richer (1672) noticed his pendulum had a longer period near the equator => Newton and Huygens used physical principles to explain why the Earth is an ellipsoid
Laplace, Gauss, Bessel, Stokes… (~1820) developed the mathematics that allowed them to precisely declare the Earth is actually best described as a lumpy blob => Geodesy.

## Slide 16: Aside #1: GNSS and the Ellipsoid
Way out at the altitudes of GNSS satellites (~20,000km), the Earth no longer looks like a lumpy blob. It looks like a perfectly smooth “egg” or more precisely, a squished sphere called the ellipsoid. GNSS allows for very accurate (~1cm) location determinations relative to this mathematically well-defined ellipsoid.
The ellipsoid model currently used by GPS is WGS84. Its origin is located at the CM of the Earth.

## Slide 17: Earth’s Gravity Field and The Geoid
W = const defines a surface of equipotential or geopotential
There are infinitely many equipotential surfaces. They are not necessarily parallel to each other, but never intersect.
Up close they’re lumpy blobs, but farther out they become more and more ellipsoidal.
Water doesn’t flow along an equipotential surface, or equivalently, such a surface is said to be “level” (even when lumpy!).
Plumb lines are always perpendicular to every surface they intersect.
The one equipotential surface that, on average, best matches sea level is known as the geoid ≡ W0.
Notes: Mention that the geoid is not an ellipsoid shape, but lumpier. Only 170m_pp though!

## Slide 18: Aside #2: Understanding Geopotential
Imagine pouring water onto a dry lake bed. If everything is level it will simply pool up. It would “like” to get to lower potential (darker lines), but the lake bed is in the way.
If the lake bed is tilted (it’s now the side of a hill), the water can move towards lower potential (towards darker lines). Water appears to flow because of a change in height
If the lake bed appears flat, but there is a mass anomaly under one end, the resulting geopotential difference causes water to flow to lower potential (again, from light to dark lines). It appears to flow because of gravity.
In all scenarios, water only flows when it has a path to lower geopotential – this is always a combination of gravity and height, -∫g dH.
Notes: Mention that the geoid is not an ellipsoid shape, but lumpier. Only 170m_pp though!

## Slide 19: A Few Words about the Geoid
Is the shape of the surface of the oceans under gravity and rotation alone
Still well-defined “under” the continents (imagine very long canals)
Locally lumpy, but actually quite smooth on a global scale:
  Min undulation: -106m southern India
  Max undulation: +85m Iceland
  Smallest horizontal features are ~20km in size
The geoid is a natural starting point for heights, and this will be our “fancy new sea level” – the new datum!
Notes: Mention that the geoid is not an ellipsoid shape, but lumpier. Only 170m_pp though!

## Slide 20
+  H

## Slide 21: Putting it all together…
Your “cellphone” (actually, geodetic grade GNSS receivers) will give you ~1cm Ellipsoidal Height, h, in a few tens of minutes.
NGS will provide (via your cellphone) the Geoidal Undulation (or geoid height), NG , at your latitude and longitude, accurate to ~1cm.
Your (orthometric) height* above “sea level” is then simply H = h – NG; good to about 2cm. Voila!
*measured along the plumb line from your location to the geoid

## Slide 22: A few, minor, details….
Getting NG isn’t trivial…
  You’ve got to know the difference in true surface gravity from what you’d expect if the earth was a perfect ellipsoid. This is referred to as the gravity anomaly, ∆g.
  Then solve Stokes’ integral:
  Which also means you need to know ∆g over the entire surface of the earth (or, at least a continental-sized chunk of it…)
  (R is the mean radius of the earth, ɣ0 is mean surface gravity on an equivalent ellipsoidal earth, S is an analytic (geometrical) function of position.)
And then, once you know NG “everywhere”, you still need to be able to communicate it somehow…

## Slide 23: Aside #3: Spherical Harmonics
* must be an “harmonic function”
**sphere or ellipsoid…
***feel free to confuse “special” and “spatial”
n = 0
n = 1
n = 2
n = 3
n = 4
n = 5
Like a Fourier decomposition, there are low-order, long wavelength terms, and successively higher-order, shorter wavelength terms.

## Slide 24: Wait, one last detail!
We still have to choose the W value that will define which geopotential surface is the geoid. Again, it’s nice if it’s pretty close to what people have been using as “mean sea level”.
W0 ≡ 62,636,856.0 m2s-2
(Note: W0 ~ GMe/Re. The above definition effectively defines the combination of the gravitational constant and the mass and radius of the Earth.)
The North American-Pacific Geopotential Datum of 2022 (NAPGD2022) will contain information for:
  Orthometric heights
  Geoid undulations (GEOID2022 – purely gravity)
  Gravity anomalies (GRAV2022)
  Deflections of the vertical (DEFLEC2022)
  & other gravity field information (GM2022)

## Slide 25
How to Build a Gravity Field
Long Wavelengths
(≥ 250 km)
GRACE/GOCE/Satellite Altimetry
Intermediate Wavelengths
(500 km to 20 km)
Airborne Measurement
Surface Measurement and
Predicted Gravity from Topography
Short Wavelengths
(< 100 km)
+
+

## Slide 26: GRAV-D Operations
Gravity for the Redefinition of the American Vertical Datum
From the Science Fundamentals link at http://www.ngs.noaa.gov/GRAV-D/:
“The specific goal of GRAV-D is … to model and monitor Earth’s geoid (a surface of the gravity field, very closely related to global mean sea level) to serve as a zero reference surface for all heights in the nation.”’
This is done by using airborne gravity as a high(er) resolution enhancement to space-based gravity (GRACE, GOCE)

## Slide 27: Data Collection Scope
Entire U.S. and territories
  Total Square Kilometers: 15.6 million
  ~200 km buffer around territory or shelf break if possible
  Initial target area for 2022 deadline
Notes: Project Scope:
Scope of the project: cover roughly 15.6 million square kilometers – contiguous united states, Alaska, Hawaii, Guam, and American Samoa
In order to blend with satellite altimetry data the airborne survey is done to the continental shelf where possible or ~ 200 km beyond the shoreline or border, whichever is further
Deadline of 2022 for datum rollout, which means a target of 2021 to finish the airborne survey
Priority areas were defined as Alaska and coastal areas
Challenges:
Fixed annual budget and time  design of surveys had to fit within an annual budget of $3.5 million and meet the deadline
This was a major factor in setting altitude and line spacing

## Slide 28: GRAV-D Status July 2018: 68%

## Slide 29: Survey and Block Plans
Data lines spaced 10 km apart
Cross lines spaced 60-80 km apart (QC purposes)
Flight altitude 20,000 ft
Nominal speed 220-250 kts
Notes: Block layout based on aircraft, adjust size of block if needed

## Slide 30: Experimental Geoids
The gravity data from satellites, airborne, corrected surface data, and terrain predictions will be blended into a gravity anomaly field, ∆g, and then used to calculate geoid undulations, NG.
Methods for blending will be tested to prepare for 2022
Available on the Website: http://beta.ngs.noaa.gov/GEOID/xGEOID/

## Slide 31: Geoid Slope Validation Surveys
How do we know any of this is going to work?
The Geoid Slope Validation Surveys (GSVSs) use high precision, high resolution (~1.5km spacing), ground-based survey techniques to determine the shape of the geoid consistently along a large (~300km) distance.
This allows for the direct comparison of the geoid shape predicted by various, gravity-based geoid models.
This also allows for a quantification of the airborne gravity’s contribution to the improvement of these models.

## Slide 32
Principles of the GSVSs
Why compare the shape of the models?
Rather than using “absolute” values of the geoid at specific locations to compare models, it is actually more useful to look at the changes in the shape of the geoid over various distance scales (i.e. looking at slopes)
Method 1:
Leveling & Gravity provide terrain-corrected geodetic heights (“Rise”)
GNSS provides horizontal distance (“Run”)
Slopei = Risei / Runi
Run 1
Run 2
Run 3
Rise 1
Rise 2
Rise 3
Ellipsoid
Geoid
Geoid Slope

## Slide 33
Principles of the GSVSs (cont.)
Method 2:
GNSS provides ellipsoidal position (lat, lon)
Deflection of Vertical measured directly with Astro-geodetic Camera (difference from normal to ellipsoid and local plumb line)
The camera knows what stars it “should” see normal to the ellipsoid at a specific time and location. The DoV is difference between that and with what is actually “straight up”
Slope = Vector sum of North and East deviations of camera axis
Ellipsoid
Geoid
Geoid Slope

## Slide 34
Example of slopes over various distance scales:
Objective of the GSVSs (cont.)
Every 1 interval
Every 2 intervals
Every 3 intervals
Every 4 intervals
We thus have two independent methods of measuring geoid slopes.
Next, we look at the changes in the shape of the geoid over various distance scales (i.e. looking at the slope between various pairs of survey points separated by 1, 2, 5, 10, 20, 50, 100, 200 km, etc.)
Finally, we compare these “ground truth” results to various geoid models.
Further, we can compare models with/without airborne gravity to quantify the contribution

## Slide 35: Previous GSVS Surveys
South Texas, 2011
Flat, close to the geoid
Iowa, 2014
Higher elevation and geologically interesting terrain (traversing the Midcontinent Rift System).

## Slide 36: GSVS17 Colorado
The third (and likely final) GSVS took place along US160, from Durango to Walsenburg, in southern Colorado in the summer of 2017.
High elevation and rugged topography. “Worst case” for geoid modeling.
Variation from 6,000’ (MSL) to 11,000’, over two passes. 223 bench marks

## Slide 37: Survey Techniques: Long Period GPS
Calibrated, fixed-height antennas, all identical models
In Colorado 2017:
  24 complete sets of equipment (2 parties, 10 sets each)
  Each party set up on 5 new stations each day
  24 hours & 16+ hours of observation on each station
  Project processed with OPUS Projects

## Slide 38: Survey Techniques: Leveling and Gravity
The entire line was leveled (double-run). Geodetic heights provided at each benchmark.
Leveling and gravity are both needed for orthometric height determination. Usually gravity is modeled, but in this case was actually measured at every point.
  Absolute gravity (A10 and/or FG5) at every benchmark
  Vertical gravity gradient (CG6) at every benchmark

## Slide 39: Survey Techniques: Deflection of the Vertical (DoV)
In Colorado, 2017:
  223 stations (14 repeat observations)
  39 nights
  ~6 stations/night
  Observing with Swiss CODIAC (COmpact DIgital Astrometric Camera), courtesy Technical University of Zurich.
Measure the slope of the geoid directly!
Precision tilt meters provide alignment “level” to the geoid.
Celestial almanacs provide predicted alignment with star field (relative to ellipsoid).
The difference between the two vectors (broken into orthogonal components) are the Deflections of the Vertical (or “slopes”).

## Slide 40: Results from Texas and Iowa*
Measured slopes were compared with NGS (and other) geoid models
Texas and Iowa GSVS both confirmed 1-2cm geoid accuracy, as expected!
"Confirming regional 1 cm differential geoid accuracy from airborne gravimetry: the Geoid Slope Validation Survey of 2011", Smith et al., Journal of Geodesy, 2013.
* Again, the 2017 Colorado data are still being analyzed
“The Geoid Slope validation Survey 2014 and GRAV-D airborne gravity enhanced geoid comparison results in Iowa", Wang et al., Journal of Geodesy, 2017 91:1261-1276.
Texas 2011
Iowa 2014
(The new system works here, at least!)

## Slide 41: Summary
The nation’s new vertical height system, NAPGD2022, will use a surface of constant geopotential as the vertical datum (the geoid).
NGS will provide the geoid undulation “correction”, NG, to get orthometric heights, H, from easily-obtained (GNSS) ellipsoidal heights, h.
To verify geoid precision, ground-based geoid slope measurements (derived from both classic techniques and direct measurements of DoV) over varying distance scales were used to compare various geoid models.
Comparing this “ground truth” to the models also allows for a direct quantification of the improvement when airborne gravity data are included.
To date, two such surveys have been conducted successfully in reasonably flat terrain.
Colorado has now been observed for a final, challenging test. Look for results later in 2018!

## Slide 42
Questions, comments?
Please don’t hesitate to contact me: derek.vanwestrum@noaa.gov

## Slide 43: Geoid Height Change Over Time
How often will updates be needed to maintain a 1-2 cm accuracy geoid?
Which areas of U.S. will see the most change?
Their Answer: Approximately every 10 years for the Nation; Local adjustments may be needed after disasters