## Slide 1
adapted from:
The State Plane Coordinate System: History, Policy, and Future Directions
Michael L. Dennis
NGS SPCS2022 Project Manager
ASCE-UESI Surveying & Geomatics 2018 Conference
April 23, 2018
Geometric Design of LDP
Dave Zenk PE, LS
NGS Northern Plains Regional Advisor
MSPS Annual Meeting, February 23, 2023
Brooklyn Park MN

## Slide 2: More Information
geodesy.noaa.gov

## Slide 3: New State Plane Coordinate System
State Plane Coordinate System of 2022 (SPCS2022)
  Referenced to new 2022 Terrestrial Reference Frames (TRFs)
  Based on same reference ellipsoid (GRS 80)
  Same 3 conformal projection types
    Lambert Conformal Conic (LCC)
    Transverse Mercator (TM)
    Oblique Mercator (OM)
NGS in process of specifying SPCS2022 characteristics
  Draft policy and procedures for public comment
  Federal Register Notice (FRN) on policy and procedures
  New report on State Plane history, policy, and future (done!)
NOTE: SPCS2022 policy, procedures, and FRN currently in review
  Approved version may differ from what is presented here

## Slide 4: Announcements
SPCS2022 Federal Register Notice
August 31, 2018 for public comment on draft policy & procedures
Includes “special purpose” zones
SPCS2022 procedures
December 31, 2019 for SPCS2022 zone requests and proposals
  Requests are for zone designs by NGS
  Proposals are for zone designs by others
December 31, 2020 for submittal of approved designs by others
  Proposal must first be approved by NGS
  Designs must be complete before NGS review
After deadlines, requests will be for changes to SPCS2022

## Slide 5: History and Future of State Plane
SPCS created 85 years ago
  SPCS 27: 1933 – 1986 (53 years, with some changes)
  SPCS 83: 1986 – 2022 (36 years, with some changes)
  SPCS2022: 2022 – ? (at least a few decades…)
SPCS2022 will likely be around for a long time
  Honor the history and legacy of SPCS…
  …while building a system for the future
High visibility and big impact
  SPCS used by many in US geospatial community
  NGS already contacted by 16 states about SPCS2022

## Slide 6: SPCS Special Publication
History of NGS projections (1853 to present)
SPCS policies and legislation
Departures from policy and convention
Recent developments in projected coordinate systems
Appendices
  Defining parameters for ALL zones of ALL versions of SPCS, plus additional information
  Status of SPCS 83 legislation and foot conversions
https://geodesy.noaa.gov/library/pdfs/ NOAA_SP_NOS_NGS_0013_v01_2018-03-06.pdf

## Slide 7
geodesy.noaa.gov/SPCS/
On “Learn More” page will soon add:
Spreadsheets with complete definitions for all SPCS 27 and SPCS 83 zones
Shapefiles of all SPCS 27 and SPCS 83 zones with parameters as attributes

## Slide 8: An interesting and varied history
Initially created for North Carolina at customer request
  Gave practical access to National Spatial Reference System (NSRS)
  SPCS 27 started in 1933, completed in 1934(!)
Changes from SPCS 27 to SPCS 83:
  Multi-zone to single-zone for some states (SC, NE, MT)
  Change in grid origin and units (US feet to meters)
  American Samoa has no SPCS 83 zone
Departures from policy and convention:
  Guam used non-conformal projection for SPCS 27
  Michigan used “scaled” ellipsoid for SPCS 27 (after 1963)
  California added small Los Angeles County zone for SPCS 27
  Kentucky has “layered” (overlapping) SPCS 83 zones
  Montana single SPCS 83 zone greatly exceeds 1:10,000 scale error

## Slide 9
State Plane Coordinate Systems of 1927 (134 zones) and 1983 (125 zones)
Guam SPCS 27 zone a non-conformal projection
American Samoa only in SPCS 27, not SPCS 83
Two zones in SPCS 27, one in SPCS 83
Guam SPCS 83 zone added in 1995

## Slide 10
Original SPCS 27, as of 1934 (110 zones total)

## Slide 11
Final SPCS 27, as of 1968 (112 zones in CONUS, 131 zones total)
Reduced distortion zones added: CA 7 (1945) MI (1964)

## Slide 12
Final SPCS 83, as of 2001 (108 zones in CONUS, 125 zones total)
KY statewide zone added in 2001

## Slide 13
Alaska State Plane Coordinate Systems of 1927 and 1983 (10 zones)
Islands in Zone 9 are referenced to local datums other than NAD 27

## Slide 14
Hawaii State Plane Coordinate Systems of 1927 and 1983 (5 zones)
“SPCS 27” version referenced to Old Hawaiian Datum
Puerto Rico and U.S. Virgin Islands State Plane Coordinate Systems of 1927 (2 zones) and 1983 (1 zone)
“SPCS 27” version referenced to
Puerto Rico 1940 Datum

## Slide 15: Issues with SPCS 83
Incomplete NGS documentation (until now)
Inconsistent zone definitions
  Highly variable linear distortion
  “Layered” zones exist (Kentucky)
  Inconsistent specification of grid origins
  Scale explicitly defined for some zones, implicitly for others
  Incomplete coverage of U.S. territories
Note common usage of SPCS “at ground”
  Many surveyors & engineers scale SPCS to topo surface
  NGS used to give workshops on this methodology
  Process incorporated in most surveying software
  Shows desire to work “at ground”

## Slide 16: Map projection concepts
Linear distortion (“scale error”)
  Amount map projection “grid” distance differs from true (curved) horizontal distance
    Usually at topographic surface (“grid” vs. “ground” distance)
    Can also be at ellipsoid surface (“grid” vs. ellipsoid distance)
Conformal map projection
  Linear distortion unique at a point (same in every direction)
  Lines on Earth intersect at same angle on map
    Meridians and parallels intersect at right angles on map
    Shapes of areas on Earth are locally preserved on map
  Simple relationship between grid and geodetic azimuth
  SPCS2022 will only use conformal projections
    Same for SPCS 83 and SPCS 27 (with one exception in Guam)

## Slide 17: SPCS2022 characteristics (draft)
Technical requirements
  Linear distortion design criterion at topographic surface (not at ellipsoid surface)
    Difference in distance between “grid” and “ground”
  Use 1-parallel definition for LCC projections
Other characteristics
  Default designs (if no consensus stakeholder input)
  “Layered” zones
  Low-distortion projections (LDPs)
  “Special purpose” zones

## Slide 18
Gnomonic projection (non-conformal)
Stereographic projection (conformal)
Orthographic projection (non-conformal)
Ray source
at infinity
Ray source at opposite side of Earth
Ray source at center of Earth
Projection surface
Projection surface
Projection surface
Can think of projection as “light rays” projecting onto surface
However, this only works for a few sphere-based projections

## Slide 19
e.g., Lambert conformal conic
(used for SPCS)
Polar aspect
Oblique aspect
Central parallel
Standard parallels
Origin
e.g., stereographic (not used for SPCS)
One-parallel (tangent)
Two-parallel (secant)
Conic projections
Planar (azimuthal) projections
Developable surfaces: Planes and cones
Examples given are CONFORMAL projections
Standard parallel

## Slide 20
Cylindrical projections
Central meridian
Skew axis
Equator
“Regular” aspect
Transverse aspect
Oblique aspect
e.g., Mercator
(not used for SPCS)
e.g., transverse Mercator
(used for SPCS)
e.g., oblique Mercator
(used for SPCS)
Developable surfaces: Cylinders
Examples given are CONFORMAL projections

## Slide 21
Projection axis
Tangent ( = 1)
A map projection is a mathematical function
Grid distance > ellipsoid distance
Ellipsoid distance
Ellipsoid surface
Grid distance = ellipsoid distance
is projection axis scale factor
is constant value applied to conformal projection “grid”
= 1 by default if not defined

## Slide 22
Projection axis
Tangent ( = 1)
A map projection is a mathematical function
Grid distance > ellipsoid distance
Ellipsoid distance
Non-intersecting ( > 1)
Secant ( < 1)
Ellipsoid surface
Grid distance < ellipsoid distance
Grid distance > ellipsoid distance
Grid distance = ellipsoid distance
Grid distance = ellipsoid distance
Grid distance = ellipsoid distance
Ellipsoid distance
Can “move” conformal projection surface “up” or “down” by changing
Grid distance > ellipsoid distance everywhere

## Slide 23
Projection axis
“Secant” conformal map projection
Ellipsoid distance
Secant ( < 1)
Ellipsoid surface
Grid distance < ellipsoid distance
Grid distance > ellipsoid distance
Grid distance = ellipsoid distance
Grid distance = ellipsoid distance
Ellipsoid distance
Zone width to balance positive and negative distortion (scale error) with respect to ellipsoid
14.5%
71%
14.5%

## Slide 24
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Ellipsoid surface
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface

## Slide 25
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Ellipsoid surface
Topographic surface

## Slide 26
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
Only way to reduce variation in distortion is to change projection axis location.
IMPORANT: For large areas, there is no single defining ellipsoid height, h, for scaling the projection.
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface

## Slide 27: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Nominal distortion criterion (on ellipsoid) for SPCS 27 and 83 zones (although greatly exceeded for some zones in SPCS 83).

## Slide 28: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion range (at ground) for zones designed by NGS, as proposed in draft SPCS2022 policy and procedures.

## Slide 29: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion criterion (at ground) often used for “low distortion projection” (LDPs); designed by others for SPCS2022 (not by NGS)

## Slide 30: SPCS2022 characteristics (draft)
Technical requirements
  Linear distortion design criterion at topographic surface (not at ellipsoid surface)
    Difference in distance between “grid” and “ground”
  Use 1-parallel definition for LCC projections
Other characteristics
  Default designs (if no consensus stakeholder input)
  “Layered” zones
  Low-distortion projections (LDPs)
  “Special purpose” zones

## Slide 31: Lambert Conformal Conic projection
Conical developable surface
Used for many State Plane zones
Can define scale two different ways:
  Define scale explicitly on central standard parallel
  Compute scale implicitly
    From separation between two “standard” parallels
    Scale (at ellipsoid) is exactly 1 for standard parallels
The two types are mathematically identical!
  “Projection axis” for both is central standard parallel

## Slide 32: Why only a 1-parallel LCC?
Consistency
  Explicitly define projection scale (same as TM and OM)
  Can use same number of parameters as TM
  Applicable to both “secant” and “non-intersecting” cases
Simplicity
  Easier to design with respect to topography
  Scale due to separation of 2 standard parallels not obvious
  Can more readily use “clean” values for parallels
Mathematically identical to 2-parallel
  Any 2-parallel LCC can be recast as 1-parallel that behaves exactly the same

## Slide 33: Consider North Carolina SPCS 83 Zone
Central “standard” parallel
Ellipsoid
North standard parallel
South standard parallel
(projection axis)
Scale = 1
Scale = 1
(1:7849)
Scale = 0.9998 7259…
Secant Lambert Conformal Conic projection, 2-parallel definition:
Standard parallels
North = 36°10’N (exact)
South = 34°20’N (exact)
It is EXACTLY the same as this 1-parallel definition:
Central standard parallel
35°15’06.33096…”N
Scale = 0.9998 7259…
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 34: Secant Lambert Cone
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
35°15’06.33096
Scale = 0.9998 7259…
Not Fitting Terrain
What Can We Do?
Note: Perpendicular Line to Cone (blue) is also Perpendicular to ellipsoid (yellow) at the Projection Axis

## Slide 35: Tangent Lambert Cone
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
35°15’06.33096
Scale = 1
Move Cone Up
Same Projection Axis, Different scale factor

## Slide 36: Non-Intersecting Lambert Cone
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
35°15’06.33096
Scale = 1.001
Move Cone Up Again
Same Projection Axis, Different scale factor

## Slide 37: Design to Fit Terrain 1
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Change Cone Angle
New Projection Axis, and Different scale factor
Scale = 1.010
36°00’00”

## Slide 38: Design to Fit Terrain 2
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Scale = 1.020
Change Cone Angle Again
New Projection Axis, and Different scale factor
37°00’00”

## Slide 39: Design to Fit Terrain 3
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Scale = 1.030
Change Cone Angle Again
New Projection Axis, and Different scale factor
38°00’00”

## Slide 40: Design to Fit Terrain 4
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Central “standard” parallel
(projection axis)
Scale = 1.001
Move Cone Down
Retain Projection Axis, Different scale factor
38°00’00”

## Slide 41: SPCS2022 characteristics (draft)
Technical requirements
  Linear distortion design criterion at topographic surface (not at ellipsoid surface)
    Difference in distance between “grid” and “ground”
  Use 1-parallel definition for LCC projections
Other characteristics
  Default designs (if no consensus stakeholder input)
  “Layered” zones
  Low-distortion projections (LDPs)
  “Special purpose” zones

## Slide 42: Default SPCS2022 designs (draft)
Default needed in absence of stakeholder input
Same projections and zones for most SPCS 83 zones
Performance and coverage very similar to SPCS 83
Characteristics that differ from SPCS 83:
  Projection scale modified to minimize distortion at ground
  Lambert Conformal Conic converted to one-parallel type
  Most geodetic origins with arc-minutes evenly divisible by 3
  A few zones with different projection & zone extents

## Slide 43
 |  | SPCS 83 NC | 
Central parallel |  | 35°15’06.33…”N | 
Cen parallel scale |  | 0.9998 7259… | 
 | Height (m) | Distortion (ppm) | 
Min | -41 | -413 | 
Max | 1939 | +176 | 
Mean | 197 | -93 | 
SPCS 83 North Carolina (Lambert Conformal Conic 2-parallel)

## Slide 44
 |  | SPCS 83 NC | SPCS2022
Central parallel |  | 35°15’06.33…”N | 35°15’N
Cen parallel scale |  | 0.9998 7259… | 0.99996
 | Height (m) | Distortion (ppm) | 
Min | -41 | -413 | -325
Max | 1939 | +176 | +263
Mean | 197 | -93 | -5
SPCS2022 “default” NC (Lambert Conformal Conic 1-parallel)
No change in projection type or zone extents

## Slide 45
 |  | SPCS 83 AZ C | 
C.M. |  | 111°55’W | 
Scale |  | 0.9999 | 
 |  | Distortion (ppm) | 
Min |  | -660 | 
Max |  | +102 | 
Mean |  | -224 | 
SPCS 83 Arizona Central Zone (Transverse Mercator)
 | Height (m)
Min | 96
Max | 3607
Mean | 1177

## Slide 46
 |  | SPCS 83 AZ C | SPCS2022
C.M. |  | 111°55’W | 112°W
Scale |  | 0.9999 | 1.0001
 |  | Distortion (ppm) | 
Min |  | -660 | -455
Max |  | +102 | +277
Mean |  | -224 | -24
SPCS2022 “default” Arizona Central Zone (Transverse Mercator)
 | Height (m)
Min | 96
Max | 3607
Mean | 1177
No change in projection type or zone extents

## Slide 47: “Layered” zones (draft)
Limitations
  Max of TWO layers: Statewide and sub-zones
  If two layers, one MUST be statewide
  Minimum sub-zone dimension > 50 km
States often want statewide and small zones
  Statewide: Single geometry required for state GIS
  Sub-zones: Lower distortion for surveying/engineering
Accommodates state needs, but with restrictions
  Prevent poor design choices for statewide zones
  One already exists in SPCS 83…
But not a 3rd Layer

## Slide 48: Kentucky layered zones
 |  | North | South | Statewide
N parallel |  | 38°58’N | 37°56’N | 38°40’N
S parallel |  | 37°58’N | 36°44’N | 37°05’N
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | -166
Max |  | +17 | +42 | +181
Mean |  | -56 | -67 | -58
“Layered” zones
SPCS 83 Kentucky statewide zone (Lambert Conformal Conic)

## Slide 49: Kentucky layered zones
 |  | North | South | 
N parallel |  | 38°58’N | 37°56’N | 
S parallel |  | 37°58’N | 36°44’N | 
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | 
Max |  | +17 | +42 | 
Mean |  | -56 | -67 | 
“Layered” zones
SPCS 83 Kentucky N and S zones (Lambert Conformal Conic)

## Slide 50: Linear distortion design criteria (draft)
NGS design of zones requested by stakeholders
  Limited to zones with 50-400 ppm distortion criterion
    50 ppm = 5 cm/km = 0.3 ft/mi = 1:20,000
    400 ppm = 40 cm/km = 2.1 ft/mi = 1:2,500
Design criterion < 50 ppm (“low distortion”)
  Min criterion 20 ppm = 2 cm/km = 0.1 ft/mi = 1:50,000
  Must be designed by others (not by NGS)
  Proposed and final design reviewed by NGS
What is the current situation with “low distortion” projected coordinate systems?

## Slide 52
Kansas Map
Note county lines
https://www.kansas.gov/khp-crashlogs/search/index

## Slide 54: “Special purpose” zones (FRN)
For areas with inadequate SPCS zone coverage
  Usually areas that are in more than one zone
Categories:
  Major urban areas (e.g., New York, Chicago, St. Louis)
  Large Indian reservations (e.g., Navajo Nation)
  Federal applications covering large areas (e.g., coastal mapping of Atlantic Coast; Grand Canyon)
Permitted for metro areas in 1977 policy (but never used)
Only in FRN, not in draft policy & procedures
  Intent is to get input on concept first
Twin Cities “Metro” Zone?

## Slide 55: Minnesota Shaded Relief
https://eros.usgs.gov/sites/all/files/external/imagegallery/2523.jpg

## Slide 56: North Dakota Shaded Relief
https://eros.usgs.gov/imagegallery/states-ned-shaded-relief#https://eros.usgs.gov/sites/all/files/external/imagegallery/2535

## Slide 57: South Dakota Shaded Relief
https://eros.usgs.gov/imagegallery/states-ned-shaded-relief#https://eros.usgs.gov/sites/all/files/external/imagegallery/2542

## Slide 58: Nebraska Shaded Relief
https://eros.usgs.gov/imagegallery/states-ned-shaded-relief#https://eros.usgs.gov/sites/all/files/external/imagegallery/2528

## Slide 59: Iowa Shaded Relief
https://eros.usgs.gov/imagegallery/states-ned-shaded-relief#https://eros.usgs.gov/sites/all/files/external/imagegallery/2516

## Slide 60: Wrap-up
State Plane has a long and varied history
Main characteristics of SPCS2022 (draft)
  Designed with respect to “ground”
  Use 1-parallel definitions for LCCs
  Default designs similar to existing State Plane
  Can include a statewide zone plus a sub-zone layer
  LDPs can be used but must be designed by others
Stakeholder input on zones for their states
Next State Plane webinar on April 12 – register at:
  https://geodesy.noaa.gov/web/science_edu/webinar_series/Webinars.shtml
NOTE: SPCS2022 policy, procedures, and FRN currently in review
  Approved version may differ from what is presented here but should be finalized before April 12 webinar