## Slide 1: Modernizing the National Spatial Reference System (NSRS)
2022 Rocky Mountain Survey Summit
Brian Shaw
brian.shaw@noaa.gov
March 2022

## Slide 2
Brian Shaw
Rocky Mountain Advisor
brian.shaw@noaa.gov

## Slide 3
Importance of Coordination
14 Advisors
36 Coordinators
Notes: NGS Regional Geodetic Advisors
https://geodesy.noaa.gov/ADVISORS/
State Geodetic Coordinators
https://geodesy.noaa.gov/ADVISORS/state-geodetic-coordinators.shtml

## Slide 4
NSRS Modernization Delay
https://geodesy.noaa.gov/datums/newdatums/delayed-release.shtml
https://geodesy.noaa.gov/datums/newdatums/FAQNewDatums.shtml
Operational, workforce retention and other issues have delayed NSRS Modernization
SPCS2022 zones should be finalized in 2022 but will not be rolled out until all of the NSRS is modernized.
GPS on Bench Marks deadline extended
December 31, 2022

## Slide 5
  https://geodesy.noaa.gov/web/science_edu/webinar_series/
NGS Resources –Webinar Series
  *Certificates of Attendance

## Slide 6: NGS Geospatial Resources Webinar

## Slide 7
(2021, 2019 recorded sessions) https://geodesy.noaa.gov/geospatial-summit/
NGS Resources – Geospatial Summits
The NGS Geospatial Summit provided updated information about the planned modernization of the National Spatial Reference System (NSRS).
NGS plans to replace the North American Datum of 1983 (NAD 83) and the North American Vertical Datum of 1988 (NAVD 88) in the coming years.
NSRS Modernization will impact federal mapping agencies, engineers, surveyors, and many other geospatial applications and user groups.

## Slide 8
NGS Resources – NGS Training Center
https://geodesy.noaa.gov/web/science_edu/training/

## Slide 9
NGS Resources – NGS Training Center
Leveling
Training

## Slide 10
  https://geodesy.noaa.gov/datums/newdatums/WatchVideos.shtml
NGS Resources – Educational Videos

## Slide 11
  https://geodesy.noaa.gov/web/science_edu/online_lessons/index.shtml
NGS Resources – Online Lessons

## Slide 12
  https://geodesy.noaa.gov/web/science_edu/presentations_library/
NGS Resources – Presentation Library

## Slide 13
NOAA and NGS
Our Nation’s First Civilian Science Agency
1807
Thomas Jefferson
Survey of the Coast
1811
Ferdinand Hassler
Superintendent
1836
U.S. Coast
Survey
1878
U.S. Coast and
Geodetic Survey
1970
NOAA is established
Notes: NGS has been around a long time. For more than 200 years, NGS and its predecessor agencies have collaborated with public and private organizations to establish reference stations at precisely determined locations.
We began on a mission established by Thomas Jefferson in 1807 to conduct a “Survey of the Coast” (as the United States Coast Survey).
(Pictured are Thomas Jefferson and Ferdinand Hassler, the first Superintendent of the Coast Survey). We were renamed the U.S. Coast and Geodetic Survey in 1878. NOAA was established in 1970.
Traditionally, precise positioning locations have been identified by setting a survey mark—usually a brass, bronze, or aluminum disk. Locations might also be identified by a deeply driven rod, or a prominent object, such as a water tower or church spire.

## Slide 14
NGS’ Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
…………………………………………….........................
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, orientation, and shoreline throughout the United States.
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 15
NGS’ History Horizontal Network 1900
http://www.geodesy.noaa.gov/PUBS_LIB/NADof1983.pdf
  US Standard Datum
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 16
http://www.geodesy.noaa.gov/PUBS_LIB/NADof1983.pdf
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 17
The Bilby Tower was basically a giant Erector set.
It helped NGS to survey the entire nation before the modern era.
The first Bilby Tower ever built was constructed in Minnesota in 1927.
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 18
Status of Horizontal Control 1983
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 19
Status of Vertical Control 1983
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 21
The Importance of Geodesy
1816-1817
1969
Today
Notes: In 1807 Thomas Jefferson created the Survey of the Coast. Ferdinand Hassler was later appointed the first superintendent and completed the first survey of New York Harbor. Commerce from shipping has always been important and for safe shipping you need to know the bathymetry of the harbors. To understand the bathymetry accurately requires you to know where the land is and the bathymetry relative to these points on land which is where geodesy comes in. This is the reason why in 1878 the name was changed to the U.S. Coast and Geodetic Survey and remained in the name until it was combined with other agencies to form the National Oceanic and Atmospheric Administration.

## Slide 22
The Earth is Infinitely Complex
Build Models to Simplify
Notes: Models are used to simplify complex phenomena for humans and computers to understand and perform calculations and analysis.
The geoid is an approximation of sea level and used to calculate elevations (orthometric heights) above this “sea level” surface
Spheroid image https://www.kisspng.com/png-sphere-shape-ball-grid-line-circle-draw-5378189/
Ellipsoid image https://www.kisspng.com/png-figure-of-the-earth-oblate-spheroid-ellipsoid-4129812/
Geoid Image https://www.reddit.com/r/MapPorn/comments/3xf6a0/geoid_height_of_new_global_gravity_field_models/

## Slide 23
Datums and Reference Frames
A reference surface or framework to reference your data to for consistency
aka P(Lat,Lon,Ht)
= lat.
= long.
= ht.
X,Y,Z vs Lat,Lon,Ht
60”, 2019
52”, 2018
46”, 2017
Notes: What is a datum? https://oceanservice.noaa.gov/facts/datum.html
Datums Overview https://geodesy.noaa.gov/datums/
New Datums https://geodesy.noaa.gov/datums/newdatums/
Horizontal and Geometric Datums https://geodesy.noaa.gov/datums/horizontal/
Vertical Datums https://geodesy.noaa.gov/datums/vertical/
A Datum or reference frame is in essence a reference surface or framework to reference your data to for consistency.
In the first image on the right there is a person who has been measuring their height over time (2017-2019 in this example). For consistency you can imagine that the floor next to the wall they are being measured is this ‘reference surface’ or datum. Lets say the first measurement was taken when the floor was carpet and you installed hard wood floors before the 2018 measurement you would have in essence changed the ‘reference surface’ and it would be inaccurate to compare the 2018 and 2019 values without a proper transformation, or height offset value.
The second image (when animating) shows why you should not try to compare values when using two different reference surfaces.

## Slide 24
Gravity is Fundamental
Aristotle (350BC)
Al-Khazini (1121)
Galileo (1590)
Newton (1687)
Einstein (1913)
Objects fall proportional to mass
Gravitational potential energy
Terminal velocity
Gravity inverse-square law
Theory of general relativity
Notes: Galileo graphic https://commons.wikimedia.org/wiki/File:GalilEXP.jpg
Spacetime curvature graphic https://www.nasa.gov/mission_pages/gpb/gpb_012.html
Aristotle (384–322 BCE)
Objects fall at a speed proportional to their mass.
The Aristotelian explanation of gravity is that all bodies move toward their natural place. For the elements earth and water, that place is the center of the (geocentric) universe;
al-Khazini (11th to 12th centuries)
In 1121, al-Khazini, in The Book of the Balance of Wisdom, proposed that the gravity and gravitational potential energy of a body varies depending on its distance from the centre of the Earth.
Galileo Galilei (1564-1642)
Leaning Tower of Pisa Experiment (1589-92) - Law of Falling Bodies
Objects fall at the same speed, independent of their mass or shape
Isaac Newton (1643-1727)
In 1687, English mathematician Sir Isaac Newton published Principia, which hypothesizes the inverse-square law of universal gravitation.
Albert Einstein (1879-1955)
Between 1911-1915 Einstein developed the theory of general relativity. In general relativity, the effects of gravitation are ascribed to spacetime curvature instead of to a force. To deal with this difficulty, Einstein proposed that spacetime is curved by matter, and that free-falling objects are moving along locally straight paths in curved spacetime. (This type of path is called a geodesic).

## Slide 25
Gravity for the Redefinition of the
American Vertical Datum
GRAV-D
94.6% Complete (5/2/2022)
Notes: More information on GRAV-D
https://geodesy.noaa.gov/GRAV-D/
Data Download for GRAV-D blocks
https://geodesy.noaa.gov/GRAV-D/data_products.shtml

## Slide 26
Why Modernize the NSRS
Current models built on old technology
  NAD 83 not truly Geocentric (~2.2m)
  NAVD 88 relies on marks in the ground
  and is not easily maintained
  Today’s technology needs better accuracy
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 27
Main Benefits of Modernized NSRS
Fast, Accurate, Consistent Elevations Everywhere
Improved Public Safety
  Flood Plain Maps
  Emergency Route Planning
Accurate Positioning
  Autonomous vehicles, BIMs, Smart Cities
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 28: NAVD 88 Issues
NAVD 88 suffers from a known bias and tilt
(about 1 meter across CONUS) relative to the gravimetric geoid
Date of this slide: Sept 3, 2020
Modernized NSRS: 4 hour version
PID: EZ0840

## Slide 29
The Future Reference Frames
Tectonic Plate based:
North America
Caribbean
Pacific
Mariana
The tectonic plates “fixed” for the
2022 Terrestrial Reference Frames
NATRF2022
PATRF2022
MATRF2022
CATRF2022
Notes: NSRS Modernization Naming Conventions https://geodesy.noaa.gov/datums/newdatums/naming-convention.shtml

## Slide 30
NAPGD2022 Geopotential Datum
Not a vertical datum, it is more than just heights.
Models included:
        Geopotential
        Deflection
        Gravity
        Geoid
Guam/CNMI
American Samoa
¼ Earth’s Surface
Notes: Experimental Geoid Models
https://beta.ngs.noaa.gov/GEOID/xGEOID20/
As noted in the Blueprint 2 document
https://geodesy.noaa.gov/library/pdfs/NOAA_TR_NOS_NGS_0064.pdf
NAPGD2022 will include all of the following
Geopotential Model of 2022 (GM2022) will include:
Static Geopotential model of 2022 (SGM2022)
Dynamic Geopotential model of 2022 (DGM2022)
GEOID2022 will include:
Static Geoid model of 2022 (SGEOID2022)
Dynamic Geoid model of 2022 (DGEOID2022)
DEFLEC2022 will include:
Static Deflection of the Vertical model of 2022 (SDEFLEC2022)
Dynamic Deflection of the Vertical model of 2022 (DDEFLEC2022)
GRAV2022
Static Gravity model of 2022 (SGRAV2022)

## Slide 31
New NSRS Mod Catch Phrase
Shift and Drift
Notes: New Datums What to expect https://geodesy.noaa.gov/datums/newdatums/WhatToExpect.shtml
NGS is not shifting the land, merely shifting the reference surfaces to which we reference the geospatial data to.

## Slide 32
Shift and Drift
A sudden shift
  Horizontal change: 0.5 to 4 m (1.5 to 13 ft)
  Ellipsoid height change: ±2 m (±6 ft)
  Elevation change: -0.5 to +2 m (-1.5 to +6 ft)
A continuous drift
  Coordinates associated with specific dates
Two components of drift:
  Tectonic plate rotation (easy to model, 2D only)
  All other residual motion (hard to model, 3D)
Notes: New Datums What to expect https://geodesy.noaa.gov/datums/newdatums/WhatToExpect.shtml
NGS is not shifting the land, merely shifting the reference surfaces to which we reference the geospatial data to.

## Slide 33
~1 to 1.5 meters North America
~2.5 to 4 meters in Pacific
0 to 1.3 meters CONUS
Shift: datum changes
Notes: New Datums What to expect https://geodesy.noaa.gov/datums/newdatums/WhatToExpect.shtml
NGS is not shifting the land, merely shifting the reference surfaces to which we reference the geospatial data to.

## Slide 34
Drift: Plate Tectonics and Velocities
Annual changes to
ITRF2014 coordinates
Notes: All plates are moving and through the constant collection of GNSS data using CORS we can now model where the land is moving. In the center of tectonic plates there is generally motion that can be measured but where plates converge can be thought of as a crunch zone and the modeling has much more uncertainty due to geophysical phenomena.

## Slide 35
Continuously Operating Reference Stations
COBK
Breckenridge
Colorado
STBT
Steamboat Springs
Colorado
Notes: All plates are moving and through the constant collection of GNSS data using CORS we can now model where the land is moving. In the center of tectonic plates there is generally motion that can be measured but where plates converge can be thought of as a crunch zone and the modeling has much more uncertainty due to geophysical phenomena.

## Slide 36
Vertical Motion
Subsidence
  Ground fluid withdrawal, sedimentation
Glacial Isostatic Adjustment (GIA)
  Crustal rebound from glaciers (uplift)
Geophysical Phenomena
  Earthquakes, calderas, Earth tides

## Slide 37
8.5 meters
50 years
San Joaquin Subsiding
20-24” in 16 months
May 2015
to
Sept 2016
Hudson Bay Uplifting
8 -13 mm/year
Vertical Motion
Notes: San Joaquin Subsidence article
http://www.digitaljournal.com/tech-and-science/technology/sinking-san-joaquin-valley-of-california-seen-from-space/article/487393
Hudson Bay Uplift article
https://www.researchgate.net/figure/Contour-map-of-observed-CBN-vertical-rates-Preliminary-results-from-the-combination-of_fig3_286867540
GIA

## Slide 38
Puerto Rico
16 cm Vertically
China Lake, CA
6-10 feet Horizontally
Horizontal and Vertical Motion - Earthquakes
Notes: China Lake Earthquake
https://www.usgs.gov/news/update-magnitude-71-earthquake-southern-california?qt-news_science_products=7#qt-news_science_products
Puerto Rico Earthquake
https://cunycis.maps.arcgis.com/apps/webappviewer/index.html?id=5f516f41baa84f9ba9e8207c2005ee4d
GIA

## Slide 39
GPS on Bench Marks
Web Map Application
Dashboard
~3,400 Completed in 2020
~4,500 Completed in 2021
Notes: GPS on Bench Marks Web Map
https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=6093dd81e9e94f7a9062e2fe5fb2f7f5
GPS on Bench Marks Dashboard
https://noaa.maps.arcgis.com/apps/dashboards/449e3051fbf44202ba6606e2dbcb0e29

## Slide 40
GPS on Bench Marks in Colorado
Notes: GPS on Bench Marks Web Map
https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=6093dd81e9e94f7a9062e2fe5fb2f7f5
GPS on Bench Marks Dashboard
https://noaa.maps.arcgis.com/apps/dashboards/449e3051fbf44202ba6606e2dbcb0e29

## Slide 41
GPS on Bench Marks in Wyoming
Notes: GPS on Bench Marks Web Map
https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=6093dd81e9e94f7a9062e2fe5fb2f7f5
GPS on Bench Marks Dashboard
https://noaa.maps.arcgis.com/apps/dashboards/449e3051fbf44202ba6606e2dbcb0e29

## Slide 42: OPUS Shared Solutions Dashboard
Dashboard enables sorting and visualization of Shared Solutions by
Month & Year, State, Agency Type, and submitting agency
Agency type | # Shared Solutions on NGS marks
State | ~33,700
Private Sector | ~5,900
Federal | ~3,700
Academic | ~1200
2018
2020
2021
Note the impact of GPSonBM Campaigns
Notes: Links on the slide.

## Slide 43: OPUS Shared Solutions in Colorado
Agency type | # Shared Solutions
State | 269
Private Sector | 159
Federal | 75
Notes: Links on the slide.

## Slide 44: OPUS Shared Solutions in Wyoming
Agency type | # Shared Solutions
State | 256
Private Sector | 126
Federal | 59
Notes: Links on the slide.

## Slide 45
NGS Mark Recovery Webpage
Crowd sourced mark recoveries help update the GPSonBM map, let NGS and others know if the mark is still usable, and pictures make it easier to find.
https://geodesy.noaa.gov/surveys/mark-recovery
Now with Find Marks Near Me!
Maintain you local control network: Submit a Recovery Note for each mark you find (up to once per year)
Did you find it?
Is it GPSable?
Got new photos?
Notes: Links on the slide.

## Slide 46: Mark Recovery Dashboard
https://noaa.maps.arcgis.com/apps/dashboards/a61976366d1f4a19b3bc8a2d5a0d5498
Notes: Links on the slide.

## Slide 47: Mark Recoveries in Colorado (627)
https://noaa.maps.arcgis.com/apps/dashboards/a61976366d1f4a19b3bc8a2d5a0d5498
Notes: Links on the slide.

## Slide 48: Mark Recoveries in Wyoming (144)
https://noaa.maps.arcgis.com/apps/dashboards/a61976366d1f4a19b3bc8a2d5a0d5498
Notes: Links on the slide.

## Slide 49: Best ways to determine coordinates in Modernized NSRS
Resurvey: Return to the field and collect new observations, relying upon geodetic control that has coordinates in the new datum
Readjust: Using existing observations, re-compute new coordinates based upon geodetic control (CORS) that has been defined in the new datum
Transform: Take finished products which have coordinates in the old datum and use transformation software to estimate coordinates in the new datum
Notes: Links on the slide.

## Slide 50
How Can You Prepare
Metadata is essential
    Improves reliability and accuracy of data
    Increases value and usefulness
Transform and collect data in current datums
    NAD 83 (2011), NAVD 88
Make sure to note Geoid Models used for GNSS data

## Slide 51
Recent Publications
Blueprint Documents for 2022 (Updated in 2021)
  Part 1: Geometric Coordinates
  Part 2: Geopotential Coordinates
  Part 3: Working in the Modernized NSRS
The State Plane Coordinate System History, Policy, and Future Directions
  NOAA Special Publication NOS NGS 13
Notes: Links on the slide.

## Slide 52: Blue Print 3: Working in the Modernized NSRS 2020 Updated Edition with Use Cases
Working in the modernized NSRS:
NOAA TR NOS NGS 67
Notes: Links on the slide.

## Slide 53
https://geodesy.noaa.gov/SPCS/
State Plane Coordinate System of 2022 (CONUS, Alaska and Hawaii)
Three territory zones not shown:
    Puerto Rico and U.S Virgin Islands
  American Samoa
  Guam and Commonwealth of the
  Northern Mariana Islands
Notes: State Plane Coordinate System
https://geodesy.noaa.gov/SPCS/index.shtml
2022 Policy Changes
https://geodesy.noaa.gov/SPCS/draft-policy.shtml

## Slide 54
Beta NGS Map
https://noaa.maps.arcgis.com/apps/webappviewer/index.html?id=190385f9aadb4cf1b0dd8759893032db
Notes: Links on the slide.

## Slide 55: NGS ArcGIS Online Resources
NGS Datasheets
NOAA CORS Network
GPS on Benchmarks Priority List
(4 layers - marks, hexagons)
GEOID18 GPS on Benchmarks
GEOID12B GPS on Benchmarks
OPUS Shared Solutions
Mark Recoveries Submitted to NGS
Feature Services
Raster Tile Services
GEOID18 Height (CONUS, PRVI)
GEOID18 Difference (CONUS, PRVI)
GEOID18 Uncertainty (CONUS, PRVI)
GEOID18 Improvements (CONUS, PRVI)
*Geospatial Resources Webinar
Notes: Links on the slide.

## Slide 56
Beta Passive Marks Page
Notes: Links on the slide.

## Slide 57
Beta Leveling Projects Page
Notes: Links on the slide.

## Slide 58: Beta OPUS-Projects 5.0 for RTK/RTN Vectors
NGS is developing a new Standardized GNSS Vector EXchange Format (GVX) that will be used to ingest vectors into OPUS Projects
Notes: Links on the slide.

## Slide 59
Beta OPUS-Projects 5.0 for RTK/RTN Vectors : Please Test
Notes: Links on the slide.

## Slide 60
Questions?
2022 Rocky Mountain Survey Summit
Brian Shaw
brian.shaw@noaa.gov
Magnitude of the Deflection of the Vertical