## Slide 1: Changes Afoot After 2022
State Plane and the Death of the U.S. Survey Foot
Michael L. Dennis, PhD, PE, PLS
SPCS2022 Project Manager
NGS Webinar Series
November 10, 2022

## Slide 2: Poll question
Are you aware that NGS is in the process of modernizing the National Spatial Reference System (NSRS)?

## Slide 3: Poll question
Did you know that existing State Plane will be replaced by a new version as part of modernizing the NSRS?

## Slide 4: Why should you care about modernizing the NSRS?
Geodesy: the science of where things are

## Slide 5: “Modernizing” the NSRS means:
Updating all NSRS coordinates
  Replace existing datums with new datums
  Replacing existing State Plane with new State Plane
  Accounting for coordinates changing with time
Improving NGS products and services
Simplifying customer contributions
Making the NSRS:
  More accurate
  More accessible
  More efficient
Rollout in
2025

## Slide 6: The plan for today’s webinar
State Plane Coordinate System of 2022 (SPCS2022)
  Design philosophy
  Understanding linear distortion (with a wee bit of math)
  Status and timing of completion
U.S. survey and international foot
  Some background information
  “Deprecating” the U.S. survey foot
Adopting the modernized NSRS in state legislation
  History and status of existing legislation
  Recommendations on new legislation
  Dealing with the “foot” in statute

## Slide 7
SPCS2022
Making the Earth flat again
…one zone at a time
Surveyors (and engineers) projected coordinate systems
(geodesists, not so much)

## Slide 8
How surveyors and engineers see the Earth…

## Slide 9: A “flat” Earth for the future
State Plane Coordinate System of 2022 (SPCS2022)
Similar to existing State Plane…
  Same 3 map projection types
  Same ellipsoid (GRS 80)
But different…
  Based on new datums instead of NAD 83
  Designed to reduce difference between “grid” and “ground”
  Many more “zones”
  Zones “layers” will exist in most states
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 10: Getting acquainted with SPCS2022
Overall distortion design philosophy
  Linear distortion minimized (or “optimized”) at topographic surface (not at ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
What is linear distortion?
  Defined at a point (infinitesimal distances)
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm per km
Linear distortion | = | δ | = | Projected minus actual distance
 |  |  |  | Actual distance

## Slide 11: Map projection linear distortion
Distortion at a point computed as:
  where
    k = grid point scale factor (distortion due to Earth curvature)
    h = ellipsoid height of point (distortion due to change in height)
    R = Earth geometric mean radius curvature
  < 0  projected (grid) distance shorter than true (ground) distance
  > 0  projected (grid) distance longer than true (ground) distance
Height (“elevation”) factor
Grid point scale factor
Combined factor

## Slide 12
Grid distance < ellipsoid distance < ground distance (k < 1 and δ < 0)
Grid distance > ellipsoid distance < ground distance (k > 1 and δ < 0)
Projection axis (k0 < 1)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to ellipsoid surface
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
12
k0 = scale on projection axis
LCC: central parallel
TM: central meridian
OM: skew axis

## Slide 13
Projection axis (k0 > 1)
Projection surface (non-intersecting)
Ellipsoid distance
Topographic surface
Horizontal ground distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
h
R
Grid distance > ellipsoid distance ≈ ground distance (k > 1 and δ ≈ 0)
13
Ellipsoid surface

## Slide 14: Minimizing linear distortion
Distortion function of both and
  = distance from projection axis (kilometers)
  = change in ellipsoid height (meters)
Minimize both and simultaneously
  increases with square of distance
  increases linearly with change in height
  Treating separately can lead to poor results

## Slide 15
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface
15
Ellipsoid surface

## Slide 16
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Topographic surface
16
Ellipsoid surface

## Slide 17
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
ONLY way to reduce variation in distortion is to change projection axis location (or change projection).
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
IMPORANT: For large areas, there is no single defining ellipsoid height for scaling the projection.
17
This design approach used for SPCS2022 (minimizes distortion with respect to topography)
Projection axis scale can be less than 1 for steeply sloping areas even if heights are large.
R2
R1

## Slide 18
Projection axis
Non-intersecting
( > 1)
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Topographic surface
h2
h1
Ellipsoid height of surface not constant:
h1 ≠ h2
IMPORANT: For large areas, there is no single defining ellipsoid height for scaling the projection – even if there is no attempt to account for topographic slope.
NOT changing projection axis to reduce distortion variation
18
Ellipsoid surface

## Slide 19: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio
20 ppm | 2 cm/km | 0.1 ft/mile | 1:50,000
50 ppm | 5 cm/km | 0.3 ft/mile | 1:20,000
100 ppm | 10 cm/km | 0.5 ft/mile | 1:10,000
400 ppm | 40 cm/km | 2.1 ft/mile | 1:2,500

## Slide 20: Status of zone layout and designs
Designs by NGS
  159 zones (including 54 statewide)
  Plus 3 “special use zones” (in more than one state)
Designs by state stakeholders
  806 zones in 28 states
  Most are “low-distortion projections” (LDPs)
Total = 968 zones for 56 states and territories
  Number will likely decrease slightly
Compare to 125 zones in existing State Plane

## Slide 21: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 22: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 23: Number of SPCS2022 zones (preliminary)
CONUS, Alaska, and Hawaii
Three island zones not shown:
Puerto Rico and U.S. Virgins Islands
American Samoa
Guam and the Commonwealth of the Northern Mariana Islands

## Slide 24: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
24

## Slide 25: SPCS2022 linear distortion (prelim)
49 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 14% | 12% | 7%
±50 | 27% | 26% | 18%
±100 | 48% | 48% | 36%
±400 | 91% | 93% | 88%
City and area statistics (ppm): |  |  | 
 | Min | -1512 | -1627
 | Max | +2888 | +2987
 | Range | 4400 | 4614
 | Mean | -86 | -120
Mean weighted by pop = -100 |  |  | 
25

## Slide 26: SPCS2022 linear distortion (prelim)
646 zones (35 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 70% | 54%
±50 | 92% | 88% | 73%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -400 | -684
 | Max | +245 | +295
 | Range | 644 | 979
 | Mean | -5 | -23
Mean weighted by pop = -4 |  |  | 
26

## Slide 27: SPCS2022 linear distortion (prelim)
187 zones (10 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 78% | 78% | 73%
±50 | 91% | 90% | 88%
±100 | 99.8% | 99% | 97%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -261 | -465
 | Max | +120 | +240
 | Range | 381 | 705
 | Mean | -3 | -12
Mean weighted by pop = -1 |  |  | 
27

## Slide 28: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 29: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
29

## Slide 30: Existing SPCS 83 linear distortion
10 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 4% | 10% | 4%
±50 | 16% | 23% | 11%
±100 | 40% | 62% | 36%
±400 | 100% | 100% | 99.1%
City and area statistics (ppm): |  |  | 
 | Min | -263 | -967
 | Max | +86 | +342
 | Range | 349 | 1308
 | Mean | -83 | -135
Mean weighted by pop = -92 |  |  | 
30
Statistics are for land areas only

## Slide 31: SPCS2022 linear distortion (prelim)
21 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 77% | 38% | 17%
±50 | 90% | 67% | 38%
±100 | 98% | 93% | 68%
±400 | 100% | 100% | 99.8%
City and area statistics (ppm): |  |  | 
 | Min | -177 | -794
 | Max | +321 | +331
 | Range | 498 | 1125
 | Mean | -7 | -53
Mean weighted by pop = -4 |  |  | 
Statistics are for land areas only

## Slide 32: SPCS2022 linear distortion (prelim)
38 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 89% | 93% | 49%
±50 | 98% | 99.7% | 74%
±100 | 99.7% | 100% | 88%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -59 | -937
 | Max | +49 | +190
 | Range | 108 | 1127
 | Mean | +0.4 | -34
Mean weighted by pop = -8 |  |  | 
Statistics are for land areas only

## Slide 33: SPCS2022 linear distortion (prelim)
45 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 86% | 85% | 47%
±50 | 97% | 98% | 73%
±100 | 99.5% | 99.7% | 88%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -60 | -937
 | Max | +321 | +335
 | Range | 380 | 1272
 | Mean | -3 | -35
Mean weighted by pop = -10 |  |  | 
Statistics are for land areas only

## Slide 34: Existing SPCS 83 linear distortion
10 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 4% | 10% | 4%
±50 | 16% | 23% | 11%
±100 | 40% | 62% | 36%
±400 | 100% | 100% | 99.1%
City and area statistics (ppm): |  |  | 
 | Min | -263 | -967
 | Max | +86 | +342
 | Range | 349 | 1308
 | Mean | -83 | -135
Mean weighted by pop = -92 |  |  | 
34
Statistics are for land areas only

## Slide 35: About the timing of it all…
Timeline
  Complete review of stakeholder submittals (DONE)
  Late 2022-Early 2023: Preliminary designs for stakeholder review
  Mid-2023: Finalize all zone designs
Other things in 2023
  Provide machine-readable definitions
  Modify NGS algorithms (e.g., 1-parallel Lambert)
  Document new projection algorithms
Release with rollout of modernized NSRS
  Final definitions available by late 2023
  Release with new “datums” in 2025
Rollout in
2025

## Slide 36: Poll question
Did you know that the U.S. survey foot will be retired (“deprecated”) on December 31, 2022?

## Slide 37: A tale of two feet
Two versions of “foot” in current use:
“Old” U.S. survey foot
“New” international foot
1 ft = 0.3048 m exactly
‭1 ft = 1200/3937 m = 0.3048006096…‬ m
Differ by
2 parts per million (ppm) or ~0.01 ft (~1/8 inch) per mile
  A real problem with real costs

## Slide 38: A tale of two feet
Who uses U.S. survey feet?
  Surveyors in most (not all) states
  But it impacts everyone
  It is a major issue for the National Spatial Reference System (NSRS), especially State Plane coordinates (and other projected coordinate systems)

## Slide 39: Horizontal error when mixing up feet
SPCS 83 AZ Central Zone
UTM 83 12 North Zone

## Slide 40: Requiem for the U.S. survey foot
Will be “deprecated” on December 31, 2022
  Identified as being redundant or a source of confusion
  Deemed obsolete
  Its use should be avoided
After that date, international foot used for everything (sort of)
  Can call it “international foot” or just “foot”
  Use U.S. survey foot only for historical and legacy applications
December 31, 2022 is coming
  But NSRS modernization will occur in (mid) 2025
  What should you do between those dates?

## Slide 41: The clock is ticking…
DECEMBER
2022
December 31, 2022 is almost here
Are you prepared?
20
21
22
23
24
25
26
27
28
29
30
31
31

## Slide 42: To help get prepared, let’s talk about legislation

## Slide 43: Why have State Plane legislation?
Proposed to state legislatures in 1945 by Council of State Governments to:
  Establish legal status
  Insure uniformity and definiteness in use
  Impose reasonable standards when coordinates become part of public record
Additional reasons:
  To make corners “indestructible”
  Save time and money by providing specifications on using State Plane
Other things:
  Use of system is permissive, not mandatory
  Uniformity of legislation is desirable
  Legislation not required to establish State Plane

## Slide 44: History of State Plane in legislation
First nine states with State Plane laws:
  1935 (NJ), 1937 (PA), 1938 (NY), 1939 (MD, NC, GA), 1941 (MA), 1943 (TX), 1944 (LA)
Model act provided to state legislatures in 1945
  Included zone projection parameters
  Specified ½ mile max distance to 2nd order control (for public recording)
Some changes in model act for SPCS 83 (created 1977)
  Specified U.S. survey foot for SPCS 27; meter for SPCS 83 (but not U.S. survey foot)
  Max distance to 2nd order control changed from ½ mile to 1 km
  Interesting note at end of SPCS 83 model act (ca. 1989):
“In light of GPS technology, the 1 km limitation… should be reevaluated.”

## Slide 45: State Plane legislation for SPCS 83 and 27
56 U.S. jurisdictions
  41 with SPCS 83 and 27
  9 with only SPCS 83
  1 with only SPCS 27
  5 with no legislation

## Slide 46: What about the U.S. survey foot?
Will be deprecated on Dec 31, 2022
  Per final determination Federal Register Notice issued on Oct 5, 2020
  Collaborative action by National Institute of Science and Technology (NIST) and NGS
  Describes public comments received, along with the plan, resources, training, and other information for an orderly transition with minimum disruption
(this image is hyperlinked to the Federal Register page)

## Slide 47: SPCS 83 legislation and foot version
56 U.S. jurisdictions
Legislation
  International foot: 6
  U.S. survey foot: 28
  Neither: 16
  No legislation at all: 6
Fed Register Notice
  U.S. survey foot: 12
  In lieu of legislation
  Done 2006-2009
47
47

## Slide 48: Putting the “best” foot forward
U.S. survey foot will be retired
  Not supported for State Plane Coordinate System of 2022 (or any part of modernized NSRS)
  Only international foot will be supported by NGS
In some states, law specifies U.S. survey foot for boundary surveys
  A separate issue since not part of NSRS (not dealt with here)
Effective December 31, 2022
  Independent of NSRS modernization
  U.S. survey foot will still be supported for legacy products (e.g., existing State Plane)…

## Slide 49: Rumor of U.S. survey foot death greatly exaggerated
U.S. survey will be foot deprecated on December 31, 2022
But use can continue for SPCS 83 (and SPCS 27)
  The 40 states that “officially” use U.S. foot for SPCS 83
  All SPCS 27 zones
  NGS will support such “legacy” use forever
  But NOT supported for ANY zones in SPCS2022
Please repeat:
NGS will always support U.S. survey foot for SPCS 83 and 27
Thank you.

## Slide 50: Why allow U.S. survey foot after Dec 31, 2022?
Key idea: done in an “orderly fashion with minimum disruption”
  Sudden switch for existing coordinate system too disruptive
  Will give states more time to prepare
  U.S. survey foot usage will diminish over time (especially after 2025)
Recommend enabling in legislation
  Include SPCS 83 and SPCS 27 in statute as “legacy” systems
  Gives way to keep using U.S. survey foot after Dec 31, 2022
Better to have change occur with new State Plane
  Change in length of foot “hidden” in change of projection scale
  Projection scale change much greater than 2 ppm for most zones
NGS and NIST are not regulatory agencies, so can’t “enforce” change

## Slide 51: Poll question
Are you associated with any of the following SPCS2022 stakeholder groups in your state? (select all that apply)

## Slide 52: Modernized NSRS in legislation
National Spatial Reference System will change in 2025
NGS recommends updating legislation for modernized NSRS
Template and example legislation available on NGS website
geodesy.noaa.gov

## Slide 53: Template state legislation https://geodesy.noaa.gov/datums/newdatums/GetPrepared.shtml
Created by NSPS, AAGS, and NGS
  Intended to augment existing legislation
  Defined by NGS OR by state (not both)
Reduce need for later legislation updates
  Do not include specific names of datums, etc.
  Do not include zone projection parameters
Foot version
  Must be 1 ft = 0.3048 m for new State Plane
  Can be 1 ft = 1200/3937 m for previous State Plane

## Slide 54: Example state legislation https://geodesy.noaa.gov/datums/newdatums/GetPrepared.shtml
Washington and South Dakota
  Uses “foot” definition 1 ft = 0.3048 m
  Nothing about previous State Plane
Kentucky
  Uses name “international foot”
  Refers to administrative regs for details
  Added SPCS 27 (not previously legislated)
Alaska
  “Alaska Coordinate System of 2022”
  Uses name “international foot”

## Slide 55: Recommendations on NSRS legislation
Do not include specific technical information
  No zone parameters, accuracy, or performance specifications
Retain previous versions (SPCS 27 and SPCS 83)
  Provides mechanism for continuing to use U.S. survey foot for SPCS 83
Goal: “future-proof” legislation
  Create statute that will not require later updates
…and to just make life easier
  Much harder to change information in statute
  Less need to explain to legislators
  Some states will have a LOT of zones (e.g., 90 in Utah, 89 in Ohio, 63 in Arizona, etc.)
  Do you really want to put all of these zones into statute?

## Slide 56: Do you really want stuff like this in statute?
Arizona Revised Statute, Title 33, Chapter 1, Article 3, Section 133:
B. For the purpose of more precisely defining the Arizona coordinate system, the following definitions of the national geodetic survey are adopted:
1. The Arizona coordinate system, 1983, west zone, is a transverse mercator projection of the North American datum, 1983, having a central meridian 113° 45' 00" west of Greenwich, on which meridian the scale is set one part in fifteen thousand too small. The origin of the coordinates is at the intersection of the meridian 113° 45' 00" west of Greenwich and the parallel of 31° 00' 00" north latitude. This origin is given the coordinates of "X" equals seven hundred thousand feet and "Y" equals zero feet.
Do you really want to explain this to legislators?
Do you want to repeat this 90 times (Utah), 89 times (Ohio),…?
What if you want or need to change something?
What if anything becomes obsolete?

## Slide 57: Or this?
Arizona Revised Statute, Title 33, Chapter 1, Article 3, Section 137:
A. Extensions and densifications of the ground marking system of the Arizona coordinate system, 1983, shall be executed in conformity with the standards and specifications of the federal geodetic control committee for first order, second order class I and second order class II surveys and computed on the North American datum, 1983.
B. The results of these surveys shall be published by a competent department of the federal government, such as the national geodetic survey, or a surveyor qualified to practice in this state, in which case the survey results shall bear a certification to the effect that the specifications of the federal geodetic control committee have been followed.
C. Extensions and densifications of the ground marking system by first order, second order class I or second order class II methods only shall be used. Such extensions and densifications shall be integrated with previously established horizontal control stations of equal or higher order to form a matrix or network no part of which shall have positional errors exceeding those specified for class II second order. The spacing intervals shall not exceed three miles.
Remember prescient words about model act in 1989:
“In light of GPS technology, the 1 km limitation… should be reevaluated.”
Obsolete

## Slide 58: Modernized NSRS in state legislation
Encouraged by NGS
  Part of NGS SPCS2022 Policy (§ III.C)
  But legislation not required to create SPCS
Please note:
  Cannot impose SPCS characteristics on NGS
  NGS has last word on SPCS
Keep in mind, NGS is a metric (SI) shop
  Have been since 1977
  We’d love it if you went metric, too! (and so would NIST)
(this image is hyperlinked to NGS policies page)

## Slide 59: Summary
Long history of State Plane in legislation (since 1935!)
Make legislation “future proof”
  Do not include specific names for modernized NSRS
  No technical info (e.g., projection parameters, surveying specifications)
Legislation template and actual examples available
U.S. survey foot will not be supported in modernized NSRS
Legislation entirely up to states; NGS can only provide guidance
  NGS can’t make states do anything…
  …but states can’t make NGS do anything, either
An incentive to cooperate

## Slide 60
So let there be questions, or let there be none.

## Slide 61: Post-webinar survey question
What is your profession?