## Slide 1
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
“Datums and State Plane Coordinate Changes for 2022”
Alabama Association of Floodplain Managers
2019 Fall Conference
Orange Beach, AL
October 28, 2019

## Slide 2: U.S. Department of Commerce National Oceanic & Atmospheric Administration National Geodetic Survey
Mission: To define, maintain & provide access to the
National Spatial Reference System (NSRS)
to meet our Nation’s economic, social & environmental needs
National Spatial Reference System
* Latitude * Scale
* Longitude * Gravity
* Height * Orientation
& their variations in time
Notes: - NSRS benefit to the nation = $2.5B/year
est. 300K precision GPS users worldwide (2008); ¼ in US
- Very exciting to us at NGS to see how it has evolved over the years – now cm-accuracy capability / tracking with time

## Slide 3: New U.S. Geometric Datums in 2022

## Slide 4: National Spatial Reference System(NSRS) Improvements in the Horizontal Datums
TIME NETWORK METHOD
NETWORK SPAN ACCURACY OF REFERENCE
NAD 27 1927-1986 10 meter
NAD83(86) 1986-1990 1 meter
NAD83(199x)* 1990-2007 0.1 meter
HARN
NAD83(2007) 2007 - 2011 0.01 meter
(CORS)
NAD83(2011) 2011 - 2022 0.01 meter
(CORS)
TRAVERSE & TRIANGULATION -
GROUND MARKS USED FOR REFERENCING THE NSRS.
GPS BECOMES MEANS OF POSITIONING – STILL GRND MARKS.
GPS – CORS STATIONS ARE MEANS OF REFERENCE FOR THE NSRS.
TERRESTRIAL BASED
REFERENCE SYSTEM
FOR NSRS
TERRESTRIAL BASED REFERENCED
SYSTEM FOR NSRS
SPACE BASED
REFERENCE SYSTEM
FOR NSRS

## Slide 5
NSRS Reference Basis
Old Method - Ground
Marks (Terrestrial)

## Slide 6
NSRS Reference Basis
New Method - GNSS Stations
(CORS)

## Slide 7
Datum based on best known information about the earth’s size and shape from the early 1980’s (≈35 years old), and the terrestrial survey data of the time.
NAD83 is NON-geocentric & hence inconsistent w/GNSS .
Necessary for agreement with future ubiquitous positioning of GNSS capability.
Why Replace NAD83?

## Slide 9: Future Geometric (3-D) Reference Frame
Blueprint for 2022: Part 1 – Geometric Datum
Replace NAD83 with new geometric reference frame – by 2022.
CORS-based, accessed via GNSS observations.
Coordinates & velocities in ITRF (IGS) & new US reference frame.
      (coordinates in time) (stable coordinates)
  Transformation tools will relate NAD83 to new US reference frame (NCAT with 2022 transformation).

## Slide 10: Datum Names
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 11
New geometric datum minus NAD 83 (horizontal)
For Alabama = 0.9 > 1.1 m (2.9 > 3.6 ft.)

## Slide 12
New geometric datum minus NAD 83 (ellipsoid height)
For Alabama = -1.27 > -1.39 m (-4.2 > -4.5 ft.)

## Slide 13: New U.S. Vertical Datum in 2022

## Slide 14
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Were determined by leveling from a single point, allowing cross-country error build up
Why isn’t NAVD 88 good enough anymore?
* NAVD 88 is a terrestrial based vertical datum that changes as the land changes.

## Slide 15
Long term fix: Re-level some/all of NAVD 88
  81,500 km of 1st order leveling at least
  625,000 km of mixed 1st and 2nd order leveling
Re-leveling NAVD 88 estimated to cost between
  $200 Million and $2 Billion
Time factor in that amount of leveling
Still would have problems related to passive control
Can NAVD 88 be fixed?
Notes: Re-leveling NAVD 88 won’t fix:
Sparseness of the bench marks
Continued subsidence or uplift of bench marks
Destruction of bench marks
Canada’s decision not to adopt NAVD 88
Whatever errors caused a continent-wide 1 meter build up in the leveling the first time around

## Slide 17: NEW VERTICAL DATUM (Rationale)
  A move away from differentially leveled passive control as the defining mechanism of the reference surface
  To be consistent with the shift in the geometric reference frame/ellipsoid (2022)
  Improvement in our technical abilities in reference surface realization (geopotential gravimetric reference surface - 1cm accuracy of the geoid (GNSS/GRAV-D))
  Goal - ability to establish 2cm orthometric height anywhere in U.S. using a minimum of 15 min. of GNSS data.
  The new geopotential reference surface will be aligned with the geometric reference frame/ellipsoid (i.e., no hybrid geoid)

## Slide 18: Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
  The New:
  The North American-Pacific
  Geopotential Datum of 2022
  (NAPGD2022)

## Slide 19
Replace the Vertical Datum of the USA by 2022 (at today’s funding)
GRAV-D is:
  An airborne gravity survey of the entire country and its holdings
  A 2022 gravimetric geoid accurate to 1 cm
  Long-term monitoring of geoid change over time
  Partnership surveys
Working to launch a collaborative effort with the USGS for simultaneous magnetic measurement
Acting Manager: Jeffery Johnson
Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
Gravity and Heights are
inseparably connected

## Slide 20
Extent of 2022 gravimetric geoid model used for NAPGD2022

## Slide 21: Expected Orthometric height Changes – NAVD88 – NAPGD2022
For Alabama = -0.2 > -0.4 m (-7 > -16 in.)

## Slide 22
Importance of Correct Positioning
Notes: NGS Regional Geodetic Advisors
https://geodesy.noaa.gov/ADVISORS/
State Geodetic Coordinators
https://geodesy.noaa.gov/ADVISORS/state-geodetic-coordinators.shtml

## Slide 23: How to Plan for 2022
Move to newest realizations
  NAD 83(2011) epoch 2010.00
  GEOID 18 (hybrid geoid)
Utilize passive marks that are up to date
  Stay aware of what marks are included in datum updates
  Use OPUS & Hgt. Mod procedures to update mark positions
Metadata
  Document positions in current datums to know what you have in the future.
NGS Outreach Efforts
  Participate in NGS webinars, Geospatial summits, contact NGS Regional Advisor, etc.
NEW

## Slide 24: State Plane Coordinates System - SPCS 2022 Project

## Slide 26: Final SPC 83 State Systems - 2001

## Slide 27: SPCS2022 Stakeholders
State groups that form the “Stakeholder Group”
  Departments transportation, Cartographer/GIS office
  Professional surveying, engineering, GIS societies
  Colleges/universities with geospatial curriculum
  Federal agencies can “sign on” with states
NGS is looking for a “consensus” response from the Stakeholders of each state

## Slide 28
SPCS2022 characteristics different from SPCS 83:
  NGS will design statewide and default zones
  Up to 3 zone “layers” allowed (including an LDP layer)
  Coordinate changes of at least 10,000 m everywhere
  Longitudes will be positive east (0° to 360°)
New State Plane Coordinate System
    (Orange Beach = 360° - 87° = 273° E)
Notes: SPCS2022 is referenced to 2022 TRFs and thus part of new “datums”, and will replace existing SPCS 83 (referenced to NAD 83)
Similar to SPCS 83 in some ways:
  Designed by state, using same reference ellipsoid and same projection types
Differs from SPCS 83 in other ways:
  Designs minimize distortion at topographic surface rather than ellipsoid surface (reduces distortion where system is actual used)
  NGS will design default zones for every state, and default zones corresponding to existing SPCS 83 zones for states that do not request or propose something different
  Can have up to 3 zone layers (where one layer must be a statewide zone). The other layers can be default zones and/or LDP zones (but not designed by NGS). Only one layer can be discontinuous (i.e., zones do not completely cover a state); it is expected that discontinuous layers will always be LDP zones.
  “Special use” zones are for major urban areas, American Indian reservations, or federal jurisdictions/applications that fall in more than one state. These must eb approved by the NGS Director on a case-by-case basis.
The stakeholder role is vitally important for states that want something other than default zones. But all requests and proposals from stakeholders must be unanimous to become part of SPCS2022.

## Slide 30
Huntsville
467,764 meters
= 1,534,658.8 iFt.
= 1,534,655.7 sFt.
Diff. = 3.1 ft.
 467.764 Km
 2 ± ppm
Mobile

## Slide 32: SPCS2022 Policy & Procedures
August 31, 2018 for Federal Register Notice comments
On policy and procedures
Includes “special purpose” zones
Deadlines for consensus input
Mar. 31, 2020 for requests and proposals
  Requests are for designs by NGS
  Proposals are for designs by stakeholders
Mar. 31, 2021 for submittal of approved designs
  Proposal must first be approved by NGS
  Designs submitted by stakeholders
  Designs must be complete before NGS review
Dec. 31, 2022 for NGS to confirm zone computations
After deadlines, will be a change request for SPCS2022
NGS.SPCS@noaa.gov

## Slide 33
? ? QUESTIONS ? ?
Denis.Riordan@noaa.gov