## Slide 1
NADCON 5
Andria Bilich
Dru Smith
NOAA’s National Geodetic Survey

## Slide 2: Outline
Historical Overview
NADCON 5

## Slide 3: Part 1

## Slide 4: History: NADCON

## Slide 5: Historical Overview: NADCON 1.0
1989 : NAD 83(1986) released
  1990: NADCON v1.0 released
    “NAD 27 to NAD 83”
      Actually:
        NAD 27 to NAD 83(1986) in CONUS
        NAD 27 to NAD 83(1986) in Mainland & Aleutian Alaska
        PR40 to NAD 83(1986) in Puerto Rico
        OHD to NAD 83(1986) in Hawaii
        SG1952 to NAD 83(1986) in St. George Island
        SP1952 to NAD 83(1986) in St. Paul Island
        SL1952 to NAD 83(1986) in St. Laurence(sp) Island

## Slide 6: Historical Overview: NADCON 1.0
DOS based
FORTRAN executable

## Slide 7: Historical Overview: NADCON 1.0
Region | Accuracy lat/lon
CONUS | 16 cm / 15 cm
Puerto Rico | 4 cm / 5 cm
Alaska | 48 cm / 46 cm
Hawaii | 22 cm / 15 cm
St. George | 3 cm / 2 cm
St. Laurence | 3 cm / 2 cm
St. Paul | 17 cm / 10 cm
Gulf of Mexico (offshore) | 1-3 meters

## Slide 8: Historical Overview: NADCON 2.1
1990 through 1997: HARNs released, state-by-state
  NADCON expands (v2.10) to include state-by-state transformations
    “NAD 83(HPGN) to NAD 83(1986)”
      State-by-state (sometimes sub-state, sometimes multi-state):
        AK, AL, FL, TN, WI, LA, CO….
        WA/OR, MD/DE, PR/VI, ME/VT/NH/CT/RI
        CA (north) , CA (south)
        TX (west), TX (east)
        American Samoa (west), American Samoa (east)

## Slide 9: Historical Overview: NADCON 2.1
DOS based
FORTRAN executable

## Slide 10: Historical Overview: NADCON 2.1
1997 through 2005: FBNs released, state-by-state
  Only 19 states saw significant changes from the HARN to have a new “datum tag”
    Examples:
      Wisconsin has NAD 83(1991) and NAD 83(1997) in the IDB
      Ohio has only NAD 83(1995)
  NADCON v2.10 continued to expand through these years.
    It is not clear if whether all grids called “hpgn” in NADCON 2.10 are actually HARN or whether some are FBN.
    There is effectively no documentation of the process.

## Slide 11: Historical Overview: NADCON 4.2
Around 2004 or so, NGS contracted out to have NADCON updated
  JAVA based, downloadable, menus/windows driven
  Released as NADCON 4.2
    Difficult to install, errors in hindsight
In 2005 NGS agreed to build a USSD to NAD 83(1986) expansion to NADCON
  “Leaping over” the NAD 27 to NAD 83(1986) transformation

## Slide 12: History: GEOCON & GEOCON11

## Slide 13: Historical Overview: GEOCON 1.0
2007: Nationwide Adjustment of all GPS vectors
  Customers began calling for a “HARN to 2007” expansion of NADCON
    NGS resisted, indicating the scale of the changes was so small as to be “gridding noise”
    Hired Dennis Milbert to investigate
      Plenty of signal, but at about the same magnitude as the noise
      A nationwide transformation program built: GEOCON v1.0
      Tied “the last pre-2007, post-1986 published coordinate” on a point to its 2007 coordinate
        Mix of HARN and FBN without distinction
      DOS based FORTRAN executable
      NGS expanded that to an online computation page

## Slide 14: Historical Overview: GEOCON11
2011: Nationwide Adjustment of all GPS vectors
  Expanded Dennis Milbert’s contract to build a 2007 to 2011 expansion to GEOCON: GEOCON 11
    A nationwide transformation program
      DOS based FORTRAN executable
      NGS expanded that to an online computation page

## Slide 15: Historical Overview: GEOCON / GEOCON11 v1.1
2012: Began work on GEOCON v1.1 and GEOCON11 v1.1
  Fixed a few bugs
  Combined a few manuals
  Allowed free-format, not just Bluebook, input/output

## Slide 16: Historical Overview: GEOCON v2
2014: GEOCON v2.0 released
  Complete overhaul of GEOCON and GEOCON v1.1
  Combined both into 1 program
  Rigorously defined “supported” transformations in each state/territory
    No more “mix of HARN and FBN” for any transformation
  HARN to FBN: State-by-State (Like NADCON’s 83/HPGN)
  FBN to 2007: Nationwide
  2007 to 2011: Nationwide
  Also supported 1993/1997/2002 realizations in Puerto Rico

## Slide 17: Historical Overview: Problems
To transform from NAD 27 to NAD 83(2011) in Kansas
  Run NADCON 4.2 to compute
    NAD 27 to NAD 83(1986) grid (nationwide)
    NAD 83(1986) to NAD 83(HPGN) grid (statewide)
  Run GEOCON 2.0 to compute
    HARN to FBN grid (statewide)
    FBN to 2007 grid (nationwide)
    2007 to 2011 grid (nationwide)
  Add everything up yourself
  Have a nice day

## Slide 18: Historical Overview: Problems
Multiple DOS based programs
Lack of documentation
Inconsistent decision making
  Accuracy reporting
  State vs nationwide grids
  Skipping over transformations
“Missteps” made by NGS…
    Too many to list and that would just be airing dirty laundry
      If you care, read the report.

## Slide 19: Part 2

## Slide 20: What is NADCON v5.0?
How?
Fresh pull of IDB
New suite of analysis tools
New grids from scratch
Skip no realizations
Make available through Geodetic Toolkit
Transformations and error estimates for any point within a regional boundary, provided through biquadratic interpolation off of a grid
Lat/lon in arcseconds
Ellipsoidal height in meters

## Slide 21: Regional Approach
CONUS
Alaska (+ St. islands)
Hawaii
Puerto Rico and US Virgin Islands
American Samoa
Guam and Commonwealth of Northern Mariana Islands
No state-wide realizations (e.g. HARN)
USSD to NAD83(1986) not supported [must go through NAD27]
NAD83_HARN and NAD83_FBN are groupings of HARN and FBN

## Slide 22: Included Datums
Region | Datums
CONUS | USSD, NAD27, NAD83(1986), NAD83(HARN), NAD83(FBN), NAD83(2007), NAD83(2011)
Alaska | NAD27, NAD83(1986), NAD83(1992), NAD83(2007), NAD83(2011)
Alaska – Saint islands | 
Hawaii | OHD, NAD83(1986), NAD83(1993), PA11
Puerto Rico and US Virgin Islands | PR40, NAD83(1986), NAD83(1993), NAD83(1997), NAD83(2002), NAD83(2007), NAD83(2011)
American Samoa | AS62, NAD83(1993), NAD83(2002), PA11
Guam/CNMI | GU63, NAD83(1993), NAD83(2002), MA11
31 transformations

## Slide 23: NADCON5 Process (1/2)
Pull from IDB
one record for every instance that a latitude, longitude, or an ellipsoid height was loaded into the NGS IDB
Outlier Removal
~6000 outliers in all transformations
Thin the Data
Most outliers: NAD83(HARN) to NAD83(FBN) [2590]
ID’d by statistical and “eyeball” methods
Coordinate Differences
Grid the Data
Vector = new_datum minus old_datum
Plots of vectors, coverage
Error analysis

## Slide 24: NADCON5 Process (2/2)
Pull from IDB
Outlier Removal
Thin the Data
Grid the Data
Use a median filter to separate data into “thinned” and “dropped”
Thinned (transformation) vs dropped: (error formulation)
Requires choosing a cell size
Fit a surface under tension to thinned data
Surface expressed as grid (lookup table)
Error analysis
Build error grid (lookup table)
All vectors used in error formulation
Coordinate Differences

## Slide 25: Pull from IDB
US Standard Datum | NAD 27
AA9371 TX 453 N301622.34000 W0974420.01000 N/A | N301622.45000 W0974419.16000 N/A
AA9372 TX 453 N301626.15000 W0974420.01000 N/A | N301626.24000 W0974419.16000 N/A
AB0076 TX 061 N255754.23000 W0971201.91000 N/A | N255754.37580 W0971200.95657 N/A
AB0225 TX 061 N260619.42900 W0971915.79500 N/A | N260619.57300 W0971914.85300 N/A
AB0289 TX 061 N260845.57000 W0972809.47200 N/A | N260845.77867 W0972808.60964 N/A
AB0338 TX 061 N260341.34400 W0971609.71700 N/A | N260341.48900 W0971608.77400 N/A
AB0917 TX 215 N260507.70300 W0975157.70400 N/A | N260507.83900 W0975156.76000 N/A
AB0992 TX 261 N263645.56300 W0974517.08600 N/A | N263645.69300 W0974516.14900 N/A
AB1366 TX 061 N255728.87000 W0971516.23000 N/A | N255729.02000 W0971515.29000 N/A
Examples:
USSD to NAD27
Notes: Adjusted only
Chronologically back to back

## Slide 26: Coordinate Differences
New datum, minus old datum
Creates a vector
Note: lat and lon are separate transformations

## Slide 27: Outlier Removal
GEOCON 1.0: all coord pairs should be reflected in transformation (grid or accuracy estimates)
NADCON5: Outliers are…
  Disruptive to creation of grid
  So far outside norm that any good surveyor would have rejected these points from their work
We identify reasons for outliers in ASCII file

## Slide 28: Thin the Data
Vectors are separated using a median filter:
Thinned – one per cell, used for transformation
Dropped – everything else, retained for error estimates

## Slide 29: Aside: Selecting Cell Size
Thinned vs. dropped requires geographically binning the data
Best cell size:
  Coarsest grid which represents the data
  Uniform distribution of vectors (no gaps, clusters)
How did we choose?
  Ran a range of grids (1’ to 30’)
  Points per cell
  Residuals of grid vs thinned/dropped vectors
Notes: 31 transformations each got the analysis of 1’ through 30’

## Slide 30: Grid the Data
Fit a surface under tension to the thinned data
Express the surface as a grid
Notes: Transformation Grid : T = 0.4

## Slide 31: Aside: Generic Mapping Tools (GMT) surface
Routine to fit a surface under tension
Tension varies:
  0.0: minimum curvature solution (undesired oscillations and false local max/min)
  1.0: harmonic surface (no local max/min except at data pts)
  NADCON5 grids: 0.4
Notes: Why 0.4? Because “experience shows” that coord diffs work well under that tension. Milbert chose it for GEOCON.

## Slide 32: Error Analysis
Total error
Method Noise
Data Noise
Disagreement between transformation grid and original vectors
GMT surface
Two types of errors
Sources

## Slide 33: Method Noise
GMT surface: tension varies 0.0 (min curvature) to 1.0 (harmonic surface)
How to summarize range of possible values?
Schwarz et al: Std of large sample = difference of high/low values of 3-element sample * 0.59070
Our 3-element sample: grids at 0.0, 1.0 and 0.4 tensions

## Slide 34: Data Noise: disagreement between grid and data
Residuals of final transformation grid (surface = 0.4) relative to original coordinate differences
In each cell, take RMS of residuals
Grid the RMSs (tension = 0.9)

## Slide 35: Error Grid
Total error
Method Noise
Data Noise
RMS combination

## Slide 36: NADCON5 in the Geodetic Toolkit
http://beta.ngs.noaa.gov/gtkweb/

## Slide 37
X, Y, Z
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83
Notes:

## Slide 38
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 39
Questions?