## Slide 1
Modernizing the National Spatial Reference System
Juliana Blackwell
Director
NOAA’s National Geodetic Survey

## Slide 2: The bottom line
If you do geospatial work in the United States and its territories,
and you work in the National Spatial Reference System,
then every product you’ve ever made…
  every survey
  every map
  every lidar point cloud
  every image
  every DEM
… WILL have NEW coordinates in 4 years.
Let’s talk about what this means, why it is happening, and how you can prepare.

## Slide 3: Who and What
The National Geodetic Survey, the federal agency responsible for establishing and maintain the positioning framework to support all federal civilian mapping and charting in the United States, is modernizing the National Spatial Reference System (NSRS).
What does this mean?
  All horizontal and vertical datums in the NSRS (NAD 83, NAVD 88, etc.) will be updated with:
    Four (4) new Terrestrial Reference Frames of 2022
    North American-Pacific Geopotential Datum of 2022
  New tools, products, services, and methodologies will be developed jointly to support the transition and access to an improved, modernized NSRS.

## Slide 4: Why and When
Why?
  The current national datums (NAD 83 and NAVD 88) were established in the 1980s, before GPS technology revolutionized surveying and positioning.
  The current datums have errors exceeding 1 meter.
  Modernization of the NSRS is driven by advancements in technology and is designed to support future growth. “Positioning America for the Future”
When? By December 31, 2022
Will it be an immediate or gradual change? Immediate

## Slide 5: “Modernizing the NSRS” means…
Replacing the current horizontal datums (NAD 83)
Replacing the current vertical datums (NAVD 88)
Improving data submission and data access
Improving online tools
Updating survey methodologies

## Slide 6: These are part of the NSRS*
Horizontal Datums and Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations and Conversions
USSD | NGVD 29 | IGLD55 | GEOID90 | NADCON
NAD 27 | NAVD 88 | IGLD85 | GEOID93 | VERTCON
NAD 83 | PRVD02 |  | ALASKA94 | 
 | ASVD02 |  | GEOID96 | SPCS 27
 | NMVD03 |  | GEOID99 | SPCS 83
 | GUVD04 |  | GEOID03 | 
 | VIVD09 |  | GEOID06 | 
 |  |  | GEOID09 | 
 |  |  | GEOID12(A,B) | 
*This not a complete list.

## Slide 7: These are not part of the NSRS*
Horizontal Datums and Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations and Conversions
WGS 84 | IHRS |  | OSU91A | CORPSCON
ITRF |  |  | EGM96 | Appendix B.6 of DMA TR 8350.2 (WGS 84)
IGS |  |  | EGM2008 | Oregon Coordinate Reference System
 |  |  |  | The Kansas Regional Coordinate System
*This is not a complete list.

## Slide 8
All coordinates and heights will change!

## Slide 9: Effect on latitude and longitude

## Slide 10
NAD 83 (MA11)
NAD 83 (PA11)
NAD 83 (2011)
North American Datum of 1983
Three frames:
NAD 83 (2011): North America and Caribbean plates
NAD 83 (PA11): Pacific plate
NAD 83 (MA11): Mariana plate

## Slide 11: Geometric: Out with the old, in with the new
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
Four (4) plate-fixed frames:
North American
Caribbean
Pacific
Mariana

## Slide 12
NMVD03
ASVD02
NAVD 88
NA and Caribbean
NAVD 88
IGLD 85
PRVD02
VIVD09
Pacific
GUVD04
NMVD03
ASVD02
Current vertical datums of the NSRS
GUVD04
PRVD02
VIVD02
IGLD 85
NAVD 88

## Slide 13: Vertical: Out with the old, in with the new
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  Will include GEOID2022 DEFLEC2022 SGRAV2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid Heights
Deflections of
the Vertical
One vertical datum from pole to equator

## Slide 14: Expected changes to orthometric heights

## Slide 15: What life will be like in the future
Vastly improved flood plain mapping
Water flows due to differences in gravity
Critically important in low-lying, flat communities
Fundamental support for new technologies
“Smart Highways” for autonomous vehicles
Revolutionize professional surveying
No more need for installing and locating bench marks
Absolute, consistent positioning autonomously, anywhere
Impacts on infrastructure
Any application requiring precise positioning -- bridges, tunnels, railways, agriculture, navigation -- will be easier and more accurate

## Slide 16: Impact
Every historic position (on a map, chart, survey, etc.) with an assumed accuracy of better than 1 meter will become obsolete.
This includes:
3DEP Elevation Datasets
National Hydrography Datasets
Flood Insurance Rate Maps

## Slide 17: What can you do to prepare?
Learn more
Become familiar with NGS models and tools
Assess data workflows in collaboration with NGS
Provide feedback
Save original data (lidar point clouds)!

## Slide 18: Information on “New Datums”
What to expect
How to prepare
Track our progress
Related projects
Educational videos
Learn more
FAQs
Contact us
Sign up for updates
geodesy.noaa.gov/datums/newdatums/

## Slide 19
Modernizing the NSRS
The “blueprint” documents: Your best source for information

## Slide 20
2019 Geospatial Summit
Geospatial Summit
Dates: May 6 - May 7, 2019
Location: Silver Spring Civic Center
Invitees: NSRS users plus NGS Subject Matter Experts
Public announcement coming soon!
SAVE THE DATE!

## Slide 21: 2018 Experimental Geoid Model
beta.ngs.noaa.gov/GEOID/xGEOID18/

## Slide 22: Coordinate Conversion and Transformation Tools
NGS Coordinate Conversion and Transformation Tool (NCAT) geodesy.noaa.gov/NCAT/
VDatum Tool (NCAT plus tidal datums) vdatum.noaa.gov
Both will run in three modes:
  Web services
  Browser interactive
  Downloadable