## Slide 1
Blueprint for 2022, Part 2:
Geopotential Coordinates
AKA “Replacing NAVD 88”
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 3: Overview
Quick topics:
  How and Why (again)
  Geodetic Control
  Why not leveling?
  Geoid modeling history
  Geopotential
Deeper dives:
  Time Dependency
  Sea Level and the geoid (or not)
  NAPGD2022
    /nap-jee-dee-twen-tee-twen-tee-too/
  Leveling? Yes!
  Updates and Replacements
  Summary

## Slide 4: Why NGS wrote it…
2007 (1st Ten Year Plan) : “Replace NAVD 88”
2012 (2nd Ten Year Plan) : “Replace NAVD 88”
Details were lacking, and therefore outreach material couldn’t properly prepare the user community for 2022

## Slide 5: How it came into being…
The idea of “blueprint” documents was fuzzy at first, but the need for details was clear
2014-2017: Driven mostly by the geometric side
  Culminated in early 2017: Blueprint Part 1: Geometric Coordinates
  Obvious follow-up was “Part 2, Geopotential Coordinates”

## Slide 6: Content: Geodetic Control
Verbatim from Blueprint, Part 1
  Additional words about vertical stability

## Slide 7: Content: Why not leveling?
Wrong tool for a continental vertical datum on a dynamic planet
Geoid accuracy has improved by 2 orders of magnitude in the last 50 years
  Including its dynamic component
GPS height accuracy has reached the cm level

## Slide 8: Content: Geopotential
If you care about any of the following things…
  Heights (orthometric, dynamic, normal)
  Gravity
  Deflections of the Vertical
    Including their impact on azimuths
…then you should care about geopotential

## Slide 9: So…what is “Geopotential”
Geo: Earth
Potential: Gravity Potential Energy
Geopotential: Gravity Potential Energy Field that surrounds the Earth.
  Mass => Geopotential (including “the geoid”)
  Mass Change => Geopotential Change (including “the geoid”)
More later, if time allows…

## Slide 10: Time Dependency

## Slide 11: Time and Mass
Mass quantity in the Earth system is effectively constant
Mass distributions in the Earth system are time dependent and some are large enough to be measurable
  Secular
    Shape change to every equipotential surface (like the geoid)
    Size change to global mean sea level
  Episodic
  Periodic

## Slide 12: Secular Mass Movement
Mass is flowing in the mantle
to coalesce under Hudson
Bay, pushing the crust up.
GPS on the crust sees this
as one effect:
An increase in ellipsoid height
A gravimeter on the crust
sees two effects:
(small) decrease in gravity as the
gravimeter location gets
farther from the geocenter
(larger) increase in gravity as the
amount of mass below the
gravimeter pulls harder
This gravity change causes the
geoid to “swell” in the area
Notes: There are two manifestations of the growing mass in the deep mantle under Hudson Bay:
Geometric – a GPS receiver will see the crust uplifting as the increase in mantle mass pushes the crust up in a displacement.
Geopotential – a gravimeter on the surface will sense the growing mass as an increase in the acceleration of gravity, BUT this will be slightly tempered by a reduction in gravity as well (because the gravimeter on the surface is getting farther from the Earth’s center). Still, the gain (from mass increase) is larger than the loss (from geometric movement) for a net gain. Because the net gain in gravity is not caused purely by being at a new crustal height, this translates into an increase in geoid undulations, or a “swelling” of the geoid in this region.
This is different than a purely geometric change caused by a compression of the crust. In that case, no significant mass is entering or leaving the region so, while GPS might sense a subsidence and a surface gravimeter might sense a slight increase as it moves closer to the Earth’s center, the geoid would not actually change.

## Slide 13: Episodic Mass Movement
Notes: Rare, but worth monitoring, large earthquakes or volcanic eruptions can move enough mass locally to cause the geoid to make a permanent local shift.

## Slide 14
Ramillien G et al. Geophys. J. Int. 2004;158:813-826
© 2004 RAS
Periodic Mass Movement
Notes: Seasonal variations of the synthetic geoids for 1987 computed using global model forecasts for the same period: atmosphere from ECMWF; oceans from POCM; total land water plus snow from LaD.
NGS sees this as a signal to be modelled and removed so users are not worried about “seasonal heights”.

## Slide 15: Geoid Monitoring Service (GeMS)
Goal: Track all changes to the geoid which would prevent 1 cm accuracy
Aspects included:
  Shape, Secular: e.g. Hudson Bay
  Shape, Episodic: e.g. Massive Earthquakes
  W0, Secular: Global Sea Level Change (see next slides)
Examples of things excluded:
  Size, Secular: Mass quantity of Earth is effectively static
  Shape, Periodic: Seasonal glacier cycle

## Slide 16
Sea Level and The Geoid

## Slide 17: Secular Sea Level Change
Special geoid-definition problem…
Consider only the mechanics of sea-level change:
  Mass is moving about (geopotential change)
    Land ice melts and joins the ocean, re-distributing mass around the globe
  Global mean sea level is rising (geometric change)
    By long standing tradition, the geoid is the one equipotential surface that fits global mean sea level

## Slide 18
Time Passes
Sea Level Rises
Scenario 1: Geoid Definition remains tied to GMSL
H
1
H
2
As Global Mean Sea Level rises, orthometric height gets smaller
Geoid
GMSL
Geoid
GMSL

## Slide 19
Time Passes
Sea Level Rises
Scenario 2: Geoid Definition decoupled from GMSL
H
1
H
2
As Global Mean Sea Level rises, orthometric height remains constant
Geoid
GMSL
Geoid
GMSL

## Slide 20: Choosing a new geoid as GMSL changes

## Slide 21
NAPGD2022

## Slide 22: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include:
  GEOID2022
  DEFLEC2022
  GRAV2022
  DEM2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 23: NAPGD2022
“North American-Pacific…”
  Because the gridded components (geoid, DoV, gravity, DEM) will cover all major USA populated territories, and these happen to fall in the general regions of “North America” and “The Pacific Ocean”
    However, the foundation of the gridded components will be a global geopotential model

## Slide 24: NAPGD2022
“…Geopotential…”
  Because it isn’t just about heights, but rather about all geodetic coordinates related to Earth’s geopotential field (geoid, deflections, etc)

## Slide 25: NAPGD2022
“…Datum…”
  Because a “geopotential reference frame” was, frankly, an unwieldy term that had no precedence in geodetic literature.
    “Reference Frame” only carries a geometric connotation in geodesy
  It is replacing, and expanding upon, the idea of a “vertical datum”

## Slide 26: NAPGD2022
“…2022”
  Because that is our target release date

## Slide 27: Expected changes to orthometric heights

## Slide 28: Expected changes to orthometric heights

## Slide 29: Definitional Relationship
Time-dependencies of ellipsoid heights
come from OPUS, where time-dependent
CORS coordinates serve as control for
your time-dependent GNSS survey.
Time-dependencies of geoid undulations
are captured in the dynamic component
of GEOID2022 (“DGEOID2022”), which
will come from the geoid monitoring
service, or GeMS.

## Slide 30: High resolution products
All will be 1 x 1 arcminute grids
All will cover three finite regions of the globe
All will have a static and dynamic component
  Dynamic surface gravity not expected to be ready by 2022
GEOID2022
  Official converter of *TRF2022 ellipsoid heights into NAPGD2022 orthometric heights
DEFLEC2022
  Surface deflections of the vertical in N/S and E/W
GRAV2022
  Surface acceleration of gravity

## Slide 31: The three gridded regions
“North American region”
¼ of the Earth
“Guam/CNMI region”
“American Samoa region”

## Slide 32
Leveling? Yes!

## Slide 33: Leveling? Yes!
Leveling yields differential heights
If you want absolute heights, you need one or more known heights
Previously this was about finding a benchmark with a published NAVD 88 height
  Does published mean “known”?
  Does it mean “trusted”?
  Does it mean “current”?

## Slide 34: When was this point last leveled?
Has an “adjusted”
NAVD 88 height to
a millimeter…
It’s in Louisiana where
accurate heights are
very important…
It was monumented in
1968 (ignore the glitch),
and was last known to be
in good condition in 2002…
It’s a trick question.
You can’t figure it out
from anything on here.
But the answer is:
Just once: 1968.
Savvy datasheet snoopers
may recognize this text as
meaning “it was adjusted
as part of the original roll-
out of NAVD 88…

## Slide 35: When was this point leveled?
You wouldn’t know it, but it was
leveled in:
1917, 1942, 1942 (again), 1945,
1951, 1981
The 1981 data went into
the NAVD 88 height
Q: But what about 64
years and 6 occupations?
A: You get a “warning” about vertical
movement, but no estimate of the rate.
Less than ¼ mile away is AH1055,
leveled once in 1981, with NO
warnings.

## Slide 36: Leveling - Control
In NAPGD2022, “known” heights for a leveling survey:
  Primary: Perform your own GPS survey
    Yields starting orthometric heights using GEOID2022
    RTK may be perfectly acceptable!
  Secondary: Find a “not stale” passive mark
    “Staleness” depends on the mark
  Tertiary: Use VERTCON 3 on an NAVD 88 height
    Please don’t do this

## Slide 37: Updates and Replacements
NAPGD2022 will come with a version number
Updates will change the version
  Bug fixes, new data, new theories, minor improvements
Replacements will change the name
  When GMSL has changed by some threshold (20 cm)
    About 50-70 years

## Slide 38: Summary
NAPGD2022
  Mutual consistency of heights, gravity, etc
  Time dependent coordinates
  Geoid definition decoupled from GMSL
  Orthometric heights defined by GPS & geoid

## Slide 39
Thank you!

## Slide 40
Questions?

## Slide 41: Extra Slides

## Slide 42: Content: Geoid Modeling History
Provides context as to why “sea level” has been a perpetual human choice for “surface of zero height”
  Attempts to model the sea level go back to the 1800s
  Knowledge of currents and global sea level change have complicated the matter in the last 30 years or so
    “Height above sea level” is too vague.
      Which “sea level” and on what date?

## Slide 43: Earth’s Geopotential Field
Surface of equal gravity potential energy
(W=62,630,000 m^2 / s^2)
Surface of equal gravity potential energy
(W=62,620,000 m^2 / s^2)
Surface of equal gravity potential energy
(W=62,610,000 m^2 / s^2)
Surface of equal gravity potential energy
(W=62,640,000 m^2 / s^2)
Surface of equal gravity potential energy
(W=62,650,000 m^2 / s^2)
Surface of equal gravity potential energy
(W=62,660,000 m^2 / s^2)
Surface of equal gravity potential energy
(W=62,636,856 m^2 / s^2 = W )
The “Holy Grail”…
“THE” geoid…
0
Notes: The derivative of potential relative to radial distance from the Earth (dW/dr) is being treated as negative here. The sense of the sign is convention, and differs based on which textbook and in which field (geodesy or physics) is being consulted.

## Slide 44: Geopotential Field
Gravity Potential
Energy…
…as a function of
geocentric co-latitude,
geocentric longitude
radial distance from the center of the Earth…
…can become…
Geoid Undulations…
Acceleration of Gravity…
Deflection of the Vertical…
Etc., ad nauseum.