## Slide 1: Geodesy for the Geographer Preparing for NSRS Modernization
NSGIC Midyear Meeting
February 2023
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 2: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
NSRS
Notes: NGS develops and maintains the National Spatial Reference System, a national coordinate system that provides the foundation for transportation, navigation, land record systems, mapping and charting efforts, and a multitude of scientific and engineering applications
CLICK
You’ve all seen this or some similar graphic I’m sure. That bottom layer… that’s our baby, the NSRS.

## Slide 3: Modernizing the NSRS
Updating all NSRS coordinates
  Replace existing datums with new datums
  Replacing existing SPCS83 with new SPCS2022
  Accounting for coordinates changing with time
Improving NGS products and services
Simplifying customer contributions
Making the NSRS:
  More accurate
  More accessible
  More efficient
Rollout in
2025

## Slide 4: Regional Geodetic Advisor Program
14 RGAs across the country
  2 positions currently filled by temporary details
    Alaska; Mid-Atlantic (being DE, MD, VA, NC, SC, GA, PR, VI)
Plus our Chief of Regional Advisor Branch
  Christine Gallagher
    Recently transitioned from other NGS role
We’re the eyes and ears of the agency
  Support NGS HQ in Silver Spring, MD
  Pester NGS HQ in Silver Spring, MD 

## Slide 5
geodesy.noaa.gov/ADVISORS/
Notes: -14 Regional Advisors, we’ve transitioned from a State-based to a Regional Program
-our advisors homepage up there at the top, also easy to find us by querying any major search engine for “ngs advisors”
-if you know Ross Mackay, he is our Chief Advisor, I report to him…
**ya know, I don’t know why they don’t make him put his photo up here
-we do have one vacant advisor position, that was recently advertised and John up there in Wisconsin is officially retired in oh… 18 days

## Slide 6: State Geodetic Coordinators
Not an NGS employee, rather:
  State/Commonwealth government
    DOT survey lead
    Geospatial Information Officer
    CORS or RTN (GPS/GNSS network) manager
  Academia
    Professor or Program Director
  Professional society representative
Serves as a liaison between that geospatial community and the NGS RGAHQ
Notes: -The State Geodetic Coordinator is not employed by NGS and is typically assigned by a state government agency or university.
-This is not a role we require or request in any way, the goal for the SGC is to allow a self-appointment from any state/commonwealth that is interested
-There are a handful of states also that have designated more than one SGC, thar

## Slide 7: State Geodetic Coordinators

## Slide 8: Regional Geodetic Advisor Program
We are here to support:
  You
  Your constituents or customers
  Our Federal Partners/Agencies
Questions about NSRS Modernization?
  Feel free to send your people to us!

## Slide 9
Conversion
    change the type of coordinate
    NAD83(2011) latitude & longitude  NAD83(2011) SPCS
  Transformation
    change the datum of coordinate
    NGVD29 height  NAVD88 height
    NAD 27 latitude & longitude  NAD 83(2011) latitude & longitude
Propagation
    change the epoch of coordinate
    NATRF2022 epoch 2020.00 to NATRF2022 epoch 2023.243
Terminology - Changing Coordinates
Notes: Historically NGS has been inconsistent with these top two words.
Going forward, we will use them as:
  Conversion: Meaning to change the type of coordinate without changing the datum or frame
  Transformation: Meaning to change the datum or frame, without changing the type of coordinate

## Slide 10
NATRF2022
North American Terrestrial Reference Frame of 2022
will replace
NAD83
North American Datum of 1983
Technically, not just NATRF2022 but also its sister TRFs…

## Slide 11: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 12: Plate-Fixed NSRS TRFs
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)
Notes: We say “NATRF2022” is “fixed” to the N.A. Plate, making it a “plate fixed” frame
-the frame is constant to itself, but rotating within ITRF, and moving in a different direction than the other 3 frames

## Slide 13
ITRF – constant frame, rotating plate

## Slide 14: Plate-Fixed
NATRF – rotating frame, constant with plate

## Slide 15
ITRF or NATRF – your choice if you know epoch
if you know epoch

## Slide 16
Passive Control

## Slide 17: NOAA CORS Network (NCN)
1695 sites
241 organizations
Active Control

## Slide 18: Remember…
  What’s the goal of NATRF2022?
    Give you the stability in positions that you expect
  That’s the point of Reference Epochs (REs)
    Akin to the different realizations of NAD83
    REs will be published every 5 or 10 years
      you choose when you update
      we expect many users will adopt our first Reference Epoch Coordinates , then stay on it long term
aka versions
Notes: REs will be published every 5 or 10 years
-you choose when you update
-in a perfect world, everyone would stay current, but we expect many users will adopt first RE and stay ther

## Slide 19
Estimated Geometric Change - Horizontal
NAD83 (2011)  NATRF2022
3.6 ft
4.3 ft
3.9 ft
Direction of Shift
4.6 ft
3.0 ft
Notes: What’s the magnitude of the horizontal datum shift across Pennsylvania?
Minimum Shift ~3.75 feet
Maximum Shift ~3.97
Remember this is just an estimation, don’t hold me to the numbers please

## Slide 20: Preparing for New Datums
  Two factors will dictate your frequency of coordinate updates
    Your accuracy needs
    The region you work in  tectonic motion
      Do manholes need cm-level updates annually?
      We accommodate that… you choose
      Just because we’re chasing the millimeter… it doesn’t mean you need to.
Notes: What’s the goal of the way NATRF2022 was designed, by including EPP2022 and IFVM2022
For a database of features in PA
Does a database of manholes in PA need cm-level coordinate updates on an annual basis? Probably not.

## Slide 21: Preparing for New Datums
  Know the epoch of your data/datasets
    consider how you will track this
      full to-the-second timestamp on every feature?
      labeling a year for each dataset?
      something in-between that works for your needs?

## Slide 22: Preparing for New Datums
  Reprocessing your data
    in a perfect world, everyone would reprocess
      What does this really mean?
        consider a hydro-enforced DEM
          start over with the raw flight data (GNSS/IMU)
          generate new point clouds
          recreate all the drainage features in new datum
      unrealistic!
Notes:     this is totally unrealistic  both from a financial and programmatic perspective

## Slide 23: Preparing for New Datums
  Transforming your data
    NGS Coordinate Conversion and Transformation Tool
      ASCII up/download, Web Services, or Download
      Source code on GitHub  github.com/noaa-ngs
      ask your software provider(s) about integration
        we envision COTS integrations as most popular method of access
Notes: Transforming your data
NCAT - NGS Coordinate Conversion and Transformation Tool
available now: ASCII upload and Web Services
ask your software providers about integration
we envision this as most popular method of access
Industry Workshops - May 2021 and August 2022
-Esri, Trimble, Blue Marble, etc… all the well known names attended
Geospatial Software Developers’ Summit – Nov/Dec
- International & Virtual  US NGS and NRCan CGS

## Slide 24
Deprecated 31 December 2022
Which begs the question
  What should you
  be doing now?
What happened to the US Survey Foot?

## Slide 25
1,000,000.00 sft = 999,998.00 ift
10,000,000.00 sft = 9,999,980.00 ift
1,000.00 sft = 999.998 ift (can you measure that?)
International  1 ft = .3048 m
US  1 ft = .30480061 m (approx.)
2 parts per million (ppm)?

## Slide 26: What should you be doing now?
Ask the right questions
  Does state law specify US Foot for SPCS83?
    40 states do that we know of
  Does it specify US Foot for boundary surveys? (Does that matter?)
    We’re not tracking that, it’s not NSRS-related
Understand that we do not enforce this
  Neither NIST or NGS are a regulatory agency
  We support education/outreach of course
Prepare for this along with new datums

## Slide 28
The Survey Foot is dead!
Long live the Survey Foot!
US Survey Foot was deprecated 31 December 2022…
But will always be available in NGS tools for NAD83 and NAD27

## Slide 29
SPCS2022
MAKING EARTH FLAT AGAIN
…ONE ZONE AT A TIME
I’ll be selling these bumper stickers in hospitality suite tonight…
Really?
No… not really!

## Slide 30
Notes: 106 zones (CONUS)

## Slide 31
Notes: 846 zones (CONUS)

## Slide 32
Notes: 49 zones (CONUS)

## Slide 33
What to do with the existing tiling scheme in NATRF2022?
Maintain same footprints, so uneven coordinates at corners?
New footprints, but cleaner coordinates? Both options?

## Slide 34
North American Vertical Datum
of 1988
NAVD88
will be replaced by

## Slide 35
North American-Pacific Geopotential Datum of 2022
NAPGD2022
(pronounced: nap-jee-dee)

## Slide 36
NAVD88 geoids
versus
NAPGD2022 geoids

## Slide 37
  Gravimetric
  Hybrid
Two types of geoid models
Notes: -believe it or not there’s more than 2 types, but the 2 types you’ll see NGS publish are…

## Slide 38
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid then best fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 39
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 40: Gravimetric vs. Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid

## Slide 41: NAVD88 uses a Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid

## Slide 42: NAPGD2022 uses a Gravimetric Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
  Datum zero surface aligned to Global Mean Sea Level (GMSL)

## Slide 43
Estimated change in orthometric heights from NAVD88 to NAPGD2022
(NAPGD2022 approximated using xGEOID16B)

## Slide 44: Quality of vertical datum transformation?
Anyone can collect and provide:
  2 OPUS-Static solutions
    ≥4 hours each
  2 photos of each setup
  Brief Description w/Ties
  Deadline = 30 September 2023
  Results increase accuracy of NAVD88<->NAPGD2022 transformation.
Web Map Application
Progress Dashboard
GPS on Bench Marks (GPSonBM)

## Slide 45: National Spatial Reference System (NSRS)
Geometric Geodesy
Horizontal Datums
Terrestrial Reference Frames
Latitude & Longitude
Ellipsoid Height
State Plane Coordinates
Physical Geodesy
Geopotential Datums
Orthometric Height
Dynamic Height
Surface Gravity
Leveling
To get to these “final products” we use a multitude of scientific methods, including Space Geodesy and Astronomical Geodesy.
And since we’re the Government… can’t forget Political Geodesy!

## Slide 46
Notes: Eligible funding applicants for this competition are institutions of higher education, state, local and Indian tribal governments.
The purpose of this notice is for us to solicit grant proposals to implement activities that modernize and improve the National Spatial Reference System (NSRS) and advance the science of geodesy in the United States.
NOAA encourages proposals submitted in response to this announcement to include student collaboration and education.

## Slide 47
https://www.ngs.noaa.gov/ADVISORS/
use any major search engine: “NGS advisors”
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486