## Slide 1: The State Plane Coordinate System for the Student of Geodesy
Ohio State University
March 2023
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 2
Notes: A sonnet composed by ChatGPT
Amidst the realm of cartography's art,
Lies a curious matter to impart,
The way our world is displayed on a map,
Takes shape in ways both complex and abstract.
From Mercator to Peters, the choices abound,
Each projection with its own unique sound,
And yet no single one can perfectly portray,
The complexities of our earth in every way.
For as we stretch and flatten and distort,
Our round globe becomes a two-dimensional court,
Where lines must bend and shapes must shrink,
To fit a rectangular canvas without a blink.
Oh, map projections, how you challenge the mind,
In your attempts to represent what we find,
A globe transformed into a map, a fascinating bind.

## Slide 3: The State Plane Coordinate System
Also referred to by some as…
State Plane – Ohio State Plane
SPCS – OH SPCS, OSPCS
SPC – Ohio SPC
_PCS – Ohio Planar Coordinate System
_CS – Ohio Coordinate System

## Slide 4: Agency History
Survey of the Coast – 1807 to 1836
  Authorized February 10th 1807
  Nation’s Oldest Scientific Agency!
U.S. Coast Survey – 1836 to 1878
  1871 began inland geodetic control mission (over 150 years now)
U.S. Coast and Geodetic Survey – 1878 to 1970
  USC&GS
National Geodetic Survey – 1970 to Present
  Over 50 years as NGS
Notes: -We are the Federal Government’s oldest scientific agency.
-In keeping with our expanding mission to survey the coasts and harbors of the United States and its interior lands, the agency’s name has evolved over the years too
Survey of the Coast
-Managed by Department of he Navy for about 4 years, but then reassigned to Department of the Treasury
US Coast Survey
-under this title is when, in 1871 the agency was tasked by Congress with responsibility to carry geodetic control inland
US Coast & Geodetic Survey (USC&GS)
-the USC&GS, the name we had for the longest! And this change came along with our current primary mission
National Geodetic Survey
-We celebrated 50 years as NGS in 2020, as did our parent agency NOAA

## Slide 5: Organizational Structure
  -Department of Commerce (DoC)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
Notes: -We are part of the Executive Branch
-I know it can seem kind of strange that NGS is part of the NOS, but goes back to origins of the agency being coastal mission

## Slide 6
  -Department of Commerce (DoC)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
≠
We’re not USGS, we’re NGS
Notes: -as you can read my slide, I like to point that out because over my 5 years at NGS I’ve seen and heard this misunderstanding quite a bit
-don’t worry! it doesn’t offend us! and we do work closely with USGS, but we are separate agencies within totally different departments of the federal government

## Slide 7: NGS Mission
Define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.

## Slide 8: National Spatial Reference System (NSRS)
A consistent coordinate system that defines…
latitude
longitude
height
scale
orientation
gravity
… and their time variants throughout the United States.
Who among us thinks in lat/long?
My house is 0.003 arc seconds down that way…
Horizontal Datums
NAD83
NAD27
Vertical Datums
NAVD88
NGVD29
Professionals in surveying, engineering, mapping desire this unified spatial reference system… but people don’t design bridges or lay out highways in angular units either (not intuitive).

## Slide 9: State Plane Coordinate System (SPCS)
A convenient, efficient way to work in the NSRS
  It’s a Projected Coordinate System (PCS)
    planar coordinates (not angular units)
  Developed by US Government (NGS and predecessors)
    Definitional parameters are publicly available
    State/Commonwealth governments utilize and adopt it
      Also widely adopted by commercial entities/companies
Notes: A convenient, efficient way to work in the NSRS
  It’s a Projected Coordinate System (PCS)
    planar coordinates (not angular units)
  Developed by US Government (NGS and predecessors)part of the Nation’s geodetic infrastructure
    Definitional parameters are publicly available
    State/Commonwealth governments utilize and adopt it
      Also widely adopted by commercial entities/companies

## Slide 10: History of SPCS
Origins date back to ~1820 (Survey of the Coast)
  Polyconic projection - for maps and charts
    Non-conformal and not equal-area
“Progressive Maps” of US in 1919 (C&GS)
  Based on the Polyconic projections
  Incorporated into World Polyconic Grid (WPG) by AMS
    Not intended for civilian applications (Army)
    But the usefulness of WPG is what led to development of SPCS
    Note that DoD was replaced WPG with UTM in the 1940s
Notes: Origins date back to ~1820 (Survey of the Coast)
  Polyconic projection - for maps and charts
    Non-conformal and not equal-area
“Progressive Maps” of US in 1919 (C&GS)
  Based on the Polyconic projections
  Incorporated into World Polyconic Grid (WPG) by Army Map Service (AMS)
    This is what led to development of UTM… and SPCS

## Slide 11: History of SPCS
Conformal Map Projections
  Desirable for surveying, engineering, military
    Preserves angles
    Scale error is same in all directions
  Useful for calculations  direction, distance, azimuth
  But… much more difficult to construct, and compute
  Around 1920, for nautical charting, USC&GS adopted:
    Lambert Conformal Conic (LCC)
    Transverse Mercator (TM)

## Slide 12: Birth of SPCS
SPCS 27 (based on North American Datum of 27)
  Request from government of NC in 1933
  Quickly led to 110 projection zones across 48 states
    Great DepressionNew Deal = Nationwide infrastructure expansion
  Education and outreach by C&GS
    Guidance on how to perform field work & computations
    Manual on using SPCS in Route Surveying for engineers
    Projection Tables, along with trig and log tables (slide rule era!)
    Formulas for electronic coordinate computation publised in 1968
Notes: SPCS of 1927 (based on NAD 27)
  Request from government of NC in 1933
  Quickly led to 110 projections across 48 states
    Great DepressionNew DealCivil Works Administration (CWA) led to Nationwide infrastructure expansion… which brought the need/desire for Federal Gov’t to be able to map & track all that
  (Funny quote that the system was “…not as a result of a brainstorm of some theoretical mathematician and geodesist.”  still rings somewhat true in that few at NGS use SPCS)
  Education and outreach by C&GS
    Guidance on how to perform field work & computations
    Manual on using SPCS in Route Surveying for engineers
    Projection Tables, along with trig and log tables (slide rule era!)
    Formulas for electronic coordinate computation publised in 1968

## Slide 13: Advancement of SPCS
SPCS 27 … moving into the 1970s
  By now with 50 states, plus other updates, 131 zones
  Procedures for scaling coordinates to the topographic surface
    Moving the “grid” to “ground” aka Modified State Plane
      Why? Surveyors collect field data on the ground
  SPCS was now mature… but was the NSRS?
    Nope! Late 70s brought progress towards NAD 83
  With a whole new datum, system of zones needs redeveloped

## Slide 14: Redesign of SPCS
SPCS 83 (based on North American Datum of 1983)
  NGS studied & considered a different approach for NAD 83
    Computer-based computations made everything easier
    Now SPCS had been around for 40+ years  familiarity
    SPCS 27 had already been codified into law in 38 states
  Changed false eastings and northings
  Same two projections: LCC or TM
  Zone design based on linear distortion w.r.t. ellipsoid surface
    Note this was same approach as SPCS 27

## Slide 15: Future of SPCS
SPCS2022 (based on NATRF2022)
  Again NGS considered a different approach for the NSRS TRFs
    GIS makes everything easier
  Changed false eastings and northings (but why?)
  Same two projections: LCC or TM
  Zone design based on linear distortion w.r.t. topographic surface
    Not previously possible at nationwide scale
    Plethora of elevation data makes this possible (USGS 3DEP, etc.)

## Slide 16: SPCS2022 – What makes it different?
Overall distortion design philosophy
  Linear distortion minimized (or “optimized”) at topographic surface (not at ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
What is linear distortion?
  Defined at a point (infinitesimal distances)
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm per km
Linear distortion | = | δ | = | Projected minus actual distance
 |  |  |  | Actual distance

## Slide 17: Map projection linear distortion
Distortion at a point computed as:
  where
    k = grid point scale factor (distortion due to Earth curvature)
    h = ellipsoid height of point (distortion due to change in height)
    R = Earth geometric mean radius curvature
  < 0  projected (grid) distance shorter than true (ground) distance
  > 0  projected (grid) distance longer than true (ground) distance
Height (“elevation”) factor
Grid point scale factor
Combined factor
Notes: How does NGS calculate linear distortion?
Let’s walk thru it
--k is our grid point scale factor, distortion due to earth curvature
--Ratio highlighted in green is the elevation factor
Together, these two are referred to as the combined factor
Items that make it up are …
Distortion = Combined Factor minus one

## Slide 18
Grid distance < ellipsoid distance < ground distance (k < 1 and δ < 0)
Grid distance > ellipsoid distance < ground distance (k > 1 and δ < 0)
Projection axis (k0 < 1)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to ellipsoid surface
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
18
k0 = scale on projection axis
LCC: central parallel
TM: central meridian
OM: skew axis
Notes: For SPCS 27 and 83, topography was ignored
Distortion was only a function of the Grid Point Scale Factor, nothing about radius of Earth, height, etc.

## Slide 19
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface
19
Ellipsoid surface
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)

## Slide 20
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Topographic surface
20
Ellipsoid surface

## Slide 21
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
ONLY way to reduce variation in distortion is to change projection axis location (or change projection).
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
IMPORANT: For large areas, there is no single defining ellipsoid height for scaling the projection.
21
This design approach used for SPCS2022 (minimizes distortion with respect to topography)
Projection axis scale can be less than 1 for steeply sloping areas even if heights are large.
R2
R1

## Slide 22: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio
20 ppm | 2 cm/km | 0.1 ft/mile | 1:50,000
50 ppm | 5 cm/km | 0.3 ft/mile | 1:20,000
100 ppm | 10 cm/km | 0.5 ft/mile | 1:10,000
400 ppm | 40 cm/km | 2.1 ft/mile | 1:2,500

## Slide 27: SPCS2022 statistics
Total of 968 zones
  Yep… 159 zones designed by NGS
  But also 806 zones designed by the states
Nowhere else (that we know of) can citizens and stakeholders directly contribute to national geodetic infrastructure

## Slide 28: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 29: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 30: Number of SPCS2022 zones (preliminary)
CONUS, Alaska, and Hawaii
Three island zones not shown:
Puerto Rico and U.S. Virgins Islands
American Samoa
Guam and the Commonwealth of the Northern Mariana Islands

## Slide 31
 |  | North | South | 
N parallel |  | 38°58’N | 37°56’N | 
S parallel |  | 37°58’N | 36°44’N | 
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | 
Max |  | +17 | +42 | 
Mean |  | -56 | -67 | 
“Layered” zones
SPCS 83 Kentucky N and S zones (Lambert Conformal Conic)

## Slide 32
 |  | North | South | Statewide
N parallel |  | 38°58’N | 37°56’N | 38°40’N
S parallel |  | 37°58’N | 36°44’N | 37°05’N
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | -166
Max |  | +17 | +42 | +181
Mean |  | -56 | -67 | -58
“Layered” zones
SPCS 83 Kentucky statewide zone (Lambert Conformal Conic)

## Slide 33
Co-existing layers within Kentucky SPCS 83
North and South Zones (KY-N, KY-S)
Statewide Zone (KY1Z)

## Slide 34
1. Statewide layer
Three zone layers concept

## Slide 35: Alaska complete “intermediate” layer
35
1. Statewide layer
2. “Intermediate” layer (complete state coverage)
Three zone layers concept

## Slide 36
36
1. Statewide layer
2. “Intermediate” layer (complete state coverage)
3. LDP layer (partial state coverage)
Three zone layers concept

## Slide 37
State Plane Coordinate System of 1983
SPCS83
North and South Zones as they exist now
Notes: We start with the SPCS83 zones as a frame of reference
NOTE that the color shading of these zones is matched to that of the Preliminary SPCS2022 Zones that follow

## Slide 38
DRAFT

## Slide 39
DRAFT

## Slide 41
State Plane Coordinate System of 2022
SPCS2022
PA stakeholders requested 4-5 zones, which NGS designed, the following are Preliminary maps
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 42
Notes: NOTE that the West Zone far surpasses the NGS design criteria of 50ppm

## Slide 43
Notes: This is the first, and likely final, draft of an Oblique Mercator projection for the Preliminary Central Zone
NOTE that even with the

## Slide 44
Notes: This is the second draft of a Preliminary North East Zone
NOTE this includes Columbia and Montour Counties, and the animation highlights the comparison between having these counties in the SE or NE Zone

## Slide 45
Notes: This is the second draft of a Preliminary South East Zone
NOTE this excludes Columbia and Montour Counties (they would fall in SE Zone)

## Slide 50
State Plane Coordinate System of 2022
SPCS2022
NGS will create a Single Statewide Zone for every State, the following is a Preliminary map

## Slide 51
Notes: This Single Statewide Zone designed by NGS is color shaded to match the following section of slides that show UTM Zones linear distortion values
It is known that some user communities with large areas of responsibility choose to maintain geospatial data and work in UTM
This graphic as compared to the UTM serves to highlight in SPCS2022, users will see better performance (lower linear distortion) if they choose to work in the SPCS2022 Single Statewide Zone rather than one of the UTM Zones that fall within Pennsylvania

## Slide 52
UTM (NAD83) Zones as
UTM
The following are maps using existing UTM zones as a Single Statewide Zone
(included to highlight the lower performance as compared to Preliminary NGS Zone)

## Slide 55
Notes: The NGS designed preliminary single statewide zone is included again here at the end for easier visual comparisons.

## Slide 56: SPCS2022 Zone Layers in PA
Both Single Statewide and Multi-Zone Layers will coexist
Think about your data, your goals, your customers
  Remember that geographic coordinates are your friend!
Smaller zones not “the best” … it all depends on usage & goals

## Slide 57: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
57

## Slide 58: SPCS2022 linear distortion (prelim)
49 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 14% | 12% | 7%
±50 | 27% | 26% | 18%
±100 | 48% | 48% | 36%
±400 | 91% | 93% | 88%
City and area statistics (ppm): |  |  | 
 | Min | -1512 | -1627
 | Max | +2888 | +2987
 | Range | 4400 | 4614
 | Mean | -86 | -120
Mean weighted by pop = -100 |  |  | 
58

## Slide 59: SPCS2022 linear distortion (prelim)
646 zones (35 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 70% | 54%
±50 | 92% | 88% | 73%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -400 | -684
 | Max | +245 | +295
 | Range | 644 | 979
 | Mean | -5 | -23
Mean weighted by pop = -4 |  |  | 
59

## Slide 60: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 61: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
61

## Slide 62: SPCS2022 linear distortion (prelim)
187 zones (10 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 78% | 78% | 73%
±50 | 91% | 90% | 88%
±100 | 99.8% | 99% | 97%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -261 | -465
 | Max | +120 | +240
 | Range | 381 | 705
 | Mean | -3 | -12
Mean weighted by pop = -1 |  |  | 
62

## Slide 63: About the timing of it all…
Timeline
  Review of stakeholder submittals is complete
  Late 2022-Early 2023: Preliminary designs for stakeholder review
  Mid-2023: Finalize all zone designs
Other things in 2023
  Provide machine-readable definitions (e.g. WKT)
  Modify NGS algorithms (e.g., 1-parallel Lambert)
  Document new projection algorithms
Release with rollout of modernized NSRS
  Final definitions available by late 2023
  Release with new “datums” in 2025
Rollout in
2025

## Slide 64: NSRS Modernization
Geometric (LLh)
NAD 83
will be replaced by
North American Terrestrial Reference Frame of 2022
NATRF2022
Orthometric (H)
NAVD 88
will be replaced by
North American Pacific Geopotential Datum of 2022
NAPGD2022

## Slide 65: Who uses SPCS?
Surveyors
  Used extensively, with all sorts of data/projects
GIS Professionals
  Very popular PCS, along with UTM
Engineers
  Many are unfamiliar with anything other PCS
Notes: Surveyors
  Used extensively, with all sorts of data/projects
GIS Professionals
  Very popular PCS, along with UTM
Engineers
  Many are unfamiliar with anything other PCS

## Slide 66: Why use SPCS?
Zone parameters built-in to COTS software
States sometimes require it for surveyors
Surveying↔Engineering common ground
  Coordinates - field data matched to design data
More efficient than assumed/local system

## Slide 67: How to use SPCS?
Click a few buttons in your favorite software
  Right? Not always that easy!
NGS Coordinate Conversion and Transformation Tool (NCAT)
  ASCII up/download, Web Services, or Download
  Library of modules used are on GitHub  github.com/noaa-ngs
Definitional parameters published by NGS
  Go to the source… please!
    Questions, ambiguities? Contact NGS  Regional Advisor, etc.

## Slide 68: Units in SPCS
Two versions of “foot” in current use:
“Old” U.S. survey foot
“New” international foot
1 ft = 0.3048 m exactly
‭1 ft = 1200/3937 m = 0.3048006096…‬ m
Differ by
2 parts per million (ppm) or ~0.01 ft (~1/8 inch) per mile
  A real problem with real costs

## Slide 69: A tale of two feet
Who uses U.S. survey feet?
  Surveyors in most (not all) states
  But it impacts everyone
  It is a major issue for the National Spatial Reference System (NSRS), especially State Plane coordinates (and other projected coordinate systems)

## Slide 70: Horizontal error when mixing up feet
SPCS 83 AZ Central Zone
UTM 83 12 North Zone

## Slide 71: SPCS 83 legislation and foot version
56 U.S. jurisdictions
Legislation
  International foot: 6
  U.S. survey foot: 28
  Neither: 16
  No legislation at all: 6
71
71

## Slide 72: What the deal with this whole U.S. survey foot thing?
Deprecated on Dec 31, 2022
  Per final determination Federal Register Notice issued on Oct 5, 2020
  Collaborative action by National Institute of Science and Technology (NIST) and NGS
  Describes public comments received, along with the plan, resources, training, and other information for an orderly transition with minimum disruption
(this image is hyperlinked to the Federal Register page)

## Slide 73: What happens now with SPCS units?
Nothing really! But why?!?!  “orderly fashion with minimum disruption”
Continue to follow state directives for SPCS 83 (and SPCS 27)
  The 40 states that “officially” use U.S. foot for SPCS 83
  All SPCS 27 zones
  NGS will support such “legacy” use forever
  But NOT supported for ANY zones in SPCS2022
Please remember…
NGS will always support U.S. survey foot for SPCS 83 and 27

## Slide 74: Reference Material
https://geodesy.noaa.gov/SPCS/
  click Learn More on left side
  Includes below, recorded webinars, and more
NOAA Special Publication NOS NGS 13
  The State Plane Coordinate System: History, Policy, & Future Directions, Michael L. Dennis, 2018
NOAA Manual NOS NGS 5
  State Plane Coordinate System of 1983, James E. Stern, 1990

## Slide 75
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
https://geodesy.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”