## Slide 1: SPCS2022 Making Earth Flat... One Zone at a Time!
URISA GIS-Pro
October 2023
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 2
How surveyors and engineers see the Earth…

## Slide 3
Estimated Geometric Change - Horizontal
NAD83 (2011)  NATRF2022
3.6 ft
4.3 ft
3.9 ft
Direction of Shift
4.6 ft
3.0 ft
Notes: What’s the magnitude of the horizontal datum shift across Pennsylvania?
Minimum Shift ~3.75 feet
Maximum Shift ~3.97
Remember this is just an estimation, don’t hold me to the numbers please

## Slide 4: New Lat/Long = New XY
With a new horizontal datum…
  NAD 83 to be replaced by NATRF2022
There comes a new set of State Plane Coordinate System zones
  SPCS 83 to be replaced by SPCS2022

## Slide 5
SPCS2022
MAKING EARTH FLAT AGAIN
…ONE ZONE AT A TIME
I’ll be selling these bumper stickers on LinkedIn…
Really?
No… not really!

## Slide 6: A “flat” Earth for the future
State Plane Coordinate System of 2022 (SPCS2022)
Similar to existing State Plane…
  Same 3 map projection types
  Same ellipsoid (GRS 80)
But different…
  Based on new datums instead of NAD 83
  Designed to reduce difference between “grid” and “ground”
  Many more “zones”
  Zones “layers” will exist in most states
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 7: SPCS2022 Zone Layers in Ohio
Both Single Statewide and Multi-Zone Layers will coexist
Think about your data, your goals, your customers
  Remember that geographic coordinates are your friend!
Smaller zones not “the best” … it all depends on usage & goals

## Slide 8
Grid distance < ellipsoid distance < ground distance (k < 1 and δ < 0)
Grid distance > ellipsoid distance < ground distance (k > 1 and δ < 0)
Projection axis (k0 < 1)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to ellipsoid surface
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
8
k0 = scale on projection axis
LCC: central parallel
TM: central meridian
OM: skew axis

## Slide 9
Projection axis (k0 > 1)
Projection surface (non-intersecting)
Ellipsoid distance
Topographic surface
Horizontal ground distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
h
R
Grid distance > ellipsoid distance ≈ ground distance (k > 1 and δ ≈ 0)
9
Ellipsoid surface

## Slide 10: Minimizing linear distortion
Distortion function of both and
  = distance from projection axis (kilometers)
  = change in ellipsoid height (meters)
Minimize both and simultaneously
  increases with square of distance
  increases linearly with change in height
  Treating separately can lead to poor results

## Slide 11
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface
11
Ellipsoid surface

## Slide 12
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Topographic surface
12
Ellipsoid surface

## Slide 13
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
13
This design approach used for SPCS2022 (minimizes distortion with respect to topography)

## Slide 14
State Plane Coordinate System of 1983
SPCS83
North and South Zones as they exist now
Notes: We start with the SPCS83 zones as a frame of reference
NOTE that the color shading of these zones is matched to that of the Preliminary SPCS2022 Zones that follow

## Slide 16
State Plane Coordinate System of 2022
SPCS2022
NGS designed a Single Statewide Zone for every State

## Slide 19
State Plane Coordinate System of 2022
SPCS2022
Ohio stakeholders designed 88 zones
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 22: SPCS2022 Zone Layers and LDPs
Each state may have max of 3 zone “layers”
  One layer must be statewide zone
    Ohio Single Statewide
  Other layers have two or more zones
    Ohio County Coordinate System (designed by ODOT)
  A third layer can exist… but must be discontinuous coverage
    A few states with Low Distortion Projection (LDP) zones

## Slide 23
What to do with the existing tiling scheme in NATRF2022?
Maintain same footprints, so uneven coordinates at corners?
New footprints, but cleaner coordinates? Both options?
Points to ponder…

## Slide 24
State Plane Coordinate System of 2022
SPCS2022
Not just Ohio!
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 25: Status of zone layout and designs
Designs by NGS
  159 zones (including 54 statewide)
  Plus 3 “special use zones” (in more than one state)
Designs by state stakeholders
  806 zones in 28 states
  Most are “low-distortion projections” (LDPs)
Total = 968 zones for 56 states and territories
  Number will likely decrease slightly
Compare to 125 zones in existing SPCS83!

## Slide 26: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 27: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 28: Number of SPCS2022 zones (preliminary)
CONUS, Alaska, and Hawaii
Three island zones not shown:
Puerto Rico and U.S. Virgins Islands
American Samoa
Guam and the Commonwealth of the Northern Mariana Islands

## Slide 29: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
29

## Slide 30: SPCS2022 linear distortion (prelim)
49 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 14% | 12% | 7%
±50 | 27% | 26% | 18%
±100 | 48% | 48% | 36%
±400 | 91% | 93% | 88%
City and area statistics (ppm): |  |  | 
 | Min | -1512 | -1627
 | Max | +2888 | +2987
 | Range | 4400 | 4614
 | Mean | -86 | -120
Mean weighted by pop = -100 |  |  | 
30

## Slide 31: SPCS2022 linear distortion (prelim)
646 zones (35 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 70% | 54%
±50 | 92% | 88% | 73%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -400 | -684
 | Max | +245 | +295
 | Range | 644 | 979
 | Mean | -5 | -23
Mean weighted by pop = -4 |  |  | 
31

## Slide 32: SPCS2022 linear distortion (prelim)
187 zones (10 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 78% | 78% | 73%
±50 | 91% | 90% | 88%
±100 | 99.8% | 99% | 97%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -261 | -465
 | Max | +120 | +240
 | Range | 381 | 705
 | Mean | -3 | -12
Mean weighted by pop = -1 |  |  | 
32

## Slide 33: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 34: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
34

## Slide 35: Existing SPCS 83 linear distortion
10 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 4% | 10% | 4%
±50 | 16% | 23% | 11%
±100 | 40% | 62% | 36%
±400 | 100% | 100% | 99.1%
City and area statistics (ppm): |  |  | 
 | Min | -263 | -967
 | Max | +86 | +342
 | Range | 349 | 1308
 | Mean | -83 | -135
Mean weighted by pop = -92 |  |  | 
35
Statistics are for land areas only

## Slide 36: SPCS2022 linear distortion (prelim)
21 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 77% | 38% | 17%
±50 | 90% | 67% | 38%
±100 | 98% | 93% | 68%
±400 | 100% | 100% | 99.8%
City and area statistics (ppm): |  |  | 
 | Min | -177 | -794
 | Max | +321 | +331
 | Range | 498 | 1125
 | Mean | -7 | -53
Mean weighted by pop = -4 |  |  | 
Statistics are for land areas only

## Slide 37: SPCS2022 linear distortion (prelim)
38 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 89% | 93% | 49%
±50 | 98% | 99.7% | 74%
±100 | 99.7% | 100% | 88%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -59 | -937
 | Max | +49 | +190
 | Range | 108 | 1127
 | Mean | +0.4 | -34
Mean weighted by pop = -8 |  |  | 
Statistics are for land areas only

## Slide 38: SPCS2022 linear distortion (prelim)
45 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 86% | 85% | 47%
±50 | 97% | 98% | 73%
±100 | 99.5% | 99.7% | 88%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -60 | -937
 | Max | +321 | +335
 | Range | 380 | 1272
 | Mean | -3 | -35
Mean weighted by pop = -10 |  |  | 
Statistics are for land areas only

## Slide 39: Existing SPCS 83 linear distortion
10 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 4% | 10% | 4%
±50 | 16% | 23% | 11%
±100 | 40% | 62% | 36%
±400 | 100% | 100% | 99.1%
City and area statistics (ppm): |  |  | 
 | Min | -263 | -967
 | Max | +86 | +342
 | Range | 349 | 1308
 | Mean | -83 | -135
Mean weighted by pop = -92 |  |  | 
39
Statistics are for land areas only

## Slide 40: About the timing of it all…
Timeline
  Complete review of stakeholder submittals
  Late 2022-Early 2023: Preliminary designs for stakeholder review
  Mid-2023: Finalize all zone designs
Other things in 2023
  Provide machine-readable definitions
  Modify NGS algorithms (e.g., 1-parallel Lambert)
  Document new projection algorithms
Release with rollout of modernized NSRS
  Final definitions available by late 2023
  Release with new “datums” in 2025
Rollout in
2025

## Slide 41
geodesy.noaa.gov/ADVISORS/
Regional Geodetic Advisor Program
14 RGAs across country
We are here to support:
  You
  Your constituents
  Our Federal Partners
Questions about
NSRS Modernization?
  Reach out now
  Be prepared
Notes: -14 Regional Advisors, we’ve transitioned from a State-based to a Regional Program
-our advisors homepage up there at the top, also easy to find us by querying any major search engine for “ngs advisors”
-if you know Ross Mackay, he is our Chief Advisor, I report to him…
**ya know, I don’t know why they don’t make him put his photo up here
-we do have one vacant advisor position, that was recently advertised and John up there in Wisconsin is officially retired in oh… 18 days