## Slide 1
The New 2022 U.S. Datums and Preparing for Them
Denis Riordan, PSM
NOAA, National Geodetic Survey
denis.riordan@noaa.gov
University of Florida Geomatics Program
2nd Annual NSRS 2022 Workshop
September 18, 2020

## Slide 2: Presentation Topics 1. Review of coming new Datums 2. Recent Announcements on the Modernization of the NSRS 3. Coordinate transformations - NCAT 4. Metadata and Preparing for 2022

## Slide 3: 2022 U.S. Geometric Datum

## Slide 5: Names and Reference Frames
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 6: Replacing NAD83
Develop four "plate-fixed" reference frames
Remove non-geocentricity of NAD83
Align to ITRF2014 at epoch 2020.00
Remove most of tectonic plate rotation
from ITRF2014 via Euler Pole Parameters
(pronounced: “oiler”)
SHIFT
DRIFT

## Slide 7
Drift…

## Slide 8: The Non-Geocentricity of NAD83
~2.2 meters
NAD83
origin
ITRF2014
origin
Earth’s
Surface
h83
h14
GRS80
ellipsoid
SHIFT
The position for the center-mass of the earth has been held fixed
for all epochs of NAD83.

## Slide 9: Two Types of Drift
Tectonic Plate Rotation
    horizontal
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
simple to model
complex

## Slide 10
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.
NSRS Plate Rotation Modeling
EULER Pole
10
EPP = Euler Pole Parameters
* Will be an EPP for each
TRF.

## Slide 11
EPP2022
NATRF2022
CATRF2022
PATRF2022
MATRF2022
Rotation of the
North American Plate
Rotation of the
Caribbean Plate
Rotation of the
Pacific Plate
Rotation of the
Mariana Plate
ITRF2014
ITRF2014 + EPP2022 = TRF2022

## Slide 12: Euler Poles and “Plate-Fixed”
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)

## Slide 13
ITRF – constant frame, rotating plate

## Slide 14: “Plate-Fixed”
NATRF – rotating frame, constant with plate

## Slide 15
ITRF or NATRF – your choice, just use EPP

## Slide 16: Two Types of Drift
Tectonic Plate Rotation
    horizontal
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
simple to model
complex

## Slide 17: CORS Velocities – IGS08
Crustal motion to be removed by Intra Frame Velocity Models for each TRF.
Notes: These velocities were arrived at by taking IGS08 velocities and removing the 3 parameter Euler Pole rotation of the North American plate as currently known (ITRF08 plate motion model).
These residual velocities will then be modeled into the IFVM for NATRF2022

## Slide 18
A model of all residual velocities, after removal of tectonic rotation via EPP:
  Horizontal residual motion
  Total vertical motion (ellipsoid heights)
  Replaces / Improves upon HTDP
IFVM2022 Model - Likely will be built upon CORS data, geodynamic models and InSAR, but not yet finalized
Given t1 and t2, compute Δλ, Δϕ, Δh at any point, accounting for all motions
Intra-Frame Velocity Model - IFVM

## Slide 19
New geometric datum minus NAD 83 (horizontal)
For Florida = 0.8 > 1.0 m (2.6 > 3.3 ft.)
NATRF2022

## Slide 20
NATRF2022
For Florida = -1.4 > -1.6 m (- 4.5 > - 5.3 ft.)

## Slide 21: 2022 U.S. Vertical Datum

## Slide 22
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Were determined by leveling from a single point, allowing cross-country error build up
Why isn’t NAVD 88 good enough anymore?
* NAVD 88 is a terrestrial based vertical datum that changes as the land changes.

## Slide 24: Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 25
Replace the Vertical Datum of the USA by 2022 (at today’s funding)
GRAV-D is:
  An airborne gravity survey of the entire country and its holdings
  A 2022 gravimetric geoid accurate to 1 cm
  Long-term monitoring of geoid change over time
  Partnership surveys
Working to launch a collaborative effort with the USGS for simultaneous magnetic measurement
Acting Proj. Manager: Jeffery Johnson
Jeffery.Johnson@noaa.gov
Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
Gravity and Heights are
inseparably connected
Notes: GRAV-D is the NGS project designed to replace NAVD88 with a vertical datum based upon a gravimetric geoid accurate to 1 cm. Heights above this datum will be accessed via GNSS measurements. Three thrusts of project. Launch USGS collaboration for simultaneous mag measurement.

## Slide 26
GRAV-D Status as of September 2020

## Slide 27: Geoid Monitoring Service (GeMS)
Goal: Track all changes to the geoid which would prevent 1 cm accuracy
Aspects included:
  Shape, Secular: e.g. Hudson Bay
  Shape, Episodic: e.g. Massive Earthquakes
  W0, Secular: Global Sea Level Change (see next slides)
Examples of things excluded:
  Size, Secular: Mass quantity of Earth is effectively static
  Shape, Periodic: Seasonal glacier cycle
Bottom Line: An accurate, up-to-date, and maintainable vertical datum.

## Slide 28
Extent of 2022 gravimetric geoid model used for NAPGD2022

## Slide 29: Expected changes to orthometric heights – NAVD88 to NAPGD2022
For Florida = 0.1 > -0.3 m (4 > -11 in.)

## Slide 30: Recent 2022 Announcements

## Slide 31: What is “the Modernized NSRS”?
It is a replacement for the entire current National Spatial Reference System (NSRS)
  Datums
  Coordinates
  Orbits
  Database
  Software
  Policies, procedures and philosophies
  And….skills! New hires, new training!

## Slide 32: Original Timeline
In 2007, NGS assumed we would be done by 2018
  Optimistic GRAV-D planning
  Incomplete picture of the entire modernized NSRS
By 2013, a finish of 2022 seemed correct
  Still, the “big picture” wasn’t clear
  Optimism and enthusiasm within NGS was high for many years
By 2020 three issues derailed that date:
  Final clarity on the complexity of the task
  Loss of personnel without backfill
  “2020”
Notes: A friend called 2020 “the longest decade of our lives”

## Slide 33: Drivers of delay
Growing complexity
  As new components were thought of, they often led to additional projects and unforeseen work
  Example: “We need to have time-dependent coordinates”
    But the IDB doesn’t support this
      We need a new database!
        But we also need to define things like “adjustment windows” and “redundancy” and “simultaneous”
        And we need new least squares adjustment software which supports this
          But we have to treat leveling differently from GPS
            And speaking of which, why are we still a GPS-only shop?
              We need multi-GNSS software!
                But that’ll take years! Better get started!

## Slide 34: Rebooting the timeline
The “long pole in the tent” is GRAV-D
  Much of the GRAV-D remaining work is in the Pacific, which raises the question of “phased rollouts”
  Pacific is expensive, difficult to schedule
Correct, On Budget, On Time: Pick two
  With the likelihood of a multi-year delay, we picked “Correct” and “On Budget”
    Do the work right
    Do it with the resources we have

## Slide 35: Conclusion
The modernized NSRS is delayed beyond 2022
  2024-2025 most likely
There is no way to accelerate this
  Can’t make people work faster or harder when they are already at maximum capacity
  Can’t make the troubles of 2020 go away
Phased roll-outs have been considered
  For now, they are off the table

## Slide 37: NGS Products Update Coordinate Conversion and Transformation Tool – NCAT using NADCON v5.0

## Slide 38
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022
NADCON
GEOCON
GEOCON 11

## Slide 39
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022
NCAT (NADCON 5)

## Slide 40: NADCON 5

## Slide 41: Example Grid of NADCON 5
* 15 minute cell size

## Slide 42: NCAT

## Slide 43: NCAT

## Slide 44: NCAT
Look for “converted” coordinates (state plane, etc.) under
the highlighted (green) Menu bar.

## Slide 45: NCAT
NOTE: If input includes “heights”, NCAT utilizes VERTCON 3,
not the NGVD29 to NAVD88 VERTCON

## Slide 46: Conversion or Transformation?
How NGS uses these terms:
  Conversion: Changing the type of coordinate without changing the datum or frame
    e.g. change NAD 83(1986) latitude and longitude to NAD 83(1986) State Plane Coordinates
  Transformation: Changing the datum or frame, without changing the type of coordinate
    e.g. changing an NAD 27 latitude & longitude to an NAD 83(1986) latitude & longitude

## Slide 47: NCAT vs. CORPSCON (NADCON4.2)

## Slide 48: NCAT vs. CORPSCON (NADCON4.2)

## Slide 49: NCAT vs. CORPSCON (NADCON 4.2)
NADCON 4.2 (or earlier versions) was not designed to transform to any NAD83 epoch later than the HARN or FBN (depending on the State you are working in.

## Slide 50: Is it NCAT or
METADATA ?
NAD83 (2011)
NAD83 (2007)
NAD83 (HARN)
NAD83 (86)
NAD27 X & Y
WHAT STATE?
WHAT ZONE?
WHAT ARE THE UNITS?
FEET?  uSFt or Intl?

## Slide 51: How to Plan for 2022
Move to newest realizations
  NAD 83(2011) epoch 2010.00
  GEOID18 (hybrid geoid)
Move to NAVD 88
  understand the accuracy of VERTCON in your area
Utilize passive marks that are up to date
  Stay aware of what marks are included in datum updates
Uses NGS OPUS Share for out of date marks
  Observe marks with GPS and submit to OPUS Share to have up to date positions before the new dates are released.
Metadata
  Document positions in current datums to know what you have in the future.

## Slide 52
? ? QUESTIONS ? ?
Denis.Riordan@noaa.gov