## Slide 1
U.S. Department of Commerce National Oceanic & Atmospheric Administration
National Geodetic Survey (NGS)
Understanding The Information Found On NGS Datasheets
John Ellingson – NGS Geodetic Advisor
WISCONSIN - GREAT LAKES REGION
john.ellingson@noaa.gov, 202-306-6904
1

## Slide 2
Learn alternate ways to obtain datasheets while in the office, or in the field.
Learn about the different sections of datasheets
Learn about important differences in the information that is found in certain sections of the datasheet –avoid using it incorrectly.
Goal today: To improve understanding of NGS datasheets
2

## Slide 3
METHODS TO OBTAIN DATASHEETS
“Classical” NGS website retrieval
“DSWorld” software with Google Earth
NGS “Data Explorer” option
Smart Phone App - “FindAControl” *
3
FindAControl
*NOT an NGS Product
CLASSICAL METHOD
DSWorld
NGS DATA EXPLORER

## Slide 4
“CLASSICAL” NGS Website retrieval….
http://www.ngs.noaa.gov/cgi-bin/datasheet.prl
4
Interactive Map Option
You can also find a Project ID using a PID
Useful information

## Slide 5
“DSWorld” - software program developed by Malcolm Archer-Shee
Download this free program from the NGS website at – http://www.ngs.noaa.gov/PC_PROD/PARTNERS/index.shtml
5

## Slide 6
“DSWORLD” Screen Capture
6

## Slide 7
“NGS Data Explorer” found here….
http://www.ngs.noaa.gov/
Click here to reach
“DATA EXPLORER”
7

## Slide 8
8
Interactive map method
Statewide datasheet extractions- latest month is available here
Go To “classical method”
“Text format” datasheet retrievals, or…
“Shapefile format” for GIS functionality

## Slide 9
Sample search using NGS “Data Explorer” tool
9

## Slide 10
SMART PHONE or TABLET APP --- “FindAControl”
Android and iOS Application - NOT an NGS product
10

## Slide 11
11
OPUS SHARED SOLUTION
CLASSICAL DATASHEET

## Slide 12
DATASHEET SECTIONS:
Basic Metadata
Current Survey Control
Accuracy
Data Determination Methodology
Projections
Azimuth Marks (old hz marks only)
Superseded Survey Control
Monumentation
National Grid
History
Description and Recoveries
12

## Slide 13
THE “PID”….. IT IS IMPORTANT
BASIC METADATA SECTION OF EACH DATA SHEET
VERSION # matters to some vendor software programs
13
dsdata.txt is a guide to understanding datasheet info

## Slide 14
Why is the “PID” important?
The PID is the key to the NGS database which contains more than 1.5 million marks
Four stations are named “ADAMS” in Indiana
Each one has a unique PERMANENT IDENTIFIER (six character PID)
14

## Slide 15
Five Stations have the designation “BM”
Again, each has a unique PID…..
ME0908, MD0784, MD0358, LA1409, HZ1997
15

## Slide 16
Three Primary Types of “MODERN” Geodetic Marks:
Leveled only
GPS-Observed only
Leveled and GPS-Observed on same mark
16
NOTE: there are many old triangulation stations that still exist in the NGS database…. CAUTION: avoid mixing old triangulation data with modern GPS-surveyed marks!

## Slide 17
Published “CURRENT SURVEY CONTROL” for a LEVELED-ONLY mark. (NOT GPS observed)
Note Handheld GPS Pos.
Another Vertical Mark Example
Note Position
SCALED from Topo map
17

## Slide 18
This mark was observed only with GPS (it WAS NOT leveled) -
published height was GPS derived using Geoid model
use the meters value
18
?? use this value??
This mark is also…. GPS-Only

## Slide 19
15 vertical
source options
This mark WAS observed with GPS, and it WAS separately leveled
Sources: ADJUSTED, ADJ_UNCH, POSTED, READJUST, N_HEIGHT, RESET, COMPUTED, GPSCONLV, LEVELING, H_LEVEL, GPS_OBS, VERT_ANG, SCALED, U_HEIGHT, VERTCON
Each type is explained in the “dsdata.txt” document
19

## Slide 20
“…CONTROL” Section continued
Cartesian
Coordinates
Laplace Correction - combined with astronomic azimuth, yields the geodetic azimuth
Geoid Height -separation between Geoid and the reference ellipsoid (negative in contig. U.S.)
Dynamic Height -geopotential value at the mark (NOT an orthometric height).
Modeled Gravity – interpolated from observed gravity values
Vertical Order Will be 2nd order (or better). NGS does not accept 3rd order, except on “Resets”
20

## Slide 21
ACCURACY STANDARDS SECTION
replaces Hz Order & Class for marks
Clicking on the “here” link generates the following table
Local Accuracies
21

## Slide 22
THE NEXT SECTION EXPLAINS HOW THE PUBLISHED VALUES WERE DETERMINED
22

## Slide 23
23
Leveled
in ~1934
Adjusted
in 1991
(re-adjusted)
Caution: don’t overlook the age of the observations

## Slide 24
PHOTOGRAPH SECTION
24
This is station “C 43” - located just northwest of the Indiana State Fairgrounds

## Slide 25
SECTION PROVIDING
STATE PLANE COORDINATES and
UTM COORDINATES
25

## Slide 26
SECTION SHOWING SUPERSEDED VALUES
*
*
*
*
“KOLLATH”
26

## Slide 27
SECTION PROVIDING THE MARK’S
NATIONAL GRID ADDRESS
U. S. National Grid (USNG) system is a FGDC standard, developed to improve public safety and commerce.
http://www.fgdc.gov/usng
27

## Slide 28
Mark Description Section - Two examples
28
(Coast and Geodetic Survey disk)
Station
“C 43”
Station
“MOOSE EAR”
(set by Barron Co. WI )

## Slide 29
SECTION SHOWING THE MARK’S
“SETTING AND RECOVERY HISTORY”
29
“Kollath” – 16 recoveries

## Slide 30
STATION RECOVERY NOTES - BE AWARE THAT RECOVERY NOTES CAN SOMETIMES BE MISLEADING!
Mark originally set by NGS (CGS) in 1948
17 YEARS LATER
30

## Slide 31
SECTION OF THE DATASHEET SHOWING THE STATION DESCRIPTION … (TO-REACH and TIES)
31
To-Reach Info
Ties

## Slide 32
FINALLY,
WATCH FOR NOTIFICATION THAT YOUR DATASHEET(S) EXTRACTION IS COMPLETE
If you do not see this message at the end, you did not get all of the datasheets that you requested.
32

## Slide 33
SUMMARY
Different types of marks (Hz- Vert) exist in the field
Datasheets contain much useful info. Info will vary depending on the type of mark.
“dsdata.txt” is a great source for understanding datasheets http://www.ngs.noaa.gov/cgi-bin/ds_lookup.prl?Item=DSDATA.TXT
There are several ways to obtain published NGS data.
Your NGS Advisor is here to assist you with understanding & using the National Spatial Reference System (NSRS)
Thank you for attending this session.
33

## Slide 34
Remember that NGS REGIONAL ADVISORS are here to help you. Find Advisors’ contact info on the NGS website at:
http://www.ngs.noaa.gov/ADVISORS/
34
QUESTIONS…