## Slide 1: Development of a Modernized NSRS in the U.S.
Michael Dennis, PhD, PE, PLS
NOAA’s National Geodetic Survey

## Slide 2: National Geodetic Survey (NGS) Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, orientation, and shoreline throughout the United States.

## Slide 3: “Modernizing” the NSRS means:
Update all NSRS coordinates
  Replace existing datums with new datums
  Account for coordinates changing with time
Improve NGS products and services
Simplify customer contributions
Make the NSRS:
  More accurate
  More accessible
  More efficient
  More compatible with GNSS
Rollout in
2025

## Slide 4
Why is NSRS Modernization important?
Because our society and economy are becoming increasingly “spatially enabled”
GPS
Cycle
Pit Stop
Pee Here
iPoo - the GPS toilet locator
Geodesy: the science of where things are

## Slide 5: NSRS Modernization “Blueprint” documents
Geometric Coordinates and Terrestrial Reference Frames
Geopotential Coordinates and Geopotential Datum
Working in the Modernized NSRS

## Slide 6
Tectonic plates

## Slide 7
Tectonic plates “fixed” for the three existing NAD 83 frames
NAD 83 (2011)
NAD 83 (PA11)
NAD 83 (MA11)
North American Datum of 1983 (2011) epoch 2010.0
North American Datum of 1983 (PA11) epoch 2010.0
North American Datum of 1983 (MA11) epoch 2010.0
All at epoch 2010.0 (Jan 1, 2010)

## Slide 8
Tectonic plates “fixed” for the four 2022 Terrestrial Reference Frames
Initially at epoch 2020.0 (Jan 1, 2020) and identical to ITRF2020
CATRF2022
North American Terrestrial Reference Frame of 2022 (NATRF2022)
Pacific Terrestrial Reference Frame of 2022 (PATRF2022)
Mariana Terrestrial Reference Frame of 2022 (MATRF2022)
Caribbean Terrestrial Reference Frame of 2022 (CATRF2022)
NATRF2022
PATRF2022
MATRF2022

## Slide 9
ITRF2020 velocities for CONUS

## Slide 10
NATRF2022 velocities for CONUS

## Slide 11: IFVM2022: Intra-Frame Velocity Model of 2022

## Slide 12: IFDM2022: Intra-Frame Deformation Model of 2022
Crustal motion models
  Current NSRS: HTDP (Horizontal Time-Dependent Positioning)
  Modernized NSRS: IFDM2022 (Intra-Frame Deformation Model of 2022)
IFDM2022 v1.0 based (in part) on HTDP and TRANS4D
Will use TRANS4D velocity grids
  Higher resolution than HTDP
  Includes vertical component
  Includes velocity uncertainty estimates
Same earthquake models as HTDP (but likely modeled differently)

## Slide 13
52 tectonic plates over entire planet modeled in HTDP v3.5.0

## Slide 14
52 tectonic plates over entire planet modeled in HTDP v3.5.0
Plus 10 horizontal-only velocity grids

## Slide 15
52 tectonic plates over entire planet modeled in IFDM2022 v1.0
Plus 10 3D velocity grids from TRANS4D (covering much larger area than HTDP)

## Slide 16: Earthquake models in HTDP v3.5.0 (and IFDM2022 v1.0)
Coseismic models
  Okada dislocation models (not grids in HTDP)
  Fault rupture surface modeled
  32 models (1934 – 2019)
Postseismic grid
  One in Alaska (2002 Denali earthquake)
  Time decay (motion decreases with time)
Problems:
  Long time lag for model development
  Models created outside NGS
  Often multiple models but must choose one
Modeled earthquakes that occurred between 2010.0 and 2020.0

## Slide 17: IFDM for NSRS Modernization
Intend to use modern Open Geospatial Consortium (OGC) standards
  Geodetic Grid Exchange Format (GGXF) for grids
  Deformation Model Functional Model (DMFM), including coseismic events
Latitude/longitude grids in ITRF2020
Will give same results as NADCON at reference epochs
  Interval of 5 or 10 years (TBD)
  First is epoch 2020.0, second will be 2025.0 (or 2030.0), etc.
Coordinate with Canada to ensure consistent results across border

## Slide 18
Ridgecrest earthquake (July 2019)
El Mayor-Cucapah earthquake (April 2010)
Current version of HTDP (3.50)
Horizontal shifts (CONUS): NAD 83 epoch 2010.0 to NATRF2022 epoch 2020.0 (meters)

## Slide 19
Ridgecrest earthquake (July 2019)
Preliminary version of IFDM2022
Horizontal shifts (CONUS): NAD 83 epoch 2010.0 to NATRF2022 epoch 2020.0 (meters)
El Mayor-Cucapah earthquake (April 2010)

## Slide 20
Current version of HTDP (3.50)
Ellipsoidal height shifts (CONUS): NAD 83 epoch 2010.0 to NATRF2022 epoch 2020.0 (meters)
Ridgecrest earthquake (July 2019)
El Mayor-Cucapah earthquake (April 2010)

## Slide 21
Preliminary version of IFDM2022
Ellipsoidal height shifts (CONUS): NAD 83 epoch 2010.0 to NATRF2022 epoch 2020.0 (meters)
Ridgecrest earthquake (July 2019)
El Mayor-Cucapah earthquake (April 2010)

## Slide 22: “Shift & Drift”
Sudden SHIFT. For CONUS at epoch 2020.0 for change from NAD 83:
  Horizontal change of about 0.8 to 3 meters
  Ellipsoid height change of about -0.1 to -1.6 meters
Continuous DRIFT due to crustal motion
  Average about 2 cm/yr in CONUS (horizontal)
  Remove most by modeling tectonic plate (horizontal only)
  Remaining 3D motion minimized with crustal motion models
Purpose:
  Minimize change in coordinates with time
  Determine coordinates at any time (epoch)
Coordinates in modernized
NSRS will always have a date

## Slide 23: NSRS Modernization “Blueprint” documents
Geometric Coordinates and Terrestrial Reference Frames
Geopotential Coordinates and Geopotential Datum
Working in the Modernized NSRS

## Slide 24
NMVD03
ASVD02
NAVD 88
North America and Caribbean
NAVD 88
IGLD 85
PRVD02
VIVD09
Pacific Ocean
GUVD04
NMVD03
ASVD02
GUVD04
PRVD02
VIVD09
IGLD 85
NAVD 88
Current vertical datums of the National Spatial Reference System

## Slide 25
Extent of the new geopotential (“vertical”) datum
North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
Includes the following (time-varying) models:
Geoid model (GEOID2022)
Surface gravity model (GRAV2022)
Deflection of the vertical model (DEFLEC2022)
American Samoa
Guam and Northern Marianas Islands

## Slide 26
Orthometric height shifts (CONUS): NAVD 88 (undefined epoch) to NAPGD2022 epoch 2020.0 (meters)

## Slide 27
Experimental Geoid 2020 (xGEOID20)
First xGEOID coordinated with Canada
GRAV-D data used for most areas (in version B of model)

## Slide 28
Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
97.0% Complete
(as of April 2023)

## Slide 29: Other things about NAPGD2022
Defined by GEOID2022 (not by leveling)
  Orthometric height = ellipsoidal height − geoid height
  Ability to determine dynamic heights using GNSS
But leveling will still be supported
  For high-accuracy orthometric height differences
  Constrained to orthometric heights from GNSS + geoid model
Will include time dependence
  Through NGS Geoid Monitoring Service (GeMS)
  Static geoid + “dynamic” geoid
  Likewise for other NAPGD2022 products

## Slide 30: NSRS Modernization “Blueprint” documents
Geometric Coordinates and Terrestrial Reference Frames
Geopotential Coordinates and Geopotential Datum
Working in the Modernized NSRS

## Slide 31: New types of coordinates
Reference Epoch Coordinates (RECs)
A temporal “snapshot” of entire network
Similar to NAD 83 (2011/PA11/MA11) epoch 2010.00
Initial epoch 2020.00
Every 5 or 10 years
Survey Epoch Coordinates (SECs)
Time-dependent!
Gives coordinates at the time of observation
Time is at midpoint of a “geometric adjustment window”
Multiple SECs can show changes over time

## Slide 32: What about (map) projected coordinates?
Surveyors (and engineers) projected coordinate reference systems
(geodesists, not so much)
SPCS2022
Making the Earth flat again
…one zone at a time

## Slide 33: State Plane Coordinate System of 2022 (SPCS2022)
Third generation of State Plane
  First in 1930s, second in 1980s
  Same 3 map projection types
  Same ellipsoid as SPCS 83 (GRS 80)
The same, but different…
  Based on new terrestrial reference frames instead of NAD 83
  Designed to reduce linear distortion at topographic surface (i.e., reduce difference between “grid” and “ground” distances)
  More zones, most designed by state stakeholders
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 34
Designs by NGS
  165 zones
  Includes 54 statewide zones and 3 “special use” zones (in more than one state)
Designs by state stakeholders
  802 zones in 28 states
Total = 967 zones for 56 states and territories
Compare to 125 zones in existing State Plane
Number of SPCS2022 zones

## Slide 35: Overall SPCS2022 distortion design philosophy
Linear distortion minimized (or “optimized”) at topographic surface (not at ellipsoid surface)
Purpose: to reduce difference between and projected “grid” and actual “ground” distances in areas where people actually work
What is linear distortion?
  Defined at a point (infinitesimal distances)
  Unique (i.e., same in every direction) only for conformal projections
  Often given in parts per million (ppm) = mm per km
Linear distortion | = | δ | = | Projected minus actual distance
 |  |  |  | Actual distance

## Slide 36: Map projection linear distortion
Distortion at a point computed as:
  where
    k = point scale factor (distortion due to Earth curvature)
    h = ellipsoid height of point (distortion due to change in height)
    R = Earth geometric mean (Gaussian) radius curvature
  < 0  projected (grid) distance shorter than true (ground) distance
  > 0  projected (grid) distance longer than true (ground) distance
Height (“elevation”) factor
Point scale factor
Combined factor

## Slide 37
Map projection linear distortion
Ellipsoid surface (~“sea level”)
Topographic surface
Grid (“map”) distance
Projection surface
Horizontal ground distance
This design approach used for SPCS 83 and 27 (minimizes distortion with respect to ellipsoid)
Grid distance < ground distance
Map projection designed to minimize linear distortion on ellipsoid (at “sea level”)

## Slide 38
Map projection linear distortion
Projection surface
Map projection designed to minimize linear distortion at ground surface
Topographic surface
This design approach is being used for SPCS2022 (minimizes distortion with respect to topography)
Ellipsoid surface (~“sea level”)
Grid distance ≈ ground distance

## Slide 39
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 
SPCS2022 linear distortion 846 zones (CONUS)
Percent within distortion (ppm):

## Slide 40
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
SPCS 83 linear distortion 106 zones (CONUS)
Percent within distortion (ppm):

## Slide 41: Other exciting NSRS Modernization progress
LASER. Least squares Adjustments: Statistics, Estimates and Residuals
  Will be used for geometric and orthometric (leveling) adjustments
M-PAGES. Multi-constellation GNSS processing software
  Currently being tested in OPUS-Static
OPUS-Projects 5.1. Released to production
  Supports real-time and 3rd party processed GNSS vectors
GDX. Geodetic Data Exchange format
  Include GVX (GNSS Vector Exchange format)
  Plus total station, leveling, and gravity obsevations
And more…

## Slide 42
geodesy.noaa.gov

## Slide 43: Summary of NSRS Modernization
Geometric based on ITRF2020
Geopotential based on GRAV-D + satellite + terrestrial gravimetry
Explicit time-dependence for all components
Updated State Plane Coordinate System
Release in 2025
  But will start releasing preliminary (”alpha”) products next month!
  First will be alpha SPCS2022 and alpha GDX
Thank you!