## Slide 1
NGS Update
Much ado about 2022
Geospatial Control Subcommittee
of the
Geospatial Data Acquisition Technologies in Design and Construction Committee (AFB80)
Michael Dennis, RLS, PE
Geodesist
michael.dennis@noaa.gov
Transportation Research Board
97th Annual Conference
Washington, DC
January 8, 2018

## Slide 2
geodesy.noaa.gov

## Slide 3
NGS Advisors

## Slide 4: State Coordinators

## Slide 5
geodesy.noaa.gov

## Slide 6: Much ado about what’s new in 2022
Modernizing the National Spatial Reference System (NSRS)
New “datums” for 2022!
  Four (4) new Terrestrial Reference Frames of 2022
  North American-Pacific Geopotential Datum of 2022
New publications!
  Geometric and geopotential blueprints (parts 1 and 2)
  NADCON 5.0 report
  History and status of State Plane
New projects, products, and services!
  GPS on Bench Marks project
  NGS Coordinate Conversion & Transformation Tool (NCAT)
  OPUS for Bluebooking (…and “OPUS for Everything”)
  New experimental geoid models
New State Plane Coordinate System of 2022!

## Slide 7
NAD 83 (MA11)
NAD 83 (PA11)
NAD 83 (2011)
North American Datum of 1983
Three frames:
NAD 83 (2011): North America and Caribbean plates
NAD 83 (PA11): Pacific plate
NAD 83 (MA11): Mariana plate

## Slide 8
NMVD03
ASVD02
NAVD 88
NA and Caribbean
NAVD 88
IGLD 85
PRVD02
VIVD09
Pacific
GUVD04
NMVD03
ASVD02
Current vertical datums of the NSRS
GUVD04
PRVD02
VIVD02
IGLD 85
NAVD 88

## Slide 9: Why replace NAD 83 and NAVD 88?
Main driver: Global Navigation Satellite System (GNSS)
ACCESS!
  GNSS equipment is fast, inexpensive, reliable (and improving)
  Reduces reliance on finding survey control (“bench marks”)
ACCURACY!
  Insensitive to distance-dependent errors; reliable
  Immune to bench mark instability (referenced to CORS)
CONSISTENCY!
  Eliminates systematic errors in current datums
  Aligned with global reference frames
  Integrated system for both positions and heights (“elevations”)

## Slide 10: Geometric: Out with the old, in with the new
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
4 plate-fixed frames North America, Caribbean, Pacific, Mariana

## Slide 11
NATRF2022
PATRF2022
CATRF2022
NAD 83 (2011/PA11/MA11) epoch 2010.00 
2022 Terrestrial
Reference Frames
Horizontal change at epoch 2022.00
(contours in meters)

## Slide 12
PATRF2022
MATRF2022
NAD 83 (2011/PA11/MA11) epoch 2010.00 
2022 Terrestrial
Reference Frames
Horizontal change at epoch 2022.00
(contours in meters)

## Slide 13
NAD 83 (2011/PA11/MA11) epoch 2010.00 
2022 Terrestrial
Reference Frames
Change in ellipsoid heights at epoch 2022.00
(contours in meters)

## Slide 14: U.S. CORS Velocity Field – ITRF2008 (IGS08 epoch 2005.0)

## Slide 15: U.S. CORS Velocity Field - NAD83(2011) epoch 2010.00

## Slide 16: “Vertical”: Out with the old, in with the new
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  Will include GEOID2022 DEFLEC2022 SGRAV2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid Heights
Deflections of
the Vertical
one vertical datum
pole-to-equator

## Slide 17
Extent of NAPGD2022 gravimetric geoid model
American Samoa
Guam and Northern Marianas Islands

## Slide 18
Estimated change in orthometric heights from NAVD 88 to NAPGD2022
NAPGD2022 approximated using xGEOID16B

## Slide 20: GPS on Bench Marks

## Slide 21: NGS GIS Map - GPS on Bench Mark

## Slide 22
beta.ngs.noaa.gov

## Slide 23
beta.ngs.noaa.gov/NCAT

## Slide 25
beta.ngs.noaa.gov/GEOID/xGEOID17

## Slide 26: New State Plane Coordinate System
State Plane Coordinate System of 2022 (SPCS2022)
  Referenced to new 2022 TRFs
  Based on same reference ellipsoid (GRS 80)
  Same 3 conformal projection types
    Lambert Conformal Conic (LCC)
    Transverse Mercator (TM)
    Oblique Mercator (OM)
NGS in process of specifying SPCS2022 characteristics
  Draft policy and procedures for public comment
  Federal Register Notice on policy and procedures
  New report on State Plane history, policy, and future
NOTE: SPCS2022 characteristics currently in review
  Approved version may differ from what is presented here

## Slide 27: SPCS Special Publication
History of NGS projections (1853 to present)
SPCS policies and legislation
Departures from policy and convention
Recent developments in projected coordinate systems
Appendices
  Defining parameters for ALL zones of ALL versions of SPCS, plus additional information
  Status of SPCS 83 legislation and foot conversions

## Slide 28
State Plane Coordinate Systems of 1927 (134 zones) and 1983 (125 zones)
Guam SPCS 83 zone added in 1995

## Slide 29
Original SPCS 27, as of 1934 (110 zones total)

## Slide 30
Final SPCS 27, as of 1968 (112 zones in CONUS, 131 zones total)
Reduced distortion zones added: CA 7 (1945) MI (1964)

## Slide 31
Final SPCS 83, as of 2001 (108 zones in CONUS, 125 zones total)
KY statewide zone added in 2001

## Slide 32
Alaska State Plane Coordinate Systems of 1927 and 1983 (10 zones)

## Slide 33
Hawaii State Plane Coordinate Systems of 1927 and 1983 (5 zones)
“SPCS 27” version referenced to Old Hawaiian Datum
Puerto Rico and U.S. Virgin Islands State Plane Coordinate Systems of 1927 (2 zones) and 1983 (1 zone)
“SPCS 27” version referenced to
Puerto Rico 1940 Datum

## Slide 34: Draft SPCS2022 Policy & Procedures
Release for 6-month public comment period
  Deadline for comments set at July 31, 2018
Stakeholder input on what they want for their zones
  DOTs, GIS offices, professional societies, universities
  Deadlines (draft):
    Dec 31, 2019 for requests and proposals
    Dec 31, 2020 for submitted designs
Includes SPCS2022 characteristics & requirements
  Projection types and parameters
  Default designs (if no consensus stakeholder input)
  “Layered” zones and low-distortion projections (LDPs)
  Linear distortion design criteria
    Difference in distance between “ground” and “grid” (projected)

## Slide 35: Linear distortion magnitudes
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum UTM value (on ellipsoid)
  Maximum design criterion for SPCS2022 zones (at ground)

## Slide 36: Default SPCS2022 designs (draft)
Most zones will keep same extents and projection type
Modifications to align with SPCS2022 policy:
  Scale redefined with respect to topographic surface
  One-parallel Lambert and local Oblique Mercator
Some possible changes in projection types and zones:
  Single OM zone for FL peninsula (replaces 2 TM zones)
  Single OM zone for Hawaii (replaces 5 TM zones)
  Group RI, CT, MA into one zone (reduces number zones by 3)
  Include Guam and CNMI in a single TM zone
  Define LCC zone for American Samoa
  Redefine AK zones to better correspond to land use
  Zone added for Washington D.C.

## Slide 37
 |  | SPCS 83 AZ C | 
C.M. |  | 111°55’W | 
Scale |  | 0.9999 | 
 |  | Distortion (ppm) | 
Min |  | -660 | 
Max |  | +102 | 
Mean |  | -224 | 
SPCS 83 Arizona Central Zone (Transverse Mercator)
 | Height (m)
Min | 96
Max | 3607
Mean | 1177

## Slide 38
 |  | SPCS 83 AZ C | SPCS2022
C.M. |  | 111°55’W | 112°W
Scale |  | 0.9999 | 1.0001
 |  | Distortion (ppm) | 
Min |  | -660 | -455
Max |  | +102 | +277
Mean |  | -224 | -24
SPCS2022 “default” Arizona Central Zone (Transverse Mercator)
 | Height (m)
Min | 96
Max | 3607
Mean | 1177
No change in projection type or zone extents

## Slide 39
 |  | SPCS 83 CO S | 
Central parallel |  | 37°50’02.98…”N | 
Cen parallel scale |  | 0.9999453985… | 
 | Height (m) | Distortion (ppm) | 
Min | 998 | -697 | 
Max | 4106 | -117 | 
Mean | 2091 | -352 | 
SPCS 83 Colorado South (Lambert Conformal Conic 2-parallel)

## Slide 40
 |  | SPCS 83 CO S | SPCS2022
Central parallel |  | 37°50’02.98…”N | 37°45’N
Cen parallel scale |  | 0.9999453985… | 1.00028
 | Height (m) | Distortion (ppm) | 
Min | 998 | -697 | -360
Max | 4106 | -117 | +209
Mean | 2091 | -352 | -19
SPCS2022 “default” CO S (Lambert Conformal Conic 1-parallel)
No change in projection type or zone extents

## Slide 41
 |  | SPCS 83 FL EW | 
Scale |  | 0.999941176… | 
 |  | Distortion (ppm) | 
Min |  | -68 | 
Max |  | +100 | 
Mean |  | -32 | 
SPCS 83 Florida
East & West zones
(Transverse Mercator)
 | Height (m)
Min | -31
Max | +63
Mean | -9

## Slide 42
 |  | SPCS 83 FL EW | SPCS2022
Scale |  | 0.999941176… | 0.99991
 |  | Distortion (ppm) | 
Min |  | -68 | -99
Max |  | +100 | +97
Mean |  | -32 | -50
SPCS2022 “default” Florida peninsula (Oblique Mercator)
 | Height (m)
Min | -31
Max | +63
Mean | -9
Change projection type and replace two zones with one

## Slide 43: “Layered” zones (draft)
Limitations
  Max of TWO layers: Statewide and sub-zones
  If two layers, one MUST be statewide
  Minimum sub-zone dimension > 50 km
States often want statewide and small zones
  Statewide: Single geometry required for state GIS
  Sub-zones: Lower distortion for surveying/engineering
  But not all states will want or need both types
Accommodates state needs, but with restrictions
  Prevent poor design choices for statewide zones
  And one already exists in SPCS 83…

## Slide 44: Kentucky layered zones
 |  | North | South | 
N parallel |  | 38°58’N | 37°56’N | 
S parallel |  | 37°58’N | 36°44’N | 
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | 
Max |  | +17 | +42 | 
Mean |  | -56 | -67 | 
“Layered” zones
SPCS 83 Kentucky N and S zones (Lambert Conformal Conic)

## Slide 45: Kentucky layered zones
 |  | North | South | Statewide
N parallel |  | 38°58’N | 37°56’N | 38°40’N
S parallel |  | 37°58’N | 36°44’N | 37°05’N
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | -166
Max |  | +17 | +42 | +181
Mean |  | -56 | -67 | -58
“Layered” zones
SPCS 83 Kentucky statewide zone (Lambert Conformal Conic)

## Slide 46: Linear distortion design criteria
NGS design of zones requested by stakeholders
  Limited to zones with 50-400 ppm distortion criterion
    50 ppm = 5 cm/km = 0.3 ft/mi = 1:20,000
    100 ppm = 10 cm/km = 0.5 ft/mi = 1:10,000
    400 ppm = 40 cm/km = 2.1 ft/mi = 1:2,500
Design criterion < 50 ppm (“low distortion”)
  Min criterion 20 ppm = 2 cm/km = 0.1 ft/mi = 1:50,000
  Must be designed by others (not by NGS)
  Proposed and final design reviewed by NGS
What is the current situation with “low distortion” projected coordinate systems?

## Slide 48
Iowa has already requested this system be part of SPCS2022

## Slide 49: Summary: NSRS Modernization
New “datums” for 2022
  Four new Terrestrial Reference Frames
  New Geopotential Datum (NAPGD2022)
New publications
  New datums, NADCON 5, State Plane
New products and services
  GPS on BMs, NCAT, OPUS for Bluebooking, xGEOID17
State Plane Coordinate System of 2022
  Designed with respect to “ground”
  Default designs similar to existing State Plane
  Can include a statewide zone plus a sub-zone layer
  Stakeholder input on zones for their states (including LDPs)
  NGS webinar on March 8 – register at:
  https://geodesy.noaa.gov/web/science_edu/webinar_series/Webinars.shtml
All of this is currently in review, not yet finalized