## Slide 1
The National Geodetic Survey
Dr. Dru Smith
Chief Geodesist
NOAA’s National Geodetic Survey

## Slide 2: About the National Geodetic Survey
Executive Branch
Department of Commerce (DOC)
National Oceanic and Atmospheric Administration (NOAA)

## Slide 3
National Ocean Service (NOS)
National Geodetic Survey (NGS)
National Oceanic and Atmospheric Administration (NOAA)
About the National Geodetic Survey

## Slide 4: NGS’s Mission and Role
  NGS Mission: “To define, maintain, and provide access to the National Spatial Reference System to meet our nation’s economic, social, and environmental needs”
  “The National Spatial Reference System is the fundamental geodetic control for the United States.”
    NAD 83
    NAVD 88
    IGLD 85
    Official Shoreline
  The Elevator Speech…
    We’re the people who define latitude, longitude and height for everything in the country

## Slide 5: What do we do?
We are performing a 15 year long airborne
gravity survey of the entire USA (“GRAV-D”)

## Slide 6: What do we do?
We manage (store, analyze, disseminate) data from over 2000 GNSS stations in the CORS network

## Slide 7: What do we do?
We compute orbits of GPS satellites, accurate to centimeters.
NGS relative to IGS ~ 1 cm

## Slide 8: What do we do?
We maintain the official geodetic control database for the nation with over 1,000,000 passive geodetic control marks.

## Slide 9: What do we do?
We perform the highest accuracy geodetic surveys in the nation.
GPS
Leveling
Traverse
Gravity Gradients
Absolute Gravity

## Slide 10: What do we do?
We calibrate GNSS antennae, gravimeters and EDM baselines.

## Slide 11: What do we do?
We write and maintain hundreds of computer programs for the NSRS user community.
FORTRAN
Java
C++
Perl
Python
SQL
MATLAB
Visual BASIC
---------
UNIX
PC

## Slide 12: What do we do?
We fly airborne LIDAR and imagery missions to delineate the official shoreline of the nation.

## Slide 13: What do we do?
We perform research on everything related to geodesy, surveying and remote sensing.

## Slide 14: What do we provide?
We provide services for users to process GPS or Leveling data and submit it to NGS.

## Slide 15: What do we provide?
We provide software for users to transform coordinates between datums and across epochs

## Slide 16: What do we provide?
We provide data to users free of charge in the form of RINEX files, datasheets, geoid grids, etc

## Slide 17: What do we provide?
We provide education to users free of charge including an online library, presentation archive, instructional videos and hands-on training classes

## Slide 18: Some surprising responsibilities
We provide emergency response imagery after major events
Hurricane Isabel
Deepwater Horizon
9/11
Hurricane Katrina

## Slide 19: Some surprising responsibilities
We survey or quality control every survey of every airport in the country

## Slide 20: Upcoming cool stuff
Recognizing modern tools, technology and knowledge, NGS is changing how perform our mission
NAVD 88, NAD 83 and IGLD 85 are all being replaced in 2022
  Geocentric , Geoid-based positioning

## Slide 21: Old vs New Datums
The old way
The new way
Geoid
Temporal Geoid Change
Text based datasheets
Observed changes viewed as
“corrections” not “movement”
Fragile, unchecked passive control
Modern datasheets
CORS
RTN

## Slide 22
NAVD 88 suffers from use of bench marks that:
  Are almost never re-checked for movement
  Disappear by the thousands every year
  Are not funded for replacement
  Are not necessarily in convenient places
  Don’t exist in most of Alaska
  Weren’t adopted in Canada
  Were determined by leveling from a single point, allowing cross-country error build up
Why isn’t NAVD 88 good enough anymore?
PID: EZ0840

## Slide 23
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface:
Why isn’t NAVD 88 good enough anymore?

## Slide 24: Terminology
Horizontal Datum
  Geometric Reference Frame
    Geocentric X, Y, Z
    Latitude, Longitude, Ellipsoid Height
Vertical Datum
  Geopotential Reference Frame
    Geoid undulation
    Orthometric height
    Gravity
    Deflection of the Vertical

## Slide 25
Approximate extent of
2022 geoid model used
for the “North American”
part of the new
geopotential reference
frame.

## Slide 26
Hawaii
Many US Pacific Territories
(not Guam, CNMI nor American Samoa)

## Slide 27
Canada
Alaska, including
entire Aleutian
Island Chain
CONUS (USA)

## Slide 28
Mexico
All Central
American Countries
All Caribbean
Countries
Bermuda

## Slide 29
Mexico
All Central
American Countries
All Caribbean
Countries
Bermuda

## Slide 30
CGVD2013*
No official
Vertical datum
NAVD 88
No official
Vertical datum
* geoid/GNSS based datum

## Slide 31: Canada Height Modernization - 2013
1. Time consuming
2. Expensive
3. Limited coverage
4. BMs are unstable
5. BMs disappear
6. Local networks
Levelling Networks:
1. Established over the
last 100 years
2. 120,000 km of levelling
lines
3. Some 80,000
benchmarks
The geoid model:
1. Entire coverage of the
Canadian territory
(land, lakes and oceans)
2. Compatible with space-
based positioning
(e.g., GNSS, altimetry)
3. Less expensive for
maintenance
4. Fairly stable reference
surface
H = hGNSS – NModel

## Slide 32
PRVD02
San José(1)
VIVD09
La Unión 1960(1)
Puerto Cortéz(1)
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
Corinto 1952(1)
Puntarenas(1)
Cristóbal(1)
Santo Domingo(1)
(1) Información cortesía de David Avalos
(1)

## Slide 33: Old vs New Datums
Step 1: Do the best scientific positioning work we can in ITRF
  Before any discussion of “plate fixed” or “map projections”
  NGS’s core goal must be the scientific integrity of positions
  New database
  Replacement of static vector-based GNSS processing

## Slide 34: Old vs New Datums
Step 2: Consider the question of “plate fixed”:
  Why do users want this?
    Fixed latitude and longitude?
  Nothing is “fixed” though
    Plate is not just rotating; more than 1 plate
  Who wins? Who defines “fixed”? Must all points maintain zero change?
    Model and remove all real motion? (aka “HTDP”)
      If not removing all motion, why remove any motion?
        ITRF minus plate rotation vs just ITRF

## Slide 35
~1.6 m
NAD 83 origin
ITRFxx origin
Earth’s Surface
hNAD83
hITRF
Simplified Concept of NAD 83 vs. ITRF
hNAD83 – hITRF varies
smoothly by latitude
and longitude

## Slide 36
1975
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2.000
2.050
2.100
2.150
2.200
2.250
2.300
2.350
H
time
Datasheets
On a point with 4 historic surveys, they
would be used to model and predict change

## Slide 37: 2015 Geospatial Summit
April 13-14, 2015, in the Washington, DC Area
As part of a broader “conference of conferences” with National Society of Professional Surveyors and Management Association for Private Photogrammetric Surveyors (MAPPS)
Follows the successful 2010 Geospatial Summit. More info at the 2015 Geospatial Summit website.
http://www.geodesy.noaa.gov/2015GeospatialSummit/

## Slide 38: Summary (1)
NGS is the oldest scientific agency in the nation (1807)
Although times change, the mission is still one of providing geodetic control to all surveys, maps and charts in the nation
Science and customer service

## Slide 39: Summary (2)
NGS engages in scientific research and applications in:
  Geodesy
  Remote Sensing
  Surveying
  Geophysics
  Mathematics

## Slide 40: Summary (3)
NGS is in a major transitional phase
  Need new, talented people who are educated in
    Geodesy, Remote Sensing, Surveying
    Traditional computational programming (Fortran/C++)
    Modern programming languages (Java, Perl, Objective-C) and platforms (ArcGIS, Google Earth)
  BS, MS, PhD all are needed!

## Slide 41: Working for NGS
Jobs in Maryland, Virginia and Colorado
Job openings in USAJOBS
Make an account
  Search “geodesy” and
  sign up for notifications

## Slide 42: Questions

## Slide 43: Thank you!

## Slide 44: Extra Slides

## Slide 45
Hawaii
Alaska
“CONUS”
Puerto Rico / Virgin Islands
Guam / Northern Marianas
American Samoa
GRAV-D
Planned
Coverage
Expected GRAV-D airborne gravity coverage by 2022

## Slide 46
The “secular” geoid change from the monthly GRACE models (2002-2008)
The solution represents the effect due to total mass changes.
The solution uses a 400-km Gaussian filter.
Deglaciation
Glacial Isostatic
Adjustment
Drought

## Slide 47: GSVS11: Proving why we need GRAV-D
Geoids without new GRAV-D data: 1-3 cm differential accuracy
over distances from 0.4 to 325 km
Geoids with new GRAV-D data:
1 cm differential accuracy over distances from 0.4 to 325 km

## Slide 48: Old vs New Datums: Origin
NAD 83 was theoretically “geocentric”
  Primarily based on pre-GNSS satellite geodesy
    Doppler, etc
  Off from ITRF2008 origin by ~ 1.5 meters
New geometric reference frame will all be “geocentric” to IGS frame circa 2020.00 or so

## Slide 49: Old vs New Datums: Access
Old datums used passive control as the primary access
  CORS / OPUS helped, but “datasheets” remain the largest download, far and away more than OPUS is used

## Slide 50: Old vs New Datums: Access
New datums
  Primary access: GNSS + geoid model
  Secondary access: Passive control
Fixed:
  CORS + geoid (coords and velocities both)

## Slide 51: Old vs New Datums: Passive Control
Roll of passive control in the future:
  Control for projects
    Depending on accuracy needs, new coordinates should be determined, rather than relying on published coordinates based on old surveys
  Monitoring sites for motion
  Calibrating RTNs

## Slide 52: Tools: Improvements
NADCON, VERTCON, SPCS, UTM, USNG, Vdatum, HTDP, VTDP will be merged into a single tool
Tool will be web-services based
  Online browser-based computations
  GIS-plug-in