## Slide 1: National Geodetic Survey NSRS OPUS

## Slide 2: CORS

## Slide 3: CORS

## Slide 4
Obtain Static Data Files for CORS Here
CORS “Data Products” Page

## Slide 5
Provide Information about your Project

## Slide 6
Enter your custom requests

## Slide 7
options:
projects & publishing
mark description
your solution
Online Positioning User Service OPUS geodesy.noaa.gov/OPUS/
JGE 2011v1
IGS & NGS base stations & site information files IGS antenna calibrations & satellite orbits & reference frames
UNAVCO teqc converter PAGES baseline processor
var. geophysical models
NGS geodetic toolkit
your GPS data
geodetic standard data

## Slide 8: OPUS
OPUS – S (2 hrs)
OPUS – RS (15 minutes)
OPUS – DB (Publish)
OPUS – Projects (Network)

## Slide 10: OPUS Submission Webpage
Your email address
Location of your data file
Your antenna type
Antenna height
Customize your solution - details on next slide

## Slide 11: Under the “OPTIONS” tab in OPUS
OPUS Projects ID
Include-Exclude CORS here
SPCS overrule
Change Geoid Model
Publish in OPUS-DB?
Select one to start computation process

## Slide 12: Why Do I Need the Antenna Type?
The antenna phase centers are located somewhere around here.
The Antenna Reference Point (ARP) is almost always located in the center of the bottom surface of the antenna.
The antenna offsets are the distance between the phase centers and the ARP
You do not need to know these offsets. They are passed to the processing software through the antenna type
Incorrect or missing antenna type  big vertical errors
ARP
phase ctr.
Notes: You can see where the ARP is.
When you enter the correct Antenna type OPUS knows the antenna offsets and passes them to the software to determine the ARP
NGS uses the ARP rather than the phase center. The ARP is a known point on the antenna whereas the phase center varies depending on the elevation angle from the antenna to the satellite.

## Slide 13: NGS Antenna Calibration – Relative vs. Absolute GNSS Antenna Calibration
relative
absolute
2 hours
GPS tracking

## Slide 14
Chart: Phase Center offsets (plan view)

## Slide 15
Chart: Phase Center offsets (side view)

## Slide 16
Chart: L2 Phase Center Variation as satellite passes overhead
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 85 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15 | 10 | 5 | 0
AOAD/M_B | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AOAD/M_R | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AOAD/M_T | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AOAD/M_TA_NGS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ASH700228C | 0 | 0 | -2 | -2.9 | -3.2 | -3.1 | -2.6 | -2.1 | -1.6 | -1.2 | -1 | -0.9 | -1 | -1.2 | -1.5 | -1.6 | -1.6 | -1.1 | 0 | -1.1 | -1.6 | -1.6 | -1.5 | -1.2 | -1 | -0.9 | -1 | -1.2 | -1.6 | -2.1 | -2.6 | -3.1 | -3.2 | -2.9 | -2 | 0 | 0
ASH700228D | 0 | 0 | -1.4 | -1.9 | -2.1 | -2 | -1.7 | -1.4 | -1.2 | -1 | -0.9 | -1 | -1.1 | -1.3 | -1.5 | -1.6 | -1.5 | -1 | 0 | -1 | -1.5 | -1.6 | -1.5 | -1.3 | -1.1 | -1 | -0.9 | -1 | -1.2 | -1.4 | -1.7 | -2 | -2.1 | -1.9 | -1.4 | 0 | 0
ASH700228E | 0 | 0 | -1.4 | -1.9 | -2.1 | -2 | -1.7 | -1.4 | -1.2 | -1 | -0.9 | -1 | -1.1 | -1.3 | -1.5 | -1.6 | -1.5 | -1 | 0 | -1 | -1.5 | -1.6 | -1.5 | -1.3 | -1.1 | -1 | -0.9 | -1 | -1.2 | -1.4 | -1.7 | -2 | -2.1 | -1.9 | -1.4 | 0 | 0
ASH700700.A | 0 | 0 | -3.7 | -2.1 | -0.6 | 0.7 | 1.7 | 2.4 | 2.8 | 3 | 2.8 | 2.5 | 1.9 | 1.2 | 0.6 | 0 | -0.4 | -0.5 | 0 | -0.5 | -0.4 | 0 | 0.6 | 1.2 | 1.9 | 2.5 | 2.8 | 3 | 2.8 | 2.4 | 1.7 | 0.7 | -0.6 | -2.1 | -3.7 | 0 | 0
ASH700700.B | 0 | 0 | -4.5 | -2.7 | -1.1 | 0.2 | 1.2 | 1.9 | 2.3 | 2.5 | 2.4 | 2 | 1.6 | 1 | 0.4 | -0.2 | -0.5 | -0.5 | 0 | -0.5 | -0.5 | -0.2 | 0.4 | 1 | 1.6 | 2 | 2.4 | 2.5 | 2.3 | 1.9 | 1.2 | 0.2 | -1.1 | -2.7 | -4.5 | 0 | 0
ASH700718A | 0 | 0 | 0 | -2.5 | -4.1 | -5.3 | -6 | -6.4 | -6.6 | -6.8 | -6.8 | -6.7 | -6.6 | -6.4 | -5.9 | -5.2 | -4.1 | -2.4 | 0 | -2.4 | -4.1 | -5.2 | -5.9 | -6.4 | -6.6 | -6.7 | -6.8 | -6.8 | -6.6 | -6.4 | -6 | -5.3 | -4.1 | -2.5 | 0 | 0 | 0
ASH700718B | 0 | 0 | 0 | -2.5 | -4.1 | -5.3 | -6 | -6.4 | -6.6 | -6.8 | -6.8 | -6.7 | -6.6 | -6.4 | -5.9 | -5.2 | -4.1 | -2.4 | 0 | -2.4 | -4.1 | -5.2 | -5.9 | -6.4 | -6.6 | -6.7 | -6.8 | -6.8 | -6.6 | -6.4 | -6 | -5.3 | -4.1 | -2.5 | 0 | 0 | 0
ASH700829.2 | 0 | 0 | 1 | -1.7 | -3.7 | -5 | -5.8 | -6.3 | -6.6 | -6.7 | -6.7 | -6.6 | -6.5 | -6.2 | -5.7 | -5 | -3.9 | -2.3 | 0 | -2.3 | -3.9 | -5 | -5.7 | -6.2 | -6.5 | -6.6 | -6.7 | -6.7 | -6.6 | -6.3 | -5.8 | -5 | -3.7 | -1.7 | 1 | 0 | 0

## Slide 17: Antenna Type, height – easy, right?
Type?
  Verify by looking up in ANTCAL
  Orient the antenna indicator to true north
  Centered over the mark? (check plummet or bubble)
Height?
  Height to what? (antenna ARP, not L1-phase center)
  Fixed-height tripods are easier than slip-legs.
  Vertical, NOT slant-height.
  Is your fixed-height tripod really fixed? (measure!)

## Slide 18: How is the Antenna Height Measured?
ARP
MARK
The height is measured vertically (NOT the slant height) from the mark to the ARP of the antenna.
The height is measured in meters.
The ARP is almost always the center of the bottom-most, permanently attached, surface of the antenna.
See GPS Antenna Calibration for photo’s and diagrams that show where the ARP is on most antennas:
http://geodesy.noaa.gov/ANTCAL/
If the default height of 0.0000 is entered, OPUS will return the position of the ARP.
Notes: The height of the antenna is measured vertically from the from the mark, to the Antenna Reference Point which is almost always the center of the bottom-most, permanently attached piece o f the antenna.
Some antennas have a short pipe or extension to them.
If in doubt you can find photo’s and diagrams of each antenna (that we have calibrated) at the URL shown.
So if you leave the antenna height as “0” this will be the height OPUS returns.

## Slide 19: OPUS Static vs. Rapid Static
 | Static | Rapid Static
Input (dual-frequency GPS) | 2-48 hours | 15 minutes-2 hours
Output | normal, extended, XML datasheet, project | normal, extended, XML
Accuracy (95%confidence) | 1-2 cm horizontal 3-6 cm ellipsoidal height | 1-2 cm horizontal 4-8 cm ellipsoidal height
Network geometry | 3 CORS, preferably within 1000 km of rover | 3-9 CORS, surrounding & within 250 km of rover
Availability | global | 90% of CONUS (subject to CORS configuration)

## Slide 20
4,000++ OPUS-Published Solutions
April 2012

## Slide 21: OPUS-DB Published Solutions

## Slide 22: Why OPUS-DB
A new easier way to capture data and have it in an NGS database
Help populate Ellipsoidal Heights on Bench Marks, help with Geoid models and future vertical datums

## Slide 23: Marks Published.
2011-03-03
23
OPUS
is showing steady growth in registered users and published marks.
Chart: marks published

## Slide 24: NGS Data Sheets
Traditional
blue booking
New
OPUS-DB

## Slide 25: NGS Data Sheets
NGSIDB
  Passive control
  Episodically refined (NRA2011)
  Traditional surveying
  A lot of (important!) numbers and text
OPUS-DB
  Actively determined from CORS
  Constantly refined
  GPS Surveying
  A lot of numbers/text and some useful graphics/images

## Slide 26: Sample OPUS DataSheet
http://www.ngs.noaa.gov/

## Slide 27: OPUS DB Requirements
Field Procedures
GPS data file ≥ 4 hour duration
quality mark setting
experienced observer
fixed height tripod recommended
brace tripod legs with sandbags or chain
verify antenna height and plumb

## Slide 28: OPUS DB Requirements
High-Quality OPUS Solution
≥ 70% observations used
≥ 70% ambiguities fixed
≤ 3 cm RMS
≤ 4 cm peak-to-peaks, lat. & lon.
≤ 8 cm peak-to-peak, el. hgt.
properly identify antenna type
precise or rapid orbits (avail. next day)

## Slide 29: OPUS DB Requirements
Mark Attributes
photos of mark & equipment
details (name, type, stability, etc.)
description to aid mark recovery
preview mark description form & help file

## Slide 30: OPUS-DB Requirements

## Slide 31: Issues to Consider
Site
  instability, multi-path
  mark ID (search database, check stamping)
Weather
  wild, local troposphere issues?
  space weather: ionospheric issues?
“Truth” (orbits, CORS, etc.)
  Rapid (next-day) orbits required for publishing

## Slide 32: A Quick Example
As an example,
2-hours of 2009-059 data from CORV, a PBO CORS in Oregon were submitted to OPUS-S.
32

## Slide 33: A Quick Example
Here is part of the report for this submission.
FYI, these results differ 2.1 cm horizontally and 1.6 cm vertically from the accepted position projected to the epoch of the data.
33
USER: mark.schenewerk@noaa.gov DATE: March 31, 2010 RINEX FILE: corv059f.09o TIME: 19:43:42 UTC SOFTWARE: page5 0909.08 master40.pl 081023 START: 2009/02/28 05:00:00 EPHEMERIS: igs15206.eph [precise] STOP: 2009/02/28 06:59:00 NAV FILE: brdc0590.09n OBS USED: 5984 / 6181 : 97% ANT NAME: ASH700936C_M NONE # FIXED AMB: 31 / 31 : 100% ARP HEIGHT: 1.521 OVERALL RMS: 0.009(m) REF FRAME: NAD_83(CORS96)(EPOCH:2002.0000) ITRF00 (EPOCH:2009.1596) X: -2498422.603(m) 0.011(m) -2498423.344(m) 0.011(m) Y: -3802821.159(m) 0.007(m) -3802819.941(m) 0.007(m) Z: 4454736.661(m) 0.021(m) 4454736.734(m) 0.021(m) LAT: 44 35 7.91060 0.016(m) 44 35 7.92618 0.016(m) E LON: 236 41 43.48046 0.013(m) 236 41 43.42207 0.013(m) W LON: 123 18 16.51954 0.013(m) 123 18 16.57793 0.013(m) EL HGT: 106.011(m) 0.014(m) 105.627(m) 0.014(m) ORTHO HGT: 128.542(m) 0.020(m) [NAVD88 (Computed using GEOID09)] UTM COORDINATES STATE PLANE COORDINATES UTM (Zone 10) SPC (3601 OR N) Northing (Y) [meters] 4936954.909 105971.559 Easting (X) [meters] 475821.304 2277335.367 Convergence [degrees] -0.21381419 -1.98897513 Point Scale 0.99960719 0.99994603 Combined Factor 0.99959057 0.99992941 US NATIONAL GRID DESIGNATOR: 10TDQ7582136954(NAD 83) BASE STATIONS USED PID DESIGNATION LATITUDE LONGITUDE DISTANCE(m) DH4503 P376 EOLARESVR_OR2004 CORS ARP N445628.313 W1230608.100 42648.2 DE6258 MCSO MARION CNTY COOP CORS ARP N445825.701 W1225720.639 51226.8 DG5352 STAY STAYTON COOP CORS ARP N444950.530 W1224915.036 47030.9

## Slide 34: A Quick Example
Again, I’m assuming familiarity with the report, but …
… at the risk of stating the obvious, there are a few items I want to draw attention to.
34
USER: mark.schenewerk@noaa.gov DATE: March 31, 2010 RINEX FILE: corv059f.09o TIME: 19:43:42 UTC SOFTWARE: page5 0909.08 master40.pl 081023 START: 2009/02/28 05:00:00 EPHEMERIS: igs15206.eph [precise] STOP: 2009/02/28 06:59:00 NAV FILE: brdc0590.09n OBS USED: 5984 / 6181 : 97% ANT NAME: ASH700936C_M NONE # FIXED AMB: 31 / 31 : 100% ARP HEIGHT: 1.521 OVERALL RMS: 0.009(m) REF FRAME: NAD_83(CORS96)(EPOCH:2002.0000) ITRF00 (EPOCH:2009.1596) X: -2498422.603(m) 0.011(m) -2498423.344(m) 0.011(m) Y: -3802821.159(m) 0.007(m) -3802819.941(m) 0.007(m) Z: 4454736.661(m) 0.021(m) 4454736.734(m) 0.021(m) LAT: 44 35 7.91060 0.016(m) 44 35 7.92618 0.016(m) E LON: 236 41 43.48046 0.013(m) 236 41 43.42207 0.013(m) W LON: 123 18 16.51954 0.013(m) 123 18 16.57793 0.013(m) EL HGT: 106.011(m) 0.014(m) 105.627(m) 0.014(m) ORTHO HGT: 128.542(m) 0.020(m) [NAVD88 (Computed using GEOID09)] UTM COORDINATES STATE PLANE COORDINATES UTM (Zone 10) SPC (3601 OR N) Northing (Y) [meters] 4936954.909 105971.559 Easting (X) [meters] 475821.304 2277335.367 Convergence [degrees] -0.21381419 -1.98897513 Point Scale 0.99960719 0.99994603 Combined Factor 0.99959057 0.99992941 US NATIONAL GRID DESIGNATOR: 10TDQ7582136954(NAD 83) BASE STATIONS USED PID DESIGNATION LATITUDE LONGITUDE DISTANCE(m) DH4503 P376 EOLARESVR_OR2004 CORS ARP N445628.313 W1230608.100 42648.2 DE6258 MCSO MARION CNTY COOP CORS ARP N445825.701 W1225720.639 51226.8 DG5352 STAY STAYTON COOP CORS ARP N444950.530 W1224915.036 47030.9

## Slide 35: A Quick Example
I apologize for stating the obvious, but …
When reviewing your OPUS solution, double check that the information you provided is correct.
35
USER: mark.schenewerk@noaa.gov DATE: March 31, 2010 RINEX FILE: corv059f.09o TIME: 19:43:42 UTC SOFTWARE: page5 0909.08 master40.pl 081023 START: 2009/02/28 05:00:00 EPHEMERIS: igs15206.eph [precise] STOP: 2009/02/28 06:59:00 NAV FILE: brdc0590.09n OBS USED: 5984 / 6181 : 97% ANT NAME: ASH700936C_M NONE # FIXED AMB: 31 / 31 : 100% ARP HEIGHT: 1.521 OVERALL RMS: 0.009(m) REF FRAME: NAD_83(CORS96)(EPOCH:2002.0000) ITRF00 (EPOCH:2009.1596) X: -2498422.603(m) 0.011(m) -2498423.344(m) 0.011(m) Y: -3802821.159(m) 0.007(m) -3802819.941(m) 0.007(m) Z: 4454736.661(m) 0.021(m) 4454736.734(m) 0.021(m) LAT: 44 35 7.91060 0.016(m) 44 35 7.92618 0.016(m) E LON: 236 41 43.48046 0.013(m) 236 41 43.42207 0.013(m) W LON: 123 18 16.51954 0.013(m) 123 18 16.57793 0.013(m) EL HGT: 106.011(m) 0.014(m) 105.627(m) 0.014(m) ORTHO HGT: 128.542(m) 0.020(m) [NAVD88 (Computed using GEOID09)] UTM COORDINATES STATE PLANE COORDINATES UTM (Zone 10) SPC (3601 OR N) Northing (Y) [meters] 4936954.909 105971.559 Easting (X) [meters] 475821.304 2277335.367 Convergence [degrees] -0.21381419 -1.98897513 Point Scale 0.99960719 0.99994603 Combined Factor 0.99959057 0.99992941 US NATIONAL GRID DESIGNATOR: 10TDQ7582136954(NAD 83) BASE STATIONS USED PID DESIGNATION LATITUDE LONGITUDE DISTANCE(m) DH4503 P376 EOLARESVR_OR2004 CORS ARP N445628.313 W1230608.100 42648.2 DE6258 MCSO MARION CNTY COOP CORS ARP N445825.701 W1225720.639 51226.8 DG5352 STAY STAYTON COOP CORS ARP N444950.530 W1224915.036 47030.9
START: 2009/02/28 05:00:00 STOP: 2009/02/28 06:59:00
RINEX FILE: corv059f.09o
ANT NAME: ASH700936C_M NONE
ARP HEIGHT: 1.521

## Slide 36: A Quick Example
I apologize for stating the obvious, but …
Check the quality control measures provided:
In this example, we have a
36
USER: mark.schenewerk@noaa.gov DATE: March 31, 2010 RINEX FILE: corv059f.09o TIME: 19:43:42 UTC SOFTWARE: page5 0909.08 master40.pl 081023 START: 2009/02/28 05:00:00 EPHEMERIS: igs15206.eph [precise] STOP: 2009/02/28 06:59:00 NAV FILE: brdc0590.09n OBS USED: 5984 / 6181 : 97% ANT NAME: ASH700936C_M NONE # FIXED AMB: 31 / 31 : 100% ARP HEIGHT: 1.521 OVERALL RMS: 0.009(m) REF FRAME: NAD_83(CORS96)(EPOCH:2002.0000) ITRF00 (EPOCH:2009.1596) X: -2498422.603(m) 0.011(m) -2498423.344(m) 0.011(m) Y: -3802821.159(m) 0.007(m) -3802819.941(m) 0.007(m) Z: 4454736.661(m) 0.021(m) 4454736.734(m) 0.021(m) LAT: 44 35 7.91060 0.016(m) 44 35 7.92618 0.016(m) E LON: 236 41 43.48046 0.013(m) 236 41 43.42207 0.013(m) W LON: 123 18 16.51954 0.013(m) 123 18 16.57793 0.013(m) EL HGT: 106.011(m) 0.014(m) 105.627(m) 0.014(m) ORTHO HGT: 128.542(m) 0.020(m) [NAVD88 (Computed using GEOID09)] UTM COORDINATES STATE PLANE COORDINATES UTM (Zone 10) SPC (3601 OR N) Northing (Y) [meters] 4936954.909 105971.559 Easting (X) [meters] 475821.304 2277335.367 Convergence [degrees] -0.21381419 -1.98897513 Point Scale 0.99960719 0.99994603 Combined Factor 0.99959057 0.99992941 US NATIONAL GRID DESIGNATOR: 10TDQ7582136954(NAD 83) BASE STATIONS USED PID DESIGNATION LATITUDE LONGITUDE DISTANCE(m) DH4503 P376 EOLARESVR_OR2004 CORS ARP N445628.313 W1230608.100 42648.2 DE6258 MCSO MARION CNTY COOP CORS ARP N445825.701 W1225720.639 51226.8 DG5352 STAY STAYTON COOP CORS ARP N444950.530 W1224915.036 47030.9
OBS USED: 5984 / 6181 : 97% # FIXED AMB: 31 / 31 : 100% OVERALL RMS: 0.009(m)
0.011(m)
0.007(m)
0.021(m)

## Slide 37: A Quick Example
I apologize for stating the obvious, but …
Check the quality control measures provided:
OBS USED > 90%
# FIXED AMB > 50%
OVERALL RMS < 3 cm
peak-to-peak < 5 cm
In this example, we have a .
37
USER: mark.schenewerk@noaa.gov DATE: March 31, 2010 RINEX FILE: corv059f.09o TIME: 19:43:42 UTC SOFTWARE: page5 0909.08 master40.pl 081023 START: 2009/02/28 05:00:00 EPHEMERIS: igs15206.eph [precise] STOP: 2009/02/28 06:59:00 NAV FILE: brdc0590.09n OBS USED: 5984 / 6181 : 97% ANT NAME: ASH700936C_M NONE # FIXED AMB: 31 / 31 : 100% ARP HEIGHT: 1.521 OVERALL RMS: 0.009(m) REF FRAME: NAD_83(CORS96)(EPOCH:2002.0000) ITRF00 (EPOCH:2009.1596) X: -2498422.603(m) 0.011(m) -2498423.344(m) 0.011(m) Y: -3802821.159(m) 0.007(m) -3802819.941(m) 0.007(m) Z: 4454736.661(m) 0.021(m) 4454736.734(m) 0.021(m) LAT: 44 35 7.91060 0.016(m) 44 35 7.92618 0.016(m) E LON: 236 41 43.48046 0.013(m) 236 41 43.42207 0.013(m) W LON: 123 18 16.51954 0.013(m) 123 18 16.57793 0.013(m) EL HGT: 106.011(m) 0.014(m) 105.627(m) 0.014(m) ORTHO HGT: 128.542(m) 0.020(m) [NAVD88 (Computed using GEOID09)] UTM COORDINATES STATE PLANE COORDINATES UTM (Zone 10) SPC (3601 OR N) Northing (Y) [meters] 4936954.909 105971.559 Easting (X) [meters] 475821.304 2277335.367 Convergence [degrees] -0.21381419 -1.98897513 Point Scale 0.99960719 0.99994603 Combined Factor 0.99959057 0.99992941 US NATIONAL GRID DESIGNATOR: 10TDQ7582136954(NAD 83) BASE STATIONS USED PID DESIGNATION LATITUDE LONGITUDE DISTANCE(m) DH4503 P376 EOLARESVR_OR2004 CORS ARP N445628.313 W1230608.100 42648.2 DE6258 MCSO MARION CNTY COOP CORS ARP N445825.701 W1225720.639 51226.8 DG5352 STAY STAYTON COOP CORS ARP N444950.530 W1224915.036 47030.9
OBS USED: 5984 / 6181 : 97% # FIXED AMB: 31 / 31 : 100% OVERALL RMS: 0.009(m)
0.011(m)
0.007(m)
0.021(m)

## Slide 38
f
CORS solution 1
solution 3
your position: averaged from the 3 CORS solutions
l
h
your peak-to-peaks: scaled from the spread of the 3 CORS solutions
solution 2
=
=
=

## Slide 39: The Extended Report
If the extended report option was selected, next you’ll see the BASE STATION section.
Here, the components contributing to the base stations’ coordinates are shown in detail. These and the following information are expressed in the ITRF currently in use.
39
BASE STATION INFORMATION STATION NAME: p376 a 2 (EOLARESVR_OR2004; Salem, OR United States) MONUMENT: NO DOMES NUMBER XYZ -2469806.7634 -3788348.6049 4482853.4377 MON @ 1997.0000 (M) XYZ -0.0141 0.0030 -0.0043 VEL (M/YR) NEU -0.0000 0.0000 0.0083 MON TO ARP (M) NEU 0.0009 0.0009 0.1068 ARP TO L1 PHASE CENTER (M) NEU 0.0002 0.0017 0.1251 ARP TO L2 PHASE CENTER (M) XYZ -0.1715 0.0365 -0.0523 VEL TIMES 12.1597 YRS XYZ -0.0032 -0.0049 0.0059 MON TO ARP XYZ -0.0402 -0.0633 0.0761 ARP TO L1 PHASE CENTER XYZ -2469806.9782 -3788348.6366 4482853.4674 L1 PHS CEN @ 2009.1596 XYZ 0.0000 0.0000 0.0000 + XYZ ADJUSTMENTS XYZ -2469806.9782 -3788348.6366 4482853.4674 NEW L1 PHS CEN @ 2009.1596 XYZ -2469806.9381 -3788348.5733 4482853.3913 NEW ARP @ 2009.1596 XYZ -2469806.9348 -3788348.5684 4482853.3855 NEW MON @ 2009.1596 LLH 44 56 28.32921 236 53 51.83975 180.9607 NEW L1 PHS CEN @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8539 NEW ARP @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8456 NEW MON @ 2009.1596 STATION NAME: mcso a 1 (MARION CNTY COOP; Salem, Oregon, U.S.A.) MONUMENT: NO DOMES NUMBER XYZ -2458668.9460 -3792427.4770 4485327.2930 MON @ 1997.0000 (M) XYZ -0.0131 0.0018 -0.0047 VEL (M/YR) NEU 0.0000 0.0000 0.0000 MON TO ARP (M) NEU 0.0025 0.0013 0.1065 ARP TO L1 PHASE CENTER (M) NEU -0.0007 0.0013 0.1254 ARP TO L2 PHASE CENTER (M) XYZ -0.1593 0.0219 -0.0572 VEL TIMES 12.1597 YRS XYZ 0.0000 0.0000 0.0000 MON TO ARP XYZ -0.0389 -0.0624 0.0770 ARP TO L1 PHASE CENTER XYZ -2458669.1442 -3792427.5176 4485327.3129 L1 PHS CEN @ 2009.1596 XYZ -0.0000 -0.0000 -0.0000 + XYZ ADJUSTMENTS XYZ -2458669.1442 -3792427.5176 4485327.3129 NEW L1 PHS CEN @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW ARP @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW MON @ 2009.1596 LLH 44 58 25.71729 237 2 39.30118 52.9227 NEW L1 PHS CEN @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW ARP @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW MON @ 2009.1596

## Slide 40: The Extended Report
This section includes a priori information.
40
BASE STATION INFORMATION STATION NAME: p376 a 2 (EOLARESVR_OR2004; Salem, OR United States) MONUMENT: NO DOMES NUMBER XYZ -2469806.7634 -3788348.6049 4482853.4377 MON @ 1997.0000 (M) XYZ -0.0141 0.0030 -0.0043 VEL (M/YR) NEU -0.0000 0.0000 0.0083 MON TO ARP (M) NEU 0.0009 0.0009 0.1068 ARP TO L1 PHASE CENTER (M) NEU 0.0002 0.0017 0.1251 ARP TO L2 PHASE CENTER (M) XYZ -0.1715 0.0365 -0.0523 VEL TIMES 12.1597 YRS XYZ -0.0032 -0.0049 0.0059 MON TO ARP XYZ -0.0402 -0.0633 0.0761 ARP TO L1 PHASE CENTER XYZ -2469806.9782 -3788348.6366 4482853.4674 L1 PHS CEN @ 2009.1596 XYZ 0.0000 0.0000 0.0000 + XYZ ADJUSTMENTS XYZ -2469806.9782 -3788348.6366 4482853.4674 NEW L1 PHS CEN @ 2009.1596 XYZ -2469806.9381 -3788348.5733 4482853.3913 NEW ARP @ 2009.1596 XYZ -2469806.9348 -3788348.5684 4482853.3855 NEW MON @ 2009.1596 LLH 44 56 28.32921 236 53 51.83975 180.9607 NEW L1 PHS CEN @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8539 NEW ARP @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8456 NEW MON @ 2009.1596 STATION NAME: mcso a 1 (MARION CNTY COOP; Salem, Oregon, U.S.A.) MONUMENT: NO DOMES NUMBER XYZ -2458668.9460 -3792427.4770 4485327.2930 MON @ 1997.0000 (M) XYZ -0.0131 0.0018 -0.0047 VEL (M/YR) NEU 0.0000 0.0000 0.0000 MON TO ARP (M) NEU 0.0025 0.0013 0.1065 ARP TO L1 PHASE CENTER (M) NEU -0.0007 0.0013 0.1254 ARP TO L2 PHASE CENTER (M) XYZ -0.1593 0.0219 -0.0572 VEL TIMES 12.1597 YRS XYZ 0.0000 0.0000 0.0000 MON TO ARP XYZ -0.0389 -0.0624 0.0770 ARP TO L1 PHASE CENTER XYZ -2458669.1442 -3792427.5176 4485327.3129 L1 PHS CEN @ 2009.1596 XYZ -0.0000 -0.0000 -0.0000 + XYZ ADJUSTMENTS XYZ -2458669.1442 -3792427.5176 4485327.3129 NEW L1 PHS CEN @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW ARP @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW MON @ 2009.1596 LLH 44 58 25.71729 237 2 39.30118 52.9227 NEW L1 PHS CEN @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW ARP @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW MON @ 2009.1596
STATION NAME: p376 a 2 (EOLARESVR_OR2004; Salem, OR United States) MONUMENT: NO DOMES NUMBER XYZ -2469806.7634 -3788348.6049 4482853.4377 MON @ 1997.0000 (M) XYZ -0.0141 0.0030 -0.0043 VEL (M/YR) NEU -0.0000 0.0000 0.0083 MON TO ARP (M) NEU 0.0009 0.0009 0.1068 ARP TO L1 PHASE CENTER (M) NEU 0.0002 0.0017 0.1251 ARP TO L2 PHASE CENTER (M)

## Slide 41: The Extended Report
Computation of the coordinates at the mean epoch of the data.
41
BASE STATION INFORMATION STATION NAME: p376 a 2 (EOLARESVR_OR2004; Salem, OR United States) MONUMENT: NO DOMES NUMBER XYZ -2469806.7634 -3788348.6049 4482853.4377 MON @ 1997.0000 (M) XYZ -0.0141 0.0030 -0.0043 VEL (M/YR) NEU -0.0000 0.0000 0.0083 MON TO ARP (M) NEU 0.0009 0.0009 0.1068 ARP TO L1 PHASE CENTER (M) NEU 0.0002 0.0017 0.1251 ARP TO L2 PHASE CENTER (M) XYZ -0.1715 0.0365 -0.0523 VEL TIMES 12.1597 YRS XYZ -0.0032 -0.0049 0.0059 MON TO ARP XYZ -0.0402 -0.0633 0.0761 ARP TO L1 PHASE CENTER XYZ -2469806.9782 -3788348.6366 4482853.4674 L1 PHS CEN @ 2009.1596 XYZ 0.0000 0.0000 0.0000 + XYZ ADJUSTMENTS XYZ -2469806.9782 -3788348.6366 4482853.4674 NEW L1 PHS CEN @ 2009.1596 XYZ -2469806.9381 -3788348.5733 4482853.3913 NEW ARP @ 2009.1596 XYZ -2469806.9348 -3788348.5684 4482853.3855 NEW MON @ 2009.1596 LLH 44 56 28.32921 236 53 51.83975 180.9607 NEW L1 PHS CEN @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8539 NEW ARP @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8456 NEW MON @ 2009.1596 STATION NAME: mcso a 1 (MARION CNTY COOP; Salem, Oregon, U.S.A.) MONUMENT: NO DOMES NUMBER XYZ -2458668.9460 -3792427.4770 4485327.2930 MON @ 1997.0000 (M) XYZ -0.0131 0.0018 -0.0047 VEL (M/YR) NEU 0.0000 0.0000 0.0000 MON TO ARP (M) NEU 0.0025 0.0013 0.1065 ARP TO L1 PHASE CENTER (M) NEU -0.0007 0.0013 0.1254 ARP TO L2 PHASE CENTER (M) XYZ -0.1593 0.0219 -0.0572 VEL TIMES 12.1597 YRS XYZ 0.0000 0.0000 0.0000 MON TO ARP XYZ -0.0389 -0.0624 0.0770 ARP TO L1 PHASE CENTER XYZ -2458669.1442 -3792427.5176 4485327.3129 L1 PHS CEN @ 2009.1596 XYZ -0.0000 -0.0000 -0.0000 + XYZ ADJUSTMENTS XYZ -2458669.1442 -3792427.5176 4485327.3129 NEW L1 PHS CEN @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW ARP @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW MON @ 2009.1596 LLH 44 58 25.71729 237 2 39.30118 52.9227 NEW L1 PHS CEN @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW ARP @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW MON @ 2009.1596
XYZ -0.1715 0.0365 -0.0523 VEL TIMES 12.1597 YRS XYZ -0.0032 -0.0049 0.0059 MON TO ARP XYZ -0.0402 -0.0633 0.0761 ARP TO L1 PHASE CENTER XYZ -2469806.9782 -3788348.6366 4482853.4674 L1 PHS CEN @ 2009.1596

## Slide 42: The Extended Report
And the coordinates at the mean epoch of the data.
42
BASE STATION INFORMATION STATION NAME: p376 a 2 (EOLARESVR_OR2004; Salem, OR United States) MONUMENT: NO DOMES NUMBER XYZ -2469806.7634 -3788348.6049 4482853.4377 MON @ 1997.0000 (M) XYZ -0.0141 0.0030 -0.0043 VEL (M/YR) NEU -0.0000 0.0000 0.0083 MON TO ARP (M) NEU 0.0009 0.0009 0.1068 ARP TO L1 PHASE CENTER (M) NEU 0.0002 0.0017 0.1251 ARP TO L2 PHASE CENTER (M) XYZ -0.1715 0.0365 -0.0523 VEL TIMES 12.1597 YRS XYZ -0.0032 -0.0049 0.0059 MON TO ARP XYZ -0.0402 -0.0633 0.0761 ARP TO L1 PHASE CENTER XYZ -2469806.9782 -3788348.6366 4482853.4674 L1 PHS CEN @ 2009.1596 XYZ 0.0000 0.0000 0.0000 + XYZ ADJUSTMENTS XYZ -2469806.9782 -3788348.6366 4482853.4674 NEW L1 PHS CEN @ 2009.1596 XYZ -2469806.9381 -3788348.5733 4482853.3913 NEW ARP @ 2009.1596 XYZ -2469806.9348 -3788348.5684 4482853.3855 NEW MON @ 2009.1596 LLH 44 56 28.32921 236 53 51.83975 180.9607 NEW L1 PHS CEN @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8539 NEW ARP @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8456 NEW MON @ 2009.1596 STATION NAME: mcso a 1 (MARION CNTY COOP; Salem, Oregon, U.S.A.) MONUMENT: NO DOMES NUMBER XYZ -2458668.9460 -3792427.4770 4485327.2930 MON @ 1997.0000 (M) XYZ -0.0131 0.0018 -0.0047 VEL (M/YR) NEU 0.0000 0.0000 0.0000 MON TO ARP (M) NEU 0.0025 0.0013 0.1065 ARP TO L1 PHASE CENTER (M) NEU -0.0007 0.0013 0.1254 ARP TO L2 PHASE CENTER (M) XYZ -0.1593 0.0219 -0.0572 VEL TIMES 12.1597 YRS XYZ 0.0000 0.0000 0.0000 MON TO ARP XYZ -0.0389 -0.0624 0.0770 ARP TO L1 PHASE CENTER XYZ -2458669.1442 -3792427.5176 4485327.3129 L1 PHS CEN @ 2009.1596 XYZ -0.0000 -0.0000 -0.0000 + XYZ ADJUSTMENTS XYZ -2458669.1442 -3792427.5176 4485327.3129 NEW L1 PHS CEN @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW ARP @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW MON @ 2009.1596 LLH 44 58 25.71729 237 2 39.30118 52.9227 NEW L1 PHS CEN @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW ARP @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW MON @ 2009.1596
XYZ -2469806.9782 -3788348.6366 4482853.4674 NEW L1 PHS CEN @ 2009.1596 XYZ -2469806.9381 -3788348.5733 4482853.3913 NEW ARP @ 2009.1596 XYZ -2469806.9348 -3788348.5684 4482853.3855 NEW MON @ 2009.1596 LLH 44 56 28.32921 236 53 51.83975 180.9607 NEW L1 PHS CEN @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8539 NEW ARP @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8456 NEW MON @ 2009.1596

## Slide 43: The Extended Report
So, if you add the a priori coordinates + ARP TO L1, + MON TO ARP + VEL offsets,
you will get the coordinates at the mean epoch of the data, shown here highlighted in yellow, used in the processing.
43
BASE STATION INFORMATION STATION NAME: p376 a 2 (EOLARESVR_OR2004; Salem, OR United States) MONUMENT: NO DOMES NUMBER XYZ -2469806.7634 -3788348.6049 4482853.4377 MON @ 1997.0000 (M) XYZ -0.0141 0.0030 -0.0043 VEL (M/YR) NEU -0.0000 0.0000 0.0083 MON TO ARP (M) NEU 0.0009 0.0009 0.1068 ARP TO L1 PHASE CENTER (M) NEU 0.0002 0.0017 0.1251 ARP TO L2 PHASE CENTER (M) XYZ -0.1715 0.0365 -0.0523 VEL TIMES 12.1597 YRS XYZ -0.0032 -0.0049 0.0059 MON TO ARP XYZ -0.0402 -0.0633 0.0761 ARP TO L1 PHASE CENTER XYZ -2469806.9782 -3788348.6366 4482853.4674 L1 PHS CEN @ 2009.1596 XYZ 0.0000 0.0000 0.0000 + XYZ ADJUSTMENTS XYZ -2469806.9782 -3788348.6366 4482853.4674 NEW L1 PHS CEN @ 2009.1596 XYZ -2469806.9381 -3788348.5733 4482853.3913 NEW ARP @ 2009.1596 XYZ -2469806.9348 -3788348.5684 4482853.3855 NEW MON @ 2009.1596 LLH 44 56 28.32921 236 53 51.83975 180.9607 NEW L1 PHS CEN @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8539 NEW ARP @ 2009.1596 LLH 44 56 28.32918 236 53 51.83971 180.8456 NEW MON @ 2009.1596 STATION NAME: mcso a 1 (MARION CNTY COOP; Salem, Oregon, U.S.A.) MONUMENT: NO DOMES NUMBER XYZ -2458668.9460 -3792427.4770 4485327.2930 MON @ 1997.0000 (M) XYZ -0.0131 0.0018 -0.0047 VEL (M/YR) NEU 0.0000 0.0000 0.0000 MON TO ARP (M) NEU 0.0025 0.0013 0.1065 ARP TO L1 PHASE CENTER (M) NEU -0.0007 0.0013 0.1254 ARP TO L2 PHASE CENTER (M) XYZ -0.1593 0.0219 -0.0572 VEL TIMES 12.1597 YRS XYZ 0.0000 0.0000 0.0000 MON TO ARP XYZ -0.0389 -0.0624 0.0770 ARP TO L1 PHASE CENTER XYZ -2458669.1442 -3792427.5176 4485327.3129 L1 PHS CEN @ 2009.1596 XYZ -0.0000 -0.0000 -0.0000 + XYZ ADJUSTMENTS XYZ -2458669.1442 -3792427.5176 4485327.3129 NEW L1 PHS CEN @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW ARP @ 2009.1596 XYZ -2458669.1053 -3792427.4551 4485327.2358 NEW MON @ 2009.1596 LLH 44 58 25.71729 237 2 39.30118 52.9227 NEW L1 PHS CEN @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW ARP @ 2009.1596 LLH 44 58 25.71721 237 2 39.30112 52.8162 NEW MON @ 2009.1596
XYZ -2469806.7634 -3788348.6049 4482853.4377 MON @ 1997.0000 (M)
XYZ -2469806.9782 -3788348.6366 4482853.4674 L1 PHS CEN @ 2009.1596
XYZ -0.1715 0.0365 -0.0523 VEL TIMES 12.1597 YRS
XYZ -0.0032 -0.0049 0.0059 MON TO ARP
XYZ -0.0402 -0.0633 0.0761 ARP TO L1 PHASE CENTER

## Slide 44: The Extended Report
Next are summaries of the solutions relative to each base station.
We’ll discuss this a few minutes, but, for now, simply be aware that OPUS “solves” each baseline separately, then compares and averages these results to create the report.
44
REMOTE STATION INFORMATION STATION NAME: corv 1 MONUMENT: NO DOMES NUMBER XYZ -2498423.7849 -3802820.9571 4454737.7025 MON @ 2009.1595 (M) NEU -0.0014 0.0010 1.5210 MON TO ARP (M) NEU 0.0014 -0.0010 0.1089 ARP TO L1 PHASE CENTER (M) NEU 0.0010 0.0005 0.1274 ARP TO L2 PHASE CENTER (M) XYZ -0.5945 -0.9067 1.0667 MON TO ARP XYZ -0.0429 -0.0635 0.0774 ARP TO L1 PHASE CENTER XYZ -2498424.4223 -3802821.9273 4454738.8466 L1 PHS CEN @ 2009.1596 BASELINE NAME: p376 corv XYZ 0.4450 1.0132 -0.9754 + XYZ ADJUSTMENTS XYZ -2498423.9773 -3802820.9141 4454737.8713 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9344 -3802820.8506 4454737.7938 NEW ARP @ 2009.1596 XYZ -2498423.3399 -3802819.9439 4454736.7271 NEW MON @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 107.2518 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92597 236 41 43.42234 107.1429 NEW ARP @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 105.6219 NEW MON @ 2009.1596 BASELINE NAME: mcso corv XYZ 0.4343 1.0202 -0.9746 + XYZ ADJUSTMENTS XYZ -2498423.9880 -3802820.9071 4454737.8721 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9451 -3802820.8436 4454737.7946 NEW ARP @ 2009.1596 XYZ -2498423.3506 -3802819.9369 4454736.7279 NEW MON @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 107.2523 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92599 236 41 43.42176 107.1434 NEW ARP @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 105.6224 NEW MON @ 2009.1596 BASELINE NAME: stay corv XYZ 0.4437 1.0153 -0.9543 + XYZ ADJUSTMENTS XYZ -2498423.9786 -3802820.9120 4454737.8923 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9357 -3802820.8485 4454737.8149 NEW ARP @ 2009.1596 XYZ -2498423.3412 -3802819.9418 4454736.7482 NEW MON @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 107.2658 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92648 236 41 43.42224 107.1569 NEW ARP @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 105.6359 NEW MON @ 2009.1596

## Slide 45: The Extended Report
Here we see the best guess for “my” site’s a priori information. This is based upon the information I provided when I uploaded the data file to OPUS-S and a crude point position solution. Remember that these are also in the ITRF.
45
REMOTE STATION INFORMATION STATION NAME: corv 1 MONUMENT: NO DOMES NUMBER XYZ -2498423.7849 -3802820.9571 4454737.7025 MON @ 2009.1595 (M) NEU -0.0014 0.0010 1.5210 MON TO ARP (M) NEU 0.0014 -0.0010 0.1089 ARP TO L1 PHASE CENTER (M) NEU 0.0010 0.0005 0.1274 ARP TO L2 PHASE CENTER (M) XYZ -0.5945 -0.9067 1.0667 MON TO ARP XYZ -0.0429 -0.0635 0.0774 ARP TO L1 PHASE CENTER XYZ -2498424.4223 -3802821.9273 4454738.8466 L1 PHS CEN @ 2009.1596 BASELINE NAME: p376 corv XYZ 0.4450 1.0132 -0.9754 + XYZ ADJUSTMENTS XYZ -2498423.9773 -3802820.9141 4454737.8713 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9344 -3802820.8506 4454737.7938 NEW ARP @ 2009.1596 XYZ -2498423.3399 -3802819.9439 4454736.7271 NEW MON @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 107.2518 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92597 236 41 43.42234 107.1429 NEW ARP @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 105.6219 NEW MON @ 2009.1596 BASELINE NAME: mcso corv XYZ 0.4343 1.0202 -0.9746 + XYZ ADJUSTMENTS XYZ -2498423.9880 -3802820.9071 4454737.8721 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9451 -3802820.8436 4454737.7946 NEW ARP @ 2009.1596 XYZ -2498423.3506 -3802819.9369 4454736.7279 NEW MON @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 107.2523 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92599 236 41 43.42176 107.1434 NEW ARP @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 105.6224 NEW MON @ 2009.1596 BASELINE NAME: stay corv XYZ 0.4437 1.0153 -0.9543 + XYZ ADJUSTMENTS XYZ -2498423.9786 -3802820.9120 4454737.8923 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9357 -3802820.8485 4454737.8149 NEW ARP @ 2009.1596 XYZ -2498423.3412 -3802819.9418 4454736.7482 NEW MON @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 107.2658 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92648 236 41 43.42224 107.1569 NEW ARP @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 105.6359 NEW MON @ 2009.1596
STATION NAME: corv 1 MONUMENT: NO DOMES NUMBER XYZ -2498423.7849 -3802820.9571 4454737.7025 MON @ 2009.1595 (M) NEU -0.0014 0.0010 1.5210 MON TO ARP (M) NEU 0.0014 -0.0010 0.1089 ARP TO L1 PHASE CENTER (M) NEU 0.0010 0.0005 0.1274 ARP TO L2 PHASE CENTER (M) XYZ -0.5945 -0.9067 1.0667 MON TO ARP XYZ -0.0429 -0.0635 0.0774 ARP TO L1 PHASE CENTER XYZ -2498424.4223 -3802821.9273 4454738.8466 L1 PHS CEN @ 2009.1596

## Slide 46: The Extended Report
In the associated “blocks”, the estimated adjustment and resulting coordinates from each baseline solution are shown.
46
REMOTE STATION INFORMATION STATION NAME: corv 1 MONUMENT: NO DOMES NUMBER XYZ -2498423.7849 -3802820.9571 4454737.7025 MON @ 2009.1595 (M) NEU -0.0014 0.0010 1.5210 MON TO ARP (M) NEU 0.0014 -0.0010 0.1089 ARP TO L1 PHASE CENTER (M) NEU 0.0010 0.0005 0.1274 ARP TO L2 PHASE CENTER (M) XYZ -0.5945 -0.9067 1.0667 MON TO ARP XYZ -0.0429 -0.0635 0.0774 ARP TO L1 PHASE CENTER XYZ -2498424.4223 -3802821.9273 4454738.8466 L1 PHS CEN @ 2009.1596 BASELINE NAME: p376 corv XYZ 0.4450 1.0132 -0.9754 + XYZ ADJUSTMENTS XYZ -2498423.9773 -3802820.9141 4454737.8713 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9344 -3802820.8506 4454737.7938 NEW ARP @ 2009.1596 XYZ -2498423.3399 -3802819.9439 4454736.7271 NEW MON @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 107.2518 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92597 236 41 43.42234 107.1429 NEW ARP @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 105.6219 NEW MON @ 2009.1596 BASELINE NAME: mcso corv XYZ 0.4343 1.0202 -0.9746 + XYZ ADJUSTMENTS XYZ -2498423.9880 -3802820.9071 4454737.8721 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9451 -3802820.8436 4454737.7946 NEW ARP @ 2009.1596 XYZ -2498423.3506 -3802819.9369 4454736.7279 NEW MON @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 107.2523 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92599 236 41 43.42176 107.1434 NEW ARP @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 105.6224 NEW MON @ 2009.1596 BASELINE NAME: stay corv XYZ 0.4437 1.0153 -0.9543 + XYZ ADJUSTMENTS XYZ -2498423.9786 -3802820.9120 4454737.8923 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9357 -3802820.8485 4454737.8149 NEW ARP @ 2009.1596 XYZ -2498423.3412 -3802819.9418 4454736.7482 NEW MON @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 107.2658 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92648 236 41 43.42224 107.1569 NEW ARP @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 105.6359 NEW MON @ 2009.1596
BASELINE NAME: p376 corv XYZ 0.4450 1.0132 -0.9754 + XYZ ADJUSTMENTS XYZ -2498423.9773 -3802820.9141 4454737.8713 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9344 -3802820.8506 4454737.7938 NEW ARP @ 2009.1596 XYZ -2498423.3399 -3802819.9439 4454736.7271 NEW MON @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 107.2518 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92597 236 41 43.42234 107.1429 NEW ARP @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 105.6219 NEW MON @ 2009.1596

## Slide 47: The Extended Report
Near the top, in light blue, you can see the pieces need to compute the estimated (NEW) L1 phase center.
Below, in light green, are the three estimates from the each baseline.
47
REMOTE STATION INFORMATION STATION NAME: corv 1 MONUMENT: NO DOMES NUMBER XYZ -2498423.7849 -3802820.9571 4454737.7025 MON @ 2009.1595 (M) NEU -0.0014 0.0010 1.5210 MON TO ARP (M) NEU 0.0014 -0.0010 0.1089 ARP TO L1 PHASE CENTER (M) NEU 0.0010 0.0005 0.1274 ARP TO L2 PHASE CENTER (M) XYZ -0.5945 -0.9067 1.0667 MON TO ARP XYZ -0.0429 -0.0635 0.0774 ARP TO L1 PHASE CENTER XYZ -2498424.4223 -3802821.9273 4454738.8466 L1 PHS CEN @ 2009.1596 BASELINE NAME: p376 corv XYZ 0.4450 1.0132 -0.9754 + XYZ ADJUSTMENTS XYZ -2498423.9773 -3802820.9141 4454737.8713 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9344 -3802820.8506 4454737.7938 NEW ARP @ 2009.1596 XYZ -2498423.3399 -3802819.9439 4454736.7271 NEW MON @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 107.2518 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92597 236 41 43.42234 107.1429 NEW ARP @ 2009.1596 LLH 44 35 7.92601 236 41 43.42229 105.6219 NEW MON @ 2009.1596 BASELINE NAME: mcso corv XYZ 0.4343 1.0202 -0.9746 + XYZ ADJUSTMENTS XYZ -2498423.9880 -3802820.9071 4454737.8721 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9451 -3802820.8436 4454737.7946 NEW ARP @ 2009.1596 XYZ -2498423.3506 -3802819.9369 4454736.7279 NEW MON @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 107.2523 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92599 236 41 43.42176 107.1434 NEW ARP @ 2009.1596 LLH 44 35 7.92603 236 41 43.42171 105.6224 NEW MON @ 2009.1596 BASELINE NAME: stay corv XYZ 0.4437 1.0153 -0.9543 + XYZ ADJUSTMENTS XYZ -2498423.9786 -3802820.9120 4454737.8923 NEW L1 PHS CEN @ 2009.1596 XYZ -2498423.9357 -3802820.8485 4454737.8149 NEW ARP @ 2009.1596 XYZ -2498423.3412 -3802819.9418 4454736.7482 NEW MON @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 107.2658 NEW L1 PHS CEN @ 2009.1596 LLH 44 35 7.92648 236 41 43.42224 107.1569 NEW ARP @ 2009.1596 LLH 44 35 7.92653 236 41 43.42219 105.6359 NEW MON @ 2009.1596
XYZ -2498423.9773 -3802820.9141 4454737.8713 NEW L1 PHS CEN @ 2009.1596
XYZ 0.4450 1.0132 -0.9754 + XYZ ADJUSTMENTS
XYZ -2498424.4223 -3802821.9273 4454738.8466 L1 PHS CEN @ 2009.1596
XYZ -2498423.3399 -3802819.9439 4454736.7271 NEW MON @ 2009.1596
XYZ -2498423.3506 -3802819.9369 4454736.7279 NEW MON @ 2009.1596
XYZ -2498423.3412 -3802819.9418 4454736.7482 NEW MON @ 2009.1596

## Slide 48: The Extended Report
Following the baseline information are some Bluebook records…
48
G-FILES Axx2009 228 9 228 B2009 228 5 0 9 228 659 1 page5 v0909.08IGS 226 1 2 27NGS 2010 7 9IFDDFX Iant_info.003 NGS 20100616 C00090001 286164051 30 144713755 32 281166583 28 X0599ACORVX0599AP376 D 1 2 9032521 1 3 -2281991 2 3 -5618980 Axx2009 228 9 228 B2009 228 5 0 9 228 659 1 page5 v0909.08IGS 226 1 2 27NGS 2010 7 9IFDDFX Iant_info.003 NGS 20100616 C00090002 397542453 32 103924818 30 305905079 27 X0599ACORVX0599AMCSO D 1 2 8318045 1 3 -1709106 2 3 -6334467 Axx2009 228 9 228 B2009 228 5 0 9 228 659 1 page5 v0909.08IGS 226 1 2 27NGS 2010 7 9IFDDFX Iant_info.003 NGS 20100616 C00090003 425824609 35 -48539879 22 193670380 18 X0599ACORVX0599ASTAY D 1 2 6847311 1 3 -1553171 2 3 -7047523

## Slide 49: The Extended Report
Following the Bluebook information are solution statistics and observation counts in tabular form ordered by satellite (rows) and baseline (columns)…
49
POST-FIT RMS BY SATELLITE VS. BASELINE
OVERALL 03 06 07 08 10 13 16 19
p376-corv| 0.009 0.010 0.016 ... 0.007 0.014 0.005 0.015 0.009
20 23 25 27 28
p376-corv| ... 0.008 0.005 ... 0.010
OVERALL 03 06 07 08 10 13 16 19
mcso-corv| 0.009 0.010 0.014 ... 0.010 0.011 0.006 0.015 0.012
20 23 25 27 28
mcso-corv| ... 0.008 0.005 ... 0.010
OVERALL 03 06 07 08 10 13 16 19
stay-corv| 0.010 0.014 0.016 ... 0.009 0.014 0.006 0.013 0.012
20 23 25 27 28
stay-corv| ... 0.011 0.005 ... 0.012
OBS BY SATELLITE VS. BASELINE
OVERALL 03 06 07 08 10 13 16 19
p376-corv| 2000 238 237 ... 238 169 238 99 187
20 23 25 27 28
p376-corv| ... 227 238 ... 129
OVERALL 03 06 07 08 10 13 16 19
mcso-corv| 1973 238 234 ... 238 169 238 93 185
20 23 25 27 28
mcso-corv| ... 211 238 ... 129
OVERALL 03 06 07 08 10 13 16 19
stay-corv| 2011 238 238 ... 238 169 238 99 199
20 23 25 27 28
stay-corv| ... 229 238 ... 125

## Slide 50: The Extended Report
These tables can be a challenge to read, especially for longer data spans, because the lines wrap in the standard 80-column format. Here’s the same table without line-wrapping and with the extra header lines removed.
50
POST-FIT RMS BY SATELLITE VS. BASELINE
OVERALL 03 06 07 08 10 13 16 19 20 23 25 27 28
p376-corv| 0.009 0.010 0.016 ... 0.007 0.014 0.005 0.015 0.009 ... 0.008 0.005 ... 0.010
mcso-corv| 0.009 0.010 0.014 ... 0.010 0.011 0.006 0.015 0.012 ... 0.008 0.005 ... 0.010
stay-corv| 0.010 0.014 0.016 ... 0.009 0.014 0.006 0.013 0.01 ... 0.011 0.005 ... 0.012
OBS BY SATELLITE VS. BASELINE
OVERALL 03 06 07 08 10 13 16 19 20 23 25 27 28
p376-corv| 2000 238 237 ... 238 169 238 99 187 ... 227 238 ... 129
mcso-corv| 1973 238 234 ... 238 169 238 93 185 ... 211 238 ... 129
stay-corv| 2011 238 238 ... 238 169 238 99 199 ... 229 238 ... 125

## Slide 51: The Extended Report
Next are covariance matrices for the XYZ and NEU vectors, and the network horizontal
and vertical accuracy…
The network horizontal and vertical accuracies are a relatively new addition and will become the standard in the future.
Because of the way OPUS-S works (now), these values are derived from empirically determined relationships in the CORS network plus statistics from the individual baseline solutions.
51
Covariance Matrix for the xyz OPUS Position (meters^2).
0.0000069978 0.0000004873 -0.0000000972
0.0000004873 0.0000053511 -0.0000002879
-0.0000000972 -0.0000002879 0.0000040822
Covariance Matrix for the enu OPUS Position (meters^2).
0.0000060540 0.0000007189 -0.0000006244
0.0000007189 0.0000048712 -0.0000010998
-0.0000006244 -0.0000010998 0.0000055059
Horizontal network accuracy = 0.00573 meters.
Vertical network accuracy = 0.00460 meters.

## Slide 52: The Extended Report.
Additional information
related to the derivation
of NAD_83(CORS96)
vector components…
You’ll see four “blocks”:
the reference sites’ ARP
and MON coordinates,
their velocities and the
solution vector
components all expressed in the NAD 83(CORS96) frame.
52
Derivation of NAD 83 vector components
Position of reference station ARP in NAD_83(CORS96)(EPOCH:2002.0000).
Xa(m) Ya(m) Za(m)
P376 -2469806.16816 -3788349.79220 4482853.31622 2002.00
MCSO -2458668.34414 -3792428.66602 4485327.16392 2002.00
STAY -2455840.11392 -3807675.15002 4474103.71103 2002.00
Position of reference station monument in NAD_83(CORS96)(EPOCH:2002.0000).
Xr(m) Yr(m) Zr(m)
P376 -2469806.16496 -3788349.78730 4482853.31032 2002.00
MCSO -2458668.34414 -3792428.66602 4485327.16392 2002.00
STAY -2455840.11392 -3807675.15002 4474103.71103 2002.00
Velocity of reference station monument in NAD_83(CORS96)(EPOCH:2002.0000).
Vx (m/yr) Vy (m/yr) Vz (m/yr)
P376 0.00440 0.00380 0.00560
MCSO 0.00550 0.00260 0.00520
STAY 0.00460 0.00290 0.00490
Vectors from unknown station monument to reference station monument
in NAD_83(CORS96)(EPOCH:2002.0000).
Xr-X= DX(m) Yr-Y= DY(m) Zr-Z= DZ(m)
P376 28616.43804 14471.37170 28116.64932 2002.00
MCSO 39754.25886 10392.49298 30590.50292 2002.00
STAY 42582.48908 -4853.99102 19367.05003 2002.00

## Slide 53: The Extended Report
The state plane coordinates expressed using the international foot rather than meters …
53
STATE PLANE COORDINATES - International Foot
SPC (3601 OR N)
Northing (Y) [feet] 347675.719
Easting (X) [feet] 7471572.725
Convergence [degrees] -1.98897513
Point Scale 0.99994603
Combined Factor 0.99992941

## Slide 54: Back To Our Quick Example
If you’re uncomfortable with your results (we’re not, but speaking hypothetically), check your data first.
Your hardware manufacturer may provide QC software.
  Use third-party software such as TEQC. Estes and Meertens, “TEQC: The Multi-Purpose Toolkit for GPS/GLONASS Data”, 1999, GPS Solutions, 3, 1, 42-49.
Resubmit requesting the extended report.
If you’re still uncomfortable, consider checking the CORS used in the OPUS processing. The performance of the CORS is reflected in your results.
54

## Slide 55: Back To Our Quick Example
The CORS selected as reference sites are listed towards the bottom of the standard report.
OPUS examined the available sites and selected P376, MCSO and STAY.
55
USER: mark.schenewerk@noaa.gov DATE: March 31, 2010 RINEX FILE: corv059f.09o TIME: 19:43:42 UTC SOFTWARE: page5 0909.08 master40.pl 081023 START: 2009/02/28 05:00:00 EPHEMERIS: igs15206.eph [precise] STOP: 2009/02/28 06:59:00 NAV FILE: brdc0590.09n OBS USED: 5984 / 6181 : 97% ANT NAME: ASH700936C_M NONE # FIXED AMB: 31 / 31 : 100% ARP HEIGHT: 1.521 OVERALL RMS: 0.009(m) REF FRAME: NAD_83(CORS96)(EPOCH:2002.0000) ITRF00 (EPOCH:2009.1596) X: -2498422.603(m) 0.011(m) -2498423.344(m) 0.011(m) Y: -3802821.159(m) 0.007(m) -3802819.941(m) 0.007(m) Z: 4454736.661(m) 0.021(m) 4454736.734(m) 0.021(m) LAT: 44 35 7.91060 0.016(m) 44 35 7.92618 0.016(m) E LON: 236 41 43.48046 0.013(m) 236 41 43.42207 0.013(m) W LON: 123 18 16.51954 0.013(m) 123 18 16.57793 0.013(m) EL HGT: 106.011(m) 0.014(m) 105.627(m) 0.014(m) ORTHO HGT: 128.542(m) 0.020(m) [NAVD88 (Computed using GEOID09)] UTM COORDINATES STATE PLANE COORDINATES UTM (Zone 10) SPC (3601 OR N) Northing (Y) [meters] 4936954.909 105971.559 Easting (X) [meters] 475821.304 2277335.367 Convergence [degrees] -0.21381419 -1.98897513 Point Scale 0.99960719 0.99994603 Combined Factor 0.99959057 0.99992941 US NATIONAL GRID DESIGNATOR: 10TDQ7582136954(NAD 83) BASE STATIONS USED PID DESIGNATION LATITUDE LONGITUDE DISTANCE(m) DH4503 P376 EOLARESVR_OR2004 CORS ARP N445628.313 W1230608.100 42648.2 DE6258 MCSO MARION CNTY COOP CORS ARP N445825.701 W1225720.639 51226.8 DG5352 STAY STAYTON COOP CORS ARP N444950.530 W1224915.036 47030.9
BASE STATIONS USED PID DESIGNATION LATITUDE LONGITUDE DISTANCE(m) DH4503 P376 EOLARESVR_OR2004 CORS ARP N445628.313 W1230608.100 42648.2 DE6258 MCSO MARION CNTY COOP CORS ARP N445825.701 W1225720.639 51226.8 DG5352 STAY STAYTON COOP CORS ARP N444950.530 W1224915.036 47030.9

## Slide 56: Back To Our Quick Example
Shown are the positions of P376, MCSO and STAY relative to our “test” site, CORV.
A similar, interactive map can be found under the CORS link at the NGS web site. http://geodesy.noaa.gov/CORS/
56

## Slide 57: Back To Our Quick Example
The NGS monitors the CORS data daily and provides summaries of those results.
Site logs and coordinate time series for the CORS can be accessed through the Logfiles option under the CORS Site Metadata.
57
http://geodesy.noaa.gov/CORS/logfiles/

## Slide 58: Back To Our Quick Example
Looking at the 60-day time-series for each CORS, we discover that the P376 data for the this day happens to be the last before an extended gap.
58

## Slide 59: Back To Our Quick Example
Although this site and the results appears fine otherwise, we may want to consider digging a little deeper.
Possible next steps in evaluating this CORS are:
Resubmit requesting the extended report.
Review the P376 site log.
Resubmit excluding P376.
59

## Slide 60: OPUS DB Requirements
High-Quality OPUS Solution
≥ 70% observations used
≥ 70% ambiguities fixed
≤ 3 cm RMS
≤ 4 cm peak-to-peaks, lat. & lon.
≤ 8 cm peak-to-peak, el. hgt.
properly identify antenna type
precise or rapid orbits (avail. next day)

## Slide 61: OPUS DB Requirements
Mark Attributes
photos of mark & equipment
details (name, type, stability, etc.)
description to aid mark recovery
preview mark description form & help file

## Slide 62: OPUS-DB Requirements

## Slide 63: Interface
The first step in publishing via OPUS is to submit data to OPUS.
The user completes the OPUS form normally, but must explicitly designate that the results should be published. This is done through the Options.
The “Submit to Data Base”, i.e. publish, option is near the bottom of the Options list.
63

## Slide 64: Interface
The user is taken to a new page where they designate the mark associated with their data as “new” or “recovered”.
64

## Slide 65: Interface
After making that selection, the user is offered the appropriate form for entering the meta-data.
In this example, we’re following the “new” mark designation.
65

## Slide 66: Interface
Many of you will recognize these fields as a subset of the information required to “blue book” a mark.
66

## Slide 67: Interface
This is not blue booking per se because the process is streamlined.
This is possible, in part, because some information is provided by the data processing itself.
67

## Slide 68: Interface
As a last step, the user is given a chance to review the submission in the form of a mock-up of the datasheet for their submission.
If the meta-data is complete, the quality control restrictions are met and the user gives the “OK”, the submission is entered into the data base after review by NGS.
68

## Slide 69: Interface
69
http://geodesy.noaa.gov/OPUS/view.jsp

## Slide 71: Interface
71
This is part of a published
data sheet.
Note the “See Also” highlight.
Note the “See Also” highlight. This provides access to other data base and IDB entries for this mark.

## Slide 72
4,000 OPUS-Published Solutions
July 2011

## Slide 74
OPUS –
Datasheet Publishing
Publishing Criteria:
NGS-calibrated GPS antenna
> 4 hour data span
> 70% observations used
> 70% fixed ambiguities
< 0.04m H peak-to-peak
< 0.08m V peak-to-peak
Uses:
  GPS on BMs
  PLSS / GCDB
  Data archive
  Data sharing

## Slide 75
OPUS –
Datasheet
Publishing
Publishing Criteria:
NGS-calibrated GPS antenna
> 4 hour data span
> 70% observations used
> 70% fixed ambiguities
< 0.04m H peak-to-peak
< 0.08m V peak-to-peak
Uses:
  GPS on BMs
  PLSS / GCDB
  Data archive
  Data sharing

## Slide 76
Orthometric Height Comparison
871.746 m Published NAVD88
871.800 m OPUS GEOID09
0.054 m (0.18 ft) Difference

## Slide 77: Why OPUS-DB
A new easier way to capture data and have it in an NGS database
Help populate Ellipsoidal Heights on Bench Marks, help with Geoid models and future vertical datums
To the extent (?) they've bluebooked in the past, they can continue into the future more easily.
If they are running RTK, this would help determine base station position and document where it was used, assuming they left a permanent mark.
Changeover to new datums; either we maintain the data or user does for highest accuracy, but models will be available for bringing old coordinates forward.

## Slide 78: OPUS Projects
Session
Manage
Create