## Slide 1: NGS-CDOT Annual Visit
Region 3
Grand Junction
January 31, 2012

## Slide 2: Agenda
OPUS Programs
  OPUS – DB – Key to heights
  OPUS- Projects
CORS/OPUS Team Efforts
NAD83 (2011), MultiYear CORS Solution
Geoid12
New Data Sheets
CBLs
NGS Advisor Program

## Slide 3: OPUS
OPUS – S (2 hrs)
OPUS – RS (15 minutes)
OPUS – DB (Publish)
OPUS – Projects (Network)

## Slide 4: OPUS-DB Published Solutions

## Slide 5: Sample OPUS DataSheet

## Slide 6: OPUS-DB
http://www.ngs.noaa.gov/

## Slide 7: OPUS DB Requirements
Field Procedures
GPS data file ≥ 4 hour duration
quality mark setting
experienced observer
fixed height tripod recommended
brace tripod legs with sandbags or chain
verify antenna height and plumb

## Slide 8: OPUS DB Requirements
High-Quality OPUS Solution
≥ 70% observations used
≥ 70% ambiguities fixed
≤ 3 cm RMS
≤ 4 cm peak-to-peaks, lat. & lon.
≤ 8 cm peak-to-peak, el. hgt.
properly identify antenna type
precise or rapid orbits (avail. next day)

## Slide 9: OPUS DB Requirements
Mark Attributes
photos of mark & equipment
details (name, type, stability, etc.)
description to aid mark recovery
preview mark description form & help file

## Slide 10: OPUS-DB Requirements

## Slide 11: Why OPUS-DB
A new easier way to capture data and have it in an NGS database
Help populate Ellipsoidal Heights on Bench Marks, help with Geoid models and future vertical datums

## Slide 12: Work to be Done (Ht Modernization) Big Picture
Assessment of Vertical Issues in CO
Gap Analysis of Where we need better vertical measurements, whether orthometric or ellipsoidal
Collect Data in those Key areas, using OPUS-DB, and determine what other means (leveling)
In the meantime, collect what you can using OPUS-DB
Write a report capturing all of this

## Slide 13: OPUS-Projects
Dave Newcomer’s Presentation
can be found at
ftp://ftp.ngs.noaa.gov/dist/pamfrom/CDOT

## Slide 14: OPUS Projects
Session
Manage
Create

## Slide 15: OPUS-Projects
Any questions ???

## Slide 16: CDOT CORS/OPUS Team
To incorporate CORS and OPUS into the CDOT Survey Manual
Present to the SAC on Feb 15, 2012
Proposed Addendum
Recommendations

## Slide 17: CDOT CORS/OPUS Team
Proposed Addendum
Surveying and mapping work, upon which all planning, studies and engineering designs are based, shall use the established CDOT project datum. Unless otherwise determined and approved by CDOT Region Survey Coordinator, the horizontal datum shall be the most recent realization of the North American Datum of 1983 (NAD83) as defined by the National Geodetic Survey (NGS). The horizontal control may utilize accepted CDOT and NGS ground based monuments (such as former HARN) and CORS (Continuous Operating Reference Stations).

## Slide 18: CDOT CORS/OPUS Team
Recommendations
  OPUS tools are valuable and use of them should be further explored and encouraged where appropriate and incorporated into re-write of Chapter 3.
  Encourage publishing of control using OPUS-DB especially on NGS vertical marks to prepare the vertical datums for the future.
  Additional CORS should be added in Colorado
  Microstation control diagrams be edited to reflect the language in the proposed (approved) Addendum
  Training to Support these Changes

## Slide 19: OPUS-RS Coverage in Colorado

## Slide 20: CORS in CO

## Slide 21: CDOT Direction

## Slide 22: Other State Use - CORS
Montana | Observation times at a mark, to a certain extent, are a function of baseline length. Table 8-1 indicates suggested occupation times for dual frequency receivers for various baseline lengths |  | 
 | Baseline Distance | Number of SVs | Time (minutes)
 | Less than 20 km (12.4 miles) | 4 | 20
 |  | 5 | 15
 |  | 6 or more | 9
 | 20 to 35km (12.4 to 21.7 miles) | 4 | 40
 |  | 5 | 30
 |  | 6 or more | 16
 | 35 to 60 km (21.7 to 37.2 miles) | 4 | 60
 |  | 5 | 12
 |  | 6 or more | 30
 | Greater that 60 km ( 37.2 miles) | 4 | 180
 |  | 5 | 135
 |  | 6 or more | 95

## Slide 23: Other State Use - OPUS
Ohio DOT * | 3 sessions; at least 4 hours per session | 
Michigan DOT ** | 2 static observations of no less than 2 hrs and no more than 4 hrs as a minimum | 
 | Dist. from farthest CORS (mi) | Horizontal only
 | Under 25 | 2 hours
 | 25 – 43 | 3 hours
 | 44 and over | 4 hours
North Dakota | occupy each PRIMARY CONTROL point for a MINIMUM of 4 hrs | 
Montana | Observations submitted to NGS for an OPUS solution should adhere to their recommended observation times | 
TEXAS | Any stations that contain 2 or more hrs of raw GPS data can be processed at this (OPUS) Web site. | 
Georgia | a minimum occupation time of 2 hrs during peak satellite cover | 
California | OPUS solutions shall not be used for producing final coordinates or elevations | 
* Use the same 3 base stations when processing; manually select base
stations to be used in OPUS processing.
** Processing of vectors for the Primary Horizontal control must be done
using OPUS.

## Slide 24: FHWA
FHWA Federal Lands Highway Project Development and Design Manual | 5.3.1.1 Horizontal Datum All surveying and mapping work, planning, studies and engineering designs must be based upon a common well-understood horizontal datum. Unless unique circumstances prescribe use of an alternate reference system, the horizontal datum standard for all mapping, planning, design, right-of-way and construction on FLH projects shall be the North American Datum of 1983 (NAD83) as defined by the National Geodetic Survey (NGS). Use of the most current realization of NAD83, from High Accuracy Reference Networks (HARN), Continuous Operating Reference Stations (CORS) or both is encouraged. Use of the NGS Online Positioning User Service (OPUS) is a convenient and efficient method of establishing the required horizontal control datum Project coordinates (northings and eastings) for mapping and design shall be expressed in terms of the State plane coordinate system zone in which the project exists. Definition of the State plane coordinate projections can be found in NGS publication NOS NGS-05.

## Slide 25: CDOT Comparison Between HARN, CORS and OPUS

## Slide 26: CDOT Comparison Between HARN, CORS and OPUS

## Slide 27: NGS NSRS Improvements
TIME NETWORK LOCAL
NETWORK SPAN ACCURACY ACCURACY
NAD 27 1927-1986 10 meter s (1 part in 100,000)
NAD83(86) 1986-1990 1 meter (1 part in 100,000)
NAD83(199x) 1990-1997 0.1 meter B-order (1 part in 1 million)
HARN A-order (1 part in 10 million)
NAD83(NSRS2007) 1996 - 0.01 meter 0.01 meter
(CORS)

## Slide 28: “PASSIVE” NETWORK National Spatial Reference System (NSRS), marks in the ground. 1.5 million marks in the National Geodetic Survey database.
These marks provide:
Horizontal position, or
Horizontal position and ellipsoid height, or
Orthometric Heights, or
Both Horizontal and Vertical values
Tidal Information

## Slide 29: “ACTIVE” Geodetic Network
This is the Geodetic Network
of
Continuously Operating Reference Stations
known as CORS

## Slide 30
Obtain Static Data Files for CORS Here
CORS “Data Products” Page

## Slide 31
Provide Information about your Project

## Slide 32
Enter your custom requests

## Slide 33: NAD83 (2011), MultiYear CORS Solution
New Reference Frame
NAD 83(2011)
Epoch 2010.00
IGS08
Epoch of Observation
Previous Reference Frame
NAD 83(CORS96)
Epoch 2002.00
ITRF00

## Slide 34: A (very) brief history of NAD 83
Original realization completed in 1986
  Consisted (almost) entirely of classical (optical) observations
“High Precision Geodetic Network” (HPGN) and “High Accuracy Reference Network” (HARN) realizations
  Most done in 1990s, essentially state-by-state
  Based on GNSS but classical stations included in adjustments
National Re-Adjustment of 2007
  NAD 83(CORS96) and (NSRS2007)
  Simultaneous nationwide adjustment (GNSS only)
New realization: NAD 83(2011) epoch 2010.00

## Slide 35: Multi-Year CORS Solution
Longer data spans
Absolute antenna calibrations
  satellite transmitting and ground receiving antennas
  most significant change
New network design—added redundancy
  Delaunay triangulation over global sites and CORS backbone
  tie remaining CORS to backbone as stars
IERS 2003 Conventions generally implemented
Updated model for station displacements due to ocean tidal loading
Updated models for troposphere propagation delays
Use current frame; first attempt to obtain a full history of products in a fully consistent framework

## Slide 36: Why a Multi-Year CORS Solution?
Consistent coordinates and velocities from combined solution
  Previous a mix of station and velocity sources, few ties to global frame
  Previous vertical velocities of zero for most CORS
Aligned with most recent realization of global frame (IGS08)
  IGS08 epoch 2005.0 (previous aligned at epoch 1997.0)
  NAD 83 epoch 2010.0 (previous epochs of 2002.0 and 2003.0)
Major processing algorithm, modeling, metadata improvements
  Conformance with current international conventions (IERS)
Absolute phase center antenna calibrations
  Both ground (receiving) and satellite (transmitting) antennas
  Previous (CORS96) used relative calibrations (significant change)
Highly accurate and consistent CORS coordinates and velocities determined using Best Available Methods
  Needed because CORS network is foundation of NSRS

## Slide 37
Mean horizontal shift = 0.2 cm (±2 cm) at epoch 2002.0

## Slide 38
Mean horizontal shift = 2.0 cm (±8 cm) from 2002.02010.0
West CONUS mean shift = 1.1 cm
East CONUS mean shift = 0.1 cm

## Slide 39
Mean vertical shift = -0.8 cm (±2 cm) from 2002.02010.0
Mean vertical shift = +0.7 cm (±2 cm) at epoch 2002.0

## Slide 41: Introducing… NAD 83(2011) epoch 2010.00
Multi-Year CORS Solution (MYCS)
  Reprocessed all CORS GPS data Jan 1994-Apr 2011
  2264 CORS & global stations
  NAD 83 computed by transformation from IGS08
National Adjustment of 2011 (NA2011)
  New adjustment of GNSS passive control
  GNSS vectors tied (and constrained) to CORS NAD 83(2011) epoch 2010.00
  Approximately 80,000 stations and more than 400,000 GNSS vectors
Realization SAME for CORS and passive marks
This is NOT a new datum! (still NAD 83)

## Slide 42: Why a New National Adjustment?
Optimally align passive control with new CORS
Add >1000 projects submitted since 2007 project
  Also observations for Hawaii, other Pacific islands
Network and local accuracies on all stations
  Including future submitted projects
More consistent results in tectonically active areas
  More current data, better tectonic modeling
Better computations and analysis techniques
  E.g., improved outlier detection
  Incorporation of lessons learned from previous national adjustment

## Slide 43: Transformation & Tectonic Complications
NAD 83(2011) transformation tools?
  NAD 83(2011)  (NSRS2007/CORS96)  (HARN)
  Under study by NGS
When is North America not North America?
  Not all stations on the North American tectonic plate
  Pacific plate: Hawaii and American Samoa
  Mariana plate: Guam and CNMI
  Caribbean plate: Referenced to North American plate
  Can relate frames (and epoch dates) with HTDP

## Slide 44: Tectonic Motions

## Slide 45: Q: Will there be another national adjustment, i.e. a new realization of NAD 83, before the new geometric datum is released?
  Why?
  Better agreement between CORS and passive control
  Better ellipsoid heights & positions on passive control
  Better transition to new datum(s)
NAD 83(2011) Epoch:2010.00
A: Yes; it’s currently underway at NGS HQ; EOY goal.
Q: Transformation Tool between NAD 83 realizations?
A: Good question – I’m not sure. NGS is beginning an evaluation of possible solutions.

## Slide 46: How to get to the New Geometric Datum
“Furthermore, NGS will provide simple transformation tools between historic and current datums and reference frames used by NGS, in four dimensions, wherever practical and possible.”
There is no NGS-sanctioned transformation from NAD 83(HARN) to NAD 83(NSRS2007). Therefore, if your data are on a realization prior to NAD 83(NSRS2007) you will either have to get them on NSRS2007 (or 2011) or ignore the position shift and transform them to the new datum. NGS’s OPUS may be the answer for you.
Shift from HARN to NSRS2007
Tucson, AZ

## Slide 47: Future Milestones of the NSRS
Multi-Year CORS solution –
  Completed (for all intents and purposes)
National Adjustment (geometric) of passive control
  2012
Hybrid Geoid Model using new ellipsoid heights
  2012
National Adjustment (vertical) of GPS passive marks
  Under consideration
  This not adjusting the leveling network
Adoption of new datums
  Geometric, could happen any time
  Vertical, requires completion of GRAV-D

## Slide 48: How to Plan for the Future
Move to a contemporary realization of NAD 83
  No NAD 83(HARN) <-> NAD 83(NSRS2007) tool
Obtain precise ellipsoid heights on NAVD 88 bench marks (OPUS, contact NGS Geodetic Advisor(s))
  Improves hybrid geoid models and provides “hard points” in new vertical datum
Move off of NGVD 29 to NAVD 88
  Understand the accuracy of VERTCON in your area
Move away from passive marks to GNSS
  Especially move off of classical passive control
Require/provide complete metadata for all survey/mapping contracts
  How did they get the positions/heights?
  Survey Manual/Spatial Data Accuracy and Georeferencing Standards

## Slide 49
A Question for You:
What is good enough with respect to the NSRS, i.e. have we reached a level of precision and accuracy where further realizations (adjustments) are unnecessary?

## Slide 50: Near-future plans & possibilities
New hybrid geoid model (GEOID12)
  Use NAD 83(2011) epoch 2010.00 ellipsoid heights on NAVD 88 benchmarks
  Might also use OPUS-Database results on NAVD 88 BMs
May perform national vertical adjustment
  Constrain vertically to NAVD 88 benchmarks
    Perform as simultaneous nationwide adjustment
  GNSS-derived orthometric heights
    NAD 83(2011) ellipsoid heights with GEOID12
    NOT a readjustment of NAVD 88 leveling

## Slide 51
-1.18 ft to +1.28 ft

## Slide 52
GPS-derived orthometric heights Warning #1
H ≈ h - N
NAVD 88 height ≈ NAD 83 ellipsoid height - GEOID03
NAVD 88 height ≈ NAD 83 ellipsoid height - GEOID09
Provide, to client(s), datum & realization, ellipsoid heights, geoid model used, methodology (e.g. OPUS or adjusted survey), along with orthometric heights.
GPS-derived orthometric heights Warning #2
H ≈ h – N
The Hybrid GEOID model is defined with respect to a particular realization of NAD 83.
GEOID09 should only be used with NAD 83(NSRS 2007)
GEOID03 should only be used with NAD 83(1992 aka HARN)
NAD 83(HARN) – NAD 83(NSRS2007) in Arizona:
Heights -> min = -20.1 cm, max = 11.5 cm, avg = -2.4 cm
-0.49 ft to +0.72 ft

## Slide 53: Announcing… A New NGS Datasheet Format
Update to new Datasheet version (8.00)
  Changed location, length, and text for many fields
  Added new fields, deleted fields, augmented existing fields
  Implemented by end of calendar year 2011
  Will add announcement and prototype to NGS web site soon
Summary of content changes
  Added country (e.g., USA) where control station located
  Hyperlinked vertical datum designation to datum web page
  Ortho height epoch date, if applicable (e.g., subsidence areas)
  Note for geoid model used on Ht Mod stations if not current geoid
  Network and (median) local accuracies
    Horizontal and ellipsoid height accuracy at 95% confidence (per FGDC)
    Includes link to detailed accuracy info, list of all local accuracies
  Superseded Ht Mod ortho heights indicate geoid model used

## Slide 54: Announcing… A New NGS Datasheet Format

## Slide 55: Announcing… A New NGS Datasheet Format

## Slide 56: Announcing… A New NGS Datasheet Format

## Slide 57: Announcing… A New NGS Datasheet Format

## Slide 58: Announcing… A New NGS Datasheet Format

## Slide 59: CBLs

## Slide 60: Advisor Status In Your State

## Slide 61
More information…
geodesy.noaa.gov

## Slide 62: Questions? Comments? Jokes?
Multi-Year CORS Solution
National Adjustment of 2011
New NGS Datasheet Format