## Slide 1: Latest Developments in NGS
CDOT Region 6
May 1, 2012

## Slide 2: Agenda
Improvements in the NSRS
MultiYear CORS Solution ->NAD83 (2011)
Geoid12/Heights/GRAV-D
New Data Sheets
DS-World
OPUS
CDOT CORS/OPUS Team Efforts
CBLs
LOCUS
RTN
NGS Advisor Program
New Datums (2022)
CHANGE
Improvements

## Slide 3: NGS National Spatial Reference System(NSRS) Improvements
TIME NETWORK LOCAL
NETWORK SPAN ACCURACY ACCURACY
NAD 27 1927-1986 10 meter s (1 part in 100,000)
NAD83(86) 1986-1990 1 meter (1 part in 100,000)
NAD83(199x)* 1990-2007 0.1 meter B-order (1 part in 1 million)
HARN A-order (1 part in 10 million)
NAD83(NSRS2007) 2007 - 0.01 meter 0.01 meter
(CORS)
* CO was completed and adjusted in 2007
CHANGE
IMPROVEMENTS

## Slide 4: National Spatial Reference System (NSRS)
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, and orientation throughout the United States.
Evolving from passive  active 
real-time augmentations
One common datum
Notes: NGS provides users with a consistent national coordinate system, which includes:
Latitude
Longitude
Height
Scale
Gravity
Orientation

## Slide 5: The NSRS has evolved
1 Million Monuments
(Separate Horizontal and Vertical Systems)

Passive Marks
(Limited Knowledge of Stability)
GPS CORS  GNSS CORS
70,000 Passive Marks
(3-Dimensional)
1,800+ CORS
(Time Dependent System Possible; 4-Dimensional)


## Slide 6: “PASSIVE” NETWORK marks in the ground 1.5 million marks in the National Geodetic Survey database NSRS
These marks provide:
Horizontal position, or
Horizontal position and ellipsoid height, or
Orthometric Heights, or
Both Horizontal and Vertical values
Tidal Information

## Slide 7: “ACTIVE” Geodetic Network
Continuously Operating Reference Stations
CORS
NSRS

## Slide 8: CORS

## Slide 9: NAD83 (2011) and the MultiYear CORS Solution
New Reference Frame
NAD 83(2011)
Epoch 2010.00
IGS08
Epoch of Observation
Previous/Current Reference Frame
NAD 83(CORS96)
Epoch 2002.00
ITRF00

## Slide 10: A (very) brief history of NAD 83
Original realization completed in 1986
  Consisted (almost) entirely of classical (optical) observations
“High Precision Geodetic Network” (HPGN) and “High Accuracy Reference Network” (HARN) realizations
  Most done in 1990s, essentially state-by-state
  Based on GNSS but classical stations included in adjustments
National Re-Adjustment of 2007
  NAD 83(CORS96) and (NSRS2007)
  Simultaneous nationwide adjustment (GNSS only)
New realization: NAD 83(2011) epoch 2010.00

## Slide 11: Multi-Year CORS Solution
Longer data spans
Absolute antenna calibrations
  satellite transmitting and ground receiving antennas
  most significant change
New network design—added redundancy
  Delaunay triangulation over global sites and CORS backbone
  tie remaining CORS to backbone as stars
IERS 2003 Conventions generally implemented
Updated model for station displacements due to ocean tidal loading
Updated models for troposphere propagation delays
Use current frame; first attempt to obtain a full history of products in a fully consistent framework

## Slide 12: Why a Multi-Year CORS Solution?
Consistent coordinates and velocities from combined solution
  Previous a mix of station and velocity sources, few ties to global frame
  Previous vertical velocities of zero for most CORS
Aligned with most recent realization of global frame (IGS08)
  IGS08 epoch 2005.0 (previous aligned at epoch 1997.0)
  NAD 83 epoch 2010.0 (previous epochs of 2002.0 and 2003.0)
Major processing algorithm, modeling, metadata improvements
  Conformance with current international conventions (IERS)
Absolute phase center antenna calibrations
  Both ground (receiving) and satellite (transmitting) antennas
  Previous (CORS96) used relative calibrations (significant change)
Highly accurate and consistent CORS coordinates and velocities determined using Best Available Methods
  Needed because CORS network is foundation of NSRS

## Slide 13: Why a Multi-Year CORS Solution?
Absolute phase center antenna calibrations used
More data used in adjustment
  Includes Velocities
  Longer data spans
  Reprocessed all CORS GPS data Jan 1994-Apr 2011
  2264 CORS & global stations
  first attempt to obtain a full history of products in a fully consistent framework
Consistent coordinates and velocities from combined solution
  Previous a mix of station and velocity sources
  Previous few ties to global frame
  Previous vertical velocities of zero for most CORS
Aligned with most recent realization of global frame (IGS08)
  IGS08 epoch 2005.0 (previous aligned at epoch 1997.0)
  NAD 83 epoch 2010.0 (previous epochs of 2002.0 and 2003.0)

## Slide 14: Why a Multi-Year CORS Solution?
Major processing algorithm, modeling, metadata improvements
  Conformance with current international conventions (IERS)
  Highly accurate and consistent CORS coordinates and velocities determined using Best Available Methods
Updated model for station displacements due to ocean tidal loading
Updated models for troposphere propagation delays
  Needed because CORS network is foundation of NSRS

## Slide 15: Positions and Velocities Change!
Plate fixed
CORS Multiyear soln.

## Slide 16: CORS IGS08 Velocity Field

## Slide 17: Changes in Horizontal NAD 83 Positions Different Epochs NAD 83(2011) epoch 2010.0 – NAD 83(CORS96) epoch 2002.0
WA+OR
4.4E,5N cm
CA+NV
10.8E, 14.4N
cm
East
1.4E, -0.2N cm
UT+CO+NM+AZ
0.5E,1.0N cm
ID+MT+ND+SD+WY
1.7E,0.5N cm

## Slide 18: Changes in Horizontal NAD 83 Positions Different Epochs NAD 83(2011) epoch 2010.0 – NAD 83(CORS96) epoch 2002.0
Avg. shifts: E = 0.055.25 (ME -0.12) cm N = 2.126.08 (ME 0.00) cm
  combination of position and velocity differences
  due mostly to updated velocities (including up to 8 more years of data)
WA+OR
4.4E,5N cm
CA+NV
10.8E, 14.4N
cm
East
1.4E, -0.2N cm
UT+CO+NM+AZ
0.5E,1.0N cm
ID+MT+ND+SD+WY
1.7E,0.5N cm

## Slide 19: Changes in Horizontal NAD 83 Positions Same Epoch NAD 83(2011) epoch 2002.00 – NAD 83(CORS96) epoch 2002.00

## Slide 20: Changes in Vertical NAD 83 Positions Different Epochs NAD 83(2011) epoch 2010.0 – NAD 83(CORS96) epoch 2002.0

## Slide 21: Changes in Vertical NAD 83 Positions Different Epochs NAD 83(2011) epoch 2010.0 – NAD 83(CORS96) epoch 2002.0
Avg. shifts: U = -0.662.24 (ME -0.80) cm
  combination of position and velocity differences from additional data, tectonics
  assuming vertical velocity ≈ 0.00 in NAD 83(CORS96)

## Slide 22: Changes in Vertical NAD 83 Positions NAD 83(2011) epoch 2002.0 – NAD 83(CORS96) epoch 2002.0
avg. shift: U = 0.801.89 (ME -0.70) cm
  random part mostly caused by switch to absolute antenna calibrations
  shifts also caused by assuming Vu = 0 in NAD 83(CORS96)

## Slide 23: Changes in Vertical NAD 83 Positions Different Epochs NAD 83(2011) epoch 2002.0 – NAD 83(CORS96) epoch 2002.0

## Slide 24
(81,055)
(970)
(798)
(172)
(80,085)

## Slide 25: Introducing… NAD 83(2011) epoch 2010.00
Multi-Year CORS Solution (MYCS)
  NAD 83 computed by transformation from IGS08
National Adjustment of 2011 (NA2011)
  New adjustment of GNSS passive control
  GNSS vectors tied (and constrained) to CORS NAD 83(2011) epoch 2010.00
  Approximately 80,000 stations and more than 400,000 GNSS vectors
Realization SAME for CORS and passive marks
This is NOT a new datum! (still NAD 83)

## Slide 26: NAD 83(2011) epoch 2010.00
Multi-Year CORS Solution (MYCS)
  Reprocessed all CORS GPS data Jan 1994-Apr 2011
  2264 CORS & global stations
  NAD 83 computed by transformation from IGS08
National Adjustment of 2011 (NA2011)
  New adjustment of GNSS passive control
  GNSS vectors tied (and constrained) to CORS NAD 83(2011) epoch 2010.00
  Approximately 80,000 stations and more than 400,000 GNSS vectors

## Slide 27: Why a New National Adjustment?
Optimally align passive control with new CORS
Add >1000 projects submitted since 2007 project
  Also observations for Hawaii, other Pacific islands
Network and local accuracies on all stations
  Including future submitted projects
More consistent results in tectonically active areas
  More current data, better tectonic modeling
Better computations and analysis techniques
  E.g., improved outlier detection
  Incorporation of lessons learned from previous national adjustment

## Slide 28
National Adjustment of 2011
Project Update
National Geodetic Survey
Observations and Analysis Division April 25, 2012 ● Silver Spring, MD
Michael L. Dennis, RLS, PE
NA2011 Project Manager michael.dennis@noaa.gov

## Slide 29: Transformation & Tectonic Complications
NAD 83(2011) transformation tools?
  NAD 83(2011)  (NSRS2007/CORS96)  (HARN)
  Under study by NGS
When is North America not North America?
  Not all stations on the North American tectonic plate
  Pacific plate: Hawaii and American Samoa
  Mariana plate: Guam and CNMI
  Caribbean plate: Referenced to North American plate
  Can relate frames (and epoch dates) with HTDP

## Slide 30: Tectonic Motions

## Slide 31: How to get to the New Geometric Datum
“Furthermore, NGS will provide simple transformation tools between historic and current datums and reference frames used by NGS, in four dimensions, wherever practical and possible.”
There is no NGS-sanctioned transformation from NAD 83(HARN) to NAD 83(NSRS2007). Therefore, if your data are on a realization prior to NAD 83(NSRS2007) you will either have to get them on NSRS2007 (or 2011) or ignore the position shift and transform them to the new datum. NGS’s OPUS may be the answer for you.
Shift from HARN to NSRS2007
Tucson, AZ

## Slide 32: Current/Future Activities of the NSRS
Multi-Year CORS solution - 2011
National Adjustment (geometric) of passive control - 2012
Hybrid Geoid Model using new ellipsoid heights -2012
  Use NAD 83(2011) epoch 2010.00 ellipsoid heights on NAVD 88 benchmarks
  Might also use OPUS-Database results on NAVD 88 BMs
New Data Sheets - 2012
National Adjustment (vertical) of GPS passive marks
  Under consideration; This not adjusting the leveling network
  Constrain vertically to NAVD 88 benchmarks
  GNSS-derived orthometric heights
    NAD 83(2011) ellipsoid heights with GEOID12
Adoption of new datums -
  Geometric, could happen any time
  Vertical, requires completion of GRAV-D

## Slide 33: Current/Future Activities of the NSRS
Multi-Year CORS solution - 2011
National Adjustment (geometric) of passive control - 2012
Hybrid Geoid Model using new ellipsoid heights -2012
New Data Sheets - 2012
National Adjustment (vertical) of GPS passive marks
  Under consideration; This not adjusting the leveling network
Adoption of new datums

## Slide 34: Current/Future Milestones of the NSRS
Multi-Year CORS solution –
  Completed (for all intents and purposes)
National Adjustment (geometric) of passive control
  2012
Hybrid Geoid Model using new ellipsoid heights
  2012
National Adjustment (vertical) of GPS passive marks
  Under consideration
  This not adjusting the leveling network
Adoption of new datums
  Geometric, could happen any time
  Vertical, requires completion of GRAV-D

## Slide 35: How to Plan for the Future
Use most recent realization of NAD 83
Move away from passive marks to GNSS
Move off of NGVD 29 to NAVD 88
  Understand the accuracy of VERTCON in your area
Collect OPUS-DB on NAVD 88 bench
Require/provide complete metadata for all survey/mapping contracts
  How did they get the positions/heights?
  Survey Manual/Spatial Data Accuracy and Georeferencing Standards

## Slide 36: How to Plan for the Future
Move to a contemporary realization of NAD 83
  No NAD 83(HARN) <-> NAD 83(NSRS2007) tool
Obtain precise ellipsoid heights on NAVD 88 bench marks (OPUS, contact NGS Geodetic Advisor(s))
  Improves hybrid geoid models and provides “hard points” in new vertical datum
Move off of NGVD 29 to NAVD 88
  Understand the accuracy of VERTCON in your area
Move away from passive marks to GNSS
  Especially move off of classical passive control
Require/provide complete metadata for all survey/mapping contracts
  How did they get the positions/heights?
  Survey Manual/Spatial Data Accuracy and Georeferencing Standards

## Slide 37
A Question to Consider:
What is good enough
with respect to the NSRS,
i.e. have we reached a level of precision and accuracy where further realizations (adjustments) are unnecessary?

## Slide 38: Near-future plans & possibilities
New hybrid geoid model (GEOID12)
  Use NAD 83(2011) epoch 2010.00 ellipsoid heights on NAVD 88 benchmarks
  Might also use OPUS-Database results on NAVD 88 BMs
May perform national vertical adjustment
  Constrain vertically to NAVD 88 benchmarks
    Perform as simultaneous nationwide adjustment
  GNSS-derived orthometric heights
    NAD 83(2011) ellipsoid heights with GEOID12
    NOT a readjustment of NAVD 88 leveling

## Slide 39: Using GNSS is cheaper, easier than leveling To use GNSS we need a good geoid model
Heights Bottom Line
GNSS – Global Navigation Satellite System

## Slide 40
Differential Leveling
(Orthometric HT)
GNSS
(Ellipsoid Ht)
Height
Modernization
-faster
-cheaper
Height Modernization

## Slide 41: Ellipsoid, Geoid, and Orthometric Heights
(NAVD88) H
H = Orthometric Height (leveling)
H = h - N
TOPOGRAPHIC
SURFACE
h = Ellipsoidal Height (GPS)
N = Geoid Height (model)
h (NAD83)
Ellipsoid
N
Geoid
Geoid Height
(GEOID09)
TRANSPORTATION
1660.6 = 1643.354 – (-17.23*) METERS
1660.6 = 1643.4 + 17.2
*56.53 feet
Notes: Orthometric height is the height on the surface above the geoid. But we can’t measure from the geoid so we use leveling. The NAVD88 is defined from the control point, B, in Quebec. Because the ortho ht at A is computed from leveling observations, where error is modeled or estimated, it probably isn’t right at the geoid, right at “sea level”.
Our vertical datum is defined. We need a geoid that we can use that is relative to the vertical datum.
Note that in this picture the geoid is shown above the ellipsoid. In the continental United States, the geoid is actually below the ellipsoid, so the value of the geoid height is negative.

## Slide 42: Exaggerated view of the Earths Gravity Measure.
Notes: The Geoid

## Slide 43: Problems in NAVD 88
A North American realization through spirit leveling networks
Pre-satellite era product (625,000 km of leveling added to the NGVD29)
Height information through passive bench marks whose positions change constantly in our changing world (e.g., PGR, subsidence, earthquakes, …)
The geoid differences between NAVD 88 and GRACE are in meter range: compare to ±2-3 cm error in typical GPS ellipsoidal heights

## Slide 44
GRAV-D
GRAV-D means fast, accurate, consistent orthometric heights everywhere in the USA
GPS already gives fast accurate ellipsoid heights
If the geoid were modeled (and monitored) to highest accuracy…
Voila… Fast, accurate orthometric heights, anywhere, anytime
No need to use leveling to “bring in the datum”

## Slide 45: The Future of Height Mod: GRAV-D Gravity for the Redefinition of the American Vertical Datum
GRAV-D
  Airborne gravity survey (10 years)
  Gravity monitoring into the future
  Coastal areas surveyed first
  All USA states and territories
  www.ngs.noaa.gov/GRAV-D
2018-2022 Targets:
  Orthometric heights (“elevations” on maps) good to 2 cm anywhere, anytime from GNSS technology
  Height changes easily monitored using new vertical datum
Gravity for the Nation’ benefits
  Imagery for the Nation
  Lidar for the Nation
  Elevation for the Nation
Notes: NOAA’s National Geodetic Survey (NGS) conducted an airborne survey in western interior Alaska in July, 2009. The National Geospatial-Intelligence Agency (NGA) is a partner in the survey. The operation will be conducted aboard a Naval Research Laboratory (NRL) C-12 King Air aircraft with a Navy aircrew.

## Slide 46
-1.18 ft to +1.28 ft

## Slide 47
GPS-derived orthometric heights Warning #1
H ≈ h - N
NAVD 88 height ≈ NAD 83 ellipsoid height - GEOID03
NAVD 88 height ≈ NAD 83 ellipsoid height - GEOID09
Provide, to client(s), datum & realization, ellipsoid heights, geoid model used, methodology (e.g. OPUS or adjusted survey), along with orthometric heights.
-0.49 ft to +0.72 ft

## Slide 48
GPS-derived orthometric heights Warning #2
H ≈ h – N
The Hybrid GEOID model is defined with respect to a particular realization of NAD 83.
GEOID09 should only be used with NAD 83(NSRS 2007)
GEOID03 should only be used with NAD 83(1992 aka HARN)
NAD 83(HARN) – NAD 83(NSRS2007) in Arizona:
Heights -> min = -20.1 cm, max = 11.5 cm, avg = -2.4 cm
-0.49 ft to +0.72 ft

## Slide 49: Leveled Bench Marks Occupied by GPS and stored in OPUS-DB
OPUS-DB shows great promise for filling gaps
Notes: 80 are in common with NGSIDB and were used in making GEOID09
57 are in common with NGSIDB and were *NOT* used in making GEOID09
285 are new points never before occupied with GPS
Distribution is fair, but you can see that some states are more active than others

## Slide 50: Work to be Done (Ht Modernization) Big Picture
Assessment of Vertical Issues in CO
Gap Analysis of Where we need better vertical measurements, whether orthometric or ellipsoidal
Collect Data in those Key areas, using OPUS-DB, and determine what other means (leveling)
In the meantime, collect what you can using OPUS-DB
Write a report capturing all of this

## Slide 51: Announcing… A New NGS Datasheet Format
Update to new Datasheet version (8.00)
  Changed location, length, and text for many fields
  Added new fields, deleted fields, augmented existing fields
  To be Implemented in 2012
  Will add announcement and prototype to NGS web site soon
Summary of content changes
  Added country (e.g., USA) where control station located
  Hyperlinked vertical datum designation to datum web page
  Ortho height epoch date, if applicable (e.g., subsidence areas)
  Note for geoid model used on Ht Mod stations if not current geoid
  Network and (median) local accuracies
    Horizontal and ellipsoid height accuracy at 95% confidence (per FGDC)
    Includes link to detailed accuracy info, list of all local accuracies
  Superseded Ht Mod ortho heights indicate geoid model used

## Slide 52: Announcing… A New NGS Datasheet Format

## Slide 53: Announcing… A New NGS Datasheet Format

## Slide 54: Announcing… A New NGS Datasheet Format

## Slide 55: Announcing… A New NGS Datasheet Format

## Slide 56: Announcing… A New NGS Datasheet Format

## Slide 57: “DSWorld” Software Program
Highly rated new NGS software tool
Developed to search the NGS database
Easy to learn/use
Multiple search options available
Displays search results using Google Earth

## Slide 58: Geodetic Control Near CDOT R6 office
Triangles – Horizontal Control
Squares – Vertical Control
Blue – First Order
Red – Second Order

## Slide 60
Datasheets Recovery
Photos Directions
Descriptions

## Slide 61: Direct Access to the NGS Datasheet

## Slide 62: Geodetic Control Near CDOT R2 office
Triangles – Horizontal Control
Squares – Vertical Control
Blue – First Order
Red – Second Order

## Slide 64
Datasheets Recovery
Photos Directions
Descriptions

## Slide 65: Direct Access to the NGS Datasheet

## Slide 66: DSWorld opening screen

## Slide 67: Where do you get DS-World?

## Slide 68: OPUS

## Slide 69: CDOT CORS/OPUS Team
To incorporate CORS and OPUS into the CDOT Survey Manual
Presented to SAC on Feb 15, 2012
Proposed Addendum
Recommendations

## Slide 70: CDOT CORS/OPUS Team
Proposed Addendum
DRAFT
DRAFT

## Slide 71: CDOT CORS/OPUS Team
Recommendations
  OPUS tools are valuable and use of them should be further explored and encouraged where appropriate and incorporated into re-write of Chapter 3.
  Encourage publishing of control using OPUS-DB especially on NGS vertical marks to prepare the vertical datums for the future.
  Additional CORS should be added in Colorado
  Microstation control diagrams be edited to reflect the language in the proposed (approved) Addendum
  Training to Support these Changes
DRAFT
DRAFT

## Slide 72: OPUS-RS Coverage in Colorado

## Slide 73: CDOT Comparison Between HARN, CORS and OPUS Region 3 Data

## Slide 74: CDOT Comparison Between HARN, CORS and OPUS Region 2 Data

## Slide 75: CBLs

## Slide 77: LOCUS Leveling OnLine Calculations User Service
Provides a means to process and adjust level data
  Has been done at NGS Headquarters
Requires *.hgz file from Translev
  Error free
Requires Description file from WinDesc
You pick stations to constrain
Helps expedite entire process
Beta Version – Needs to be tested
Data is not submitted to NGS (at this time)

## Slide 78
GOAL:
To Ensure the Proper Geodetic Basis
for Accurate Real Time Positioning
Aligned To The NSRS
NGS
Real Time Positioning Components

## Slide 79
NGS Streams Raw Data From The Backbone CORS
Provide Outreach and Education
Develop and Publish Guidelines Describing Best Practices.
Research Scientific Research Affecting Accurate Real-Time Positioning. [satellite orbits, refraction, multipath, antenna calibration, and crustal motion.]
NGS - RT Program Components

## Slide 80
>200 RTN World wide
>80 RTN in USA 35+ State DOT Many Cooperative Efforts

## Slide 81: Outreach, Cooperative Efforts & Leadership
FGCS
TSRC
LSRC
+ PUBLIC & PRIVATE RTN ADMINISTRATORS SPANNING MORE THAN 35 STATES

## Slide 82
http://www.ngs.noaa.gov/
DRAFT

## Slide 83
Summary Table
RT Single-Base Guidelines

## Slide 84: NGS Guidelines Real Time GNSS Networks
Site Considerations
Planning and Design
Administration
Obtaining Station Coordinates Consistent with NAD83 and ITRS
User Best Methods

## Slide 85: Obtaining Station Coordinates Consistent with NAD83 and ITRS
Include a subnetwork of the RTN into the National CORS network. This would be three stations If RTN has less than 30 stations, 10% of RTN with greater than 30 stations. NGS will not distribute/broadcast RTN reference station data.
Align all RTN reference stations coordinates to the CORS network at 2-cm horizontal and 4-cm vertical
For each reference station in the RTN, use the Online Positioning User Service (OPUS) at http://www.ngs.noaa.gov/OPUS/ to test for the continued consistency of its adopted positional coordinates and velocity on a daily basis, and revise the station’s adopted coordinates and/or velocity if the tests reveal a need to do so.

## Slide 86: Best methods from the Guidelines: The 7 “C’S” of NOAA’s NGS
Check Equipment
Communication
Conditions
Calibration (or not)
Coordinates
Collection
Confidence
The Control is at the Pole

## Slide 87: Expediting The Guidelines
The NGS Encourages RTN Users and Administrators to become Cooperative Partners to Provide Input that will Enable Valuable Documents to be Drafted that will Benefit the Public Welfare. - Establishing Reference Stations
- Adjusting Networks - Accuracy Expectations Vs. Obtained - Baseline Distances
- Error Modeling - Communication Issues

## Slide 88: Real Time Networks (RTN) Considerations
How Are They Established?
How Are Their Coordinates Computed? Are They Consistent?
How Is The Network Adjusted?
How Does The RTN Align To The NSRS?
Can Users Use Any Manufacturers’ Equipment In The RTN?
Do Overlapping Networks Give The Same Coordinates?
What Are The Field Accuracies?
?

## Slide 89: Real-Time Considerations
Passive / Active
Datums & Adjustment Epochs
Geoid + Ellipsoid / Calibrate
Single Base / RTN
GNSS / GPS
Grid / Ground

## Slide 90: Some RT Field Considerations
- Multipath
- Position Dilution of Precision (PDOP)
- Baseline Root Mean Square (RMS)
- Number of satellites
- Elevation mask (or cut-off angle)
- Base accuracy (datum level, local
level)
- Base security
- Redundancy, redundancy,
redundancy
- Part(s) Per Million Error (ppm) –
iono, tropo models,
orbit errors
- Space weather- sunspot numbers,
solar maximum
- Geoid quality
- Site calibrations (a.k.a. Localizations)
- Bubble adjustment
- Latency, update rate
- Fixed and float solutions
- Accuracy versus Precision
- Signal to Noise Ratio (S/N or C/N0)
- Carrier phase
- Code phase
- VHF/UHF radio communication
- CDMA/SIM/Cellular TCP/IP
communication
- WGS 84 versus NAD 83,
local datums,
- GPS, GLONASS, Galileo, Compass
Constellations

## Slide 91: Metadata
The RT Practitioner must record items not recorded in the Field. For instance:
What is the Source of the Data?
What is the Datum/Adjustment Epoch?
What are the Field Conditions?
What Equipment was used, especially what Antenna?
What firmware was in the receiver and collector?
What redundancy, if any, was used?

## Slide 93
Mesa County, Colorado RTN

## Slide 96: CSRN GPS DAY
CSRN- Colorado Spatial Reference Network (Chapter of the PLSC)
MAY 12, 2012 Saturday
10:00 – 2:00
Utah Park Aurora, CO (1800 S. Peoria St)
Free Food, Vendors, Boy and Girl Scouts

## Slide 97: Advisor Status In Your State

## Slide 98: National Geodetic Survey Ten-Year Plan
Official NGS policy as of January 2008
Replace NAVD 88 with a GPS/geoid datum
Replace NAD 83 with a geocentric GPS based datum

## Slide 99: NGS 10-Year Plan (excerpts)
Vision 1# Summary:
By 2020?, NGS has defined a new geometric datum (classically called “horizontal”) to replace NAD 83 with its many systematic errors. The primary means of accessing this new datum is GNSS technology.
Vision #2 Summary:
By 2020?, a new geopotential datum (for orthometric and dynamic heights) is defined and realized through the combination of GNSS technology and gravity field modeling.
Note: Vision #2 can not happen without Vision #1.

## Slide 100: NGS 10-Year Plan (more excerpts)
“NGS redefines the national horizontal datum to remove gross disagreements with the ITRF.”
“The primary means of accessing this new datum is GNSS technology. While passive control continues to be used as a secondary method to access the NSRS, such control will be “tied to”, not a “part of”, the NSRS.”
“Furthermore, NGS will provide simple transformation tools between historic and current datums and reference frames used by NGS, in four dimensions, wherever practical and possible.”
“In order to support users of NAVD 88, NGS will provide transformation tools between the new datum and NAVD 88 based predominantly on the few thousand measurements of GPS derived ellipsoid heights on NAVD 88 benchmarks.”
Underlining added for emphasis

## Slide 101: Why a New Datum(s)?
NAD 83
  non-geocentric, i.e. inconsistent with GNSS positioning
  NAD 83 coordinates of the Continuously Operating Reference Station (CORS) network inconsistent with passive marks
  Lack of velocities, i.e. NAD 83 does not report station motion for passive marks

## Slide 102: Why a New Datum(s)?
NAVD 88
  cross-country build up of errors (“tilt” or “slope”) from geodetic leveling
  Passive marks inconveniently located and vulnerable to disturbance and destruction
  A 0.5 m bias in the NAVD 88 reference surface from the geoid surface best approximating global mean sea level
  Subsidence, uplift, freeze/thaw, and other crustal motions invalidate heights of passive marks, and can make it difficult to detect such motions.
  Passive marks without adequate geophysical models make it difficult to reliably detect sea level change
  Changes to Earth’s gravity field cause changes in orthometric heights, but NAVD 88 does not allow/account for those changes (because it is based on a static gravity model)
  The gravity model and modeling techniques used to determine NAVD 88 are not consistent with those currently used for geoid modeling

## Slide 104: New Datums
“NGS redefines the national horizontal datum to remove gross disagreements with the ITRF.”
  In other words, ellipsoid heights will change.
“By 2020(?), a new geopotential datum (for orthometric and dynamic heights) is defined and realized through the combination of GNSS technology and gravity field modeling.”
In other words, orthometric heights will NOT be based on leveling data and they too will change.

## Slide 106
www.geodesy.noaa.gov
http://www.ngs.noaa.gov/

## Slide 107: NGS Training Center
http://www.ngs.noaa.gov/corbin/
Webinars!

## Slide 108: More information…
NGS Home Page: http://www.geodesy.noaa.gov
geodesy.noaa.gov
CORS Webpage: http://www.ngs.noaa.gov/CORS/
CORS newsletter
OPUS Webpage: http://www.ngs.noaa.gov/OPUS/
Find Your Advisor:
www.ngs.noaa.gov/ADVISORS/AdvisorsIndex.shtml
This presentation will be uploaded to:
http://www.ngs.noaa.gov/web/science_edu/presentations_archive/
FAQs on the various webpages

## Slide 109: Next Steps
OPUS-DB
OPUS - Manual
Heights

## Slide 110: Thank You
pamela.fromhertz@noaa.gov
240-988-6363

## Slide 111: Questions? Comments? Jokes?
Multi-Year CORS Solution
National Adjustment of 2011
New NGS Datasheet Format