## Slide 1: State Plane 2022
Where Things Stand in Hawai’i
and the Road Ahead
Michael L. Dennis, PhD, PE, PLS
SPCS2022 Project Manager
2023 Pacific Rim Geospatial Conference
March 17, 2023

## Slide 2
STATE PLANE
Making the Earth flat
…one zone at a time
Surveyors (and engineers) the State Plane Coordinate System

## Slide 3
How surveyors and engineers see the Earth…

## Slide 4: A “flat” Earth for the future
State Plane Coordinate System of 2022 (SPCS2022)
Third generation of State Plane
  First in 1930s, second in 1980s
  Same 3 map projection types
  Same ellipsoid as SPCS 83 (GRS 80)
The same, but different…
  Based on new terrestrial reference frames instead of NAD 83
  Designed to reduce difference between “grid” and “ground” distances
  Zone “layers” will exist in most states
  More zones, most designed by state stakeholders
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 5: Getting acquainted with SPCS2022
Overall distortion design philosophy
  Linear distortion minimized (or “optimized”) at topographic surface (not at ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
What is linear distortion?
  Defined at a point (infinitesimal distances)
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm per km
Linear distortion | = | Projected minus actual distance
 |  | Actual distance

## Slide 6
Grid distance < ellipsoid distance < ground distance (k < 1 and δ < 0)
Grid distance > ellipsoid distance < ground distance (k > 1 and δ < 0)
Projection axis (k0 < 1)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to ellipsoid surface
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
6
k0 = scale on projection axis
LCC: central parallel
TM: central meridian
OM: skew axis
h

## Slide 7
Projection axis (k0 > 1)
Projection surface (non-intersecting)
Ellipsoid distance
Topographic surface
Horizontal ground distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
h
Grid distance > ellipsoid distance ≈ ground distance (k > 1 and δ ≈ 0)
7
Ellipsoid surface

## Slide 8
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface
8
Ellipsoid surface

## Slide 9
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Topographic surface
9
Ellipsoid surface

## Slide 10
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
ONLY way to reduce variation in distortion is to change projection axis location (or change projection).
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
10
This design approach used for SPCS2022 (minimizes distortion with respect to topography)
Projection axis scale can be less than 1 for steeply sloping areas even if heights are large.

## Slide 11: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio
20 ppm | 2 cm/km | 0.1 ft/mile | 1:50,000
50 ppm | 5 cm/km | 0.3 ft/mile | 1:20,000
100 ppm | 10 cm/km | 0.5 ft/mile | 1:10,000
400 ppm | 40 cm/km | 2.1 ft/mile | 1:2,500

## Slide 12: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 13: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 14: Number of SPCS2022 zones (preliminary)
Designs by NGS
  165 zones
  Includes 54 statewide zones and 3 “special use” zones (in more than one state)
Designs by state stakeholders
  802 zones in 28 states
Total = 967 zones for 56 states and territories
Compare to 125 zones in existing State Plane

## Slide 15: SPCS2022 linear distortion (prelim)
49 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 14% | 12% | 7%
±50 | 27% | 26% | 18%
±100 | 48% | 48% | 36%
±400 | 91% | 93% | 88%
City and area statistics (ppm): |  |  | 
 | Min | -1512 | -1627
 | Max | +2888 | +2987
 | Range | 4400 | 4614
 | Mean | -86 | -120
Mean weighted by pop = -100 |  |  | 
15

## Slide 16: SPCS2022 linear distortion (prelim)
646 zones (35 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 70% | 54%
±50 | 92% | 88% | 73%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -400 | -684
 | Max | +245 | +295
 | Range | 644 | 979
 | Mean | -5 | -23
Mean weighted by pop = -4 |  |  | 
16

## Slide 17: SPCS2022 linear distortion (prelim)
187 zones (10 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 78% | 78% | 73%
±50 | 91% | 90% | 88%
±100 | 99.8% | 99% | 97%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -261 | -465
 | Max | +120 | +240
 | Range | 381 | 705
 | Mean | -3 | -12
Mean weighted by pop = -1 |  |  | 
17

## Slide 18: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 19: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
19

## Slide 20: SPCS2022 linear distortion (prelim)
21 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 77% | 38% | 17%
±50 | 90% | 67% | 38%
±100 | 98% | 93% | 68%
±400 | 100% | 100% | 99.8%
City and area statistics (ppm): |  |  | 
 | Min | -177 | -794
 | Max | +321 | +331
 | Range | 498 | 1125
 | Mean | -7 | -53
Mean weighted by pop = -4 |  |  | 
Statistics are for land areas only

## Slide 21: SPCS2022 linear distortion (prelim)
38 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 89% | 93% | 49%
±50 | 98% | 99.7% | 74%
±100 | 99.7% | 100% | 88%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -59 | -937
 | Max | +49 | +190
 | Range | 108 | 1127
 | Mean | +0.4 | -34
Mean weighted by pop = -8 |  |  | 
Statistics are for land areas only

## Slide 22: SPCS2022 linear distortion (prelim)
45 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 86% | 85% | 47%
±50 | 97% | 98% | 73%
±100 | 99.5% | 99.7% | 88%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -60 | -937
 | Max | +321 | +335
 | Range | 380 | 1272
 | Mean | -3 | -35
Mean weighted by pop = -10 |  |  | 
Statistics are for land areas only

## Slide 23: Existing SPCS 83 linear distortion
10 zones (Alaska)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 4% | 10% | 4%
±50 | 16% | 23% | 11%
±100 | 40% | 62% | 36%
±400 | 100% | 100% | 99.1%
City and area statistics (ppm): |  |  | 
 | Min | -263 | -967
 | Max | +86 | +342
 | Range | 349 | 1308
 | Mean | -83 | -135
Mean weighted by pop = -92 |  |  | 
23
Statistics are for land areas only

## Slide 24: The situation for Hawai’i
Two zone layers
  1 statewide zone (designed by NGS)
  19 zones on partial coverage layer (proposed by stakeholders)
    12 zones for the Big Island
    7 zones for Maui
  Total 20 zones
Designs in progress, preliminary ones done soon!
  Based on refined design process for steep topography
  Remaining zone designs currently underway
  Final zone number and extents may change
  Will work with Hawai’i stakeholders to finalize designs

## Slide 25: SPCS2022 linear distortion (prelim)
Hawai’i (statewide)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 73% | 58% | 23%
±50 | 95% | 87% | 40%
±100 | 98% | 97% | 56%
±400 | 100% | 100% | 95%
City and area statistics (ppm): |  |  | 
 | Min | -174 | -645
 | Max | +70 | +81
 | Range | 244 | 725
 | Mean | +6 | -120
Mean weighted by pop = -0.1 |  |  | 
25
Statistics are for land areas only

## Slide 26: Existing SPCS 83 linear distortion
Hawai’i (5 zones)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 54% | 40% | 10%
±50 | 85% | 81% | 26%
±100 | 97% | 94% | 45%
±400 | 100% | 100% | 92%
City and area statistics (ppm): |  |  | 
 | Min | -208 | -694
 | Max | +12 | +29
 | Range | 220 | 723
 | Mean | -36 | -163
Mean weighted by pop = -30 |  |  | 
26
Statistics are for land areas only

## Slide 27: Existing UTM 83 linear distortion
Hawai’i (UTM 4 North)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 0.02% | 0% | 1.0%
±50 | 0.1% | 0.9% | 1.6%
±100 | 0.4% | 2.8% | 3.6%
±400 | 77% | 54% | 25%
City and area statistics (ppm): |  |  | 
 | Min | -404 | -613
 | Max | +1908 | +1995
 | Range | 2312 | 2608
 | Mean | +376 | +659
Mean weighted by pop = +29 |  |  | 
27
Statistics are for land areas only

## Slide 28: SPCS2022 linear distortion (prelim)
Hawai’i (statewide)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 73% | 58% | 23%
±50 | 95% | 87% | 40%
±100 | 98% | 97% | 56%
±400 | 100% | 100% | 95%
City and area statistics (ppm): |  |  | 
 | Min | -174 | -645
 | Max | +70 | +81
 | Range | 244 | 725
 | Mean | +6 | -120
Mean weighted by pop = -0.1 |  |  | 
28
Statistics are for land areas only

## Slide 29: Statewide zone performance for O’ahu
Following 2 maps show statewide and SPCS 83 design performance
  Distortion increment of 20 ppm used to show more detail
  Both maps give statistics for O’ahu only
  Existing SPCS 83 Hawai’i Zone 3 is a single projection for Oahu only
Both maps give distortion design performance value in ppm, where:
  The distortion value includes at least 90% of population…
  …AND at least 75% of cities and towns (irrespective of population)
  …AND at least 50% of total land area
SPCS2022 statewide zone performance better than SPCS 83 HI Zone 3

## Slide 30: SPCS2022 linear distortion (prelim)
O’ahu (statewide)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 84% | 80% | 52%
±50 | 99.8% | 100% | 84%
±100 | 100% | 100% | 98%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -31 | -177
 | Max | +31 | +35
 | Range | 62 | 212
 | Mean | +8 | -19
Mean weighted by pop = +2 |  |  | 
30
Statistics are for land areas only
Distortion increment 20 ppm
Distortion design
performance ±30 ppm

## Slide 31: Existing SPCS 83 linear distortion
O’ahu (HI Zone 3)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 69% | 76% | 32%
±50 | 91% | 96% | 60%
±100 | 100% | 100% | 93%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -59 | -199
 | Max | -5 | +3
 | Range | 54 | 202
 | Mean | -17 | -45
Mean weighted by pop = -21 |  |  | 
31
Statistics are for land areas only
Distortion increment 20 ppm
Distortion design
performance ±50 ppm

## Slide 32: Preliminary zone designs for Maui
Based on 7 zones as proposed by stakeholders
Following 4 maps show statewide and preliminary design performance
  First 2 maps with distortion increment of 50 ppm
  Second 2 maps with distortion increment of 20 ppm to show more detail
All maps give distortion design performance value in ppm, where:
  The distortion value includes at least 90% of population…
  …AND at least 75% of cities and towns (irrespective of population)
  …AND at least 50% of total land area
The multi-zone designs are PRELIMINARY and WILL change!
  Will seek input from stakeholders before finalizing

## Slide 33: SPCS2022 linear distortion (prelim)
Maui (statewide)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 16% | 18% | 21%
±50 | 86% | 73% | 53%
±100 | 98% | 100% | 74%
±400 | 100% | 100% | 99.7%
City and area statistics (ppm): |  |  | 
 | Min | -89 | -431
 | Max | +70 | +81
 | Range | 159 | 512
 | Mean | +24 | -57
Mean weighted by pop = +23 |  |  | 
33
Statistics are for land areas only
Distortion increment 50 ppm
Distortion design
performance ±75 ppm

## Slide 34: SPCS2022 linear distortion (prelim)
Maui (7 zones)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 79% | 77% | 51%
±50 | 98% | 95% | 79%
±100 | 99.7% | 100% | 95%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -37 | -204
 | Max | +94 | +209
 | Range | 131 | 413
 | Mean | +5 | -4
Mean weighted by pop = +0.3 |  |  | 
34
Statistics are for land areas only
Distortion increment 50 ppm
Distortion design
performance ±40 ppm

## Slide 35: SPCS2022 linear distortion (prelim)
Maui (statewide)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 16% | 18% | 21%
±50 | 86% | 73% | 53%
±100 | 98% | 100% | 74%
±400 | 100% | 100% | 99.7%
City and area statistics (ppm): |  |  | 
 | Min | -89 | -431
 | Max | +70 | +81
 | Range | 159 | 512
 | Mean | +24 | -57
Mean weighted by pop = +23 |  |  | 
35
Statistics are for land areas only
Distortion increment 20 ppm
Distortion design
performance ±75 ppm

## Slide 36: SPCS2022 linear distortion (prelim)
Maui (7 zones)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 79% | 77% | 51%
±50 | 98% | 95% | 79%
±100 | 99.7% | 100% | 95%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -37 | -204
 | Max | +94 | +209
 | Range | 131 | 413
 | Mean | +5 | -4
Mean weighted by pop = +0.3 |  |  | 
36
Statistics are for land areas only
Distortion increment 20 ppm
Distortion design
performance ±40 ppm

## Slide 37: Preliminary zone designs for Big Island
Based on 12 zones as proposed by stakeholders
Following 4 maps show statewide and preliminary design performance
  First 2 maps with distortion increment of 50 ppm
  Second 2 maps with distortion increment of 20 ppm to show more detail
All maps give distortion design performance value in ppm, where:
  The distortion value includes at least 90% of population…
  …AND at least 75% of cities and towns (irrespective of population)
  …AND at least 50% of total land area
The multi-zone designs are PRELIMINARY and WILL change!
  Will seek input from stakeholders before finalizing

## Slide 38: SPCS2022 linear distortion (prelim)
Big Island (statewide)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 55% | 58% | 14%
±50 | 79% | 82% | 24%
±100 | 89% | 91% | 38%
±400 | 100% | 100% | 92%
City and area statistics (ppm): |  |  | 
 | Min | -174 | -645
 | Max | +54 | +76
 | Range | 228 | 721
 | Mean | -8 | -170
Mean weighted by pop = -26 |  |  | 
38
Statistics are for land areas only
Distortion increment 50 ppm
Distortion design
performance ±150 ppm

## Slide 39: SPCS2022 linear distortion (prelim)
Big Island (12 zones)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 79% | 76% | 49%
±50 | 99.7% | 100% | 80%
±100 | 100% | 100% | 92%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -28 | -420
 | Max | +29 | +230
 | Range | 57 | 651
 | Mean | +0.3 | -15
Mean weighted by pop = +1.4 |  |  | 
39
Statistics are for land areas only
Distortion increment 50 ppm
Distortion design
performance ±30 ppm

## Slide 40: SPCS2022 linear distortion (prelim)
Big Island (statewide)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 55% | 58% | 14%
±50 | 79% | 82% | 24%
±100 | 89% | 91% | 38%
±400 | 100% | 100% | 92%
City and area statistics (ppm): |  |  | 
 | Min | -174 | -645
 | Max | +54 | +76
 | Range | 228 | 721
 | Mean | -8 | -170
Mean weighted by pop = -26 |  |  | 
40
Statistics are for land areas only
Distortion increment 20 ppm
Distortion design
performance ±150 ppm

## Slide 41: SPCS2022 linear distortion (prelim)
Big Island (12 zones)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 79% | 76% | 49%
±50 | 99.7% | 100% | 80%
±100 | 100% | 100% | 92%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -28 | -420
 | Max | +29 | +230
 | Range | 57 | 651
 | Mean | +0.3 | -15
Mean weighted by pop = +1.4 |  |  | 
41
Statistics are for land areas only
Distortion increment 20 ppm
Distortion design
performance ±30 ppm

## Slide 42: About the timing of it all…
Timeline
  Complete review of stakeholder submittals (DONE)
  Early-mid 2023: Preliminary designs for stakeholder review
  Mid-late 2023: Finalize all zone designs
Other things in 2023
  Provide machine-readable definitions
  Modify NGS algorithms (e.g., 1-parallel Lambert)
  Document new projection algorithms
Release with rollout of modernized NSRS
  Final definitions available by late 2023
  Release with new “datums” in 2025
Rollout in
2025

## Slide 43: A tale of two feet
Two versions of “foot” in current use:
“Old” U.S. survey foot (adopted 1893)
1 ft = 0.3048 m exactly
‭1 ft = 1200/3937 m (0.3048006096…‬ m)
Differ by
2 parts per million (ppm) or ~0.01 ft (~1/8 inch) per mile
  A real problem with real costs
“New” international foot (adopted 1959)

## Slide 45: End of an era for the U.S. survey foot
U.S. survey foot has been “deprecated” (retired)
  Not supported for State Plane Coordinate System of 2022 (or any part of modernized NSRS)
  Only international foot will be supported by NGS
Effective December 31, 2022
  But U.S. survey foot will still be supported for legacy products (e.g., existing State Plane)
However, NGS will NOT support NAD 83 after NSRS Modernization complete
NGS will always support U.S. survey foot for SPCS 83 and 27
Thank you.

## Slide 46
Mahalo!
Questions? Comments?