## Slide 1
Regional Reference Frames for North America Current Status & Future Plans of Regional Sub-Commission SC1.3c
Dan Roman U.S. National Geodetic Survey
Michael Craymer
Canadian Geodetic Survey
Reference Frames for Applications in Geosciences (REFAG) COSPAR 2018 Scientific Assembly
Pasadena USA, July 14-22, 2018

## Slide 2: Outline
Regional Subcommission objectives
WG1 – North American Reference Frame
WG2 – New Plate-Fixed North American Reference Frame
WG3 – Reference Frame Transformations
Other activities

## Slide 3: Objectives
Provide international focus and cooperation for issues involving the horizontal, vertical and three dimensional geodetic networks of North America, including Greenland, Mexico and the Caribbean
Co-Chairs
  Mike Craymer, Canada
  Dan Roman, USA (replaced Neil Weston in 2015)
Working Groups
  SC1.3cWG1 – North American Reference Frame (NAREF)
  SC1.3cWG2 – New Plate-Fixed North American Reference Frame
  SC1.3cWG3 – Reference Frame Transformations

## Slide 4: WG1 – NAREF
Objective
  Densify the ITRF/IGS global reference frame in North America
  Compute weekly coordinate solutions
  Combine weekly solutions into multi-year cumulative solutions
  Integrate into ITRF via the IGS global network
  Include all public continuous GPS sites in N.A. (4500+ stations)
  Follow IGS processing guidelines
    Current IGS reference frame
    IGS orbits and EOPs
    Current absolute antenna phase center models
Products
  Weekly coordinate solutions (combinations of regional solutions)
  Periodic multi-year cumulative (velocity) solutions

## Slide 5: Regional Solutions – Canada
Network of all public GNSS stations in northern half of N.A.
  ~900 active stations & ~230 passive stations (high campaign)
  Many new stations added to densify the ITRF – see map next slide
  Mainly in targeted areas for monitoring GIA and tectonic motion
  Considering adding ~1000 commercial RTK networks in Canada
Producing weekly coordinate solutions since 2000
  Bernese GNSS Software 5.2
  IGS final orbits (current & repro2) and antenna calibrations
  Aligned to IGS14 with global IGS core stations
Producing cumulative solutions from weekly solutions
  Multi-year solutions for coordinates & velocities updated monthly with new data and stations
  Able to simultaneously estimate seasonal & post-seismic terms

## Slide 6
Active & Passive Networks

## Slide 7
Canadian NAD83
Horizontal Velocity Field

## Slide 8
Canadian NAD83
Vertical Velocity Field

## Slide 9: Regional Solutions – United States
Network of all public GNSS stations (CORS)
  ~2500 CORS stations
  Covers continental US, Mexico, Hawaii and US territories in Caribbean, American Samoa, Guam & Marianas – see map
Weekly coordinate solutions
  Reprocessing all data with PAGES software
  IGS final orbits (current & repro2) and latest antenna calibrations
  Aligning to IGS14 with global IGS core stations
Multi-year solution
  Last solution from 2011
  New solution from reprocessing results by end of year
  Using recent version of CATREF

## Slide 10
CORS Network
CORS Network

## Slide 11: NGS Multi-Year IGS08 Solution from 2011

## Slide 12: Future Plans
US repro2 processing
  Currently in internal testing; public release planned for September
Position & velocity discontinuities
  Determine a common set of position & velocity discontinuities for US & Canadian multi-year solutions
Commercial RTK networks in Canada
  Densify sparse active network with commercial RTK stations
  Already processing commercial RTK data for RTK compliance agreements
  Currently investigating stability of sites
Foundation CORS
  US National Assets to densify IGS network to meet operational needs

## Slide 13: Foundation CORS Requirements
Baseline Foundation CORS Network
Collocation:
All sites within the Foundation CORS target area of the United States, with existing space geodetic techniques (SLR, VLBI or DORIS), will have a collocated Foundation CORS.
  Additional Desired Foundation CORS Network Requirements
  Density: Install or adopt new stations within the Foundation CORS target area of the United States. (Fulfill the spacing criteria of 800 kilometers within the Foundation CORS target area.)
  Plate Rotation (Euler Pole): Install or adopt new stations within the U.S. Foundation CORS target area to raise the minimum number of Foundation CORS to three on each of the four plates of interest, once the above criteria are met.
  Additional (Gap Filling): Install or adopt new stations, on a case-by-case basis, once the above criteria is met (*).

## Slide 14: Collocated w/ NASA Spaced-Based Technology
DORIS = Doppler Orbitography and Radiopositioning Integrated by Satellite
SLR = Satellite Laser Ranging
VLBI = Very Long Baseline Interferometry

## Slide 15: Collocated + Density + Plate Rotation + Additional

## Slide 16: WG2 – Plate-Fixed N.A. Reference Frame
Problems with NAD83
  Offset ~2 m from geocentre (ITRF)
  Defined by transformation from ITRF but biased by 2 mm/yr
Objective
  Establish a new high-accuracy, geocentric reference frame, including velocity models, procedures and transformations, tied to the North American tectonic plate
  Establish similar frames for US territories in Caribbean & Pacific
  Determine intra-frame velocity models (grids) for each frame to enable propagating coordinates to different reference epochs
  Replace NAD83 & US vertical datum by 2022

## Slide 17: Current Progress
Published “blueprint” documents
  Defines implementation of new reference systems
  Part 1 on geometric and Part 2 on vertical
Reference frame definition
  Will use latest ITRF in 2022 at some adopted reference epoch
  Will estimate plate motion via Euler pole rotation to keep frames aligned to plates
Defined names of new reference frames for North America & other US territories
  NATRF2022 – North American Terrestrial Reference Frame
  CATRF2022 – Caribbean Terrestrial Reference Frame
  PATRF2022 – Pacific Terrestrial Reference Frame
  MATRF2022 – Marianas Terrestrial Reference Frame

## Slide 18: Current Progress – cont’d
US Foundation CORS
  Creating a network of ~36 highly stable CORS sites
  Densifies IGS network and provides a more stable network to define the new frames in US territories
  NGS either owns/operates or has MOAs with other US Agencies
  First site installed in Miami
Outreach efforts
  Public US Federal Geospatial Summits held in 2010, 2015 & 2017
  AGU 2016 Fall Meeting session on new reference frames
  WG2 workshop held at CGU 2018 Annual meeting in June
    Discussed different methods of determining Euler pole rotation
  AGU 2018 Fall Meeting session on new reference frames planned

## Slide 19: WG3 – Reference Frame Transformations
Objectives
  To determine consistent relationships between international, regional and national reference frames/datums in North America
  Maintain and update these relationships
  Provide tools for implementing the transformations
  Primarily involves maintaining the adopted relationship between ITRF and NAD83
NAD83 – ITRF Transformation
  NAD83 is now defined by a transformation from ITRF96
  Transformation is incrementally updated to new ITRF’s using adopted IERS transformations between ITRF realizations
  NNR-NUVEL-1A is used to keep the frame fixed to N.A.
  Updated transformation to ITRF2014

## Slide 20: WG3 – Reference Frame Transformations
Transforming NAD83 coordinates between epochs in Canada
  Required to propagate coordinates to a common reference epoch
    Different provinces in Canada use different reference epochs
  Using model (grid) of 3D crustal velocities interpolated from GPS velocity field in NAD83
  Using a “hybrid” vertical grid derived from GIA models constrained to the GPS velocity field (remove, compute, restore method)
  Estimates of uncertainties of velocity model also provided and used to target weak areas for new GNSS stations
Intra-frame velocity/deformation models will be determined for new reference frames in 2022
  These deformation models will replace HTDP in US
  Investigating different methods of determining deformation models

## Slide 21
NAD83 Vertical Velocity Model for Canada

## Slide 22
NAD83 Vertical Velocity Model Uncertainty Estimates
Uncertainties largest in areas with little or no GPS stations
New station installed in 2017
New stations planned in 2018 & 2019

## Slide 23: Other N.A. Activities
Commercial RTK network certification in Canada
  Commercial RTK networks (RTNs) effectively acting as access points to NAD83 for many users
  Problem – RTNs integrated into different realizations of NAD83 and in inconsistent ways
  Canada (CGS) has implemented “compliance” agreements with 4 largest RTN service providers
    Providing official NAD83 coordinates for all RTN stations (~1000 stations)
    Monitoring stations using weekly coordinate solutions – time series publicly available online
    Classifying stations as non-compliant when weekly coordinates differ from official values by defined tolerance (2 cm horz, 3 cm vert)

## Slide 24
Commercial RTK Networks in Canada
Commercial RTNs significantly densify public network in the Prairies

## Slide 25: Other N.A. Activities – cont’d
Commercial RTK networks in United States
  US (NGS) has no plans to certify RTNs in United States
  RTN users validate RTN services by comparing RTN positions of known geodetic markers to published positions or OPUS-Share solutions
  Developing alignment/tracking tool for RTNs and other private CORS networks

## Slide 26: Other N.A. Activities – cont’d
Existing CORS
Initiative to enhance geodetic infrastructure in Canada
  General areas of discussion for PNT initiative:
  Densification of CORS, more real-time, perhaps in partnership with industry/provincial governments
  Greater GGOS contribution
  Improved real-time PPP availability
  Resilience through integrity monitoring
  Consideration of non-geodetic uses of GNSS data (e.g., meteorology)

## Slide 27: Other N.A. Activities – cont’d
Initiative to enhance geodetic infrastructure in Canada
  General areas of discussion for PNT initiative:
  Densification of CORS, more real-time, perhaps in partnership with industry/provincial governments
  Greater GGOS contribution
  Improved real-time PPP availability
  Resilience through integrity monitoring
  Consideration of non-geodetic uses of GNSS data (e.g., meteorology)
Proposed densification

## Slide 28: Other N.A. Activities – cont’d
International Coordination
  SIRGAS
    Focus is by definition on all of the Americas
    US is now member of SIRGAS
    Coordination between IAG 1.3b and 1.3c
  UN-GGIM-Americas
    WG 3 on Geospatial Data Infrastructure
    Oversight of SIRGAS activities proposed
    Consistent with EUREF and UN-GGIM-Europe
  UN-GGIM-Asia/Pacific
    WG 1 on Reference Frames
    Aligned with APREF
    US joining in support of PATRF and MATRF development

## Slide 29
Questions?

## Slide 30: Why Update the US NSRS?
NAD83 issues
NAVD 88 issues

## Slide 31: NAPGD2022
Mutual consistency of heights, gravity, etc.
Time dependent coordinates
Geoid definition decoupled from GMSL
Orthometric heights defined by GNSS & geoid heights

## Slide 32: Definitional Relationship
Time-dependencies of ellipsoid heights
come from OPUS, where time-dependent
CORS coordinates serve as control for
your time-dependent GNSS survey.
Time-dependencies of geoid undulations
are captured in the dynamic component
of GEOID2022 (“DGEOID2022”), which
will come from the geoid monitoring
service, or GeMS.
HNAPGD2022(t) = hITRF2022(t) – NGEOID2022(t)

## Slide 33: Experimental Geoids
Combining most recent satellite, airborne, and terrestrial gravity data to test methods for 2022
Published annually
  Updated with airborne gravity data
  Available on the website
Testing methods
  Blending techniques
  Density
  Terrestrial data improvements
https://beta.ngs.noaa.gov/GEOID/xGEOID18/

## Slide 34: High resolution products
All will be 1 x 1 arcminute grids
All will cover three finite regions of the globe
All will have a static and dynamic component
  Dynamic surface gravity not expected to be ready by 2022
GEOID2022
  Official converter of *TRF2022 ellipsoid heights into NAPGD2022 orthometric heights
DEFLEC2022
  Surface deflections of the vertical in N/S and E/W
GRAV2022
  Surface acceleration of gravity

## Slide 35: The three gridded regions
North American region
¼ of the Earth
Guam/CNMI region
American Samoa region