## Slide 1: The National Spatial Reference System (NSRS) and VDatum
Juliana Blackwell
NOAA National Geodetic Survey Director
Hydrographic Services Review Panel
Portsmouth, NH
September 2017

## Slide 2
outline
The National Spatial Reference System (NSRS)
NSRS Modernization
VDatum
NOAA-S Rainier crew uses GPS to measure the position of an aid to navigation near Ketchikan, AK
(Damian Manda, 2009)
2

## Slide 3
The National Spatial Reference System (NSRS)
A consistent geospatial framework to meet the economic, social, and environmental positioning needs of our Nation.
Foundational elements include:
Latitude • Longitude • Elevation • Gravity • Shoreline Position
+ changes over time
+
+
=
Reliable charts and maps require data from disparate sources and dates to be aligned
3

## Slide 4
The NSRS of Today (simplified)
Primary elements:
Horizontal North American Datum of 1983 - NAD 83(2011) coordinates
Vertical North American Vertical Datum of 1988 - NAVD88 orthometric heights
These elements are geodetic datums that define the shape and size of the earth to enable precise positioning
System based on connections to published passive control
4

## Slide 5
NGS Provides Tools to Access the NSRS
Integrated Database (IDB) of Published Control
Online Positioning User Service (OPUS) Tool Suite
Continuously Operating Reference Stations (CORS)
Coordinate Conversion and Transformation Tools
5

## Slide 6
Supporting GPS Access to NSRS Heights
NGS is refining the gravimetric geoid model with GRAV-D Project
Ellipsoid
Geoid
Topography
Orthometric height ≈ Ellipsoid height (from GPS) - Geoid height
NAVD 88 height ≈ NAD 83 height - GEOID12B height
USGG2012
GEOID12B
A geoid is a surface of constant gravity potential
A geoid model can be used to obtain orthometric heights from GPS-derived ellipsoid heights
The current geoid model for obtaining NAVD 88 heights is GEOID12B
6

## Slide 7
Requirements
CONSISTENCY
CONVENIENCE
Expectations
Semi-CONSTANT Coordinates
COHERENCE with Sea Level
stamped with elevation
NSRS Considerations – The 4 C’s
7

## Slide 8
The NSRS of Tomorrow (2022)
8
Primary elements:
The geometric North American Terrestrial Reference Frame of 2022 (NATRF2022) plus the Caribbean, Pacific, and Mariana plates
The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
New reference system is:
Time-dependent and geocentric
Defined by relationships to a global/international ideal frame
Primarily accessed via GPS technology and a newly refined semi-dynamic geoid model

## Slide 9
NSRS Modernization: Horizontal Change
Seattle, WA
Easting Difference: 0.45 meters
Northing Difference: 1.33 meters
9

## Slide 10
NSRS Modernization: Vertical Change
Vertical offset of more than 1 meter
GEOID12B (NAVD88)
xGEOID17
Updates available online from the New Datums website and Modernization News
https://geodesy.noaa.gov/datums/newdatums/index.shtml
10

## Slide 11
Importance of Vertical Datums to Hydrographic Surveys
Container barge in Bergum, Netherlands (C. Fries, 2011)
Allure of the Seas passes under the Store Belt Bridge, Denmark (October, 2010)
Tianjin passes under the Talmadge Bridge, Georgia (Steve Bisson, 2015)



11

## Slide 12
Orthometric
3 Categories of Vertical Datums
Ellipsoidal
Tidal
Native GPS measurements
Raw Hydrographic Surveys vertically referenced with RTK-GPS
NOAA Bathymetry (MLLW)
USGS
Topography
Raw Lidar
FEMA Flood Insurance Rate Maps
Engineering and Development Site Surveys
Daily and Extreme Water Levels
Shoreline Mapping (MHW) and Regulatory Boundaries at the Coast
12

## Slide 13: Topographic and Bathymetric Reference Datums Differ
?
Ellipsoid
Geoid
MLLW
Bathymetry
Topography
?
13

## Slide 14: VDatum Links Vertical Datums
Ellipsoid
Topography
Topography of Sea Surface (TSS)
MSL
MLLW
Bathymetry
Geoid
14

## Slide 15
Development and Use of VDatum
Mapping the Land-Sea Interface: VDatum converts elevation data (heights and soundings) among different vertical datums
VDatum is a transformation tool developed jointly by:
National Geodetic Survey (NGS)
Office of Coast Survey (OCS)
Center for Operational Oceanographic
Products & Services (CO-OPS)
Bathymetry
Topography
15

## Slide 16: VDatum Website: vdatum.noaa.gov (Version 3.6 Released, May 13, 2016)
https://vdatum.noaa.gov/docs/vdatum.mp4
Available user interfaces:
Online
GUI Download
Command Line
Map of coverage
16

## Slide 17: Surveying on the Ellipsoid: A VDatum Charting Application
MLLW
Height of Ship (measured)
Chart Depth
(computed)
Datum offset known
(VDatum)
Ellipsoid
Advantages:
Decouples tide measurement from survey
Reduces vertical uncertainty from heave, dynamic draft
Depth from Ship (measured)
Sensor offset known
Requires:
Advanced TSS that extends offshore
Validation against existing hydro survey techniques (TCARI)
17

## Slide 18
Future Enhancements to VDatum
New Transformation Roadmap
based on new Gravimetric GEOID2022
GPS on benchmarks Campaign to determine new relationships
Satellite Altimetry/Derived Products to better understand offshore TSS
GPS tide buoys to be utilized for data input and validation
Re-tracked coastal altimetry data to capture nearshore sea surface height signal
Development of Next Generation TSS: (wish list)
18
Incorporation of Spatially-Varying Uncertainty Model

## Slide 19
Thank you. Up next: Part 2 – Water Level Datums
Little Koniuji Island, Alaska.
GPS Base Station in support of NOAA-S Fairweather hydrographic operations (Weston Renound, 2007).
19