## Slide 1: The Role of GNSS in Modern Reference Frames
Jim Ray, NOAA/National Geodetic Survey
GNSS replacing classical methods on non-local scales
  new space-based reference frame paradigm driven by major
  technology advances
GNSS now dominates International Terrestrial Reference
Frame (ITRF) combination
  only technique that gives autonomous user access to global frame
  but some GNSS datum weaknesses remain
Easy user access to reference frame enables many
applications
  example of studying surface pressure loads discussed
China Satellite Navigation Conference, Wuhan, China, 15 May 2013

## Slide 2: Classical Terrestrial Surveys
Since ancient times, positions measured with respect to nearby visible points
  angles & distances allow triangulation
  & trilateration of small networks
  spirit leveling used for relative heights
  simultaneous adjustment of redundant
  observations gave rise to Gauss’
  least-squares method
  accuracies can attain <~1 mm over
  <~1 km distances
Horizontal & vertical components
normally treated separately
  driven by measurement technologies
  & by applications
  horizontal control for property bounds
  vertical control for gravity variations &
  water flow
02

## Slide 3: Classical Survey Components
03
Control Mark
Control Mark
Survey Network
(inter-visible stations)
Theodolites & Total Stations
Angle, Distance &
Height Measurements

## Slide 4: Extension to National Reference Frames
For larger regional/national reference frames
  must aggregate many local survey networks
  not always well connected to each other (especially across oceans)
  gives rise to network distortions, inhomogeneous coverage, &
  variable accuracies
  local survey errors accumulate over distance
  frames not consistent between different authorities
International standards
began in 1875
  Metre Convention led
  to SI physical units
  1884 Conference led to
  Greenwich prime meridian
  for longitudes
  but accurate geocentric
  global frame not possible
  till nearly 100 yr later
04
Main Triangulation (Horizontal) Networks
(early 1980s)

## Slide 5: New Geodetic Paradigm: Technological Elements
 Era of space geodesy! 
New, high-accuracy techniques enabled on global scale:
Digital electronics & computers:
  fast switches
  broadband sampling
  massive data storage
  cross-correlators
  efficient data analysis
Atomic clocks:
  coherent obs >1 s
  accurate short-interval
  timing
  remote synchronization
  simplified modeling
Artificial satellites:
  continental scale
  inter-visibility
  geocenter sensitivity
  forced international
  cooperation for
  global tracking
  interferometry
  phase tracking at cm →
  dm wavelengths
  precise unambiguous
  group delays
  wide station separation
  measure accurate
  geopotential
  allow GNSS positioning
  anywhere, anytime
  eliminate dependence
  on dense ground nets
  absolute geocentric
  positions
  inter-station clock offsets
  estimated in data analysis
  global timekeeping <~1 µs
  accurate data time tags
  Kepler’s 3rd law constrains
  satellite radial dynamics
05

## Slide 6: Brief History of Space Geodetic Techniques (1/3)
Key inventions & early technology development ~1950s
Practical implementation phase
1960s → 1970s
          Satellite Laser Ranging (SLR)
  TRANSIT Doppler
  Very Long Baseline (Radio) Interferometry
  (VLBI)
06

## Slide 7: Brief History of Space Geodetic Techniques (2/3)
Maturation phase 1980s → 1990s
  Doppler Orbitography & Radiopositioning
  by Satellite (DORIS)
  Global Navigation Satellite Systems
  (GNSS):
  · GPS
  · GLONASS
07

## Slide 8: Brief History of Space Geodetic Techniques (3/3)
Expansion & exploitation phase 1990s/2000s →
  new GNSS: · BEIDOU · GALILEO · Regional augmentations
  routine national & international
  services established (e.g., IGS)
  many scientific/geophysical
  networks installed
08
Global Reference Network of
International GNSS Service (IGS)
GEONET displacements after
11 Mar 2011 Tohoku earthquake
Plate Boundary
Observatory (PBO)
in western USA

## Slide 9: Unique Advantages of GNSS
  relatively low user costs (not including GNSS itself)
  service available for anybody, anywhere, anytime
  user can operate autonomously
  inherently designed for real-time operations
  low-accuracy mode via GNSS broadcast open service
  high-accuracy mode via augmentation services (e.g., IGS)
  user positions reach ~1 cm accuracy in post-processing mode (24 hr data)
  real-time positions reach ~1 dm level (absolute geocentric mode)
  differential positions attain sub-cm precision over regional scales
  GNSS networks can serve many objectives simultaneously, e.g.:
  geodynamics, water vapor sensing, ionosphere monitoring,
  geodetic/survey referencing, time transfer, land cover probe, . . .
09

## Slide 10: GNSS Contributions to ITRF
GPS frame dominates International Terrestrial Reference Frame
  latest ITRF realization is 2008
  GPS co-locations link all techniques
  GPS is 60% of all ITRF stations
  (560 out of 934)
  GPS results very homogeneous &
  stable in time
  WRMS accuracy of weekly points:
  dN, dE ~ 1.5 mm; dU ~ 4.5 mm
But GNSS weaknesses remain
  GNSS cannot observe geocenter
  accurately due to parameter correlations
  → so ITRF origin based on SLR (stable at ~0.5 mm/yr)
  GNSS frame scale fixed to ITRF scale to estimate satellite antenna offsets
  → so ITRF scale based on SLR + VLBI (stable at ~0.2 mm/yr)
  GNSS position time series have many breaks due to equipment changes
  draconitic harmonics abound due to orbit-related mismodeling
10
[Z. Altamimi et al., 2011]
Station Position WRMS

## Slide 11: GNSS Contributions to Earth Orientation
GPS dominates daily Polar Motion results since mid-1990s
  due to robust global
  tracking network
  WRMS daily accuracy:
  ~ 30 µas
  equals ~1 mm global shift
  at Earth’s surface
But systematic errors
remain significant
  errors in international model for EOP 12h & 24h tidal variations
  → errors alias into orbital & other parameters
  mismodeling of orbital dynamics (empirical solar radiation pressure)
  → propagates draconitic signals & harmonics
  mishandling of frame rotational stability by Analysis Centers
  non-linear motions at most GNSS stations
  possible instabilities in ITRF realization
Length-of-day (LOD) also measured (but not UT1 or nutations)
11
[Z. Altamimi et al., 2011]
Polar Motion x,y Residuals
PMx: VLBI SLR GPS DORIS
PMy: VLBI SLR GPS DORIS

## Slide 12: GNSS User Access to ITRF
12
IGS Reference Network in ITRF
IGS tracks GNSS globally:
  reference frame of
  ITRF ground stations
  transferred to satellite
  positions & clocks
User tracks GNSS locally:
  reference frame
  transferred to user
  position
Positioning in ITRF using GNSS
  Precise Differential Positioning
  user + other nearby GNSS data
  + precise GNSS orbits (IGS)
  → user relative location
  Absolute Positioning (PPP)
  user data
  + precise GNSS orbits & clocks (IGS)
  → user geocentric (ITRF) location
Two approaches used for frame transfer:

## Slide 13: Merits of Two GNSS Positioning Approaches
13
Precise Differential Positioning
  data analysis is easier due to
  common mode error rejection
  very precise relative positions
  few mm precision, depending on
  distance of reference stations
  easier to implement in real-time
  over regional/local scales
  infrastructure requirements
  adjustable to user application
  user accuracy depends on errors in
  reference positions & data
  best performance requires dense
  ground networks
  not practical over global scales
  many operations are private
  major global infrastructure required,
  both ground network & data analysis
  user data analysis must be highly
  consistent with models used to make
  global orbit & clock products
Disadvantages:
Advantages:
Absolute Positioning (PPP)
  autonomy of operation
  works for anybody, anywhere,
  anytime
  absolute geocentric positions
  daily accuracies: ~4-5 mm N,E
  ~10 mm U

## Slide 14: Example of Crustal Loading Studied with GNSS
Surface mass load displacement time series for all GPS stations
  6-hr NCEP atmosphere model
  12-hr ECCO non-tidal ocean model
  monthly GLDAS surface ice/water, cubic detrended to remove model drift
  all computed for center-of-frame (CF) origin
  sum is linearly detrended & averaged to middle of each GPS week
  load model data from 1998.0 to 2011.0 [courtesy of T. van Dam]
GPS station position time series from 1st IGS reprocessing
  analysis generally consistent with IERS 2010 Conventions
  combined results from up to 11 Analysis Centers
  706 globally distributed stations, each with >100 weeks
  data from 1998.00 to 2011.29
  Helmert alignment (no scale) w.r.t. cumulative solution uses a well-distributed subnetwork to minimize aliasing of local load signals
  care taken to find position/velocity discontinuities
Study dN, dE, dU non-linear residuals (1998.0 – 2011.0)
  bias errors not considered here !
14

## Slide 15: GPS Position Time Series – “Best” Load Fit
Load models most effective in
height for GLSV (Kiev)
  reduce dU scatter by 51%
  reduce annual dU amplitude
  by 73%
  model not effective for dN, dE
  inland continental site
  relatively large atmosphere
  pressure variations
15
GLSV (Kiev)

## Slide 16: GPS Position Time Series – “Worst” Load Fit
Load models least effective in
height for PARC (S. Chile)
  increase dU scatter by 15%
  reduce annual dU amplitude
  by 38%
  model not effective for dN, dE
  coastal site
  atmosphere pressure effects
  damped by nearby oceans
16
PARC (S. Chile)

## Slide 17: GPS Stations With Smallest Height Scatter
17
LAGO (coast)
GLPS (island)
dN & dE scatters (~1 mm) are not the “best” . . .
dU scatters have same WRMS but different characters
possibly related to weaknesses of IB assumption or load models

## Slide 18: (GPS – Load) Comparison Statistics (706 stations)
18
WRMS Changes |  |  |  |  | 
 | median GPS WRMS (mm) | median Load RMS (mm) | median (GPS – Load) WRMS (mm) | median WRMS reduction (%) | % of stations with lower WRMS
dN | 1.4 | 0.5 | 1.3 | 3.8 | 72.0
dE | 1.45 | 0.4 | 1.4 | 1.6 | 62.9
dU | 4.6 | 2.6 | 3.8 | 15.2 | 87.4
Annual Amplitude Changes |  |  |  |  | 
 | median GPS annual (mm) | median Load annual (mm) | median (GPS – Load) annual (mm) | median annual (corr/no corr) ratio | % of stations with lower annual amp
dN | 0.9 | 0.45 | 0.65 | 0.8 | 70.7
dE | 0.8 | 0.4 | 0.7 | 0.9 | 59.3
dU | 3.6 | 2.4 | 1.7 | 0.5 | 87.1
Load corrections are effective to reduce WRMS & annual amps
  for most stations, esp for dU – but less for dN & even less for dE

## Slide 19: (GPS – Load) Comparison Statistics (706 stations)
19
WRMS Changes |  |  |  |  | 
 | median GPS WRMS (mm) | median Load RMS (mm) | median (GPS – Load) WRMS (mm) | median WRMS reduction (%) | % of stations with lower WRMS
dN | 1.4 | 0.5 | 1.3 | 3.8 | 72.0
dE | 1.45 | 0.4 | 1.4 | 1.6 | 62.9
dU | 4.6 | 2.6 | 3.8 | 15.2 | 87.4
Annual Amplitude Changes |  |  |  |  | 
 | median GPS annual (mm) | median Load annual (mm) | median (GPS – Load) annual (mm) | median annual (corr/no corr) ratio | % of stations with lower annual amp
dN | 0.9 | 0.45 | 0.65 | 0.8 | 70.7
dE | 0.8 | 0.4 | 0.7 | 0.9 | 59.3
dU | 3.6 | 2.4 | 1.7 | 0.5 | 87.1
Load corrections are effective to reduce WRMS & annual amp
But most residual variation remains, esp in dN & dE

## Slide 20: IGS Results – dN With/Without Loads
20
dN load corrections have no impact on noise floor assessment
  local site & non-load errors overwhelmingly dominate
A2 : 0.5 0.6
Error Model:
WRMS2 = WRMSo2
+ (Ai * AnnAmpi)2
+ WRMSi2
WRMSo2 = noise floor

## Slide 21: IGS Results – dE With/Without Loads
21
dE load corrections have no impact on noise floor assessment
  local site & non-load errors overwhelmingly dominate
A2 : 0.5 0.6
Error Model:
WRMS2 = WRMSo2
+ (Ai * AnnAmpi)2
+ WRMSi2
WRMSo2 = noise floor

## Slide 22: IGS Results – dU With/Without Loads
22
dU load corrections move results much closer to noise floor
  but local site & non-load errors still dominate
A2 : 0.5 0.6

## Slide 23: IGS Results – dU With/Without Loads
23
A2 : 0.5 0.6
“Best” 2 stations in dU (WRMS = 2.2 mm) are:
  LAGO (S. coast, Portugal) & GLPS (island, Pacific Ocean)
GLPS
LAGO
Error Model:
WRMS2 = WRMSo2
+ (Ai * AnnAmpi)2
+ WRMSi2
WRMSo2 = noise floor

## Slide 24: Decomposition of Weekly GPS Position Errors
24
IGS Error Budget for Weekly Integrations |  |  |  |  |  |  | 
 | WRMSo (mm) |  |  | median Annual Amps (mm) |  | median site WRMSi (mm) | median total WRMS (mm)
 | thermal (via pairs) | models + analysis | total | loads | total |  | 
dN | 0.4 | 0.5 | 0.65 | 0.45 | 0.9 | 1.0 | 1.4
dE | 0.4 | 0.6 | 0.7 | 0.4 | 0.8 | 1.1 | 1.45
dU | 1.3 | 1.7 | 2.2 | 2.4 | 3.6 | 2.9 | 4.6
Infer site WRMSi2 using:
WRMSo2 + (A * AnnAmpi)2 + WRMSi2 = WRMS2
where A2 = 0.6
Noise floor WRMSo & local site errors WRMSi dominate over loads
  esp for N & E components
Non-load GPS annual errors are as large as annual load signals
  unless load models missing ~half of total signal

## Slide 25: Summary of Current GPS Position Errors
Load corrections reduce WRMS & annual amps for most stations
  but most residual variation remains, esp for dN & dE
  implies load models are inaccurate &/or other sources of scatter/error
Station weekly scatter can be decomposed into 3 categories:
  dN dE dU
  global average floor WRMSo (mm) 0.65 0.7 2.2
  median annual amp WRMS (mm) 0.7 0.6 2.8
  (for A2 = 0.6; about half due to loads)
  median local site WRMSi (mm) 1.0 1.1 2.9
  total WRMS (mm) 1.4 1.45 4.6
Harmonics of GPS draconitic period are pervasive
  strong spatial correlations imply a major orbit-related source
  but significant draconitics in close pair differences imply smaller local contributions likely too
  1.04 cpy signal must contribute to observed annual variations but magnitude is unknown
Major non-load technique improvements still badly needed!
25

## Slide 26: Prospects for Future GNSS Evolution
GPS positioning accuracy now in plateau phase
  future progress limited by known or suspected systematic errors :
  • draconitic errors related to orbit modeling
  • errors in IERS subdaily Earth orientation tide model
  • unmodeled thermal expansion of antenna structures & Earth surface
  • multipath errors (esp due to near-field) & antenna environment
  • antenna calibration errors
  • frequent position discontinuities (equipment changes)
New GNSS systems offer hope to reduce some current errors
  different constellation designs & orbital resonances
  some better signal structures (more resistant to multipath)
  but also much greater multi-GNSS complexity (esp inter-system biases)
Major challenges for the future include:
  understanding how best to use multi-GNSS systems together
  much more robust & reliable international infrastructures
  (ground tracking networks & data analysis)
  large reduction in station discontinuities & disruptions
  secure governmental support with strong international cooperation
26

## Slide 27: Thank You!