## Slide 1: A Modernized National Spatial Reference System: How it impacts the Geospatial Community
Connecticut GIS Day 2023
November 15, 2023
Dan Martin
Northeast Regional Geodetic Advisor
Dan.martin@noaa.gov
240-676-4762

## Slide 2
National Spatial Reference System (NSRS)
NGS Mission: To define, maintain & provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social & environmental needs
Consistent National Coordinate System
Latitude/Northing
Longitude/Easting
Height
Scale
Gravity
Orientation
& how these values change with time

## Slide 3: Bottom Line Up Front
If you do geospatial work in the USA…
and you work in the National Spatial Reference System..
every product you’ve ever made…
  every survey…
  every map…
  every lidar point cloud…
  every image…
  every DEM…
  WILL have outdated coordinates on it in the next few years.
  Let’s talk about what this means, why it is happening, and how it will affect things going forward

## Slide 4: GEODETIC DATUMS
  HORIZONTAL
  2 D (Latitude and Longitude) (e.g. NAD 27, NAD 83 (1986))
  VERTICAL
  1 D (Orthometric Height) (e.g. NGVD 29, NAVD 88, Local Tidal)
  GEOMETRIC
  3 D (Latitude, Longitude and Ellipsoid Height)
  Fixed and Stable - Coordinates seldom change
  (e.g. NAD 83 (1996), NAD 83 (2007), NAD 83 (CORS96) NAD 83 (2011))
  also
  4 D (Latitude, Longitude, Ellipsoid Height, Velocities) Coordinates change with time
  (e.g. ITRF00, ITRF08, ITRF14, etc…)

## Slide 5: Horizontal Datums/Coordinates…What do we (you) use in your state?
NAD 27
NAD 83 (Lat-Lon) SPC
  Which one???
    NAD 83 (1986)
    NAD 83 (19xx) - HARN
    NAD 83 (1996) - FBN
    NAD 83 CORS96(2002)
    NAD 83 (NSRS2007)
    NAD 83 (2011) epoch 2010.00
WGS 84
  Which one???
    WGS 84 (1987)
    WGS 84 (G730)
    WGS 84 (G873)
    WGS 84 (G1150)
    WGS 84 (G1674)
    WGS 84 (G1762)
ITRFxx (epoch xxxx)
IGSxx (epoch xxxx)

## Slide 6: Why Modernize the NSRS
NAD 83 is not as geocentric as it could be (approx. 2 m)
  Positioning Professionals don’t see this - Yet
NAD 83 is not well defined with positional velocities
NAVD 88 is realized by passive control (bench marks) most of which have not been re-leveled in at least 40 years.
NAVD 88 does not account for local vertical velocities (subsidence and uplift)
  Post glacial isostatic readjustment (uplift)
  Subsurface fluid withdrawal (subsidence)
  Sediment loading (subsidence)
  Sea level rise (Up to 1.13 ft per 100 years)
    Bridgeport, CT 3.16 mm/yr (0.010 ft/yr) 1964-2022
    Montauk, NY 3.45 mm/yr (0.011 ft/yr) 1947-2022

## Slide 7: Main Benefits of Modernized NSRS
Fast, Accurate, Consistent Elevations Everywhere
Improved Public Safety
  Flood Plain Maps
  Emergency Route Planning
Accurate Positioning
  Autonomous vehicles, BIMs, Smart Cities
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 8: The Future Geometric Frames
Tectonic Plate based
Each Plate is based on the same
densified ITRF model
North America NATRF
Caribbean CATRF
Pacific PATRF
Mariana MATRF
The tectonic plates “fixed” for the
2022 Terrestrial Reference Frames
NATRF2022
PATRF2022
MATRF2022
CATRF2022
Notes: NSRS Modernization Naming Conventions https://geodesy.noaa.gov/datums/newdatums/naming-convention.shtml

## Slide 9: NAPGD2022 Geopotential Datum
North American-Pacific Geopotential Datum of 2022
Models included: Geopotential Deflection Gravity
Geoid
Guam/CNMI
American Samoa
¼ Earth’s Surface
Not a vertical datum, it is more than just heights.
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml
Experimental Geoid Models
https://beta.ngs.noaa.gov/GEOID/xGEOID20/
As noted in the Blueprint 2 document
https://geodesy.noaa.gov/library/pdfs/NOAA_TR_NOS_NGS_0064.pdf
NAPGD2022 will include all of the following
Geopotential Model of 2022 (GM2022) will include:
Static Geopotential model of 2022 (SGM2022)
Dynamic Geopotential model of 2022 (DGM2022)
GEOID2022 will include:
Static Geoid model of 2022 (SGEOID2022)
Dynamic Geoid model of 2022 (DGEOID2022)
DEFLEC2022 will include:
Static Deflection of the Vertical model of 2022 (SDEFLEC2022)
Dynamic Deflection of the Vertical model of 2022 (DDEFLEC2022)
GRAV2022
Static Gravity model of 2022 (SGRAV2022)

## Slide 10: Replacing NAD 83
Develop four "plate-fixed" reference frames
Remove non-geocentricity of NAD 83 (Shift)
Align to ITRF2020 at epoch 2020.00
Remove most of tectonic plate rotation from ITRF2020 via Euler Pole Parameters
(pronounced: “oiler”) (Drift)
Shift and Drift…
Notes: We’ll talk about that ‘plate fixed’ later.
Now wait a minute Jeff, what is the IGS? You just explained the ITRF and told us about that!!
IGS Reference Frame is pretty much equivalent to the ITRF, created by the Intl. GNSS Service, of which NGS is a contributing partner.
The Intl. GNSS Service, let’s take a look at their website for a minute.
-pronounced “oiler” poles

## Slide 11: Shift and Drift
A sudden shift
  Horizontal change: 0.5 to 4 m (1.5 to 13 ft)
  Ellipsoid height change: ±2 m (±6 ft)
  Elevation change: -0.5 to +2 m (-1.5 to +6 ft)
A continuous drift
  Coordinates associated with specific dates
Two components of drift:
  Tectonic plate rotation (easy to model, 2D only)
  All other residual motion (hard to model, 3D)
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 12: Shift: datum changes
~1 to 1.5 meters North America
~2.5 to 4 meters in Pacific
0 to 1.3 meters CONUS
Notes: New Datums What to expect https://geodesy.noaa.gov/datums/newdatums/WhatToExpect.shtml
NGS is not shifting the land, merely shifting the reference surfaces to which we reference the geospatial data to.

## Slide 13: Euler Poles and “Plate-Fixed”
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)
Notes: We say “NATRF2022” is “fixed” to the N.A. Plate, making it a “plate fixed” frame
-the frame is constant to itself, but rotating within ITRF, and moving in a different direction than the other 3 frames

## Slide 14
ITRF – constant frame, rotating plate

## Slide 15: “Plate-Fixed”
NATRF – rotating frame, constant with plate

## Slide 16
ITRF or NATRF – your choice, just use EPP

## Slide 17: Shift and Drift: Summary
Shift
Once, at rollout
Correcting systematic errors in the current datums
Decimeters-to-meters of one-time immediate coordinate changes
Will affect everyone
Drift
Impact will grow as time goes on
Embracing the dynamic planet upon which we live
Centimeters of persistent annual coordinate changes (plus potential meter-level jumps from earthquakes)
Can mostly be ignored or mitigated through NGS’s creation of plate-fixed frames and reference epoch coordinates
When?
Why?
How much?
Who?

## Slide 18
EPP2022 – Euler Pole Parameters – Simple Rotation
  Three parameters: lat, lon, rotation speed
  Horizontal only: just latitude and longitude
  Changes the frame: ITRF2020 + EPP2022 = NATRF2022
  Does not change the epoch
IFDM2022 – Intra-Frame Deformation Model - Complex
  Complex set of parameters
  Residual horizontal motion: all the motion leftover after Euler Pole rotation plus any local/regional motions
  All vertical motion: localized subsidence or uplift
  Changes the epoch
  Does not change the frame: “intra” = on the inside; within

## Slide 19
A survey done Jan 1, 2020
New Survey (same point) done Jan 1, 2030
Position of point in NATRF2022(2030)
Position of point in NATRF2022(2020)
If IFDM = 0, then NATRF2022 (2030) = NATRF2022 (2020)
Position from 2020 survey NATRF2022 (2020)
ITRF2020 (2020)
ITRF2020 (2030)
NATRF2022 (2030)
Epp2022
IFDM 2030-2020
NATRF2022
(2020.0)
fframe
fEpoch
(H)
(V)
Notes: At 2020, ITRF and NATRF are identical. As time goes on the North American plate moves, resulting in new ITRF coordinates at epoch (say 2030) for the same point. If I remove 10 years of plate motion (ITRF velocity) it puts me back where NATRF used to be....EXCEPT, there has been local motion. That is why we call the it NATRF epoch 2030, because it is where NATRF IS in 2030. We now have to apply IFVM to get back to 2020, or any other date relative to NATRF.

## Slide 20: Drift: Plate Tectonics and Velocities
Annual changes to
ITRF2014 coordinates
Notes: All plates are moving and through the constant collection of GNSS data using CORS we can now model where the land is moving. In the center of tectonic plates there is generally motion that can be measured but where plates converge can be thought of as a crunch zone and the modeling has much more uncertainty due to geophysical phenomena.

## Slide 21: Vertical Motion
Subsidence
  Ground fluid withdrawal, sedimentation
Glacial Isostatic Adjustment (GIA)
  Crustal rebound from glaciers (uplift)
Geophysical Phenomena
  Earthquakes, calderas, Earth tides

## Slide 22: Vertical Motion
8.5 meters
50 years
San Joaquin Subsiding
20-24” in 16 months
May 2015
to
Sept 2016
Hudson Bay Uplifting
8 -13 mm/year
Notes: San Joaquin Subsidence article
http://www.digitaljournal.com/tech-and-science/technology/sinking-san-joaquin-valley-of-california-seen-from-space/article/487393
Hudson Bay Uplift article (GIA)
https://www.researchgate.net/figure/Contour-map-of-observed-CBN-vertical-rates-Preliminary-results-from-the-combination-of_fig3_286867540
Photo of San Joaquin Valley Subsidence to 1977
https://lh4.googleusercontent.com/ymKsoXwZEP4rk4F4GqPD5S9FyMO4d0mrfL2GiLI0mXe7djBwYH3t0-OwncYltY8OJNmYk0DKh4pOLqS9DGItCHK3i23maqpjdDDISQH5ux0uqDVbrEnWTnFLPb7Woe2cka61EXC6

## Slide 23: New Types of Coordinates - A two-track approach to coordinates
An estimated “snapshot” of the entire network
Every 5 or 10 years
Similar to NAD 83(2011) epoch 2010.00
Reference Epoch Coordinates
Survey Epoch Coordinates
Answers: what were a mark’s coordinates when it was last surveyed?
Multiple SECs can show changes over time

## Slide 24: State Plane Coordinates

## Slide 25: Best ways to determine coordinates in Modernized NSRS
Resurvey: Return to the field and collect new observations, relying upon geodetic control that has coordinates in the new datum
Readjust: Using existing observations, re-compute new coordinates based upon geodetic control (CORS) that has been defined in the new datum
Transform: Take finished products which have coordinates in the old datum and use transformation software to estimate coordinates in the new datum

## Slide 26: How Can You Prepare
Metadata is essential
    Improves reliability and accuracy of data
    Increases value and usefulness
Transform and collect data in current datums
    NAD 83 (2011), NAVD 88
Make sure to note Geoid Models used for GNSS data

## Slide 27: How to Prepare
Do an inventory of your data
Do you have documents, manuals, contracts, etc…that include language re: datums?
Do you have clients, subcontractors, in-house staff other than survey that need to be educated about the new datums?
Are you going to have to support projects in old datums for a while? What is the plan for that?
Store Data…not just coordinates!
  If you have your original data, it can always be reprocessed later
    Maintains the integrity of your survey
    Better than a transformation

## Slide 28: NGS ArcGIS Online Resources
NGS Datasheets
NOAA CORS Network
GPS on Benchmarks Priority List
(4 layers - marks, hexagons)
GEOID18 GPS on Benchmarks
GEOID12B GPS on Benchmarks
OPUS Shared Solutions
Mark Recoveries Submitted to NGS
Feature Services
Raster Tile Services
GEOID18 Height (CONUS, PRVI)
GEOID18 Difference (CONUS, PRVI)
GEOID18 Uncertainty (CONUS, PRVI)
GEOID18 Improvements (CONUS, PRVI)

## Slide 29: NGS Resources
NGS Training Center
  https://geodesy.noaa.gov/web/science_edu/training/
Educational Videos
  https://geodesy.noaa.gov/datums/newdatums/WatchVideos.shtml
NGS Webinar Series
  https://geodesy.noaa.gov/web/science_edu/webinar_series/
Geospatial Summit (2021, 2019 recorded sessions)
  https://geodesy.noaa.gov/geospatial-summit/
Presentation Library
  https://geodesy.noaa.gov/web/science_edu/presentations_library/

## Slide 30: Importance of Coordination
39 Coordinators
14 Advisors
(1 vacant)
Notes: NGS Regional Geodetic Advisors
https://geodesy.noaa.gov/ADVISORS/
State Geodetic Coordinators
https://geodesy.noaa.gov/ADVISORS/state-geodetic-coordinators.shtml

## Slide 31: Questions?
Dan Martin
Northeast Regional Geodetic Advisor
ME, NH, VT, MA, CT, RI, NY, NJ
Dan.martin@noaa.gov
240-676-4762