## Slide 1: NSRS Modernization Update
Dru Smith | NSRS Modernization Manager
November 2016

## Slide 2: Introduction: About the NSRS

## Slide 3: Overview
The NSRS (National Spatial Reference System) is the official coordinate system for all geospatial work done by the non-military federal government
  NAD 83 (latitude, longitude, ellipsoid height)
  NAVD 88 (orthometric height)
  IGLD 85 (dynamic heights: predominantly on the Great Lakes)
These datums are often adopted, even legislated, by states, counties and municipalities

## Slide 4: Federal Users of the NSRS

## Slide 5: Why modernize?
Older Methodology
  Terrestrial, pre-space-geodesy, line-of-sight observations
  Easily destroyed, unmonitored passive control marks
PID: EZ0840

## Slide 6: Why modernize?
Evidence of systematic errors
  Decades of space geodetic observations
    All of the datums contain systematic errors (decimeters to meters)
      At scales larger than today’s accuracy capabilities (centimeters)
  Origin (center of Earth) Offset: 2+ meters
  Zero elevation Surface: 0.5 to 2+ meters

## Slide 7: What’s Being Replaced
What’s being replaced:
Horizontal Vertical
  NAD 83(2011)
  NAD 83(PA11)
  NAD 83(MA11)
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
Latitude
Longitude
Ellipsoid Height
State Plane Coordinates
Heights

## Slide 8: Details: Ten Year Plan
5 Goals:
Support the users of the National Spatial Reference System.
Modernize and improve the National Spatial Reference System.
Expand the National Spatial Reference System stakeholder base through partnerships, education, and outreach.
Develop and enable a workforce with a supportive environment.
Improve organizational and administrative functionality.

## Slide 9: Nomenclature

## Slide 10: Nomenclature
A chance to increase accuracy in naming!
  “North American”?
    Ignores Guam, Hawaii, American Samoa, Northern Mariana Islands
  Datum vs Reference Frame?
  Plate-specific?
  Vertical vs Geopotential?
6/8/2016: NGS and the Canadian Geodetic Survey negotiated a naming proposal
  Approved by NGS ESC
  Approved by the CGS leadership (with minor reservations)
  Awaiting final word from INEGI as of 10/26/2016….

## Slide 11: Objective 1 of 5: Replace NAD 83

## Slide 12: Replace NAD 83
~2.24 m
NAD 83 origin
“2022” origin
Earth’s Surface
hNAD83
h”2022”
Simplified Concept of NAD 83 vs. “2022”
fNAD83 – f”2022”
lNAD83 – l”2022”
hNAD83 – h”2022”
all vary
smoothly by latitude
and longitude

## Slide 13: Ellipsoid Height Shifts
Approximate
  IGS08(GRS-80) minus NAD 83(2011)

## Slide 14: Horizontal Shifts
Approximate
  IGS08(GRS-80) minus NAD 83(2011)
Lat:
Lon:

## Slide 15: Replace NAD 83
Access and definition
Primary: CORS
  Continuous monitoring
  OPUS
  IGS coordinates
    Transformable to any national reference frame chosen for 2022
  Static Surveys
  RTK/RTN
    Validation service
Secondary: Passive
  Time-tagged coordinates
  Will reflect each occupation of the mark
  Will generally not be accepted as “fixed control” in surveys turned in to NGS

## Slide 16: Definition of new frames
“Plate fixed +” … announcement coming soon
Deformational velocities will be modeled separately
Plate rotations will tie the new terrestrial reference frames of 2022 to the IGS frame

## Slide 17: Time Dependencies
Track cors and always know where you are
Surveying to CORS positions at survey epoch
  If we track CORS, we can do this easily
Tectonic rotations
  Easily removed for a “good east of the Rockies” solution
    Lat/Lon only
Residual deformations
  Can be modeled many ways and provided for cross-epoch checking between surveys
    3-D

## Slide 18: Objective 2 of 5: Replace NAVD 88

## Slide 19: Replace NAVD 88
H
Earth’s
Surface
The Geoid
NAVD 88 reference level
H (NAVD 88)
Errors in NAVD 88 : ~50 cm average, 100 cm CONUS tilt,
1-2 meters average in Alaska, NO tracking

## Slide 20: Replace NAVD 88
Changing from a leveling-based to a geoid/GNSS-based vertical datum
Biggest requirement: An updated,
accurate, nationwide gravity survey
  Airborne
  GRAV-D!
    Gravity for the Redefinition of the
    American Vertical Datum

## Slide 21: GRAV-D Coverage
Hawaii
Alaska
“CONUS”
Puerto Rico / Virgin Islands
Guam / Northern Marianas
American Samoa

## Slide 22: GRAV-D Status
50% mark hit in FY2016
  FY2017 target: 62%
Two planes at a time
  Occasionally three
Mix of Government and Private Industry Flights
100% by 2022

## Slide 23: Orthometric Heights
Approximate EXPECTED SHIFTS
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface:
  Does not include local subsidence issues

## Slide 24: Time Dependencies
Geoid changes cause height changes
The zero elevation surface will change with time
Heights will be time tagged to respect:
  Geoid change
  Subsidence

## Slide 25: Objective 3 of 5: Re-invent Bluebooking

## Slide 26: Bluebooking
background
Refers to the blue cover of Input Formats and Specifications of the National Geodetic Survey Data Base
  The requirements for turning in a geodetic survey to NGS
  Very DOS/FORTRAN heavy
  Horizontal (angles, distances) vertical (leveling) and gravity
    GPS surveys were force-fitted into the horizontal rules
Reputation: “Cumbersome”
  To be fair: All industry standards are cumbersome – it prevents chaos

## Slide 27: OPUS-Projects
Or “bluebooking for the 21st century”
The 2013 Survey of the
Washington Monument
had GPS, leveling and
traverse components.
An integrated OP might
allow for easier
processing and especially
cross-processing

## Slide 28: OPUS-Projects
Or “bluebooking for the 21st century”

## Slide 29: New Database
Replacing the NGS IDB
NGS IDB (“Integrated Database”)
  Current official repository of some (most?) NSRS data
  “Integrated”…2 old DBs:
    Hor / Ver
  Built for
    Passive Control
    No time dependencies
    Line of sight techniques
    Points
NSRS DB
  Being built (target: 2020)
  “Spatial” database
  Time tags for everything
  Open design for any type of data
  Things that couldn’t go into the IDB, but can go in the NSRS DB:
    Lines of airborne gravity
    LIDAR clouds
    CORS
    Superconducting Gravimeter data
    etc

## Slide 30: Objective 4 of 5: Improve the Toolkit

## Slide 31: NGS Toolkit
background
A set of (mostly FORTRAN based) geodetic tools
Little integration
Many with no online capability
No web services

## Slide 32: New Toolkit
http://beta.ngs.noaa.gov/gtkweb/
Convert to/from lat & lon
  State Plane Coordinates
  UTM
  US National Grid
Upload file of points
Web Service
Download and run offline

## Slide 33: NADCON 5
Expected in beta toolkit In december 2016
Replacing NADCON 4.2 and GEOCON 2.0
Support for nearly all horizontal datums since 1897
  Exceptions: Regional Alaska
No “state by state” grids
Fixing all existing bugs
Web Service
Consistent
Documented
Rigorous Location-Dependent Error Estimates
Ready to support 2022

## Slide 34: NADCON 5 example
USSD / NAD 27

## Slide 35: NADCON 5 example
Transformation shown in meters but actually performed in arcseconds

## Slide 36: NADCON 5 example
Errors are no longer generalized (e.g. “15 cm in CONUS”)

## Slide 37: Toolkit Future
The entire ngs toolkit will be integrated eventually
VERTCON 3.0
HTDP
VDatum
All other tools

## Slide 38: Objective 5 of 5: Better Surveying

## Slide 39: Better Surveying
overview
A focus on updating technology and field procedures
Field research
New Manuals
1981
1997
2008

## Slide 40: Better Surveying
Upcoming project
The role of leveling in a vertical datum defined by a gravimetric geoid and accessed by GNSS
  Acknowledging that leveling can not yield absolute heights
  Combining GPS and leveling observations
    New adjustment model
    New software (see earlier OPUS-Projects slides!)

## Slide 41: Summary

## Slide 42: Summary
Nsrs modernization
More than just replacing NAD 83 and NAVD 88
Affects most tools, products and services of NGS
Dozens of interdependent multi-year projects ongoing
Expect rollouts and announcements throughout the next 6 years!

## Slide 43: To learn more
New Datums Web Page
geodesy.noaa.gov/datums/newdatums/index.shtml

## Slide 44: To learn more
Attend the Geospatial Summit
Silver Spring, MD
April 24-25, 2017
FREE
geodesy.noaa.gov/geospatial-summit/index.shtml

## Slide 45: Questions?
THANK YOU!