## Slide 1
State Plane Coordinate System
Michael Dennis, PhD, PE, RLS
SPCS2022 Project Manager
michael.dennis@noaa.gov
2021 NSRS Modernization Geospatial Summit
May 5, 2021

## Slide 2: Alternative Earth models exist…

## Slide 3: A “flat earth” for the future
State Plane Coordinate System of 2022 (SPCS2022)
  Referenced to 2022 Terrestrial Reference Frames
  Based on same reference ellipsoid as SPCS 83 (GRS 80)
  Same 3 conformal projection types as SPCS 83 and 27:
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 4: SPCS 83 and 27
State Plane Coordinate Systems of 1927 (134 zones) and 1983 (125 zones)
The shape of things to come for SPCS2022

## Slide 5: Getting acquainted with SPCS2022
Distortion design philosophy
  Linear distortion minimized at topographic surface (not at ellipsoid surface)
  Purpose: to reduce difference between and projected “grid” and actual “ground” distances
Other things:
  Zone “layers”
  Status of zone designs
  The timing of it all…
Notes: Will go over main general characteristics of SPCS2022 (not enough time to go into detail)
  This is based on final SPCS2022 Policy & Procedures (not yet published but most decisions have been made on content)
  Final policy & procedures created based in part on public response to the FRN
A key element of SPCS2022 is linear distortion (“scale error”) design requirements
  Linear distortion is the difference between a “grid” distance (between the projected coordinates of a pair of points) and the true horizontal “ground” distance (at the topographic surface of the Earth)
  SPC2022 zones are designed to minimize linear distortion at the topographic surface, NOT at the ellipsoid surface (as was done for SPCS 83 and 27)
Other relevant characteristics are listed; each will be discussed in this presentation

## Slide 6
Map projection linear distortion
Ellipsoid surface (~“sea level”)
Topographic surface
Grid (“map”) distance
Projection surface
Horizontal ground distance
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
Grid distance < ground distance
Map projection designed to minimize linear distortion on ellipsoid (at “sea level”)

## Slide 7
Map projection linear distortion
Projection surface
Map projection designed to minimize linear distortion at ground surface
Topographic surface
This design approach is being used for SPCS2022 (minimizes distortion with respect to topography)
Ellipsoid surface (~“sea level”)
Grid distance ≈ ground distance

## Slide 8: SPCS2022 “layers” and designs
Max of up to 3 zone “layers” allowed
  One must be statewide zone
  Most states will have total of 2 layers
NGS designs:
  Statewide zone for every state
  Multiple zones not designed by stakeholders
Many states made requests and proposals
  Requests for zones designed by NGS
  Proposals for zones designed by stakeholders

## Slide 9: Status of zone layout and designs
One layer (statewide): 18 states and territories
  Includes combined territories sharing 1 zone
    Puerto Rico and U.S. Virgin Islands
    Guam and Commonwealth Northern Mariana Islands
Two zone layers: 28 states
Three zone layers: 10 states
NOTE: Zones within a layer cannot overlap

## Slide 10: Maps of all SPCS2022 layers
State Plane Coordinate System of 2022 (940 zones in 56 states and territories)

## Slide 11: Maps of number of layers

## Slide 12: Status of zone layout and designs
Designs by NGS
  159 zones (including 54 statewide)
  Range from 1 to 22 zones per state (max in Alaska)
Designs by state stakeholders
  810 zones in 28 states
  Range from 1 to 88 zones per layer (max in Ohio)
  Essentially all are “low distortion projections”
Total = 969 zones for 56 states and territories
  Number may decrease, but will not increase

## Slide 13: Map number of zones

## Slide 14: SPCS2022 zone designs
All designs so far are PRELIMARY
Begin finalizing designs NOW
  Compile and compare all designs
  Ensure consistent and correct
Get stakeholder input before finalizing
  Provide preliminary complete parameters
  Solicit input from stakeholders 2021/2022
  Finalize after stakeholder input

## Slide 15: About the timing of it all…
Finalize all designs in 2022 (maybe later…)
Other things in 2022 (maybe later…)
  Provide machine-readable definitions
  SPCS2022 report
  Modify NGS algorithms (e.g., 1-parallel Lambert)
Official release with rollout of modernized NSRS
  Final definitions available in 2022 (maybe later…)
  But will not release before modernized NSRS
  Likely after 2025…

## Slide 16: But I want to use SPCS2022 now!

## Slide 17: But I want to use SPCS2022 now!
Some want to use designs with NAD 83
  Same reference ellipsoid
  Near identical performance
Can reference to NAD 83, however:
  Will not become part of SPCS 83
  Will not be supported in NGS products & services
If you use designs with NAD 83:
  Change grid origins by large amount
  Will help avoid confusion with SPCS2022 version

## Slide 18: SPCS2022 summary
Minimize distortion at topo surface, not ellipsoid
Up to 3 zone “layers” allowed
  Some layers very similar to existing SPCS 83
  Some layers very different
Total 969 zone for initial rollout of SPCS2022
  NGS: 159 zones (includes 54 statewide)
  Stakeholders: 810 zones in 28 states
  Number of zones may decrease, will not increase
Will be implemented along with Modernized NSRS
  Earlier usage with NAD 83 will not be supported by NGS
  Can change/add/remove zones after modernized NSRS