## Slide 1: NGS Heights Suppression in Southeast Texas
Boris Kanazir, Geodesist, RPLS
boris.kanazir@noaa.gov
Virtual Workshop
November 19, 2020

## Slide 2: Outline
Modernized NSRS
Texas Control Issues
Heights Suppression
Tools to Densify Geodetic Control Network
  OPUS Projects
  OPUS Projects for RTK
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 3: Decision to Modernize
In 2007 NGS announced its decision to completely change how it approached its mission.
In a word, they chose to modernize the NSRS
Let’s look at the issues that drove that decision, and the direction they decided to go
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 4: Issues
NAVD 88 suffers from use of passive control that:
Is almost never re-checked for movement
Disappears by the thousands every year
Is not funded for replacement
Is not necessarily in convenient places
Doesn’t exist in most of Alaska
Wasn’t adopted in Canada
Was determined by leveling from a single point, allowing the build up of cross-country error
PID: EZ0840
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 5: Issues
House
BM
House
BM
By way of example…
1954: Leveling Performed to bench mark
1991: Original 1954 leveling data is used to compute the NAVD 88 height which is then published for this BM
Obviously the true height relative to the NAVD 88
zero surface is not the published NAVD 88 height
H88(published)
H88(true)
NAVD 88 zero height surface
NAVD 88 suffers from unknown movements before, during and after its original adjustment
1954-1991: Subsidence
House
BM
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 6: Issues
NAVD 88 suffers from a known bias (50 cm) and tilt (about 1 meter across CONUS) relative to the gravimetric geoid
PID: EZ0840
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 7: Issues
~2.24 m
NAD 83 origin
ITRF origin
Earth’s Surface
hNAD83
hITRF
NAD 83 suffers from a 2+ meter non-geocentricity (which misaligns it with ITRF and all GNSS orbits)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 8: Issues
Geodetic control is usually affixed to a crust that is moving
  Even so-called “plate fixed” frames are only as stable as:
    The rigidity of a plate
    The complete lack of subsidence or uplift
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 9: General Direction
Future details would come, but in 2007 the general direction was:
  Replace both NAD 83 and NAVD 88, at the same time
  Transition to a geoid-based vertical datum
  Leverage the rise of GNSS and RTNs
  Completely re-invent “bluebooking”
    Reduce complexity
    Retain ability to standardize geodetic survey files
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 10
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
Sep 2017
NOAA TR NOS NGS 62
32 pages
Geopotential:
Nov 2017
NOAA TR NOS NGS 64
41 pages
Working in the
Modernized NSRS:
April 2019
NOAA TR NOS NGS 67
77 pages
All three documents are being updated and re-released in 2020!!
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 11: Replacing the NAD 83s
The Old | The New
NAD 83 (2011) | NATRF2022 - The North American Terrestrial Reference Frame of 2022
NAD 83 (2011) | CATRF2022 - The Caribbean Terrestrial Reference Frame of 2022
NAD 83 (PA11) | PATRF2022 - The Pacific Terrestrial Reference Frame of 2022
NAD 83 (MA11) | MATRF2022 - The Mariana Terrestrial Reference Frame of 2022
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 12
Four Tectonic Plates
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 13: The TRFs
All are global frames (no “boundary”)
  This was true for the NAD 83s also, BTW
  But each frame will rotate with one tectonic plate
    Put another way: “The frame rotates so your coordinates don’t have to”
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 14
ITRF2020: Constant Frame, Rotating Plate
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 15: “Plate-Fixed”
NATRF2020: Constant Frame, Rotating Plate
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 16
ITRF2020 or NATRF2022 — Your choice, just use EPP2022
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 17: Shift and Drift
When transitioning off of NAD 83, your coordinates will experience shift and drift
  Shift: A one-time jump somewhere in the 0 to 4 meter range (latitude, longitude, ellipsoid height)
    From fixing NAD 83’s non-geocentricity
  Drift: Coordinates are now time-dependent. The shift will take you to 2020.00. Working at any other epoch means you must account for the drift (velocity) of your coordinates
    As well as any other motions over time
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 18: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 19: Shift and Drift
When transitioning from NAVD 88 or another vertical datum, your coordinates will shift and drift:
  Shift: A one-time jump somewhere in the 0 to 2 meter range (orthometric height)
    From fixing biases and/or tilts in NAVD 88 and others
  Drift: Coordinates are now time-dependent. The shift will take you to 2020.00. Working at any other epoch means you must account for the drift (velocity) of your coordinates
    As well as any other motions over time
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 20: NAVD 88 (epoch ?) to NAPGD2022 Epoch 2020.00 (estimate)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 21: GEOID18 Estimated Uncertainty
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 22: GEOID18 Gulf Coast Selected Marks
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 23: GPS on BM in Texas
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 24: GPS on BM in Texas
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 25: GPS on BM in Houston-Galveston
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 26: GEOID18 Post Modeled Residuals
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 27: Houston Case
Harris County Floodplain Reference Marks and Flood Insurance Rate Maps (FIRMs) are referenced to locally defined NAVD88 2001 elevations (not published by NGS)
Elevation errors and outdated maps could have a major effect on flood zones determination and flood risk assessment
This highlights the reasons for and the importance of NGS’ shift to time-dependent positioning in the NSRS Modernization in 2022
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 28: Good published heights in the SE Texas
The box includes approximately 7,500 marks in the NGS database
More than 4,000 heights created by VERTCON (Vertical Datum Conversion) = suspect heights!
Only 28 marks out of 7,500 in this box are considered to have good heights!
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 29: Good heights in the US - 30 km buffer
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 30: History of Leveling in the U.S.
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 31: What NGS did about it
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 32: What NGS did about it
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 33: What NGS is doing about it now
Plan by end of January 2021:
  Valid NAVD 88 heights will be published
    only 28 marks (until new surveys are completed) will remain published in Current Survey Control section
  Suspect NAVD 88 heights will get suppressed
    Current Survey Control will not show NAVD 88 height
    If requested, NAVD 88 height will be shown in Superseded Survey Control section
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 34: Valid NAVD 88 Heights
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 35: Suspect NAVD 88 heights (not requested)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 36: Suspect NAVD 88 heights (requested)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 37: Suspect NAVD 88 heights (requested)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 38: Suspect NAVD 88 heights (requested)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 39: Suspect NAVD 88 heights (requested)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 40: Suspect NAVD 88 heights (requested)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 41: Suspect NAVD 88 heights (requested)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 42: What can Texas do about it?
Densify geodetic control (with good heights) by conducting new Leveling & GPS projects
  Submit data for inclusion into the NSRS (FCGS Bluebook)
  Update elevations on a select set of marks (where good heights don’t exist)
  Improved survey network will provide enhancements for rebuilding and improvement of infrastructure in the area
  It will help with flood plain management, flood hazard identification and risk assessment, elevation certificates…
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 43: How can NGS support these efforts?
NGS can provide:
  Trainings
  Technical support
  Projects QA/QC
  Analyzing, ingesting and storing new data
  Online tools to access the NSRS
NGS cannot conduct field work for you!
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 44: What tools can Texas use?
BETA OPUS Projects - New way of Bluebooking!
  Makes bluebooking process easier and less intimidating
  Provides an interactive visual interface
  Automates the processing and creation of complex files
  Provides improved QA/QC process and better display & visualization of statistics
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 45: What tools can Texas use?
BETA OPUS Projects
  It requires minimum of two 2-hours sessions for your stations
  It is used for submitting static, campaign-style GNSS surveys resulting in network survey solution intended for inclusion in the NGS database
  New stations will have published adjusted position on a datasheet
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 46: Datasheet and Shared Solution
Geodetic Control
Not Geodetic Control
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 47: Project Objectives
What are your objectives?
Accurate lat/lon/Eh on new “passive marks”
Accurate GNSS-derived NAVD 88 heights on passive marks
Accurate positions on active GNSS stations (not CORS; e.g. RTN stations)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 48: Project Control
Leveled heights (Adjusted and Reset, Orders One - Three)
Height Mod Heights
“HT_MOD”
Height accurate to 2 decimal places
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 49: Planning Your Project
Orthometric Height Accuracy Requirements
Number of occupations
Length of occupations
Spacing of valid control
*Future developments of OP will permit real-time vectors from shorter occupations
Minimum of 2 NAVD 88 control marks per new mark observed
OPUS is currently restricted to a minimum of 2-hour occupations
Maximum distance between new marks and NAVD 88 control is between 30-50 km, based on occupation length
Chart: NAVD 88 Control Spacing (km)
| 30 | 50
 | 2 | 6
Recommended/Permitted
Not Permitted*
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 50: Planning Your Project
Orthometric Height Accuracy Requirements: a look at control mark spacing
Occupy bench marks with “valid” NAVD 88 orthometric heights
  Distributed every ~30-50 km
  Two (2) valid control marks per new mark
  Adhere to distance-occupation requirement
Use latest hybrid geoid model (i.e., GEOID18)
Perform constrained vertical least squares adjustments of the GNSS network holding the bench marks as control
30
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 51: Planning Your Project
How many valid NAVD 88 bench marks would you need at a 30 km spacing?
30
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 52: Planning Your Project
How many valid NAVD 88 bench marks would you need at a 30 km spacing?
6 valid NAVD 88 control marks within 30 km would cover requirements for only three new marks!
30 km spacing require a minimum of only 2-hr occupations
30
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 53: Planning Your Project
50 km radius
Increasing your spacing to 50 km would require only 4 valid NAVD 88 control marks to cover 9 new marks.
Only one mark would require additional control
However, minimum occupation time would increase from 2 to 6 hours
30
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 54: Planning Your Project
Now that we’ve discussed distance (X-axis), let’s talk Occupation Length (Y-axis)
*Future developments of OP will permit real-time vectors from shorter occupations
Chart: NAVD 88 Control Spacing (km)
| 30 | 50
 | 2 | 6
Recommended/Permitted
Not Permitted*
Two important considerations:
Redundancy (how many reps)
Duration (how long an observation)
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 55: OPUS Accuracies
How long should each occupation be?
-A look at OPUS Accuracies
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify
RMS at 1σ

## Slide 56: Occupation Time
Vertical Network Accuracies, OPUS Projects
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify
TOTAL time on mark
95% CI values shown

## Slide 57: Project Recommendation
Summary of Vertical Accuracy of OPUS Projects
Vertical Standard | Total Time on Mark (h) | Recommended Sessions and duration
3.0 cm | 4 | (2) 2-h
2.5 cm | 8 | (2) 4-h or (3) 3-h
2.0 cm | 22 | (2) 10-h or (3) 7-h
1.7 cm | 48 | (2) 24-h
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 58: OPUS Projects for RTK
Builds upon OPUS Projects
It supports all types of GNSS vectors (real-time and post-processed):
  Single-base RTK vectors
  Network RTK vectors
  Vectors processed in other software
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 59: Baseline and Vector
Baseline: the line connecting two GNSS marks
Vector: a mathematical representation of a measurement of the baseline, expressed in delta X,Y,Z components (along with error estimates)
So, one baseline measured repetitively five times will have five vectors
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 60: Design for OPUS-Projects and GVX
GVX file (from RTK survey or baseline processing in other software)
OPUS-Projects (from static GNSS session processing)
RTK Base or “From” Mark
RTK Rover or “To” Mark
Vector
Vector in GVX File
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 61: Example: Upload RTN Vectors to OPUS-Projects
User Mark
Processed Vector (OPUS-Projects)
Uploaded Vector
CORS
LEGEND
Upload Vectors
Modernized NSRS
TX Control Issues
Heights Suppression
Tools to Densify

## Slide 62: Contact your NGS Regional Geodetic Advisor