## Slide 1
A new, comprehensive least-squares adjustment engine for the Modernized NSRS
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
History and motivation for change
Current status
Future work

## Slide 3: History and motivation for change

## Slide 4: A (probably incomplete) history of LSA software at NGS
INERT1 (1982)
HOACOS (1979)
HAVAGO (1979)
ADJUST
GPSCOM/LLSOLV
ASTA
NETSTAT
APOGEE
CALIBRATE
Additionally, LSAs are encompassed within this NGS software tool:
PAGES
Also, there is the following stand-alone set of matrix manipulation subroutines:
Heart Of Gold (1984)

## Slide 5: A (probably incomplete) history of LSA software at NGS
INERT1 (1982) – For Inertial Surveying Systems (NOAA TR NOS 97 NGS 26)
HOACOS (1979) – A precursor to ADJUST (NOAA TM NOS NGS 19 & 25)
HAVAGO (1979) – A precursor to ADJUST for 3-D adjustments (NOAA TM NOS NGS 17)
ADJUST – Initially built for horizontal observation adjustments, but modified over the years to allow for 3-D GPS-based vectors and Height Mod style GPS adjustments. Serves as the primary LSA tool in current “Bluebooking” of GPS projects. Can also be used to adjust “classical” surveying, but hasn’t been used that way, with the exception of the 2013 Washington Monument project, in a decade or more. Works in a DOS environment as an EXE file. Recently enveloped into the OP2IDB project. Initially documented in NOAA TM NOS NGS 47.
GPSCOM/LLSOLV -- Helmert blocking program designed to work with the output of PAGES, and thus as the core of OPUS-Projects (before the OP2IDB project)
ASTA – The leveling adjustment software, used in Bluebooked leveling projects and also the (unnamed) engine behind LOCUS.
NETSTAT – Developed for NGS to perform the NSRS2007 adjustment of GPS vectors, and used again in the 2011 national adjustment of GPS vectors. The primary reason for developing this, rather than relying on ADJUST, was efficiency and Helmert Blocking to handle the tens of thousands of vectors in the national adjustment. Generally unused at NGS with the exception of large national adjustments.
APOGEE – Developed in MATLAB for adjustment of relative gravity surveys, but has no direct connection to the NGS IDB.
CALIBRATE – Used to process data from calibrating an EDMI at a CBL
Additionally, LSAs are encompassed within this NGS software tool:
PAGES – While PAGES is thought of predominantly as a GPS processor, it has inherent LSA functions coded inside of it.
Also, there is the following stand-alone set of matrix manipulation subroutines:
Heart Of Gold (1984) – Sparse matrix package called by ADJUST (NOAA TM NOS NGS 39)

## Slide 6: Concerns: General
Inconsistency
  Different languages, different variable names, and different times lead to inconsistency in code
    Some programs might be perfectly compatible, but it’s difficult to know with such a vast number of authors and code over the years.
Lack of generality
  Code written to adjust only one type of geodetic observation has limited usefulness to other applications
Languages: FORTRAN, C++, MATLAB are all in use today
Scalability

## Slide 7: Concern: Approximations
NGS uses many approximations in our various LSA programs which are less than optimal, relative to more robust approaches
  “Downweighting” of observations rather than mathematical removal of them from the normal equations
  “Upweighting” of constraints rather than using the fixed constraint equation
  “Hold a mark fixed/minimally constrained adjustment” instead of a true “inner constraint” adjustment
  Many others…

## Slide 8: Solution
Start from first principles and develop an entirely new LSA code library
  C++
  Generalized
    (Effectively) all geodetic observation types
  Scalable
    Including Helmert Blocking if necessary
  Most common LESS approaches
    Gauss-Markov Models
    Variance Component Models
    (Partial) MINOLESS (i.e., minimally constrained adjustments using inner constraints)
  Pre- and post-adjustment data snooping
    Bias determination, outlier detection, hypothesis testing
  Up-to-date with recent research
    Colored noise, as applicable
Insert this code into all NGS tools which use LSA

## Slide 9: Current Status

## Slide 10: LASER
Least squares Adjustments: Statistics, Estimates and Residuals
  This is a working title only for now
Contract began in August 2020 and runs until July 2021 (with the possibility of a 1 year extension)
  About halfway done (of 2 years work), but already…
    Solves many LSA problems
    Has been tested on historic NGS archives
  Uses the pre-existing Eigen library of linear algebra routines

## Slide 11: LASER accomplishments
Experiments with the NA2011 national adjustment
    Primary and secondary combined
    79,546 points = 238,638 unknowns
    1,148 CORSs and secondary points constrained = 3,444 constraints
    398,792 vectors = 1,196,376 observations
    Redundancy = 961,182
  Successfully (automatically) identified and treated 13 independent networks within the overall network
  Successfully (automatically) identified vectors of questionable quality
  Performed the entire adjustment:
    On a desktop computer with 6 cores (12 logical processors)
    Without Helmert Blocking
    In under 2 hours (1 hour 54 minutes)

## Slide 12: Future Work

## Slide 13: Future Work
Test a large or nationwide leveling adjustment
Incorporate:
  Variance Component Model
  Colored noise, e.g., for time-series analysis
  Mixed constraints
  Sequential Adjustments
Training
Documentation

## Slide 14: Thank you!

## Slide 15: Questions?