## Slide 1
Positioning in a multi-Global Navigation Satellite Systems (GNSS) World
Jacob Heck
December 14, 2017
NGS Webinar Series

## Slide 2
Geodesist at NOAA’s National Geodetic Survey since 2016.
Previously a graduate research associate at The Ohio State University as well as a surveyor in private industry and for county and state governments.
Ph.D. Candidate in Geodetic Science at Ohio State.
M.S. in Geodetic Science from Ohio State.
B.S. in Surveying Engineering from Michigan Technological University in Houghton, Michigan.
About me

## Slide 3: Outline
Overview of the history of GNSS
Describe the different constellations
Advantages/challenges of a multi-constellation solution
Show some examples of improvements when using extra satellites

## Slide 4: GNSS Timeline
1982: First GLONASS satellite launched
1978: First GPS satellite launched
1960: First Transit satellite launched
1983: First Network GPS project, Summit County, Ohio
1995: GPS, GLONASS fully operational
2001: GLONASS only has 6 satellites
1960
1970
1980
1990
2000
2010
2020
1994: International GPS Service (IGS) forms

## Slide 5: GNSS Timeline
2003: First GLONASS-M satellite launched
2007: First BeiDou satellite launched
2020: Galileo and BeiDou constellations expected to be complete
2016: Galileo declared initially operational
2017: 113 GNSS satellites in the sky, multi-GNSS smartphones fit in your pocket
2005: First Galileo satellite launched
2000
2010
2020
2011: GLONASS fully operational (again)
2011: BeiDou initially operational over the Asia-Pacific Region
Notes: Google Pixel 2 has GPS+GLO+GAL+BDS+QZSS

## Slide 6: GNSS Timeline
1960
1970
1980
1990
2000
2010
2020
31
GPS
24
GLONASS
GALILEO
27
BEIDOU
35
QZSS
4
NAVIC
7

## Slide 7: The Constellations
Name | Country | Began | #now | FOC | Type
GPS | USA | 1978 | 31 | 30 | MEO
GLONASS | Russia | 1982 | 24 | 24 | MEO
Galileo | European Union | 2005 | 22 | 30 | MEO
BeiDou | China | 2007 | 25 | 35 | MEO (27),GEO (5), IGSO (8)
QZSS | Japan | 2010 | 4 | 4 | IGSO
NavIC | India | 2013 | 7 | 7 | 3 GEO,4 GSO
TOTAL |  |  | 113 | 130 | 
Notes: 4 Galileo satellites were just launched on Tuesday. MEO – Medium Earth Orbit; GEO – Geostationary Earth Orbit; IGSO – Inclined Geo-Synchronous Orbit

## Slide 8: GPS Signals
https://www.labsat.co.uk/

## Slide 9: GLONASS Signals
https://www.labsat.co.uk/

## Slide 10: Galileo Signals
https://www.labsat.co.uk/

## Slide 11: BeiDou Signals
https://www.labsat.co.uk/

## Slide 12: QZSS Signals
https://www.labsat.co.uk/

## Slide 13: NavIC Signals
https://www.labsat.co.uk/
Notes: NAVigation with Indian Constellation
Formerly called IRNSS (Indian Regional Navigation Satellite System)

## Slide 14: GNSS Signals
https://www.labsat.co.uk/
Notes: NAVigation with Indian Constellation
Formerly called IRNSS (Indian Regional Navigation Satellite System)

## Slide 15: Now we have
7 constellations each with 2-5 available wavelengths
Over 200 observables!
Currently: 113 satellites
Planned: 130 satellites

## Slide 16
A GNSS satellite passes overhead broadcasting a signal:
I’m SV 1 at XYZ1 (1) at Time1(1).
I’m SV 1 at XYZ1 (2) at Time1(2).
I’m SV 1 at XYZ1 (3) at Time1(3).
•
•
•
How GNSS works in 5 slides. (1/5)
Notes: Note that we’re introducing some symbols. Superscript numbers will represent satellites.

## Slide 17
At the same time, other satellites are saying:
I’m SV 2 at XYZ2 (1) at Time2(1). I’m SV 3 at XYZ3 (1) at Time3(1).
I’m SV 2 at XYZ2 (2) at Time2(2). I’m SV 3 at XYZ3 (1) at Time3(2).
I’m SV 2 at XYZ2 (3) at Time2(3). I’m SV 3 at XYZ3 (1) at Time3(3).
• •
• •
• •
How GNSS works in 5 slides. (2/5)

## Slide 18
Your receiver hears all this just a fraction of a second later:
SV 1 said its at XYZ1 (1) at Time1(1), but I think it is TimeA(1).
SV 2 said its at XYZ2 (1) at Time2(1), but I think it is TimeA(1).
SV 3 said its at XYZ3 (1) at Time3(1), but I think it is TimeA(1).
•
•
•
How GNSS works in 5 slides. (3/5)
Notes: More symbols. Subscript letters represent receivers.

## Slide 19
Your receiver knows that these signals are travelling at the speed of light, c, so it starts doing a some math:
c × (TimeA(1) – Time1(1)) means I’m RangeA1(1) from XYZ1(1).
c × (TimeA (1) – Time2(1)) means I’m RangeA2(1) from XYZ2(1).
c × (TimeA (1) – Time3(1)) means I’m RangeA3(1) from XYZ3(1).
•
•
•
How GNSS works in 5 slides. (4/5)

## Slide 20
If your receiver has enough ranges, then it can compute its position: XYZA(1) at time TimeA(1). Repeat ad nauseum.
How GNSS works in 5 slides. (5/5)

## Slide 21: How is this going to improve my positioning?

## Slide 22: Dilution of Precision (DOP)
HDOP: Horzontal DOP
VDOP: Vertical DOP
PDOP: Position DOP =
TDOP: Time DOP
GDOP:Geometric DOP=
Obstruction diagram
Notes: DOP is a factor that multiplies the uncertainty associated with User Equivalent Range Error. For example, a DOP of about 2 doubles the uncertainty associated with UERE. Therefore, low DOP is good and high DOP is bad. DOP values greater than 6 are really bad and should not be used for surveying. PDOP values of 1-2 are really good for a solution
On the obstruction diagram, areas between the outer gray circle and the blue segments represent obstructions of the sky. To properly read the diagram, imagine you are lying on your back looking up at the sky. 0 degrees is north, 90 degrees is east, etc. The concentric circles represent 0 degrees above the horizon, then 30 degrees and 60 degrees as one moves from the outside in. The center of the plot is at 90 degrees elevation.

## Slide 23
Notes: Study will first show a 10-deg cut-off, 24 hours beginning at UTC midnight Dec. 13, 2017, at a location in Silver Spring, MD (mid-latitude), Barrow, AK (high-latitude), and Guam (low-latitude) and then show a sky full of obstructions at Low-latitude
Silver Spring -77.03 38.99
Barrow -156.47 71.39
Guam 144.80 13.48

## Slide 24: Mid-latitude, no obstructions 10 degree mask

## Slide 25: Satellite Elevation
http://www.gnssplanningonline.com/
GPS only
GPS+GLO
GPS+GLO+GAL+BDS+QZSS

## Slide 26: Satellite Visibility
http://www.gnssplanningonline.com/
GPS only
GPS+GLO
GPS+GLO+GAL+BDS+QZSS
Notes: Mid-latitude,, 10 degree mask

## Slide 27: DOP
http://www.gnssplanningonline.com/
GPS only
GPS+GLO
GPS+GLO+GAL+BDS+QZSS
Notes: Mid-latitude,, 10 degree mask

## Slide 28: High-latitude, no obstructions 10 degree mask

## Slide 29
http://www.gnssplanningonline.com/
Satellite Elevation
GPS only
GPS+GLO
GPS+GLO+GAL+BDS+QZSS
Notes: High latitude, 10 degree mask

## Slide 30
http://www.gnssplanningonline.com/
Satellite Visibility
GPS only
GPS+GLO
GPS+GLO+GAL+BDS+QZSS
Notes: High latitude, 10 degree mask

## Slide 31
http://www.gnssplanningonline.com/
DOP
GPS only
GPS+GLO
GPS+GLO+GAL+BDS+QZSS
Notes: High latitude, 10 degree mask

## Slide 32: Low-latitude, no obstructions 10 degree mask

## Slide 33
http://www.gnssplanningonline.com/
Satellite Position
GPS only
GPS+GLO+GAL+BDS+QZSS
Notes: Low latitude, 10 degree mask

## Slide 34
Why does Guam see so many satellites?
Lou et al 2014
http://www.navipedia.net/index.php/QZSS
BeiDou
QZSS
Notes: Low latitude, 10 degree mask

## Slide 35
http://www.gnssplanningonline.com/
DOP
GPS only
GPS+GLO+GAL+BDS+QZSS
Notes: Low latitude, 10 degree mask

## Slide 36: Low-latitude, with obstructions

## Slide 37: Obstruction Diagram
http://www.gnssplanningonline.com/

## Slide 38: Satellite Elevation
http://www.gnssplanningonline.com/
GPS only
GPS+GLO+GAL+BDS+QZSS
Notes: Low latitude with obstructions (Guam, N13.48 E144.80)

## Slide 39
http://www.gnssplanningonline.com/
Satellite Visibility
GPS only
GPS+GLO+GAL+BDS+QZSS
Notes: Low latitude with obstructions (Guam, N13.48 E144.80)

## Slide 40
http://www.gnssplanningonline.com/
DOP
GPS only
GPS+GLO+GAL+BDS+QZSS
Maximum PDOP: 2.4
Notes: Low latitude with obstructions (Guam, N13.48 E144.80)

## Slide 41: GPS+GLONASS RMSE results
From Gillins 2017
Notes: This is from Dan Gillins’ presentation from November 9, 2017.

## Slide 42: Convergence Times
From Cai et al 2017
Notes: FTNA is an IGS station in the French Polynesia, SEYG is an IGS station in the Seychelles in the Indian Ocean

## Slide 43: DOP
From Cai et al 2017

## Slide 44: Software Development Challenges
Inter-system biases
Inter-frequency biases
Availability of precise data products
Reference system differences, scale factors
Time system differences (Leap seconds)
Data formats
Orbit modeling
Antenna phase models
Notes: Every satellite system is designed differently so orbits and forces that affect those orbits need to be modeled independently.
GLONASS is FDMA (frequency division multiple access) whereas the other GNSSs are CDMA (code division multiple access). The next generation of GLONASS, GLONASS-K, will be CDMA as well as FDMA

## Slide 45: Challenges for the user
Bigger files
Software, hardware must be up to date
Resources to keep this online

## Slide 46: Summary
By 2020, the sky will be very full
NGS currently only has GPS capability
Using more satellites, convergence times, sky coverage, and DOP will improve

## Slide 47: Acknowledgements
Thanks to Andria Bilich, Steve Hilla, Mark Schenewerk, Xiaopeng Li for your help with this presentation

## Slide 48: References
http://www.gnssplanningonline.com
https://www.labsat.co.uk/index.php/en/applications/labsat-frequency-guide
Cai, C.; Gong, Y.; Gao, Y.; Kuang, C. An Approach to Speed up Single-Frequency PPP Convergence with Quad-Constellation GNSS and GIM. Sensors 2017, 17, 1302.
Gillins, D (2017) Deriving High-accuracy Ellipsoid Heights Using OPUS-Projects. NGS Webinar Series
Lou YD, Liu Y, Shi C, Yao XG, Zheng F (2014) Precise orbit determination of BeiDou constellation based on BETS and MGEX network. Sci Rep 4:4692.

## Slide 49: QUEstions