## Slide 1
Online Positioning User Service (OPUS) Part 2
NGS Geospatial Summit
May 5, 2021
Phillip McFarland
Spatial Reference Systems phillip.mcfarland@noaa.gov
Dru Smith
Modernization Manager
dru.smith@noaa.gov
Dan Gillins
Observation and Analysis
daniel.gillins@noaa.gov

## Slide 2: Poll Question
For those familiar with OPUS, how useful would you find a tool that auto selects the best CORSs to use as geodetic control?
Extremely useful
Probably useful
Neutral
Probably not useful
Definitely not useful
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 3: Motivation
Use OPUS to process data the way you want
“We will build significant flexibility into OPUS for you to process your data your way.”
-NGS Blueprint for 2022 Part 3 p. 63
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 4: Motivation
Use OPUS to process data the way you want
“We will build significant flexibility into OPUS for you to process your data your way.”
-NGS Blueprint for 2022 Part 3 p. 63
…but if you want your solution “tied to the NSRS” you must follow OPUS Recommendations.
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 5: Motivation
Use OPUS to process data the way you want
“We will build significant flexibility into OPUS for you to process your data your way.”
-NGS Blueprint for 2022 Part 3 p. 63
…but if you want your solution “tied to the NSRS” you must follow OPUS Recommendations.
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 6
OPUS
Survey data
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 7
OPUS
Survey data
data processing
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 8
OPUS
Survey data
Did you follow OPUS recommendations?
data processing
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 9
OPUS
Survey data
Did you follow OPUS recommendations?
OPUS Coordinates that are
“tied to the NSRS”
yes
data processing
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 10
OPUS
Survey data
Did you follow OPUS recommendations?
OPUS Coordinates that are
“tied to the NSRS”
OPUS Coordinates that are
“not tied to the NSRS”
yes
no
data processing
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 11
OPUS
Survey data
Did you follow OPUS recommendations?
OPUS Coordinates that are
“tied to the NSRS”
OPUS Coordinates that are
“not tied to the NSRS”
yes
no
data processing
If you choose to deviate from the OPUS recommendations:
OPUS will warn you when you do so
You will receive an explanation why your coordinates are not tied to the NSRS
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 12
OPUS
Survey data
Did you follow OPUS recommendations?
OPUS Coordinates that are
“tied to the NSRS”
OPUS Coordinates that are
“not tied to the NSRS”
yes
no
Do you want to “share” your results with the world?
data processing
If you choose to deviate from the OPUS recommendations:
OPUS will warn you when you do so
You will receive an explanation why your coordinates are not tied to the NSRS
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 13
OPUS
Survey data
Did you follow OPUS recommendations?
OPUS Coordinates that are
“tied to the NSRS”
OPUS Coordinates that are
“not tied to the NSRS”
yes
no
Do you want to “share” your results with the world?
Unique, public URL for this survey which you can share with anyone
yes
data processing
If you choose to deviate from the OPUS recommendations:
OPUS will warn you when you do so
You will receive an explanation why your coordinates are not tied to the NSRS
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 14
OPUS
Survey data
Did you follow OPUS recommendations?
OPUS Coordinates that are
“tied to the NSRS”
OPUS Coordinates that are
“not tied to the NSRS”
yes
no
Do you want to “share” your results with the world?
Unique, public URL for this survey which you can share with anyone
Your results are shown to you on screen or via email only
yes
no
data processing
If you choose to deviate from the OPUS recommendations:
OPUS will warn you when you do so
You will receive an explanation why your coordinates are not tied to the NSRS
Notes: - this is the modernized NSRS
- OPUS 6.0

## Slide 15
So what are the OPUS Recommendations going to be?
Notes: - you are welcome to do whatever you like – you just won’t be tied to the NSRS

## Slide 16
So what are the OPUS Recommendations going to be?
DISCLAIMER – many OPUS Recommendations are still TBD
Notes: - you are welcome to do whatever you like – you just won’t be tied to the NSRS

## Slide 17
So what are the OPUS Recommendations going to be?
DISCLAIMER – many OPUS Recommendations are still TBD
General
Classical surveying techniques
Leveling
GNSS
Notes: - you are welcome to do whatever you like – you just won’t be tied to the NSRS

## Slide 18
So what are the OPUS Recommendations going to be?
DISCLAIMER – many OPUS Recommendations are still TBD
General
Classical surveying techniques
Leveling
GNSS
✓ = “tied to the NSRS” ✘ = “not tied to the NSRS”
Notes: - you are welcome to do whatever you like – you just won’t be tied to the NSRS

## Slide 19: OPUS Recommendations – general
Coordinate epochs
  Representative epoch – at or very near collection time of observations ✓
  Most recently passed reference epoch - ( see “Two Types of Coordinates”, Kanazir, NGS GSS, 2021) ✓
  Some other epoch of your choosing ✘
Notes: - you are welcome to do whatever you like – you just won’t be tied to the NSRS

## Slide 20: OPUS Recommendations – classical surveys
One set of redundant GNSS occupations on at least three control points ✓
  Required to transform from
  local horizon to global
  Earth-centered-Earth-fixed frame
No (or not enough) GNSS data ✘
x
z
y
A
X
Y
Z
Notes: - river crossings during a levelling project are classical data

## Slide 21: OPUS Recommendations - leveling
Absolute heights – 3 options
  Collect GNSS to obtain orthometric heights on selected points ✓
    Projects 4 weeks or shorter – one set of redundant GNSS observations on primary control marks
    Projects between 4 weeks and 6 months – two separate sets of redundant GNSS observations at beginning and end of survey
    Projects between 6 and 12 months – additional intermediary set of GNSS observations
    Projects longer than 12 months – should be broken up into multiple projects

## Slide 22: OPUS Recommendations - leveling
Absolute heights – 3 options
  Collect GNSS to obtain orthometric heights on selected points ✓
    Projects 4 weeks or shorter – one set of redundant GNSS observations on primary control marks
    Projects between 4 weeks and 6 months – two separate sets of redundant GNSS observations at beginning and end of survey
    Projects between 6 and 12 months – additional intermediary set of GNSS observations
    Projects longer than 12 months – should be broken up into multiple projects
  Use heights from NSRS database for selected points ✓
    NSRS heights must have been obtained within X number of years from time of survey - X is a TBD quantity

## Slide 23: OPUS Recommendations - leveling
Absolute heights – 3 options
  Collect GNSS to obtain orthometric heights on selected points ✓
    Projects 4 weeks or shorter – one set of redundant GNSS observations on primary control marks
    Projects between 4 weeks and 6 months – two separate sets of redundant GNSS observations at beginning and end of survey
    Projects between 6 and 12 months – additional intermediary set of GNSS observations
    Projects longer than 12 months – should be broken up into multiple projects
  Use heights from NSRS database for selected points ✓
    NSRS heights must have been obtained within X number of years from time of survey - X is a TBD quantity
  Provide no absolute heights – yields only differential heights ✘

## Slide 24: OPUS Recommendations - GNSS
NOAA CORS Network (NCN) station selection – 3 options
  Automated ✓
    OPUS will automatically select the best stations for your survey

## Slide 25: OPUS Recommendations - GNSS
NOAA CORS Network (NCN) station selection – 3 options
  Automated ✓
    OPUS will automatically select the best stations for your survey
  Manual selection from OPUS recommendations ✓
    The user will be able to select stations from a list of OPUS recommended stations that fall above a TBD quality threshold

## Slide 26: OPUS Recommendations - GNSS
NOAA CORS Network (NCN) station selection – 3 options
  Automated ✓
    OPUS will automatically select the best stations for your survey
  Manual selection from OPUS recommendations ✓
    The user will be able to select stations from a list of OPUS recommended stations that fall above a TBD quality threshold
  Manual selection ignoring OPUS recommendations
    The station can be used – but not as control – and coordinates may still be labelled “tied to the NSRS” ✓
    If the station is used as control – the resulting coordinates will not be tied to the NSRS ✘

## Slide 27: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Geographic criteria
  Quantitative criteria
  Qualitative criteria

## Slide 28: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Geographic criteria
  Quantitative criteria
  Qualitative criteria

## Slide 29: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Geographic criteria
0 < r < dmax

## Slide 30: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Geographic criteria
dmin < r < inf

## Slide 31: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Geographic criteria
  Quantitative criteria
  Qualitative criteria

## Slide 32: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Quantitative criteria
Historical temporal stability –
Goodness of fit of the coordinate function to the data that went into the most recent multi-year CORS solution (MYCS)

## Slide 33: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Quantitative criteria
Recent temporal stability –
Goodness of fit of the coordinate function to data that has been collected since the end of the most recent multi-year CORS solution (MYCS)

## Slide 34: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Quantitative criteria
Spatial stability –
How well does the estimated velocity at a CORS agree with the velocities of its neighbors?
Notes: - baseline length; distance from rover – geographic criteria

## Slide 35: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Geographic criteria
  Quantitative criteria
  Qualitative criteria

## Slide 36: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Qualitative criteria
    Data availability
    Uptime of station
    Well-defined GRP?
    Monumentation quality
    Observing multi-GNSS
    Recency of photos
    Estimated vs modeled velocities

## Slide 37: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Qualitative criteria
    Data availability
    Uptime of station
    Well-defined GRP?
    Monumentation quality
    Observing multi-GNSS
    Recency of photos
    Estimated vs modeled velocities

## Slide 38: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Qualitative criteria
    Data availability
    Uptime of station
    Well-defined GRP?
    Monumentation quality
    Observing multi-GNSS
    Recency of photos
    Estimated vs modeled velocities
Geometric
Reference
Point
(GRP)

## Slide 39: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Qualitative criteria
    Data availability
    Uptime of station
    Well-defined GRP?
    Monumentation quality
    Observing multi-GNSS
    Recency of photos
    Estimated vs modeled velocities
MOCN
KYTL
NVAG
P025

## Slide 40: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Qualitative criteria
    Data availability
    Uptime of station
    Well-defined GRP?
    Monumentation quality
    Observing multi-GNSS
    Recency of photos
    Estimated vs modeled velocities
GPS
GLONASS
Galileo
QZSS
Beidou
IRNSS

## Slide 41: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Qualitative criteria
    Data availability
    Uptime of station
    Well-defined GRP?
    Monumentation quality
    Observing multi-GNSS
    Recency of photos
    Estimated vs modeled velocities
INVI

## Slide 42: OPUS Recommendations – GNSS cont’d
Station selection criteria
  Qualitative criteria
    Data availability
    Uptime of station
    Well-defined GRP?
    Monumentation quality
    Observing multi-GNSS
    Recency of photos
    Estimated vs modeled velocities

## Slide 43: The Big Takeaway
OPUS 6.0 will be built so that you can process your data the way you want…
…but if you want your coordinates to be “tied to the NSRS” you will need to follow NGS-prescribed best practice – i.e. OPUS Recommendations.

## Slide 44
Thank You!