## Slide 1: NGS Progress Towards 2022
MN Society of Professional Surveyors
68th Annual Meeting
Dave Zenk PE LS
NGS Northern Plains Regional Advisor
February 19-21, 2020
Duluth MN

## Slide 2: Session Outline
The New Datums for 2022 (NATRF2022, NAPGD2022)
State Plane and Local Coordinate Systems (SPCS2022)
Coordinate Conversion Tools (NCAT, VERTCON)
Preparatory (timeline) steps for local users
Deadlines:
March 31, 2020 - SPCS2022 Proposals due
March 31, 2021 - SPCS2022/LDP Final Designs due
December 31, 2022 - Deprecation of US Survey Foot
(see Federal Register Notice #2019-22414)

## Slide 3: Why replace NAVD 88 and NAD 83?
It’s the next logical step in a century old progression.
  Migration from assumed coordinates, height, and direction to worldwide need to share unified datasets.
US Standard Datum -> NAD27 -> NAD83 -> NATRF2022
Assumed NORTH
N=5,000
E=10,000
Ht=100

## Slide 4: Why replace NAVD 88 and NAD 83?
EXPANDS ACCESS!
  easier to find the sky than to find a 60-year-old bench mark
  GNSS equipment is cheap and fast
ENSURES ACCURACY!
  easier to trust the sky than to trust a 60-year old bench mark
  immune to passive mark instability
GEOPHYSICS!
  Plate tectonics = motion
  Gravity defines level surfaces
  Satellite orbits based on gravitational center of mass
GLOBAL STANDARDS!
  systematic errors of many meters across the US
  aligns with GPS and with Canada, Mexico
3 WORDS
- Access
- Trust
- Motion
Notes: Things are looking up! GNSS technologies simplify and improve access to and accuracy of our spatial reference system.
While we can continue to leverage this technology to maintain the old datums, it makes sense to adopt GRAV-D results in an unpolluted form, and align it to modern global standards.

## Slide 5: Access / Trust / Motion
PID: JU2963 Designation: COXALL Location: Cape May NJ
Found washed up 2 miles from original 1933 location !

## Slide 6
Dense as it is, it’s not everywhere!
Access?

## Slide 7: North Dakota Passive Mark Network
Shows only NGS Database marks.
Local marks exist, too
12 mile radius

## Slide 8: Minnesota Level Network
blue = 1992 and newer red = 1991 and older
Dense as it is, it’s not everywhere!

## Slide 9
Velocities, relative to IGS08 epoch 2005.00
Motion?

## Slide 10
Velocities, relative to NAD83(2011) epoch 2010.00
Motion?

## Slide 11
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent NATRF2022
coordinates from time-dependent
IGS coordinates.
EULER Pole
North American Plate rotates CCW around its Euler Pole
Motion?
Euler Pole Parameters (EPP)

## Slide 12
ITRF – constant frame, rotating plate

## Slide 13
NATRF – rotating frame, constant with plate

## Slide 14
ITRF or NATRF – your choice, just use EPP
If we align the Grids at say 2020.00, then allow time to pass, we can see changing coordinates in ITRF, but also convert to/from NATRF at a date of interest!

## Slide 15: Behind the Scenes
https://www.ngs.noaa.gov/web/science_edu/webinar_series/2019-webinars.shtml
When you submit a GPS data file (say to OPUS STATIC) NGS will
process it in ITRF,
then apply Euler Pole Parameters (EPP),
to obtain the NATRF2022 results for you.
See Blueprint Part 3 for details

## Slide 16
These arrows are ~ 1.1 meters long
These arrows are ~ 1.5 meters long
Comparison of IGS08 and NAD83
Expected HORZ Change

## Slide 17
NAD 83(2011) to IGS08 at epoch 2022.0
~ 1.4 meters (NW) in MN

## Slide 18
NAD 83(2011) to IGS08 at epoch 2022.0
~ -0.8 meters in MN
Notes: NGS has not yet determined the co-definitional epoch between IGSxx and the four TRFs. The epoch 2022.0 is for reference purposes only, and does not constitute a policy choice at this time

## Slide 19
NAVD88 to NAPGD2022
~ -0.80 meters in MN

## Slide 20
ITRF is now mature – smaller changes each epoch
ITRF2014

## Slide 21: Access to New Datum – Now and Future
In the future vertical datum (NAPGD2022), access will be via GPS, OPUS, and a GEOID model. Here’s a sample of current OPUS extended output with highlighted items:
REF FRAME: NAD_83(2011)(EPOCH:2010.0000) ITRF2014 (EPOCH:2016.7527) LAT: 44 59 16.25806 0.004(m) 44 59 16.28545 0.004(m) E LON: 266 30 48.71581 0.003(m) 266 30 48.67189 0.003(m) W LON: 93 29 11.28419 0.003(m) 93 29 11.32811 0.003(m) EL HGT: 274.804(m) 0.011(m) 273.876(m) 0.011(m) ORTHO HGT: 301.779(m) 0.027(m) [NAVD88 (Computed using GEOID18)]h
And at bottom of the extended OPUS report:
APPROX ORTHO HGT: 300.978 (m)
[PROTOTYPE (Computed using xGeoid19B,GRS80,ITRF2014)]
Black = current datums
Red = future datums
Location west of Minneapolis, MN
Lat = + 0.843 m
Lon = + 0.951 m
Ell Ht = - 0.928 m
Ortho Ht = - 0.801 m
File date: 2016-10-02
OPUS date: 2019-11-29

## Slide 22: Summary: The NSRS in 2022…
Four semi-dynamic reference frames
Geoid/GPS based vertical datum
All data will be time tagged
All coordinates will come from GNSS surveys

## Slide 23: New Names
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 24: New Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 25: Intra-frame velocities
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748
This is the velocity of the
point in ITRF. Includes all
movements, but the
dominant one is the
rotation of the N.A. Plate.
This is the velocity of the
point in NATRF2022.
Rotation of plate removed.
It is not constant because
the point still suffers small
“intra-frame” velocities.
Such IFVs will be captured
in a model by NGS.

## Slide 26: Blueprints for 2022
Part 1: Geometric – now available
Part 2: Geopotential – now available
Part 3: Working in the Modernized NSRS – now available
https://www.ngs.noaa.gov/datums/newdatums/policy.shtml
https://www.ngs.noaa.gov/web/science_edu/webinar_series/2019-webinars.shtml

## Slide 27
The State Plane Coordinate System
History, Policy, and Future Directions
Michael L. Dennis
NGS SPCS2022 Project Manager
March 8, 2018
Edited by
Dave Zenk PE, LS
NGS Northern Plains Regional Advisor

## Slide 28: SPCS and LDP Design Goals
To minimize (not eliminate) scale factors between GRID and GROUND, the projections should be designed with TOPOGRAPHY in mind.
This was not feasible in NAD27 or NAD83, but now we have accurate and detailed surface maps (DEM / DTM) and computational power.

## Slide 29: Consider North Carolina SPCS 83 Zone
Central “standard” parallel
Ellipsoid
North standard parallel
South standard parallel
(projection axis)
Scale = 1
Scale = 1
(1:7849)
Secant Lambert Conformal Conic projection, 2-parallel definition:
Standard parallels
North = 36°10’N (exact)
South = 34°20’N (exact)
It is EXACTLY the same as this 1-parallel definition:
Central standard parallel
35°15’06.33096…”N
Scale = 0.9998 7259…
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Ellipse to Grid Scale
= 0.99987
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 30: Secant Lambert Cone
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
35°15’06.33096
Not Fitting Terrain
What Can We Do?
Note: Perpendicular Line to Cone (blue) is also Perpendicular to ellipsoid (yellow) at the Projection Axis
Ellipse to Grid Scale
= 0.99987
Grid to Ground Scale not ~ 1.0
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 31: Tangent Lambert Cone
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
35°15’06.33096
Move Cone Up
Same Projection Axis, Different scale factor
Ellipse to Grid Scale
= 1.000
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 32: Non-Intersecting Lambert Cone
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
35°15’06.33096
= 1.001
Move Cone Up Again
Same Projection Axis, Different scale factor
Ellipse to Grid Scale
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 33: Design to Fit Terrain 1
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Change Cone Angle
New Projection Axis, Different scale factor
36°00’00”
Ellipse to Grid Scale
= 1.010
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 34: Design to Fit Terrain 2
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
= 1.020
Change Cone Angle Again
New Projection Axis, Different scale factor
37°00’00”
Ellipse to Grid Scale
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 35: Design to Fit Terrain 3
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
= 1.030
Change Cone Angle Again
New Projection Axis, Different scale factor
38°00’00”
Ellipse to Grid Scale
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 36: Design to Fit Terrain 4
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Central “standard” parallel
(projection axis)
Move Cone Down
Retain Projection Axis, Different scale factor
38°00’00”
= 1.001
Ellipse to Grid Scale
Grid to Ground Scale ~ 1.0
2 defining parameters
Angle at apex
Scale at central parallel

## Slide 37: Louisiana (existing SPCS 83)
+/- 20 ppm
+/- 20 ppm
- 80 ppm

## Slide 38: Louisiana (preliminary SPCS 2022)
+/- 20 ppm
+/- 20 ppm
- 40 ppm

## Slide 39: Colorado (existing SPCS 83)
- 200 ppm
- 400 ppm

## Slide 40: Colorado (preliminary SPCS 2022
+/- 50 ppm
- 250 ppm
+ 150 ppm
+/- 50 ppm

## Slide 41: Montana
-300 ppm
-600 ppm

## Slide 42: Montana
+/- 100 ppm
+/- 100 ppm
-300 ppm

## Slide 43
Kansas Map
Note county lines
https://www.kansas.gov/khp-crashlogs/search/index

## Slide 44
Salina 1227 feet
Kanarado 3907 feet
Dodge City 2493 feet
Independence 804 feet

## Slide 45: Statewide Kansas 1-zone & 2-zone Lambert

## Slide 46: Statewide Kansas UTM Zone 14

## Slide 48
+ 200 ppm
+/- 50 ppm
- 150 ppm
+/- 50 ppm
- 100 ppm
+ 200 ppm

## Slide 50: North Dakota Counties
https://www.ndstudies.gov/gr4/geology-geography-and-climate/part-2-geography/section-9-major-cities

## Slide 51: North Dakota Shaded Relief
https://eros.usgs.gov/sites/all/files/external/imagegallery/2534.jpg
Pembina 778 feet
Bowman 2963 feet
Bismarck 1686 feet
Devils Lake 1447 feet
Peace Garden 2314 feet

## Slide 52: Rainbow Map of ND
https://water.usgs.gov/edu/gallery/rainbows-nordvik.html

## Slide 55: Minnesota SPCS & LDP Design
Minnesota has a preliminary SPCS & LDP now under study.
Contact: MNDOT Geodetic Unit for details.
Will likely be similar to Nebraska, Kansas, and Iowa
SPCS Proposals due by March 31, 2020
SPCS / LDP Designs due by March 31, 2021

## Slide 56: Example Proposals
https://www.ngs.noaa.gov/SPCS/policy.shtml

## Slide 57: NGS Tools NADCON, VERTCON, and NCAT

## Slide 58: Historical Overview: Problems
Multiple DOS based programs
Lack of documentation
Inconsistent decision making
  Accuracy reporting
  State vs nationwide grids
  Skipping over transformations
Read the Report:
https://www.ngs.noaa.gov/PUBS_LIB/NOAA_TR_NOS_NGS_63.pdf

## Slide 59: Historical Overview: Problems
All these programs led to a patchwork of solutions and confusion.
Steps to transform from NAD 27 to NAD 83(2011) in Kansas - - - - >
  Run NADCON 4.2 to compute
    NAD 27 to NAD 83(1986) grid (nationwide)
    NAD 83(1986) to NAD 83(HPGN) grid (statewide)
  Run GEOCON 2.0 to compute
    HARN to FBN grid (statewide)
    FBN to 2007 grid (nationwide)
    2007 to 2011 grid (nationwide)
  Add everything up yourself
  Have a nice day

## Slide 60: Need for New Conversion Tools

## Slide 61: Biquadratic Interpolation
80
82
83
78
Straight (sharp breaks at grid cells)
Biquadratic (smooth breaks at grid cells)
80
82
83
78

## Slide 62: Included Datums
Region | Datums
CONUS | USSD, NAD27, NAD83(1986), NAD83(HARN), NAD83(FBN), NAD83(2007), NAD83(2011)
Alaska | NAD27, NAD83(1986), NAD83(1992), NAD83(2007), NAD83(2011)
Alaska – Saint islands | 
Hawaii | OHD, NAD83(1986), NAD83(1993), PA11
Puerto Rico and US Virgin Islands | PR40, NAD83(1986), NAD83(1993), NAD83(1997), NAD83(2002), NAD83(2007), NAD83(2011)
American Samoa | AS62, NAD83(1993), NAD83(2002), PA11
Guam/CNMI | GU63, NAD83(1993), NAD83(2002), MA11
31 transformations
7 transformations
HARN means the first post-1986 GPS-survey-based realization in a state/region; FBN means the second (if it existed) post-1986 GPS-survey-based realization in a state

## Slide 63: NADCON5 Process (1/2)
Pull from IDB
one record for every instance that a latitude, longitude, or an ellipsoid height was loaded into the NGS IDB
Outlier Removal
~6000 outliers in all transformations
Thin the Data
Most outliers: NAD83(HARN) to NAD83(FBN) [count = 2590]
ID’d by statistical and “eyeball” methods
Coordinate Differences
Grid the Data
Vector = new_datum minus old_datum
Plots of vectors, coverage
Error analysis

## Slide 64: NADCON5 Process (2/2)
Pull from IDB
Outlier Removal
Thin the Data
Grid the Data
Use a median filter to separate data into “thinned” and “dropped”
Thinned (transformation) vs dropped: (error formulation)
Requires choosing a cell size
Fit a surface under tension to thinned data
Surface expressed as grid (lookup table)
Error analysis
Build error grid (lookup table)
All vectors used in error formulation
Coordinate Differences

## Slide 65: Pull from IDB
PID ST US Standard Datum | NAD 27
AA9371 TX 453 N301622.34000 W0974420.01000 N/A | N301622.45000 W0974419.16000 N/A
AA9372 TX 453 N301626.15000 W0974420.01000 N/A | N301626.24000 W0974419.16000 N/A
AB0076 TX 061 N255754.23000 W0971201.91000 N/A | N255754.37580 W0971200.95657 N/A
AB0225 TX 061 N260619.42900 W0971915.79500 N/A | N260619.57300 W0971914.85300 N/A
AB0289 TX 061 N260845.57000 W0972809.47200 N/A | N260845.77867 W0972808.60964 N/A
AB0338 TX 061 N260341.34400 W0971609.71700 N/A | N260341.48900 W0971608.77400 N/A
AB0917 TX 215 N260507.70300 W0975157.70400 N/A | N260507.83900 W0975156.76000 N/A
AB0992 TX 261 N263645.56300 W0974517.08600 N/A | N263645.69300 W0974516.14900 N/A
AB1366 TX 061 N255728.87000 W0971516.23000 N/A | N255729.02000 W0971515.29000 N/A
Examples:
USSD to NAD27
Notes: Adjusted only
Chronologically back to back

## Slide 66: Coordinate Differences
New datum, minus old datum
Creates a vector
Note: lat and lon are separate transformations
Examples:
USSD to NAD27

## Slide 67: Outlier Removal
GEOCON 1.0: all coord pairs should be reflected in transformation (grid or accuracy estimates)
NADCON5: Outliers are…
  Disruptive to creation of grid
  So far outside norm that any good surveyor would have rejected these points from their work
We identify reasons for outliers in ASCII file
Examples:
USSD to NAD27

## Slide 68: Thin the Data
Vectors are separated using a median filter:
Thinned
  Retained one per cell, used for transformation
Dropped
  everything else, retained for error estimates
dropped
thinned
Examples:
USSD to NAD27

## Slide 69: Error Grid
Total error
Method Noise
Data Noise
RMS combination
Method Noise
Data Noise

## Slide 70: NADCON 5 / NCAT
http://beta.ngs.noaa.gov/gtkweb/

## Slide 71
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
X, Y, Z
USNG
UTM
SPC
f, l, h
2022
future

## Slide 72: NADCON 5 (NCAT)
NADCON 4.2 requires download and install – but note previous slide 9 comment about installation difficulty.
Prefer to focus on the ONLINE version of NADCON 5 (NCAT)
  Nothing to install or to keep updated.
First, go to NGS Home Page (https://www.ngs.noaa.gov/)
Then, TOOLS, and Datum Transformation (NADCON)

## Slide 73: NADCON 5 (NCAT)
Type of Interaction
Input Coordinate Style
Action Type
Action Button
In / Out Datum Selection
Input Entry Work Area
Output Area w/options
This is the Single Point Conversion Screen

## Slide 74: NADCON 5 (NCAT)
Let’s use example Station I90 265.5 located near Chamberlain SD

## Slide 75: NADCON 5 (NCAT)
Station I90 265.5 (OR1034) datasheet
National Geodetic Survey, Retrieval Date = DECEMBER 18, 2017
OR1034 CBN - This is a Cooperative Base Network Control Station.
OR1034 DESIGNATION - I90 265.5
OR1034 PID - OR1034
OR1034 *CURRENT SURVEY CONTROL
OR1034* NAD 83(2011) POSITION- 43 46 25.48906(N) 099 19 08.23572(W) ADJUSTED
OR1034* NAD 83(2011) ELLIP HT- 494.569 (meters) (06/27/12) ADJUSTED
OR1034* NAD 83(2011) EPOCH - 2010.00
OR1034* NAVD 88 ORTHO HEIGHT - 520.270 (meters) 1706.92 (feet) ADJUSTED
OR1034 ______________________________________________________________________
OR1034 GEOID HEIGHT - -25.673 (meters) GEOID12B
OR1034 NAD 83(2011) X - -747,026.601 (meters) COMP
OR1034 NAD 83(2011) Y - -4,552,375.841 (meters) COMP
OR1034 NAD 83(2011) Z - 4,390,315.858 (meters) COMP
OR1034 LAPLACE CORR - -0.05 (seconds) DEFLEC12B
OR1034 DYNAMIC HEIGHT - 520.127 (meters) 1706.45 (feet) COMP
OR1034 MODELED GRAVITY - 980,329.7 (mgal) NAVD 88
OR1034
OR1034 VERT ORDER - FIRST CLASS II
INPUT to NCAT

## Slide 76: Enter Data
Station I90 265.5 (OR1034) datasheet - continued
OR1034
OR1034; North East Units Scale Factor Converg.
OR1034;SPC SD S - 160,516.649 681,658.675 MT 0.99991054 +0 41 59.2
OR1034;SPC SD S - 526,628.37 2,236,408.50 sFT 0.99991054 +0 41 59.2
OR1034;UTM 14 - 4,846,793.342 474,331.136 MT 0.99960810 -0 13 14.4
OR1034
OR1034! - Elev Factor x Scale Factor = Combined Factor
OR1034!SPC SD S - 0.99992245 x 0.99991054 = 0.99983300
OR1034!UTM 14 - 0.99992245 x 0.99960810 = 0.99953058
OR1034
OR1034_U.S. NATIONAL GRID SPATIAL ADDRESS: 14TMP7433146793(NAD 83)
OR1034
OR1034 SUPERSEDED SURVEY CONTROL
OR1034
OR1034 NAD 83(2007)- 43 46 25.48902(N) 099 19 08.23661(W) AD(2002.00) 0
OR1034 ELLIP H (02/10/07) 494.594 (m) GP(2002.00)
OR1034 NAD 83(1996)- 43 46 25.48887(N) 099 19 08.23647(W) AD( ) A
OR1034 ELLIP H (06/23/03) 494.589 (m) GP( ) 3 1
OR1034 NAVD 88 520.27 (m) 1706.9 (f) LEVELING 3
OR1034
Expected OUTPUT from NCAT

## Slide 77: Enter Data
INPUT to NCAT

## Slide 78: CONVERT
Actual OUTPUT from NCAT
Note Sigma Estimates

## Slide 79: Compare
Component | Datasheet | NCAT | Diff (ft) | Diff (m)
LAT | 43 46 25.48887 | 43 46 25.48864 | 0.023 ft | 0.007 m
LON | 099 19 08.23647 | 099 19 08.23638 | 0.006 ft | 0.002 m
EllHT | 494.589 | 494.589 | 0.000 ft | 0.000 m
Compare Datasheet NAD83(HARN)
to NCAT output NAD83(HARN)
Q. Why are these not exact?
A. NCAT is interpolated, not adjusted.

## Slide 80: OPTIONS
Use OPTION to change State Plane Zone or UTM Zone
Change to SD – North Zone
No need to click COMPUTE again

## Slide 81: OPTIONS
Export to a file – PDF, XLS, CSV, or XML

## Slide 82: Convert a File of Points
Gives samples and instructions
Use defined HEADER LINE, CSV File
Need at least 2 input lines
Can use “auto”, or specify SPC or UTM Zone

## Slide 83: Convert a File of Points
Lat/Lon in decimal degrees or DMS
EHT or n/a
IN and OUT Datum
(must use list for region):
USSD, NAD27, NAD83(1986), NAD83(HARN), NAD83(FBN), NAD83(NSRS2007), NAD83(2011)
SPC Zone
UTM Zone or auto

## Slide 84: Convert a File of Points
ID,LAT,LON,EHT,INDATUM,OUTDATUM,SPCZONE,UTMZONE
AC7981,N455444.43661,W1000432.77619,502.834,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7899,N454601.69620,W0992818.85403,568.153,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7926,N454323.50362,W0990551.62061,576.348,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7948,N454318.29122,W0984558.19454,426.597,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7851,N454729.66086,W0980909.48374,369.827,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7877,N454729.34323,W0974923.77080,370.116,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7853,N435059.17740,W0962712.07293,461.276,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7873,N455616.71916,W1014121.88889,665.663,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7895,N455511.86759,W1012417.38523,679.516,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7920,N455402.52456,W1010335.14792,630.918,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7941,N454756.80820,W1004723.74443,590.900,NAD83(2011),NAD83(1986),AUTO,AUTO
AE9575,N453208.94593,W1000549.83992,528.460,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7871,N452704.85159,W1000205.85046,568.807,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7896,N452656.23351,W0994228.79667,576.351,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7917,N452654.94831,W0992558.98765,534.713,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7938,N452653.99579,W0990609.16319,472.234,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7958,N452642.55592,W0984548.98014,414.538,NAD83(2011),NAD83(1986),AUTO,AUTO
AE9652,N452729.65222,W0981908.17472,372.402,NAD83(2011),NAD83(1986),AUTO,AUTO
DF6324,N452426.43636,W0975128.34962,444.348,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7884,N452421.65405,W0975121.02718,447.520,NAD83(2011),NAD83(1986),AUTO,AUTO
AB9893,N451422.63479,W0964804.27110,358.302,NAD83(2011),NAD83(1986),AUTO,AUTO
AE9751,N451728.84092,W0962805.07722,296.328,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7866,N432646.97257,W1025154.48512,919.810,NAD83(2011),NAD83(1986),AUTO,AUTO
AC7947,N440345.93381,W1011336.68400,562.966,NAD83(2011),NAD83(1986),AUTO,AUTO
AB9891,N452446.70412,W0964601.95134,328.348,NAD83(2011),NAD83(1986),AUTO,AUTO
466 marks sample file for SD

## Slide 85: Convert a File of Points
1
2
3

## Slide 86: Convert a File of Points
Done processing – ready for download!

## Slide 87: Convert a File of Points
Output File

## Slide 88: VERTCON
VERTCON’s limited function is to convert orthometric heights between NAVD88 and NGVD29.
On-Line one point at a time:
  https://www.ngs.noaa.gov/cgi-bin/VERTCON/vert_con.prl
Off-Line version needs to be downloaded and installed.
  Includes grids and software
  A bit cumbersome to install and to keep current.

## Slide 89: VERTCON
Off Line Version
Download and Install

## Slide 90: VERTCON
On-Line Conversion Example
  Input Lat Lon in correct format
Positions may be entered in any of the following three formats:
1. degrees, minutes and decimal seconds (including leading zeros)
Lon: (XXX XX XX.XXX) Lat: (XX XX XX.XXX)
Lon: 098 33 23.232 good Lat: 45 33 23.232 good
Lon: 98 33 23.232 bad Lat: 5 33 23.232 bad
Lon: 098 03 23.342 good Lat: 45 03 03.232 good
Lon: 098 3 23.342 bad Lat: 45 3 3.232 bad
2. degrees and decimal minutes (including leading zeros)
Lon: (XXX XX.XXX) Lat: (XX XX.XXX)
Lon: 098 23.232 good Lat: 45 33.232 good
Lon: 98 23.232 bad Lat: 5 23.232 bad
Lon: 098 03.342 good Lat: 45 03.232 good
Lon: 098 3.342 bad Lat: 45 3.232 bad
3. decimal degrees (including leading zeros)
Lon: (XXX.XXX) Lat: (XX.XXX)
Lon: 098.232 good Lat: 45.232 good
Lon: 98.232 bad Lat: 5.232 bad
Note: There MUST be one or more blanks between entry fields
Decimals can be keyed commensurate with the field's precision, but are not required.
common formats

## Slide 91: VERTCON
Use mark C 300 (OR0485) as example near Chamberlain SD
1 National Geodetic Survey, Retrieval Date = DECEMBER 19, 2017
OR0485 ***********************************************************************
OR0485 DESIGNATION - C 300
OR0485 *CURRENT SURVEY CONTROL
OR0485 ______________________________________________________________________
OR0485* NAD 83(1986) POSITION- 43 46 26. (N) 099 18 46. (W) SCALED
OR0485* NAVD 88 ORTHO HEIGHT - 517.279 (meters) 1697.11 (feet) ADJUSTED
OR0485 ______________________________________________________________________
OR0485 GEOID HEIGHT - -25.673 (meters) GEOID12B
OR0485 DYNAMIC HEIGHT - 517.137 (meters) 1696.64 (feet) COMP
OR0485 MODELED GRAVITY - 980,328.6 (mgal) NAVD 88
OR0485
OR0485 VERT ORDER - SECOND CLASS 0
OR0485
OR0485 SUPERSEDED SURVEY CONTROL
OR0485
OR0485 NGVD 29 (??/??/92) 516.937 (m) 1695.98 (f) ADJ UNCH 2 0
INPUT to VERTCON
Expected OUTPUT from VERTCON

## Slide 92: VERTCON
INPUT to VERTCON
https://www.ngs.noaa.gov/cgi-bin/VERTCON/vert_con.prl

## Slide 93: VERTCON
Questions concerning the VERTCON process may be mailed to NGS
  Latitude: 43 46 26
  Longitude: 099 18 46
  NAVD 88 height: 517.279
  Datum shift(NAVD 88 minus NGVD 29): 0.343 meter
  Converted to NGVD 29 height: 516.936 meters
Actual OUTPUT from VERTCON
Expected NGVD29 Height (Datasheet) | Output NGVD29 Height (VERTCON) | Difference
516.937 meters | 516.936 meters | 0.001 meters
Compare Results

## Slide 94: VERTCON
If the ORTHOMETRIC height is not known, VERTCON will compute just the SHIFT at that location.
Questions concerning the VERTCON process may be mailed to NGS
Latitude: 43 46 26
Longitude: 099 18 46
NAVD 88 height:
Datum shift(NAVD 88 minus NGVD 29): 0.343 meter
INPUT to VERTCON
Actual OUTPUT from VERTCON

## Slide 95: VERTCON
Upper Midwest Area
IA
MN
SD
ND
NE
0
20
40
60
~ 20 to 60 cm in ND

## Slide 96: VDATUM
While VERTCON is a limited focus product, some of you may need to consider other datums.
  IGLD 1985
  Various tidal datums – such as
    Mean lower low water
    Mean higher high water
For those purposes, NGS has produced VDATUM.
  Includes some horizontal reference frame conversions
  And vertical reference conversions
I recommend
  NCAT for horizontal as it is state-of-the-art and comprehensive.
  VDATUM for vertical as it is versatile (single points or input file)

## Slide 97: Good News
NCAT will incorporate the functionality of VERTCON to convert heights.
NAPGD2022
NAVD88
NGVD29

## Slide 98: Beta NCAT Interface
Good news - NGS just released new version of NCAT to include HEIGHT conversions in January 2020.

## Slide 99: Good Advice
Whatever conversion software you use, whether NGS or commercial, be SURE you TEST using NGS Datasheets as “truth”.
Compare “expected” results (from datasheet) to “output” (from software).
You or software could be wrong.
Verify, then Trust

## Slide 100: Change and Preparedness

## Slide 101: NGS “New Datums” Pages

## Slide 102: SHIFTS: 1.25 meters N&W x 0.75 meters VERT
Changes in Lat/Lon/EllHT and OrthoHt not negligible
Systematic shift over local areas
Paper maps – at scale of 1”=100 feet, change = 0.04” (1 mm)
  So, overlays of old and new data may be a concern.

## Slide 103: Databases and Software
Many databases were designed with coordinate conversions in mind, but not all.
Some cannot handle datum conversions, even if they handle coordinate conversions.
NGS has released NCAT to assist in managing datum and coordinate conversions.
  How big are your datasets?
Will your software be ready to handle a new datum?
If datasets are big, let us know.

## Slide 104: Client and Employee Education
Many clients and employees may not understand what datums are.
NGS has resources available to help explain the concepts.
Prepare handouts.
Teach up the organization.
see Educational Videos

## Slide 105: Correct and Current Metadata
There are many existing data sets that lack correct and current metadata.
Now would be a good time to inventory and update/correct any such records in your possession.
A clever practitioner could search the FGDC Metadata record in Section 4:
  FGDC section 4.1.4.1 Horizontal Coordinate System Definition
    Often filled in inconsistently: NAD83 or NAD 83 or North American Datum of 1983 or ???
If metadata are correct, then some softwares can convert on-the-fly to desired coordinate system.

## Slide 106: Laws and Rules
Many states embody requirements for datums in state law or agency rules.
These requirements will need changing in order for transition to new datums.
Work with Legislative Committee and others, refer to NSPS Model Legislation updated October 16, 2019:
  https://cdn.ymaws.com/www.nsps.us.com/resource/resmgr/ngs/NSRS-Model-Legistation-Templ.pdf
State | NAD83 | NAD27 | NAVD88 | NGVD29 | SPCS27 | SPCS83
Iowa | x |  |  |  |  | x
Minnesota | x | x |  |  | x | x
North Dakota | x | x |  |  | x | x
Nebraska | x |  |  |  |  | x
South Dakota | x | x |  |  | x | x
50 State TOTALS | 45 | 33 | 2 | 5 | 30 | 43

## Slide 107: Plan for the Future
National Geodetic Survey has created a working group specifically for this task.
Working with partners from
  National Society of Professional Surveyors
  American Association of Geodetic Surveying
The NSPS/AAGS/NGS Advisory Committee on NSPS Legislation has produced this flyer - - >
https://www.ngs.noaa.gov/datums/newdatums/nad-83_state-plane-leg-coord_flyer.pdf

## Slide 109: Plan for the Future
The flyer states the following major points:
  NAD83 and NAVD88 will be replaced.
  the new datums will have different names.

## Slide 110: Plan for the Future
The flyer states the following major points:
  State laws will not reflect the new names – unless the laws are changed!

## Slide 111: Plan for the Future
The flyer recommends that the laws be changed because 3 important reasons:

## Slide 112: Plan for the Future
The flyer recommends that the laws be changed because 3 important reasons:

## Slide 113: Plan for the Future
The flyer recommends that the laws be changed because 3 important reasons:

## Slide 114: How to Plan for the Future
Move to newest realizations
  NAD 83(2011) epoch 2010.00
  GEOID18 (hybrid geoid)
Obtain precise ellipsoid heights on NAVD 88 bench marks (GPS on BM via OPUS-SHARE, contact NGS Geodetic Advisor)
  Improves hybrid geoid models and provides “hard points” in new vertical datum
  Follow new NGS Guidelines when released
Move off of NGVD 29 to NAVD 88
  Understand the accuracy of VERTCON in your area
Move away from passive marks to GNSS
  Especially move off of classical passive control
Require/provide complete metadata for all mapping contracts
  How did they get the positions/heights? Document it!!

## Slide 115: NGS Webinars
https://geodesy.noaa.gov/web/science_edu/webinar_series/Webinars.shtml

## Slide 116: NGS Webinars
https://geodesy.noaa.gov/web/science_edu/webinar_series/Webinars.shtml

## Slide 117: NGS Webinars

## Slide 118: Homework Assignment
I strongly urge survey leaders to carefully read:
  NOS 2 NAD83 Report, by Charles R. Schwartz, 1989. Chapter 21 – User Participation and Impact on pages 237-247
  NOAA Manual NOS NGS 5, State Plane Coordinate System of 1983, by James E. Stem, 1989, pages 1-12
Discuss impacts of new datum on mapping activities, legislation to enable, desired changes to SPCS, and action plan to implement.
Work with local surveying and mapping leaders (NSPS, SDSPLS, SDDOT) and NGS Advisor.

## Slide 119: Contact
David Zenk PE LS Geodesist, National Geodetic Survey
Northern Plains Regional Advisor
MN, ND, SD, NE, IA
University of Minnesota, Geography Department
414A Social Sciences Building
267 19th Ave S
Minneapolis, MN 55455
763-600-6912 office
612-414-9522 mobile
dave.zenk@noaa.gov (federal business)