## Slide 1: The Modernized National Spatial Reference System
Where Things Stand and the Road Ahead
Michael Dennis, PhD, PE, PLS
SPCS2022 Project Manager
Alaska Society of
Professional Land Surveyors
2024 Conference
Anchorage, AK ● Feb 20, 2025

## Slide 2: What is the National Spatial Reference System?
A set of consistent nationwide coordinate systems
Created in 1807 to support commerce and science
Defined and maintained by NOAA’s National Geodetic Survey
…and why should you care?
Geodesy: the science of where things are

## Slide 3
Things are moving
Modernized NSRS accounts for crustal motion
              Tectonic plate rotation
        Local deformation
        Earthquakes
        Subsidence
        Earth center well known
        Reduces systematic errors
        Global rather than regional
            Compatible with international reference systems
Why is the NSRS being modernized?
CATRF2022
NATRF2022
PATRF2022
MATRF2022

## Slide 4: IFDM2022: Intra-Frame Deformation Model of 2022
New preliminary version nearly completed
  Single 0.1° (6 arc-minute) grid covering entire Earth
  3D velocities and their standard deviations
Built from best available information
  Mainly latest Global Strain Rate Model and Global Land Vertical Motion Model
  Augmented by:
    NGS-computed rotations for North America, Pacific, Caribbean, and Mariana plates
    NGS Multi-Year CORS Solution 3
    Trans4D and NGS velocity computations in limited areas
    Earthquake displacement grids
Replaces Horizontal Time-Dependent Positioning (HTDP) software
  Combined with Helmert transformations to transform and project through time

## Slide 11: New types of coordinates
Reference Epoch Coordinates (RECs)
Temporal “snapshot” of entire network
Similar to NAD 83 (2011/PA11/MA11) epoch 2010.00
Initial epoch 2020.00
Every 5 or 10 years (TBD)
Survey Epoch Coordinates (SECs)
Time-dependent!
Gives coordinates at time of observation
Multiple SECs can show changes over time
Likely not included in initial rollout of Modernized NSRS

## Slide 12: National adjustments of passive control
Initial adjustment underway, constrained to latest CORS coordinates
  Geometric (latitude, longitude, ellipsoid height) and orthometric (elevation)
  Geometric includes OPUS-Share solutions (currently 2126 in AK)
  Observations transformed and time projected to ITRF2020 at epoch 2020.00
Two national adjustments
  First being done now, results will be used for new NADCON and VERTCON grids
  Second done when new datums released, constrained to results of first
New coordinates on passive control at epoch 2020.00
  All 5 frames the same at that epoch (but only at that epoch)
  ITRF2020 = NATRF2022 = PATRF2022 = CATRF2022 = MATRF2022
  Beta release this year on new NSRS Datasheets
  Will include beta SPCS2022 coordinates

## Slide 13
The problem: we have this

## Slide 14
Credit: Scott Gelber, The Atlantic
But we want this

## Slide 15
Just click this button in your favorite geospatial software!
My Map Projection
My Map Projection
What is the solution?
Powered by AI
What could possibly go wrong?

## Slide 16: State Plane Coordinate System of 2022 (SPCS2022)
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Widely used in surveying, engineering, and GIS
  Same 3 map projection types
  Same ellipsoid as SPCS 83 (GRS80)
Same as existing State Plane, but different…
  Based on new terrestrial reference frames instead of NAD 83
  More zones, most designed by state stakeholders
  Designed to reduce linear distortion at topographic surface (i.e., reduce difference between “grid” and “ground” distances)
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 17: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states plus Gulf of Mexico
3 layers: 9 states
Plus 10 special use zones (2 zones overlap 5 states)
Every state and territory has a statewide zone layer

## Slide 18: Number of SPCS2022 zones (preliminary)
Designs by NGS
  153 zones
  Includes 54 statewide zones…
  …and 10 “special use” zones (in more than one state or no state at all)
Designs by state stakeholders
  819 zones in 28 states
Total = 972 zones for 56 states and territories
Compare to 125 zones in existing State Plane (SPCS 83)

## Slide 19: ArcGIS Online SPCS2022 Experience
Online interactive maps
Shows distortion and gives zone definitions
Recently updated
Accessible on mobile devices

## Slide 21: NSRS Modernization is nearly done!
Beta releases (for testing and evaluation only!) TENTATIVE schedule
  National CORS Network station pages: May 2025
  NSRS Datasheets for passive control: July 2025
  NCAT v.01 (SPCS2022, IFDM2022, 14H, GEOID2022): July 2025
  OPUS-Static v5.2 with M-PAGES: Sep 2025
  NCAT v.02 (NADCON, VERTCON): Dec 2025
  We encourage you to test each component as it is released
Replaces current datums in 2026
  At least 6 months after last item added to beta release
  After Federal Geodetic Control Subcommittee votes to approve in 2026
  Current NSRS supported through rollout and testing of the modernized NSRS

## Slide 22: Where to learn more…
geodesy.noaa.gov
Thank you!
Questions?