## Slide 1
2013 AGU Fall Meeting – 9 December 2013 – San Francisco, CA – Poster #G13B-0933
Status of IGS Core Products
J. Griffiths (jake.griffiths@noaa.gov)
NOAA, Silver Spring, Maryland, USA 20910
Abstract
The International GNSS Service (IGS) generally aims to provide ~1 cm satellite orbits and ~1 mm terrestrial frame products to meet the most demanding user needs. While the goal has not yet been met, the IGS has made good progress. The current Global Positioning System (GPS) Final orbits have accuracies better than 2.5 cm; the Rapids are of similar quality; and the near real-time parts of the Ultra-rapids have an accuracy of ~3.0 cm, while the real-time parts have an accuracy of about 5 cm. About half of the total error in the GPS orbits can be attributed to systematic time-varying rotational misalignment of the orbital frames; the other half is dominated by errors in the model for sub-daily tidal variations in Earth orientation. Near-field multi-path errors, anthropogenic changes at tracking stations, and the presence of uncalibrated GNSS antenna radomes at multi-technique sites continue to be a significant source of error. While recent model and analysis changes have reduced some errors, others will remain for the foreseeable future. This paper summarizes the quality state of the IGS core products since the switch to daily terrestrial reference frame integrations (Aug. 2012), and as preparations for the next reprocessing campaign continue.
IGS Core Product Series
Series |  |  | ID |  | Latency |  | Issue times (UTC) |  |  | Data spans (UTC) |  |  | Remarks |  |  | 
Ultra-Rapid (predicted half) |  |  | IGU |  | real-time |  | @ 03:00, 09:00, 15:00, 21:00 |  |  | +24 hr @ 00:00, 06:00, 12:00, 18:00 |  |  | ● for real-time apps ● GPS & GLONASS ● issued with prior IGA |  |  | 
Ultra-Rapid (observed half) |  |  | IGA |  | 3 - 9 hr (near real-time) |  | @ 03:00, 09:00, 15:00, 21:00 |  |  | -24 hr @ 00:00, 06:00, 12:00, 18:00 |  |  | ● for near real-time apps ● GPS & GLONASS ● issued with following IGU |  |  | 
Rapid |  |  | IGR |  | 17 - 41 hr |  | @ 17:00 daily |  |  | ±12 hr @ 12:00 |  |  | ● for near-definitive, rapid apps ● GPS only |  |  | 
Final |  |  | IGS |  | 12 - 19 d |  | weekly each Thursday |  |  | ±12 hr @ 12:00 for 7 d |  |  | ● for definitive apps ● GPS & GLONASS |  |  | 
Analysis Center Contributions
Series |  | Product Types |  |  |  |  | Accuracies |  |  | Output Intervals |  | 
Ultra-Rapid (predicted half) |  | GPS orbits |  |  |  |  | ~ 5 cm (1D) |  |  | 15 min |  | 
 |  | GLONASS orbits |  |  |  |  | ~10 cm (1D) |  |  | 15 min |  | 
 |  | GPS SV clocks |  |  |  |  | ~3 ns RMS / ~1.5 ns Sdev |  |  | 15 min |  | 
 |  | ERPs: PM + dLOD |  |  |  |  | ~250 µas / ~50 µs |  |  | 6 hr |  | 
Ultra-Rapid (observed half) |  | GPS orbits |  |  |  |  | ~ 3 cm (1D) |  |  | 15 min |  | 
 |  | GLONASS orbits |  |  |  |  | ~5 cm (1D) |  |  | 15 min |  | 
 |  | GPS SV clocks |  |  |  |  | ~150 ps RMS / ~50 ps Sdev |  |  | 15 min |  | 
 |  | ERPs: PM + dLOD |  |  |  |  | <50 µas / ~10 µs |  |  | 6 hr |  | 
Rapid |  | GPS orbits |  |  |  |  | ~2.5 cm (1D) |  |  | 15 min |  | 
 |  | GPS SV & station clocks |  |  |  |  | ~75 ps RMS / ~25 ps Sdev |  |  | 5 min |  | 
 |  | ERPs: PM + dLOD |  |  |  |  | <40 µas / ~10 µs |  |  | daily |  | 
Final |  | GPS orbits |  |  |  |  | <2.5 cm (1D) |  |  | 15 min |  | 
 |  | GLONASS orbits |  |  |  |  | <5 cm (1D) |  |  | 15 min |  | 
 |  | GPS SV & station clocks |  |  |  |  | ~75 ps RMS / ~20 ps SDev |  |  | 30 s (SVs) + 5 min |  | 
 |  | ERPs: PM + dLOD |  |  |  |  | <30 µas / ~10 µs |  |  | daily |  | 
 |  | Terrestrial frames |  |  |  |  | ~2.5 mm N&E / ~6 mm U |  |  | daily |  | 
Accuracy of Core IGS Products
Product | GNSS |  | Total Hits |  | SP3 (%) |  | ERP (%) | CLK (%) | SNX (%) | SUM (%)
Ultra-rapid | GPS |  | 11,711,506 ( 4 * 2,927,877 daily) |  | 93.7 |  | 3.1 |  |  | 3.2
Final (IGS) | GPS |  | 1,359,656 |  | 60.7 |  | 6.8 | 24.8 | 5.8 | 2.0
Rapid | GPS |  | 887,986 |  | 65.6 |  | 8.7 | 16.9 |  | 6.4
Final (IGL) | GLO | 225,515 |  |  |  | 99.1 |  | 0.3 |  | 0.6
Ultra-rapid (IGV) | GPS & GLO | 223,562 |  |  |  | 95.0 |  |  |  | 5.0
Popularity of Core IGS Products
FTP download logs courtesy of C. Noll (NASA/CDDIS)
Based on FTP download statistics for 1/2012 thru 6/2012
>3.6 million file downloads per month
5 biggest users of CDDIS/IGS files:
  U.S. 64.3%, Indonesia 19.3%, Canada 1.64%, Sweden 1.57%, Belgium 1.16%
Preparations for 2nd Reprocessing (Repro2)
Cen | Name | Final (IGS) |  |  |  | Rapid (IGR) |  |  | Ultra (IGU) |  | 
 |  | SP3 | ERP | SNX | CLK | SP3 | ERP | CLK | SP3 | ERP | CLK
cod* | Centre for Orbit Determination in Europe, Bern, CHE |  |  |  |  |  |  |  |  |  | brd
emr* | Natural Resources Canada, Ottawa, CAN |  |  |  |  |  |  |  |  |  | 
esa* | European Space Agency, Darmstadt, DEU |  |  |  |  |  |  |  |  |  | 
gfz* | GeoForschungsZentrum, Potsdam, DEU |  |  |  |  |  |  |  |  |  | brd
gop | Geodetic Observatory Pecny, CZE |  |  |  |  |  |  |  |  |  | brd
grg* | CNES Groupe de Recherche de Geodesie Spatiale, Toulouse, FRA |  |  |  |  |  |  |  |  |  | 
iac+ | Information and Analysis Center of Navigation, Korolyov, RUS |  |  |  |  |  |  |  |  |  | 
jpl | Jet Propulsion Laboratory, Pasadena, USA |  |  |  |  |  |  |  |  |  | 
mit | Massachusetts Institute of Technology, Boston, USA |  |  |  |  |  |  |  |  |  | 
ngs | National Geodetic Survey, Silver Spring, USA |  |  |  | brd |  |  | brd |  |  | brd
sio | Scripps Institution of Oceanography, La Jolla, USA |  |  |  |  |  |  |  |  |  | 
usn | U.S. Naval Observatory, Washington, USA |  |  |  |  |  |  |  |  |  | 
whu* | Wuhan University, Wuhan, CHN |  |  |  |  |  |  |  |  |  | 
 = AC included = AC partially included  = AC excluded brd = excl. brdc clock empty = none
Performance of Latest Products Using PPP
Series | North (mm) | East (mm) | Up (mm)
Final IGS | 4.1 ±0.4 | 4.8 ±0.4 | 9.5 ±0.7
Final IGR | 3.8 ±0.3 | 4.5 ±0.4 | 9.3 ±0.7
Rapid IGR | 3.8 ±0.4 | 4.5 ±0.4 | 9.3 ±0.6
Rapid IGA | 4.3 ±0.5 | 5.1 ±0.6 | 10 ±0.8
Series | Mean RX (µas) | Mean RY (µas) | Mean RZ (µas)
Final IGS | -11 ±22 | -8 ±26 | -28 ±44
Final IGR | -24 ±26 | 26 ±29 | -9 ±34
Rapid IGR | -24 ±24 | 27 ±25 | -6 ±35
Rapid IGA | -32 ±50 | 3 ±42 | -3 ±50
~180d RZ feature (IGR & IGS) predominantly from EMR, JPL & MIT
Mean RX, RY, RZ offsets (below) due to misalignment of orbital frame
The table below was presented at the EGU General Assembly in 2012 [Ray and Griffiths, 2012]. It represents a best effort to quantify the accuracy of IGS products from: combination statistics and PPP analysis results (http://acc.igs.org); spectral analyses of station position time series [Ray, 2006; Collilieux et al., 2007; Ray et al., 2008; Ray et al., 2013]; spectral analyses of midnight GPS orbit jumps [Griffiths and Ray, 2009; Griffiths and Ray, 2013 ] and midnight discontinuities in ERPs [Ray and Griffiths, 2011]; along with comparisons to loading models [Ray et al., 2011]. Very little has changed since EGU 2012, with exception for improvements in the rotational alignment of Final GPS orbits to the IGS terrestrial frame (IGb08) due to refined combination procedures.
1 µas = ~0.03 mm shift @ Earth surface
Large majority (>80%) of users rely on combined satellite orbits and clocks. To monitor the quality of these products, a PPP analysis is performed as part of the routine Final and Rapid combinations for the IGS, IGR and IGA series (http://acc.igs.org/index_igsacc_ppp.html). Similarity comparisons between each series’ network of PPP-derived station positions and IGb08 give important insight into the quality of the combined products.
Latest Results from the Orbit Combinations
  RX[(IGS-IGR)/2] = -9.2 (± 62.2) μas, or -1.2 (± 8.1) mm shift @ GPS
  RY[(IGS-IGR)/2] = -20.5 (± 73.5) μas, or -2.7 (± 9.5) mm shift @ GPS
  RZ[(IGS-IGR)/2] = 14.8 (± 55.9) μas, or -1.9 (± 7.3) mm shift @ GPS
Preparations are underway to reanalyze the full-history of GPS (and maybe GLONASS) data using the latest analysis models and methodologies. The expected outcome is a set of homogeneous reprocessed IGS solutions for:
daily GPS & GLO orbits & GPS satellite clocks in SP3 format
daily GPS satellite & tracking station clocks (5m & 30s) in CLK RINEX format
daily ERPs from SINEX (official product) & classic orbit combinations (for comparison only)
terrestrial coordinate frames with ERPs, with
  full variance-covariance matrix and Z-offset parameters for satellite antennas
  Repro2 results are intended for inclusion in ITRF2013, and to support advancements in Earth science research and other applications of high-precision GNSS. Details about repro2 analysis standards are available at: http://acc.igs.org/reprocess2.html.
Weighted RMS (WRMS) of residuals from comparisons of AC GPS orbits to the IGS Finals measure inter-AC agreement and provide an internal estimate of IGS precision (1D)
IGS precision ranges from 11 mm (= 16 mm/√2) given by EMR, to 4.5 mm (= 6.4 mm/√2) given by ESA, and possibly down to 3.5 mm (= 5 mm/√2) given by IGR
Time-varying rotations (see plot to the right) of orbit frames are small, but significant—dominated by ESA issues before Wk 1730
Differences in Mean RMS of daily residuals (below) is probably dominated by differences in satellite clock errors between products.
IGS Tracking Stations Used in Latest Products
IGS network currently consists of ~430 GNSS stations distributed globally, with relatively dense coverage in Europe
92 IGS stations (current & former) are co-located with VLBI, SLR and/or DORIS, which is an important contribution to ITRF
Antennas at 30.4% of co-located stations are covered with uncalibrated radomes—see poster G13B-0946 for efforts to mitigate effects at some stations
ACs use data from ~326 IGS stations—as shown in plot to right—for their GPS and GLONASS contributions to Finals combinations (Wk 1765)
The other ~145 stations used by the ACs (again, Finals GPS Wk 1765) are from regional networks (not shown)
Table focuses on GPS; all GLO-only (+) and GNSS AC (*) products are included in GLO combinations.