## Slide 1
The Modernized National
Spatial Reference System (NSRS)
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
Acknowledgements
BLUF
What I’ll be skipping…
Refresher / Shift and Drift
  Replace NAD 83
  Replace NAVD 88
EPP2022 and IFVM2022
Reference Epoch Coordinates from Time-Dependent Coordinates
Terminology
Using the modernized GNSS
Miscellaneous

## Slide 3: Acknowledgments
Blueprint for 2022, Part 3 is the result of significant TEAM efforts over 18 months
  GNSS Standard Operating Procedure (SOP) Team
    Choi, Roman, Jalbrzikowski, Sun, Dennis, Prusky, Gillins, W. Wang, Saleh, Yoon, Damiani, Kanazir, Evjen, Sellars, Schenewerk, Caccamise, Heck, Hilla, Bilich, McFarland
  Leveling Standard Operating Procedure (SOP) Team
    Zenk, Kanazir, Dennis, Breidenbach, Fancher, Hanson, Hensel, Paudel, Ward, Zilkoski, Gillins, Geoghegan
  BP3 Writing Team
    Kinsman, Kanazir, Hensel, Jordan, Stone, Vogel, Heck, Dennis, Fromhertz, Winester, Zenk, Silagi, Roman, Grosh, Ahlgren
It is a team document, with input from dozens of individuals around NGS

## Slide 4: Bottom Line, Up Front
If you teach any geospatial topics…
and those topics cover the current National Spatial Reference System (NAD 83, NAVD 88, etc.)
Every piece of educational material you have…
  every lecture…
  every book…
  every figure…
  WILL have the wrong information in 3 years…
  Let’s talk about what this means, why it is happening, and how it will affect things going forward

## Slide 5: What I’ll be skipping…
Not included today:
  What is…
    NGS and its mission
    The NSRS
    Bluebooking
    GRAV-D
    ITRF
  Why we are modernizing in 2022
All of these topics have been covered extensively in multiple forums in the last few years

## Slide 6: Refresher

## Slide 7: “Modernizing the NSRS” means…
Replacing NAD 83
Replacing NAVD 88
Re-inventing Bluebooking
Improving the Geodetic Toolkit
Better Surveying Methodologies
Blueprint for 2022, Part 3
Blueprint for 2022, Part 1
Blueprint for 2022, Part 2
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 8
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
Sep 2017
NOAA TR NOS NGS 62
32 pages
Geopotential:
Nov 2017
NOAA TR NOS NGS 64
41 pages
Working in the modernized NSRS:
April 2019
NOAA TR NOS NGS 67
77 pages

## Slide 9: Replacing NAD 83
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 10: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  Will include:
  GEOID2022
  DEFLEC2022
  GRAV2022
  DEM2022
  More
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 11: The preeminence of ITRF
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
Rotation of the
North American Plate
Rotation of the
Caribbean Plate
Rotation of the
Pacific Plate
Rotation of the
Mariana Plate
ITRF2014
EPP2022
EPP for “Euler Pole Parameters”
(a way of describing a plate’s rotation)

## Slide 12: Shift and Drift

## Slide 13: Shift
One of the two major changes you’ll see in 2022 is a shift in coordinates
  Latitude, Longitude, Ellipsoid Height: -2 to +4 meters
    Non-geocentricity of NAD 83
  Orthometric Height: -0.5 to +2.0 meters
    Bias and tilt in NAVD 88
  Other shifts will occur in non-CONUS, non-Alaska regions of the USA
  There will be outliers!
    “Old” unsurveyed points might be off by meters if they’ve moved!

## Slide 14: NAD 83(2011) epoch 2010.0 to NATRF2022 epoch 2020.00 (estimate)

## Slide 15: NAVD 88 to NAPGD2022 epoch 2020.00 (estimate)

## Slide 16: Drift
The second major change you’ll see in 2022 is a drift in coordinates
  Everything in the world moves
  Coordinates will be associated with the actual date when the data was taken!

## Slide 17: The wrong question, circa 2022:
“What is the latitude of that point?”
The right question, circa 2022:
“What is the latitude of that point, on some specific date?”

## Slide 18: Drift
The second major change you’ll see in 2022 is a drift in coordinates
  Everything in the world moves
  Coordinates will be associated with the actual date when the data was taken!
  Velocities at all marks can be estimated
    Using a new tool, called the Intra-Frame Velocity Model (IFVM2022)
  Two things will mitigate the pain of time-dependent coordinates:
    “Plate Fixed” frames
    “Reference Epoch” coordinates

## Slide 19
Euler Poles and “Plate Fixed”
  In the ITRF, many tectonic plates have one dominant motion: rotation
    Plus plenty of other motions
  The point about which a continent rotates is called its “Euler Pole”
  In summary:
    Under ITRF
      Frame = constant
      N.A. Plate = rotating
  It is a fairly simple matter to reverse this and define a rotating frame in which the plate is not rotating.
    Under NATRF2022:
      Frame = rotating (relative to ITRF)
      N.A. Plate = constant (relative to NATRF2022 frame)
  We say “NATRF2022” is “fixed” to the N.A. Plate, making it a “plate fixed” frame

## Slide 20: CORS Velocities – ITRF2014

## Slide 21: CORS Velocities – NATRF2022

## Slide 22: EPP2022 and IFVM2022: The two tools that make time dependent geodetic control useable

## Slide 23: There’s really two drifts
The plate rotation is simple (3 parameters per plate)
  Captured in EPP2022
  Horizontal (latitude/longitude) only
  Changes the frame
    ITRF2014 to NATRF2022, PATRF2022, CATRF2022 & MATRF2022
  Doesn’t change the epoch
The residual motions (after removing plate rotation) are complex
  Captured in IFVM2022
  Residual horizontal motion
  All vertical motion
  Changes the epoch
  Doesn’t change the frame
    IFVM = “Intra-frame” velocity model

## Slide 24: Example
It’s 2039 and you are working in San Diego using NATRF2022
You need to compare your work against a competitor’s survey
  Done in 2028, using PATRF2022
NATRF2022
ep. 2028.048
PATRF2022
ep. 2028.048
ITRF2014
ep. 2028.048
NATRF2022
ep. 2039.704
ITRF2014
ep. 2039.704
PATRF2022
ep. 2039.704
EPP2022
EPP2022
EPP2022
EPP2022
IFVM2022
IFVM2022
Important: This slide only covers geometric coordinates.

## Slide 25: Reference Epochs
It seems highly unlikely that surveyors will embrace coordinates with such diversity of epochs
To mitigate that, NGS will issue “snapshots” of the NSRS every five years (called “Reference Epochs”)
  Estimates of coordinates at specific 5 year intervals, based on historic time-dependent coordinates and the IFVM2022
    …and the Geoid Monitoring Service (GeMS), for non-geometric quantities
Beginning with 2020.00
  Each “snapshot” will be published 2-3 years after the reference epoch
    Thus the 2020.00 Reference Epoch Coordinates get published by the end of calendar year 2022

## Slide 26: Reference Epoch Coordinates from Time-Dependent Coordinates

## Slide 27
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
Assume “h” was determined four different times:
1990: 2.100
1994: 2.110
2002: 2.190
2009: 2.180
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30

## Slide 28
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the modernized NSRS these time-dependent
coordinates, estimated at the actual date when
the surveys took place, will be called
“Final Discrete Coordinates”
All measurements have error. Shown here are the same
Values of “h”, but with their error estimates.
1990: 2.100 +/- 0.0375 (3.75 cm)
1994: 2.110 +/- 0.0250 (2.50 cm)
2002: 2.190 +/- 0.0200 (2.00 cm)
2009: 2.180 +/- 0.0250 (2.50 cm)

## Slide 29
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In today’s NSRS, a height is held fixed until
replaced. So plotting the height as seen on a datasheet
over time would look like this:

## Slide 30
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the modernized NSRS we will also have an estimate of
crustal motion from IFVM2022
Combining Final Discrete Coordinates
with IFVM2022 allows
NGS to estimate Reference Epoch Coordinates

## Slide 31
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
The IFVM2022 model will (statistically)
match reference epoch coordinates.
This will allow for the elimination of a
stand-alone “NADCON” product for
coordinates after 2020.0, instead relying
entirely upon IFVM2022

## Slide 32
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the absence of new survey data, error estimates will
grow through time.

## Slide 33
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
The (in)ability of current approach to
properly inform users of the height of
this mark can be seen in green below.

## Slide 34: Example (v2)
It’s 2039 and you are working in San Diego using NATRF2022 (epoch 2035.00)
You need to compare your work against a competitor’s survey
  Done in 2028, using PATRF2022 (epoch 2025.00)
NATRF2022
ep. 2025.00
PATRF2022
ep. 2025.00
ITRF2014
ep. 2025.00
NATRF2022
ep. 2035.00
ITRF2014
ep. 2035.00
PATRF2022
ep. 2035.00
EPP2022
EPP2022
EPP2022
EPP2022
IFVM2022
IFVM2022
This would’ve been a “NADCON” function in the past

## Slide 35: Terminology

## Slide 36: Terminology
The following terms (and more) are defined meticulously in BP3 in a coordinated effort within NGS and with the IERS:
  Point, Mark, Station, Site, ARP, GRP, Site Marker, CORS, the NOAA CORS Network
    GRP = Geometric Reference Point – the official point on a station to which all coordinates refer
As a direct fallout: NGS will no longer provide CORS coordinates at an ARP, only to a GRP
  An antenna has an ARP.
    A CORS only sometimes has an antenna.
      Therefore a CORS only sometimes has an ARP.
      But it always has a GRP.
        The ARP and GRP are only sometimes coincident in space when the antenna is mounted at a CORS
  The GRP gets a Permanent Identifier (PID)

## Slide 37: ARP vs GRP
The purpose of a CORS can be debated
  But at NGS: the continuous collection of GNSS data for the express purpose of determining the continuous coordinates of a unique, permanent, physical point on each CORS
    Such a point is called the Geometric Reference Point, or GRP
    Not to be confused with the Antenna Reference Point, or ARP
      Which is part of each antenna, not a permanent, unique physical part of a CORS
  Identification of GRPs has begun
    Coordinates on a CORS will eventually be fully transitioned to be “coordinates of the GRP of the CORS”. Right now they are…unclear.

## Slide 38: Terminology
“CORS” is an acronym
  It is singular (S means “Station”, not “Stations”)
  It will no longer be used to describe the network of all such stations
    That will, for now, be called the NOAA CORS Network, or NCN
      Which has a subset of stations called the NOAA Foundation CORS Network, or NFCN
  Its plural form is CORSs
    No apostrophe, No “es” and no skipping the “s”
    GODE is a CORS
      Not “a CORS site”
        And definitely NOT “a CORS Station”
          That’s like “an ATM machine”
    GODE and 1LSU are CORSs
    GODE and 1LSU belong to the NOAA CORS Network
    TMG2 is a NOAA Foundation CORS
    TMG2 and FLF1 are NOAA Foundation CORSs
    TMG2 and FLF1 belong to the NOAA Foundation CORS Network

## Slide 39: The NOAA CORS Network (NCN)
As of 2019, this is the official name of the network managed at NGS
  Historically referred to as “CORS” or “the CORS”

## Slide 40: GPS Month
A span of four consecutive GPS weeks, where the first GPS week in the GPS month is an integer multiple of 4
  GPS Month 0 = GPS weeks 0, 1, 2 and 3
  GPS Month 1 = GPS weeks 4, 5, 6 and 7
  Etc.

## Slide 41: New Types of Coordinates

## Slide 42: Five types of coordinates
Name | Generally on… | Description
Reported | Passive | “Quick and Dirty”. Smartphone accuracy.
Preliminary | Passive | Computed by you with OPUS using your data. Unchecked by NGS.
Final Discrete | Passive | Most accurate. Time-dependent. Computed by NGS every four weeks.
Final Running | CORS | Continuous time-dependent CORS coordinates. Checked by NGS every day.
Reference Epoch | Passive and CORS | Modeled from Final Discrete, Final Running, IFVM2022 and GeMS. Computed by NGS every five years.

## Slide 43: New Types of Coordinates
Reported
  “These are from any source where the coordinate is directly reported to NGS without the data necessary for NGS to replicate the coordinate.”
    Scaled
    From NCAT or Vdatum
      NGS Coordinate Conversion and Transformation Tool (NCAT)
    Hand Held / Smartphone
    Reported directly from an RTK rover without data files

## Slide 44: Reported Coordinates

## Slide 45: New Types of Coordinates
Preliminary
  “These are coordinates at survey epoch that have been computed from OPUS, but not yet quality checked and loaded into the National Spatial Reference System Database (NSRS DB).”
    User-computed values, such as they might get today from either OPUS-S or OPUS-Projects
    “Preliminary” coordinates are the only coordinates a user will get directly from OPUS

## Slide 46: New Types of Coordinates
Reference Epoch
  “These are coordinates which have been estimated by NGS, from time-dependent (final discrete and final running) coordinates, at an Official NSRS Reference Epoch (ONRE)”
    NAD 83(2011) epoch 2010.00 (sort of) would’ve fallen under this category
    These will be computed by NGS every 5 years
      On a schedule 2-3 years past ONRE
        2020.00 coordinates will be computed in CY 2022
        2025.00 coordinates will be computed in CY 2027

## Slide 47: New Types of Coordinates
Final Discrete
  “These are coordinates computed by NGS using submitted data and metadata, checked and adjusted and referenced to a single survey epoch.”
    These represent the best estimates NGS has of the time-dependent coordinates at any mark
    Survey epochs:
      GNSS: Each GPS Month
        Stand-alone occupations, RTK/RTN, Campaigns, etc
      Leveling: Annually
        Orthometric heights: Leveling adjusted to GNSS-based orthometric heights

## Slide 48: New Types of Coordinates
Final Running
  “Of all types of coordinates on a mark, these are the only ones which will have a coordinate at any time.”
    Generally will only be available at each CORS
      Also being called the coordinate function
      Which will be generated by a “fit” to daily processed data

## Slide 49: Using the modernized NSRS
OPUS
  Will include stand-alone GNSS (like “OPUS-S” and “OPUS-RS”)
  Will include mark discovery, recovery and reporting
  Will include project management and analysis for:
    GNSS (including RTK and RTN!)
    Leveling
    Classical
    Gravity
    All in one project!
  Will have a “submit to NGS” button which replaces “bluebooking”

## Slide 50: Using the modernized NSRS
OPUS
  Guidance (such as pre-selected CORSs and assistance in locating marks in project areas)
  Users will decide what control to hold fixed and what epochs they wish to set for the adjustment
    “Preliminary coordinates”
  If submitted to NGS, we will harvest your raw data and use it to compute Final Discrete coordinates

## Slide 51: Using the modernized NSRS
GNSS is your only entry (for now)
  Leveling and Classical surveys will need some GNSS if you wish to submit your survey to NGS for inclusion in the NSRS database
    Some GNSS = RTK or RTN is fine
    No decision yet on whether OPUS will operate if projects have no GNSS
      If it does, this tends to encourage reliance upon passive control
        which is “so 90’s”
          (1890s!)

## Slide 52: So much more…
New version of PAGES
  GPS, Galileo, GLONASS, Beidou, QZSS, etc.
  Target: 15 minute occupations
OPUS expansion plan
  RTK/RTN: 2019
  Leveling, Classical, Gravity: 2020-2025
  Fully integrated (GPS projects with leveling and gravity? No problem!)
  Ease of submission to NGS for inclusion in the NSRS
New Mark Recovery Tool
  Smart-phone enabled. In beta now! beta.ngs.noaa.gov/cgi-bin/recvy_entry_www.prl
Fully integrated toolkit
  NCAT and VDatum

## Slide 53: 2020 NSPS National Student Competition
The 2022 North American and Pacific Terrestrial Reference Frames (NATRF2022 and PATRF2022) and the North American-Pacific Geopotential Datum of 2022 (NAPGD2022) and their application in your jurisdiction.
Observation: The Puerto Rico students may feel left out, without CATRF2022 explicitly called out.
Ideas for students:
  Preparing massive coordinate files for transformation into NATRF2022 epoch 2020.00
  Comparison of NATRF2022 and PATRF2022 in the deformation zone of CONUS
  Designing GNSS surveys to work within GPS Month restrictions

## Slide 54: Thank you!

## Slide 55: Questions?

## Slide 56: Extra Slides

## Slide 57: Terminology
The following terms (and more) are defined meticulously in BP3 in a coordinated effort within NGS and with the IERS:
  Point, Mark, Station, Site, ARP, GRP, Site Marker, CORS, the NOAA CORS Network
    GRP = Geometric Reference Point – the official point on a station to which all coordinates refer
As a direct fallout: NGS will no longer provide CORS coordinates at an ARP, only to a GRP
  An antenna has an ARP.
    A CORS only sometimes has an antenna.
      Therefore a CORS only sometimes has an ARP.
      But it always has a GRP.
        The ARP and GRP are only sometimes coincident in space when the antenna is mounted at a CORS
  The GRP gets a Permanent Identifier (PID)

## Slide 58: Terminology
“CORS” is an acronym
  It is singular (S means “Station”, not “Stations”)
  It will no longer be used to describe the network of all such stations
    That will, for now, be called the NOAA CORS Network, or NCN
      Which has a subset of stations called the NOAA Foundation CORS Network, or NFCN
  Its plural form is CORSs
    No apostrophe, No “es” and no skipping the “s”
    GODE is a CORS
      Not “a CORS site”
        And definitely NOT “a CORS Station”
          That’s like “an ATM machine”
    GODE and 1LSU are CORSs
    GODE and 1LSU belong to the NOAA CORS Network
    TMG2 is a NOAA Foundation CORS
    TMG2 and FLF1 are NOAA Foundation CORSs
    TMG2 and FLF1 belong to the NOAA Foundation CORS Network

## Slide 59: Terminology
“OPUS”
  Online Positioning User Service
  Adopted as the general term for all of our online positioning software
    Rather than “-Projects” , “-S” , etc
    Basically “do it with OPUS” should be applicable to a wide variety of tasks
      Recon, Mark Recovery, GPS, Leveling, Gravity, Classical

## Slide 60: New Way of Operating the NOAA CORS Network (NCN)

## Slide 61: New Way of Operating the NOAA CORS Network (NCN)
Each CORS will get a coordinate function
  Actually three functions, X(t), Y(t), Z(t), in the ITRF2014 frame
  In the strict mathematical definition of “function”
    For any given “t”, there is one and only one X , Y and Z
    We actually do this today, just that the functions are piecewise linear
  We are NOT limiting our “modernized NSRS” discussions of CORS coordinate functions to linear functions only!
    But have made no further decisions yet

## Slide 62: Examples of what non-linear CORS coordinate functions look like

## Slide 63: New Way of Operating the NOAA CORS Network (NCN)
Philosophy:
  The NOAA CORS Network (NCN) will be self-consistent, meaning:
    The impact of a user’s CORS choices within their project will not exceed a small, statistically acceptable value:
      Horizontal < 5 mm, Vertical < 10 mm
  On a daily basis NGS must be able to detect, and react to, persistent disagreement between daily solutions and the current “coordinate function” assigned to any CORS in the NOAA CORS Network (NCN)

## Slide 64: Persistent Disagreement
The point:
  It’s not enough to say “each CORS is good to 1 cm in ellipsoid height”.
    That phrase is vague, lacking what it means to be “good to 1 cm”.
  NGS will define and publish “persistent disagreement”
    Possible component: A persistent non-zero average disagreement
    Possible component: A persistently deviating disagreement
  And NGS will define what happens when a CORS exhibits “persistent disagreement”

## Slide 65: New Way for USERS to Process GNSS Projects

## Slide 66: GNSS: Time Span…
GNSS projects have no time limit.
  (Leveling does. More on that later)
  But they will be processed by NGS in GPS Months
*

## Slide 67: GNSS: Processing by users in OPUS
GNSS projects, processed by users using OPUS, must always be processed by GPS month as a first step
  Multiple occupations on a point within a GPS month will be adjusted together
  Coordinate functions from the IGS network or the NOAA CORS Network are the only allowable control
  These are effectively the identical steps NGS will use in-house to compute Final Discrete Coordinates (FDCs) from your data
    Except NGS will merge your data with all other data in the nation during each GPS month
  This process will be built into OPUS as the default, making it easy for users to quickly perform the adjustment
  Afterwards, users may move on to a second step…
*

## Slide 68: GNSS: Processing by users in OPUS
As a second step, a user may do many alternative things…
  Adjust to some epoch that is convenient to them…
  Hold any CORSs or passive control as constraints…
This two-step approach is a form of sequential adjustments and allows a win-win:
  NGS gets to see the user-computed time-dependent “preliminary” coordinates, which have been computed by GPS Month
    Which will be checked against “final discrete” coordinates computed by NGS
  The user gets whatever adjustment and/or coordinates fulfill their contractual needs
  Redundancy checks can occur both within a GPS month (at step 1, if multiple occupations occur in 1 GPS month) and across GPS months (at step 2, if occupations occur in different GPS months)

## Slide 69: New Way of Processing Leveling Projects

## Slide 70: Leveling: Time Span…
Leveling projects must not exceed 12 sequential months
  Longer projects must be broken into sub-projects each spanning less than 12 sequential months
A compromise between:
  Treating “1 GPS Month” as “simultaneous” in the GNSS arena, and
  Acknowledging that leveling surveys often take weeks to months to conduct
Mixed with the reality that:
  You can’t solve for time-dependent orthometric heights in most leveling projects

## Slide 71: Leveling: GNSS required
For the immediate years following 2022, NGS will require that all leveling projects turned in have GNSS on primary control
  Minimum of 3 points
  Maximum spacing of 30 km
  At least two occupations:
    +/- 14 days of beginning of leveling
      But also within the same GPS month
    +/- 14 days of ending leveling
      But also within the same GPS month
  If leveling exceeds 6 months, must have a 3rd, middle occupation
A GNSS “occupation” can mean “RTK/N”!

## Slide 72: Leveling: Step 1 Identify project marks

## Slide 73: Leveling: Step 2 Identify primary control marks (PCM)
Each PCM is within 30 km of at least one other PCM
< 30 km
< 30 km
< 30 km
< 30 km

## Slide 74: Leveling: Step 2 Identify primary control marks (PCM)
No point over 30 km from a PCM

## Slide 75: Leveling: Step 3 Initial GNSS on all PCMs
All PCMs, required: within +/- 2 weeks of the start of leveling
Each PCM, required: 2+ occupations within the same GPS month
All PCMs, recommended: Use the same GPS month

## Slide 76: Leveling: Step 4 Leveling
Finished in under 12 months
If greater than 6 months, need a mid-project GNSS set on PCMs

## Slide 77: Leveling: Step 5 (if 6-12 months) Mid-project GNSS on all PCMs
All PCMs, recommended: Near midpoint of project
Each PCM, required: 2+ occupations within the same GPS month
All PCMs, recommended: Use the same GPS month

## Slide 78: Leveling: Step 6 Final GNSS on all PCMs
All PCMs, required: within +/- 2 weeks of the end of leveling
Each PCM, required: 2+ occupations within the same GPS month
All PCMs, recommended: Use the same GPS month

## Slide 79: Leveling: Processing
All GNSS data processed into GPS months, as per normal processing
These are then adjusted to a mean epoch of the entire leveling survey to yield “representative” orthometric heights that serve as control over the entire leveling project
Stochastic but no time dependency

## Slide 80: Leveling: Processing
The pre-computed GNSS-based orthometric heights are held as stochastic constraints in the adjustment of leveling data
Use math model from NOAA TM NOS NGS 74
Separates out errors in GNSS from Leveling:
  Absolute heights will have standard deviations that are “at GNSS accuracy levels”
  Differential heights will have standard deviations that are “at leveling accuracy levels”

## Slide 81: Leveling: Absolute errors
Consider this quote from a concerned user:
  “In the old NSRS, I could pull the datasheet for a point in California and see that NGS trusted the NAVD 88 height to 1 millimeter. Now, you’re telling me to use RTN to establish orthometric heights in the same area, and I’m getting heights with 4 cm standard deviations! Why are your heights less accurate today than in the past?”

## Slide 82: New Way for NGS to Process and store GNSS Data: Final Discrete Coordinates (FDCs)

## Slide 83: GNSS: Monthly workflow…
Every GPS month (say the first Monday of that GPS month), NGS will “process the GPS month of 12-16 weeks ago” by doing the following:
  Ensure that the “final” IGS orbits for the GPS month that spans 12-16 weeks prior are available
    If not, hold off on this until they are
  Create an in-house project named for that prior GPS month
  Farm all data (collected during that GPS month) from all projects submitted to NGS, and put them all into the in-house project

## Slide 84: Processing by GPS Month…
GPS Month 587
GPS Month 588
GPS Month 589
GPS Month 590
GPS Month 591
GPS Month 592
GPS Month 593
GPS Month 594
All GNSS data collected in this
GPS month…
…are processed in this GPS month…
…to create Final Discrete coordinates for
this GPS month….
…which are loaded into the
NSRS database in this GPS month.

## Slide 85: Processing by GPS Month…
GPS Month 587
GPS Month 588
GPS Month 589
GPS Month 590
GPS Month 591
GPS Month 592
GPS Month 593
GPS Month 594
All GNSS data collected in this
GPS month…
…are processed in this GPS month…
…to create Final Discrete coordinates for
this GPS month….
…which are loaded into the
NSRS database in this GPS month.

## Slide 86: GNSS: Monthly workflow…
Adjust all that data together
Take the results of this adjustment and load them into the NSRS database as “final discrete” coordinates

## Slide 87: GNSS: Monthly workflow…
Q: What about users’ projects that span more than 12-16 weeks?
A: NGS will provide a way for a user to “allow NGS to farm my data as it is loaded to my ongoing project”
  Thus NGS needn’t wait for them to finish their project and click “submit”.
  Will require some sort of metadata validity statement from the user for each data file uploaded

## Slide 88: GNSS: Monthly workflow…
Q: What if a user turns in data more than 12-16 weeks after it was collected?
A: NGS will have a “holding bin” for such data. Occasionally, but not more than 1/year, NGS will sweep up all data in the holding bin, and put that data into the proper in-house GPS-month-based projects, depending on the GPS month of that data.
  Since those in-house projects have already been adjusted once before using data that WAS submitted within the 12-16 week limit, and “final discrete” coordinates were computed on those early-submitted data, NGS will hold the “final discrete” coordinates on that early-submitted data as “fixed”, and adjust the later-submitted data only.

## Slide 89: New Way for NGS to Process and store GNSS Data: Reference Epoch Coordinates (RECs)

## Slide 90: GNSS: Every five years…
Official NSRS Reference Epochs (ONREs) will happen every five years, beginning with 2020.00.
Every ONRE will have a project associated with it
  To estimate the Reference Epoch Coordinates (RECs) at each ONRE
  That project will begin 2 years after the ONRE and will end 3 years after it
    Thus the project to create 2020.00 RECs will run January 1-December 31, 2022
    Using data collected through the end of 2021
Error estimates in RECs will grow larger every five years for those points which are not regularly observed
Once computed, the REC at an ONRE for a point will stand forever, unless corrected for a blunder

## Slide 91: Miscellaneous

## Slide 92: Miscellaneous
OPUS-RS will be modified to work in the modernized NSRS online, but will not be used to populate the NSRS Database
  To use the new terminology: it will provide preliminary coordinates
  To acknowledge the problems with integrating this software with any other version of OPUS
  In preparation for its eventual mothballing / replacement by the new multi-GNSS PAGES

## Slide 93: Future Discussions/Decisions:
What will be the nature of the coordinate functions at each CORS?
How will those functions be used to detect, and correct, persistent disagreement between daily solutions and the coordinate functions?

## Slide 94: Future discussions: What will be the nature of the “coordinate functions” at each CORS? How will those functions be used to detect, and correct, persistent disagreement between daily(?) final discrete coordinates and the coordinate functions?

## Slide 95: CORS Processing
This is from the most recent
“short term” plots of GODE
Note, what could be called a “persistent
non-zero average disagreement” between
daily solutions and the assigned coordinate
function (about 5 mm in North, for example)
Not “persistently growing disagreement”, as
the average disagreement isn’t getting
worse.

## Slide 96: CORS Processing
This is from the most recent
“long term” plots of GODE

## Slide 97: CORS Processing
An example of
how OSU processes
daily data (blue) into
“coordinate functions”
(red).
Coordinate functions
contain:
Linear terms
Polynomials (to 4)
Annual/Semi-Annual
Exponentials
Discontinuities

## Slide 98: CORS Processing
An example of
how OSU processes
daily data (blue) into
“coordinate functions”
(red).

## Slide 100: Why “1 GPS Month”?
The NSRS should be more accurate than everything built upon it
Has everything to do with systematic movement of passive marks, not random error in GPS
In order to properly adopt time-dependent coordinates, NGS must pick some time span that we call “simultaneous”
During that time span, the mark must not move systematically (in the ITRF2014 frame) by more than some set threshold

## Slide 101: Why “1 GPS Month”?
What threshold to pick?
  Do NOT confuse random errors with systematic movement
Chart: UP (cm)
To the left is a daily
set of GPS-derived heights (blue) collected from an antenna which was systematically lowered by 1 mm every week over 14 weeks.
Random error: +/- 0.5 cm (OP)
See that the “mm/week” trend is definitely manifest in the blue curve, despite the “half cm of noise”!

## Slide 102: Why “1 GPS Month”?
What threshold to pick?
  Because we are an agency that has long cared about millimeters…
    See, for example, leveling accuracy. See, for example, XYZ coordinates of all CORSs.
  Because one half millimeter is the most systematic error one can absorb before rounding error could make you “off by a millimeter”…
  Because GPS noise is not the same as systematic mark movement…
  Because a SOP which works for the worst case will work for all cases…
  Because the “worst case” (fastest horizontal movement) in the USA is in Hawaii at 0.5 mm in 3 days…
  Because the “worst case” (fastest subsidence we’ve ever observed in the USA) is around 0.5 mm in 1 day…
  The right answer should be “1 day”, but instead…
  NGS has proposed that we call “1 GPS Month” as “Simultaneous”, which is worse than the “1 day” or even “3 days” we should use, but which is a round number, easy to work with and not too far outside of capturing 0.5 mm of movement everywhere in the USA.
    Plus when we do the “GPS month” adjustments, we will ALSO introduce the IFVM, which will help account for any systematic movement over the four week time span
    And four weeks is the median length of time of most projects turned in to NGS

## Slide 103: New Way of Operating The CORS Network
100% of CORS available to OPUS every day will pass a regular statistical test for persistent disagreement
  One possible definition of “persistent disagreement”: For 14 days in a row, the absolute value of the average of the difference between “daily solutions” and the “coordinate function” assigned to that CORS, since the last known discontinuity at that CORS, exceeds 5 mm in latitude or longitude or 10 mm in ellipsoid height
    Just as reasonable, we might say “…since the last 6 months…” rather than “…since the last known discontinuity…” – More on that later.
    If the CORS fails this test pull CORS out of OPUS
      Watch, evaluate, update coordinate function and get the CORS back into OPUS as soon as the coordinate function has been updated so that the statistical test is passed
      Likely: Do NOT update function for any days BEFORE the failure, only AFTER. This may mean introducing a derivative discontinuity, but not a functional discontinuity
        This prevents users from having to continually respond to a changing historical function at each CORS

## Slide 104: Persistent Disagreement
Notes: Begin with daily solutions on a CORS, and an assigned coordinate function, in this case for ellipsoid height. While subtle, it should be clear that the daily solutions are drifting away from the assigned coordinate function.
And while, day to day, there is a large (5-10 cm) disagreement between the daily solutions and the coordinate function, due *mostly* to noise in the daily solutions, that disagreement begins to show a small (mm/year) non-random nature as time goes on. That is, there is seen a “persistent disagreement”. The question is “how to quantify that persistent disagreement”. The answer is: “by looking at the average of daily disagreements over some period of time, and seeing a consistent deviation from zero”.

## Slide 105: Persistent Disagreement…
Notes: We now introduce the “absolute value of the average difference between daily solutions and coordinate functions over ‘some span of time’ ”. The time span for the averages shown is:
Yellow: Just the last 6 months of data
Gray: The lifespan of the CORS

## Slide 106: Persistent Disagreement…
Notes: For the first 6 months or so, the absolute value of the average disagreement between the daily solutions and the assigned coordinate function is highly unstable, ruled mostly by the noise in the daily solutions

## Slide 107: Persistent Disagreement…
Notes: After six month, things settle down.
Note that, as would be expected, the good disagreement during the early life of the CORS causes the gray line to grow SLOWER than the yellow line. That is because the statistics of the gray line are always influenced by early, good data. The yellow line grows more quickly because it dismisses any data older than 6 months and so, as the systematic disagreement persists (see what I did there? “persistent disagreement”…), each new 6 month window gets a little worse than its predecessor and is not “improved” by good data at the beginning of the life of the CORS.

## Slide 108: Persistent Disagreement…
14 days in a row, the absolute
average disagreement (looking
back the life of this CORS)
exceeded 1 cm.
CORS went “bad” at 2 ½ years
after last known discontinuity
Notes: The persistent disagreement test might read “For 14 days in a row, the absolute value of the average disagreement between daily solutions and the CORS coordinate function exceeded 1 cm”, where “average” is over some time span:
Yellow: Just the last 6 months
Gray: Since the last discontinuity
In this case, it means that it takes 2 ½ years for persistent disagreement to occur at this CORS, under the “since last discontinuity” average.

## Slide 109: Persistent Disagreement…
14 days in a row, the absolute average
disagreement (looking back just 6 months)
exceeded 1 cm.
CORS went “bad” at 1 ½ years
after last known discontinuity
Notes: In this case, it means that it takes only 1 ½ years for persistent disagreement to occur at this CORS, under the “last six months” average.