## Slide 1: Modernizing the National Spatial Reference System
GEO Week 2024
February 12, 2024
Brian Shaw
brian.shaw@noaa.gov

## Slide 2
Brian Shaw
Rocky Mountain Advisor
brian.shaw@noaa.gov

## Slide 3
NGS Resources
NGS Training Center
  https://geodesy.noaa.gov/web/science_edu/training/
Educational Videos
  https://geodesy.noaa.gov/datums/newdatums/WatchVideos.shtml
NGS Webinar Series
  https://geodesy.noaa.gov/web/science_edu/webinar_series/
Geospatial Summit (2021, 2019 recorded sessions)
  https://geodesy.noaa.gov/geospatial-summit/
Presentation Library
  https://geodesy.noaa.gov/web/science_edu/presentations_library/

## Slide 4
NGS’s Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
…………………………………………….........................
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, orientation, and shoreline throughout the United States.
Sectors that Rely on Geodesy
Land
Surveying

## Slide 5
The Earth is Infinitely Complex
Build Models to Simplify

## Slide 6
Datums and Reference Frames
A reference surface or framework to reference your data to for consistency
aka P(Lat,Lon,Ht)
= lat.
= long.
= ht.
X,Y,Z vs Lat, Lon, Ht
60”, 2019
52”, 2018
46”, 2017

## Slide 7
Why Modernize the NSRS
Current models built on old technology
  NAD 83 not truly Geocentric (~2.2m)
  NAVD 88 relies on marks in the ground
  and is not easily maintained
  Today’s technology needs better accuracy

## Slide 8
The Future Reference Frames
Tectonic Plate based
Each Plate is based on the same
densified ITRF model
North America NATRF
Caribbean CATRF
Pacific PATRF
Mariana MATRF
The tectonic plates “fixed” for the
2022 Terrestrial Reference Frames
NATRF2022
PATRF2022
MATRF2022
CATRF2022

## Slide 9
NAPGD2022 Geopotential Datum
North American-Pacific Geopotential Datum of 2022
Models included: Geopotential Deflection Gravity
Geoid
Guam/CNMI
American Samoa
¼ Earth’s Surface
Not a vertical datum, it is more than just heights.

## Slide 10
Shift and Drift
A sudden shift
  Horizontal change: 0.5 to 4 m (1.5 to 13 ft)
  Ellipsoid height change: ±2 m (±6 ft)
  Elevation change: -0.5 to +2 m (-1.5 to +6 ft)
A continuous drift
  Coordinates associated with specific dates
Two components of drift:
  Tectonic plate rotation (easy to model, 2D only)
  All other residual motion (hard to model, 3D)

## Slide 11
Shift: datum changes
~1 to 1.5 meters North America
~2.5 to 4 meters in Pacific
0 to 1.3 meters CONUS

## Slide 12
Drift: Plate Tectonics and Velocities
Annual changes to
ITRF2014 coordinates

## Slide 13
How Can You Prepare
Metadata is essential
    Improves reliability and accuracy of data
    Increases value and usefulness
Transform and collect data in current datums
    NAD 83 (2011), NAVD 88
Make sure to note Geoid Models used for GNSS data

## Slide 14
Questions?
Brian Shaw
brian.shaw@noaa.gov
Magnitude of the Deflection of the Vertical