## Slide 1: Dynamic Heights from GNSS
Daniel R. Roman, Ph.D.
Chief Geodesist

## Slide 2: NGS Vision
Everyone accurately knows where they are and where other things are anytime, anyplace.
NGS 10 Year and Strategic Plans provide a more detailed description of NGS and the vision for the future looking ten years out.

## Slide 3: Replace NAD 83
~2.24 m
NAD 83 origin
“2022” origin
Earth’s Surface
hNAD83
h”2022”
Simplified concept of NAD 83 vs. “2022”
fNAD83 – f”2022”
lNAD83 – l”2022”
hNAD83 – h”2022”
all vary smoothly by latitude and longitude

## Slide 4: Vertical Shifts
Ellipsoidal
Orthometric

## Slide 5: NSRS Modernization
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CTRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PTRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MTRF2022)

## Slide 6: NSRS Modernization
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical
=> International Great Lakes Datum of 1985

## Slide 7: HC vs. NAVD 88 Datum Defect

## Slide 8: GL WLS Stations
Notes: Of 53 WLS, 14 are CORS. At all sites, BM are adjacent to WLS. CO-OPS levels between BM’s and WLS table. NGS GPS’ BM. Results in transfer of geometric coordinates to table and then to water surface.
Will be exchanging CO-OPS leveling on US side with Canada for their WLS. Canada has completed their GPS analysis on BM (US still processing). Will look at various averages (Summer, yearly). Look forward to models removing metorological impacts as well as any standing topography.

## Slide 9: Method
WLS Housing
CORS Antenna
Receiver
ETG
IGLD 85 Datum surface
BM
ETG Table
(datum)
Great
Lake
Inverted rod
leveling
Geometric coordinates of water surface

## Slide 10: Conceptual Plan
Each Lake surface conforms to a specific geopotential value (Wi) and dynamic height
ellipsoid
C0 (geoid)
C1
C2
C3
DH3 = W0 – W3
gamma45
DH2 = W0 – W2
gamma45
DH1 = W0 – W1
gamma45
Notes: (1) Neglects any standing water topography (wind set)
(2) Assumes sufficient resolution of geopotential number

## Slide 11: Practical Aspects
Need 1’ resolution(1) (d/o 10,800) SHM
Only have 5’ resolution (2) (d/o 2160) SHM plus 1’ geoid grid
ellipsoid
C0 (geoid)
C1
C2
C3
Notes: (1) Previous analysis shows that omission from > 1’ resolution exceeds cm-level
(2) xGEOID16B available at https://beta.ngs.noaa.gov/GEOID/xGEOID16/
(3) W0 by is defined as 62,636,856.00 m2/s2
N (1’)
N (5’)
W(5’) g(5’)

## Slide 13: Method
Ideally, use 1’ reference model – degree 10,800
Only 5’ models available
To approximate:
  NP from final geoid (1’)
  NP from ref. model (5’)
  WP from ref. model (5’)
  P from ref. model (5’)
First is from xGEOID16B
Rest from xGEODI16B_Ref
Use residual geoid to approximate residual geopotential value:
= – W0
= -
*
= +
= / γ45
Note that approximates

## Slide 14: Geometric Coordinates of WS (CORS)
Column | A | F | G | L | M | O
Station | Location | 2015 mean WL HT | Summer mean (HC) WL HT | Latitude of CORS ARP | Longitude of CORS ARP | HAE of Summer mean WL
Units |  | m | M | dec. deg. (N) | dec. Deg. (E) | m
Datum |  | IGLD85 | IGLD85 | IGS08 | IGS08 | IGS08
9063020 | Buffalo | 174.306 | 174.559 | 42.87755697 | 281.10955496 | 138.214
9063063 | Cleveland | 174.314 | 174.559 | 41.54074488 | 278.36485371 | 139.091
9063079 | Marblehead | 174.310 | 174.606 | 41.54368360 | 277.26854509 | 137.971
9099004 | Pt. Iroquois | 183.565 | 183.660 | 46.48458324 | 275.36915966 | 146.043
9099018 | Marquette | 183.597 | 183.694 | 46.54554809 | 272.62130392 | 147.845
9099090 | Grand Marais | 183.592 | 183.692 | 47.74855226 | 269.65874853 | 151.946

## Slide 15: Geopotential Model-Derived Heights (CORS)
A | Q | R | S | T | U | V
Location | Ortho Height | Dynamic Height | Dynamic Height | Dynamic Height | Dynamic Height | Dynamic Height
 | m | m | m | m | m | m
 | xGEOID16B | EGM2008 | EIGEN6c4 | xGEOID16A_REF | xGEOID16B_Ref | xGEOID16B
Buffalo | 174.052 | 174.014 | 173.997 | 174.016 | 174.011 | 174.004
Cleveland | 174.087 | 174.023 | 174.011 | 174.011 | 174.033 | 174.019
Marblehead | 174.088 | 174.002 | 174.005 | 174.024 | 174.026 | 174.016
Pt. Iroquois | 182.983 | 182.981 | 182.977 | 183.000 | 182.990 | 182.992
Marquette | 182.976 | 182.997 | 183.012 | 183.026 | 183.013 | 182.992
Grand Marais | 182.935 | 182.970 | 182.970 | 182.986 | 182.995 | 182.980
Notes: This is only for 2015 values. Will look at prior solutions (2010, 2005, 1997) to evaluate geopotential models at different Lake levels.

## Slide 16: Geometric Coordinates of WS (Campaign GPS-Canadian solution)
Location | BM Eht | ETG EHt | Latitude * | Longitude * | HAE of Summer mean WL | CORS-BM Diff.
Units | m | m | dec. deg. (N) | dec. Deg. (E) | m | m
Datum | IGS08 | IGS08 | IGS08 | IGS08 | IGS08 | IGS08
Buffalo | 140.135 | 141.988 | 42.87744444 | 281.10952778 | 138.241 | 0.027
Cleveland | 142.230 | 141.650 | 41.54086111 | 278.36452778 | 139.098 | 0.007
Marblehead | 140.573 | 144.389 | 41.54083333 | 277.26861111 | 137.993 | 0.022
Pt. Iroquois | 150.318 | 148.610 | 46.48450000 | 275.36911111 | 147.179 | 0.136
Marquette | 152.148 | 151.702 | 46.54555556 | 272.62138889 | 147.890 | 0.045
Grand Marais | 155.183 | 154.415 | 47.74855556 | 269.65872222 | 151.868 | -0.078
* Latitude/longitude are from hand held GPS at WLS station – height transferred from BM

## Slide 17: Geopotential Model-Derived Heights (Campaign GPS-Canadian solution)
Location | Latitude * | Longitude * | Eht | N | Oht | DHt
 | dec. deg. (N) | dec. Deg. (E) | m | m | m | M
 | IGS08 | IGS08 | IGS08 | xGEOID16B | xGEOID16B | xGEOID16B
Buffalo | 42.87744444 | 281.10952778 | 138.241 | -36.804 | 175.045 | 174.031
Cleveland | 41.54086111 | 278.36452778 | 139.098 | -35.896 | 174.994 | 174.026
Marblehead | 41.54083333 | 277.26861111 | 137.993 | -37.009 | 175.002 | 174.038
Pt. Iroquois | 46.48450000 | 275.36911111 | 147.179 | -36.945 | 184.124 | 183.128
Marquette | 46.54555556 | 272.62138889 | 147.890 | -36.007 | 183.897 | 183.037
Grand Marais | 47.74855556 | 269.65872222 | 151.868 | -31.748 | 183.616 | 182.902
Notes: This is only for 2015 values. Will look at prior solutions (2010, 2005, 1997) to evaluate geopotential models at different Lake levels.

## Slide 18: Summary
Dynamic Heights can be derived from a geopotential model and GNSS
A one arc-minute model would be ideal
Otherwise, approximations are required
CORS better than campaign GPS
Further evaluation awaits final adjustment of GPS campaign data
Water topography issues still remain

## Slide 19: Questions?
Daniel R. Roman
Chief Geodesist
National Geodetic Survey