## Slide 1
The U.S. National Spatial Reference System in 2022
Daniel R. Roman, (Chief Geodesist)
NOAA’s National Geodetic Survey

## Slide 2: Outline
Why change?
Naming conventions of NSRS 2022
Geometric component
  Regional Terrestrial Reference Frames
  Intra Frame Velocity Models
Geopotential component
  Static
  Time-varying
Future Plans and Summary

## Slide 3: NGS Vision
Everyone accurately knows where they are and where other things are anytime, anyplace.
NGS 10 Year and Strategic Plans provide a more detailed description of NGS and the vision for the future looking ten years out.

## Slide 4: Replace NAD 83
~2.24 m
NAD 83 origin
“2022” origin
Earth’s Surface
hNAD83
h”2022”
Simplified concept of NAD 83 vs. “2022”
fNAD83 – f”2022”
lNAD83 – l”2022”
hNAD83 – h”2022”
all vary smoothly by latitude and longitude

## Slide 5: Vertical Shifts
Ellipsoidal
Orthometric

## Slide 6: Outline
Why change?
Naming conventions of NSRS 2022
Geometric component
  Regional Terrestrial Reference Frames
  Intra Frame Velocity Models
Geopotential component
  Static
  Time-varying
Future Plans and Summary

## Slide 7: NSRS Modernization
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CTRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PTRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MTRF2022)

## Slide 8: NSRS Modernization
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 9: NSRS Modernization
  The Old:
  Bluebooking
  (PAGES, ADJUST, B files, G files, FORTRAN)
  The New:
  OPUS-Projects for Everything
  GPS
  Leveling
  Traverse
  Gravity
  RTK/RTN
  More?

## Slide 10: Outline
Why change?
Naming conventions of NSRS 2022
Geometric component
  Regional Terrestrial Reference Frames
  Intra Frame Velocity Models
Geopotential component
  Static
  Time-varying
Future Plans and Summary

## Slide 11: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Remove long-standing non-geocentricity of NAD 83 frames
All four : identical to IGSxx at a TBD epoch
  2020.00?
All four : differ from IGSxx by plate rotation only
  Updated Euler Pole determination for rigid plate only

## Slide 12: Plate-(pseudo)fixed frames
NAD 83(NSRS2007)
Epoch 2002.0
NAD 83(2011)
Epoch 2010.0
If NAD 83 were truly “plate
fixed” then an 8 year
epoch change would not
yield the systematic
plate rotation seen here.
(*)TRF2022 will determine
a new Euler Pole rotation
for each of 4 plates.
(*)=NA, C, T or P
NAD 83(2011) minus NAD 83(NSRS2007)

## Slide 13: Four Frames/Plates in 2022
Previous NGS frames (Snay 2003)
  North America
  Pacific
  Mariana
Caribbean will be treated as 4th frame

## Slide 14
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.

## Slide 15: Fixed-Epoch Transformation NAD 83 to “2022”

## Slide 16: NATRF2022 frame is rigid and fixed to rigid part of the N.A. plate
Non-rigid part of the N.A. plate
(deformation)
area

## Slide 17: Outline
Why change?
Naming conventions of NSRS 2022
Geometric component
  Regional Terrestrial Reference Frames
  Intra Frame Velocity Models
Geopotential component
  Static
  Time-varying
Future Plans and Summary

## Slide 18: So if not HTDP, then what?
NATRF2022 would account for most horizontal velocity over time
Remaining signal typically modeled by HTDP (now)
In future, a TBD velocity model would be applied to account for that and vertical
The simplest solution is gridded CORS velocities

## Slide 19: Horizontal velocities after Repro1
Note scale difference between West (10 mm/yr) and east (2 mm/yr)

## Slide 20: CORS Implied Vertical Velocities - Control
Courtesy Galen Scott

## Slide 21: CORS Implied Vertical Velocities – Heat Map
Courtesy Galen Scott

## Slide 22: How to use this information?
Assuming CORS spacing is sufficient – grid
  Yields horizontal (NEV & GIA) plus vertical signal
Vertical important for orthometric heights:
  Ht = (ht0 + (t-t0)*dh/dt) - (Nt0 + (t-t0)*dN/dt)
    Where Ht is orthometric height at desired time
    ht0 is ellipsoidal height at epoch (maybe 2020.0)
    Nt0 is geoid height at epoch
    dh/dt is change in ellipsoid height over time
    dN/dt is change in geoid height over time

## Slide 23: What if this isn’t enough?
Will investigate sufficiency of gridded CORS
Concern is dynamic areas: horizontal & vertical
Will look at other models to evaluate
Cost versus benefit
  What we can easily do in-house and support
  increased complexity from outside models
Alternatively, users can model their own …

## Slide 24: Outline
Why change?
Naming conventions of NSRS 2022
Geometric component
  Regional Terrestrial Reference Frames
  Intra Frame Velocity Models
Geopotential component
  Static
  Time-varying
Future Plans and Summary

## Slide 25: NAPGD2022
Begins with a 3-D global geopotential model
Then, derivative products are built
  GEOID2022
  DEFLEC2022*
  NGRAV2022*
* Names not yet finalized

## Slide 26: NAPGD2022
GEOID2022 (et al.) over the North America/Pacific/Caribbean/Central America/Greenland region will range from
0 to 90 latitude and from 170 to 350 longitude.
GEOID2022 (et al) over Guam/CNMI:
11-22, 143-148
GEOID2022 (et al) over American Samoa:
-16 to -10, 186-193

## Slide 27: Outline
Why change?
Naming conventions of NSRS 2022
Geometric component
  Regional Terrestrial Reference Frames
  Intra Frame Velocity Models
Geopotential component
  Static
  Time-varying
Future Plans and Summary

## Slide 28: NAPGD2022: Pre-decisional items
Three types of geoid change will be tracked
  Size, Shape, Change to W0
Time/Space span evaluated for cost/benefit ratio
Examples:
Issue | Type of Change | Temporal Period | Temporal Duration of Geoid Change | Spatial Impact | Magnitude of geoid change | Decision
Accretion of Space Dust | Size | Secular | Permanent | Global | 4x10-7 mm / y | Ignore
Earthquakes | Shape | Episodic | Permanent-ish | Local | Can be as large as a few cm | Study further
GMSL rise | W0 value | Secular | Permanent | Global | 1.7 mm / y | Provide as optional correction

## Slide 29: Time-Varying Geoid
GRACE/GFO
GeMS
Geoid Monitoring Service
Part of GRAV-D
Theresa Damiani, Ph.D. lead
SG and other meters to monitor select gravity BM’s
Supplements and validates satellite-derived models
GIA signals over Hudson Bay, Greenland, and Alaska
Figure 3 from
Tregoning et al.
(2009)
Non-Stationary
GRACE Signals

## Slide 30: Outline
Why change?
Naming conventions of NSRS 2022
Geometric component
  Regional Terrestrial Reference Frames
  Intra Frame Velocity Models
Geopotential component
  Static
  Time-varying
Future Plans and Summary

## Slide 31: Future Plans and Summary
IGS Stations => Foundation CORS (FCORS)
  Sites collocated with other techniques (IERS)
  Adopt some/build others/cover all plates
Foundation CORS => Regional CORS/Repro’s
  Constrain Euler solutions/CORS positions to FCORS
  Standing up IAG NA WG on Euler Pole
  Forms four separate Frames

## Slide 32: Future Plans and Summary
Models of Intraplate velocities (hor. & ver.)
  Could be simply modeled from existing CORS
    Density and quality of CORS impacts
    GIA signal must be taken into account (hor. & ver. vel.)
  Could be as complicated as Trans4D or equivalent
    How to maintain?
    Earthquakes? Re-surveys?
Orthometric heights in 2022: H(t) = h(t) – N(t) h(t) = survey epoch N(t) = N(t0) +N (t – t0)

## Slide 33: To Learn More
Visit the New Datums web page
geodesy.noaa.gov/datums/newdatums/index.shtml

## Slide 34: To Learn More
Silver Spring, MD
April 24-25, 2017
FREE
geodesy.noaa.gov/geospatial-summit/index.shtml
Attend the Geospatial Summit

## Slide 35: Questions?