## Slide 1: How NGS is Modernizing the National Spatial Reference System
Jacob Heck
Great Lakes Regional Geodetic Advisor
NOAA/National Geodetic Survey

## Slide 2: Who is NGS?
The National Geodetic Survey (1970–present)
  U.S. Coast and Geodetic Survey (1878–1970)
  U.S. Coast Survey (1836–1878)
  U.S. Survey of the Coast (1807–1836)
Nation’s Oldest Scientific Agency
U.S. Government Executive Branch
  Department of Commerce
      National Oceanic and Atmospheric Administration (NOAA)
        National Ocean Service (NOS)
          National Geodetic Survey (NGS)

## Slide 3: Regional Geodetic Advisor Program
www.ngs.noaa.gov/ADVISORS/

## Slide 4
NGS defines, maintains and provides access to the NSRS to meet our Nation’s economic, social & environmental needs
North American Datum of 1983 (NAD 83)
North American Vertical Datum of 1988 (NAVD 88)
The National Spatial Reference System (NSRS)
Latitude • Longitude • Elevation • Gravity • Shoreline Position
+ changes over time
Today’s NSRS

## Slide 5
NGS defines, maintains and provides access to the NSRS to meet our Nation’s economic, social & environmental needs
Latitude • Longitude • Elevation • Gravity • Shoreline Position
+ changes over time
North American Terrestrial Reference Frame (NATRF 2022)
Caribbean Terrestrial Reference Frame (CATRF 2022)
Pacific Terrestrial Reference Frame (PATRF 2022)
Marianas Terrestrial Reference Frame (MATRF 2022)
North America and Pacific Geopotential Datum (NAPGD2022)
Tomorrow’s NSRS
The National Spatial Reference System (NSRS)

## Slide 6
geodetic control (the NSRS) is the foundation for all geospatial products.
without Geodetic Control as a “base map” layer, GIS applications will not work properly
Accurate positioning begins with accurate coordinates
Source: Zurich-American Insurance Group

## Slide 7
A
Find the coordinates of point A
Somewhere on Earth…
You are presented with this problem…
Without any other information, the problem is unsolvable.

## Slide 8
A
Find the coordinates of point A
Wouldn’t it be fantastic if someone just provided you with a coordinate system?
Unfortunately, the Earth doesn’t come with lines of latitude and longitude just drawn all over it…
“The Earth is not a globe”
1
2
3
4
1
2
3
4
(x=1.8,y=2.6)

## Slide 9
Find the coordinates of point A
But what if someone gave you enough other points with pre-determined coordinates?
With a little measuring and trigonometry, you could certainly determine the coordinates of point A!
These “other points with pre-determined coordinates” are “geodetic control”
A
B (x=3.1,y=1.4)
C (x=2.7,y=3.9)
D (x=0.8,y=0.9)

## Slide 10
Find the coordinates of point A
Although the coordinate axes are not visible, their location and scale are implied by the given coordinates of the points B, C, and D.
It is often the job of surveyors, mappers and other geospatial professionals to determine the coordinates of many points on Earth.
It is the job of NGS to provide the geodetic control to the nation to make those jobs possible.
1
2
3
4
1
2
3
4
B (x=3.1,y=1.4)
C (x=2.7,y=3.9)
D (x=0.8,y=0.9)

## Slide 11: Horizontal Datums of the NSRS
CONUS
U.S. Standard Datum
NAD 27
NAD 83(1986)
NAD 83(“HARN”)
NAD 83(“FBN”)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
Alaska
NAD 27
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
St. Lawrence I.
St. Lawrence 1952
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
St. Matthew I.
St. Matthew 1952
St. George I.
St. George 1897
St. George 1952
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
St. Paul I.
St. Paul 1897
St. Paul 1952
NAD 83(1986)
NAD 83(2002:AK)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
CNMI
Guam 1963
NAD 83(1993:GU)
NAD 83(2002:GU)
NAD 83(MA11) epoch 2010.00
Guam
Guam 1963
NAD 83(1993:GU)
NAD 83(2002:GU)
NAD 83(MA11) epoch 2010.00
American Samoa
American Samoa 1962
NAD 83(1993:AS)
NAD 83(2002:AS)
NAD 83(PA11) epoch 2010.00
Puerto Rico
Puerto Rico 1940
NAD 83(1986)
NAD 83(1993:PR)
NAD 83(1997:PR)
NAD 83(2002:PR)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00
Hawaii
Old Hawaiian Datum
NAD 83(1986)
NAD 83(1993:HI)
NAD 83(PA11) epoch 2010.00
U.S. Virgin Islands
Puerto Rico 1940
NAD 83(1986)
NAD 83(1993:PR)
NAD 83(1997:PR)
NAD 83(2002:PR)
NAD 83(NSRS2007)
NAD 83(2011) epoch 2010.00

## Slide 12
STEEL BILBY TOWER

## Slide 14: Replacing the NAD 83s
The Old | The New
NAD 83 (2011) | NATRF2022 - The North American Terrestrial Reference Frame of 2022
NAD 83 (2011) | CATRF2022 - The Caribbean Terrestrial Reference Frame of 2022
NAD 83 (PA11) | PATRF2022 - The Pacific Terrestrial Reference Frame of 2022
NAD 83 (MA11) | MATRF2022 - The Mariana Terrestrial Reference Frame of 2022

## Slide 15
Four Tectonic Plates

## Slide 16: Euler Poles and “Plate-Fixed”
  In the ITRF, many tectonic plates have a dominant motion: rotation
  Euler Pole - point about which a plate rotates (yellow star)
NATRF2022 Euler Pole

## Slide 17
ITRF2020: Constant Frame, Rotating Plate

## Slide 18: “Plate-Fixed”
NATRF2022: Constant Frame, Rotating Plate

## Slide 19
ITRF2020 or NATRF2022

## Slide 20
Continuously Operating Reference Station (CORS) Network
2000 sites
225 organizations

## Slide 21: State Plane Coordinate System of 1983 (SPCS 83)

## Slide 22
https://geodesy.noaa.gov/SPCS/
State Plane Coordinate System of 2022 (CONUS, Alaska and Hawaii)
Three territory zones not shown:
    Puerto Rico and U.S Virgin Islands
  American Samoa
  Guam and Commonwealth of the
  Northern Mariana Islands

## Slide 23: Vertical Datums of the NSRS
CONUS
NGVD 29
NAVD 88
Alaska
NGVD 29
NAVD 88
St. Lawrence I.
- None -
St. Matthew I.
- None -
St. George I.
- None -
St. Paul I.
- None -
CNMI
NMVD 03
Guam
GVD 63
GUVD 04
American Samoa
ASVD 02
Puerto Rico
PRVD 02
Hawaii
- None -
U.S. Virgin Islands
VIVD 09

## Slide 24
NGVD 29
NAVD 88

## Slide 25: Leveling

## Slide 26: Replacing NAVD 88
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include geoid model GEOID2022
  - Surface gravity model GRAV2022
  - Deflection of the vertical model DEFLEC2022
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID18
  DEFLEC18
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 27: Gravity for the Redefinition of the American Vertical Datum (GRAV-D)
10 km data lines
70 km cross lines
20,000 ft altitude
230 kt flight speed
Hawaii
Alaska
American Samoa
Guam & CNMI

## Slide 30: NSRS Modernization: Delay
It’s official: we are delayed beyond 2022
How long is the delay?
    Unknown. Years.
Will names change?
    No, “GEOID2022”, “NATRF2022”, etc. will remain the same

## Slide 31: NGS ArcGIS Online Resources
NGS Datasheets
NOAA CORS Network
GPS on Benchmarks Priority List
(4 layers - marks, hexagons)
GEOID18 GPS on Benchmarks
GEOID12B GPS on Benchmarks
OPUS Shared Solutions
Mark Recoveries Submitted to NGS
Feature Services
Raster Tile Services
GEOID18 Height (CONUS, PRVI)
GEOID18 Difference (CONUS, PRVI)
GEOID18 Uncertainty (CONUS, PRVI)
GEOID18 Improvements (CONUS, PRVI)

## Slide 32
Application Programming Interfaces (APIs)
https://geodesy.noaa.gov/web_services/

## Slide 33: Online Resources
Monthly webinar series
  All webinars are recorded and available online
Online lessons
Video library
Publication library
NSRS Modernization News

## Slide 34: Thank You!
Jacob Heck, Ph.D., P.S.
Great Lakes Regional Geodetic Advisor (WI, MI, IN,IL)
U.S. National Geodetic Survey, NOAA
jacob.heck@noaa.gov
c/o NOAA Great Lakes Environmental Research Laboratory
4840 S. State Road
Ann Arbor, MI 48108
For more information, visit https://geodesy.noaa.gov

## Slide 35: Extra Slides

## Slide 36: National Spatial Reference System (NSRS)
Geometric Geodesy
Horizontal Datums/Geometric Reference Frames
Latitude
Longitude
Ellipsoid Height
State Plane Coordinates
Physical Geodesy
Geopotential Datums
Orthometric Height
Dynamic Height
Surface Gravity
Leveling
Main Components: latitude, longitude, height, origin, scale, gravity, and orientation

## Slide 37: NAVD 88 (epoch ?) to NAPGD2022 Epoch 2020.00 (estimate)

## Slide 38: The Geoid, and Heights
Topography
The geoid
A chosen
ellipsoid
h
h: ellipsoidal height
H: orthometric height
N: geoid undulation
h
N
H
= H
+ N

## Slide 39: Typical GNSS Setups

## Slide 40: A tale of two feet
Two versions of “foot” in current use:
“Old” U.S. survey foot
“New” international foot
1 ft = 0.3048 m exactly
‭1 ft = 0.3048006096…‬ m
differ by
2 parts per million (ppm) or ~0.01 ft/mile
  A real problem with real costs

## Slide 42: Bye, bye, U.S. survey foot…
In modernized NSRS, NGS will support only one definition of the “foot”
  Previously called the “international foot”
  Now, just the “foot”
  1 foot = 0.3048 meter (exact)
However
  Recommend using term “international foot” when there is potential for confusion with other foot
  NGS will continue to support U.S. survey foot for legacy applications (e.g., SPCS 83 and 27)
For more information on the foot: https://www.youtube.com/watch?v=b_NL8NHFlIU

## Slide 43
What is Geodesy?
Geodesy (geodetic control) is a foundational science that defines position & height
The Earth is an irregular surface and is difficult to model. Accurate positions are required for a wide variety of applications
(e.g. monitoring climate change impacts/sea level change)
Why is Geodesy important?

## Slide 44
Horizontal
Vertical