## Slide 1
The Coastal Mapping Program
and VDatum:
Impact of NSRS Modernization
Mike Aslaksen and Stephen White
April 25, 2016

## Slide 2
The Coastal Mapping Program
A congressional mandate to conduct remote sensing surveys of coastal regions of the United States and its possessions for demarcating the nation’s legal coastline.
Goals:
  Provide the Nation With Accurate,
  Consistent, Up-to-Date
  National Shoreline
  Acquire Nearshore
  Elevation Data
Sources:
  Lidar
  Digital Cameras
  High Resolution Satellites
Notes: Support of other applications:
  NOAA nautical charts
  Used in defining the United States’ territorial limits
  Coastal resource management
  Storm surge and coastal flooding modeling
  Coastal geomorphology studies
  GIS analysis
Coastal Intelligence, Resiliency and Place-Based Conservation Applications
  Integrated Ocean and Coastal Mapping : ! Map Once-Use Many Times !

## Slide 3
Operational Impacts:
Base stations, control/check points, direct georeferencing – consistency!
Proprietary sensor and exploitation software utilized to process data will need to support new reference frames
Shoreline Product Impacts:
Horizontal displacements – user dependent; minimal to charting (scale)
Tidal Datums not impacted, only roadmap for how we get to it - currently
National Tidal Datum Epoch update (~2020) will compound NSRS impact to shorelines going forward – this needs to be detailed and educated
Transitioning issues - horizontal transformations to shoreline will be needed if Nautical Charts are not updated to latest reference frames, metadata, SOWs, etc.
IOCM Products:
New products will be tied to latest reference frames
Older products will need to be transformed by delivery mechanism or RS/GIS software – ideally on-the-fly
Confusion of different reference frames and ensuring consistency
VDatum
Impact of NSRS Modernization
Outreach
&
Education

## Slide 4: Changes to the NSRS: Horizontal
Seattle, WA
Easting Difference: 0.45 meters
Northing Difference: 1.33 meters

## Slide 5: Changes to the NSRS: Horizontal
Long Beach, CA
Easting Difference: 0.41 meters
Northing Difference: 1.29 meters

## Slide 6: Changes to the NSRS: Horizontal
Charleston, SC
Easting Difference: 0.75 meters
Northing Difference: 0.46 meters

## Slide 7
Puget Sound
Palm Beach

## Slide 8
Palm Beach, FL
NGS/RSD Topobathy
General Bare Earth Routine
NGS/RSD Topobathy
NAD83 Ellipsoidal

## Slide 9: Palm Beach, FL
Approximately 6-10 meter offsets

## Slide 10
Puget Sound, WA
Puget Sound Lidar Consortium
General Bare Earth Routine
Puget Sound Lidar Consortium
NAD83 Ellipsoidal

## Slide 11: Puget Sound, WA
Approximately 80 meter offsets

## Slide 12
Applying the new GEOID incorrectly: Gridded Surfaces
Notes: NAD83 and the new GEOID on one side and NAD83 and the old GEOID on the other side

## Slide 13
Applying the new GEOID incorrectly: Gridded Surfaces
Greater than 1 meter discrepancy
Notes: NAD83 and the new GEOID on one side and NAD83 and the old GEOID on the other side

## Slide 14
Applying the new GEOID incorrectly: Point Clouds
Notes: NAD83 and the new GEOID on one side and NAD83 and the old GEOID on the other side

## Slide 15
Point Cloud Discrepancies
There should not be a crack in the bottom of pool !!
Notes: NAD83 and the new GEOID on one side and NAD83 and the old GEOID on the other side

## Slide 16
18m Offset
4-6 Degree sloping beach
Applying the new GEOID incorrectly
Notes: NAD83 and the new GEOID on one side and NAD83 and the old GEOID on the other side

## Slide 17
Development and Use of VDatum
Mapping the Land-Sea Interface: VDatum converts elevation data (heights and soundings) among different vertical datums
VDatum is a Java application developed jointly by :
National Geodetic Survey (NGS)
Office of Coast Survey (OCS)
Center for Operational Oceanographic
Products & Services (CO-OPS)
NOAA Bathymetry
USGS Topography
Notes: Vertical Datum Transformation (VDatum) is a free software tool under development jointly by NOAA's National Geodetic Survey (NGS), Office of Coast Survey (OCS) and Center for Operational Oceanographic Products and Services (CO-OPS). VDatum is designed to vertically transform geospatial data among a variety of tidal, orthometric and ellipsoidal vertical datums - allowing users to convert their data from different vertical references to a common system , enabling the fusion of diverse geospatial data onto a preferred vertical datum.

## Slide 18
Foundational Data
Observations
(Geodetic and Tidal)
Modeling
(Hydrodynamic and
TSS)
and Uncertainty Development
Software Development
and Outreach/
Training/
Coordination
VDatum

## Slide 19: VDatum Website: vdatum.noaa.gov (Version 3.6 Released, May 13, 2016)

## Slide 20
What’s Being Replaced with the Modernization of Reference Frames
Horizontal Vertical
  NAD 83(2011)
  NAD 83(PA11)
  NAD 83(MA11)
Latitude
Longitude
Ellipsoid Height
State Plane Coordinates
Heights
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
Approximate level of geoid mismatch known to exist in the NAVD 88 zero surface.
Does not include local subsidence issues

## Slide 21
Vertical Datum Transformation “Roadmap”

## Slide 22
VDatum: Updated NSRS

## Slide 23
Future Enhancements: Next Generation TSS Development
A Must: GPS Campaign on benchmarks to determine new relationships
Satellite Altimetry/Derived Products to better understand offshore TSS
Wish List: GPS tide buoys to be utilized for data input and validation
Re-tracked coastal altimetry data to capture nearshore sea surface height signal

## Slide 24
Foundational Data: Geodetic

## Slide 25
Foundational Data: Geodetic

## Slide 26
Refined TSS grid created using the derived TSS points at CNES MSS points (Gaussian filtered), and newly determined geodetic relationships at tide stations
Future Enhancements: Next Generation TSS Development

## Slide 27
National Tidal Datum Epoch (NTDE)
Official time period of tidal observations that are used for primary datum calculations
  Time it takes the Earth, Moon, & Sun to complete an epoch tidal cycle
  19 year time period (Current NTDE is 1983-2001)
  Considered for revision every ~20-25yrs
  Includes the longest period tidal variations (18.6 year node cycle)
  Averages out seasonal fluctuations
  Provides a nationally consistent tidal datum network by accounting for seasonal and apparent environmental trends in sea level that affect the accuracy of tidal datums
1983-2001 EPOCH
  Anticipated release 2022-2023 time frame
  Next NTDE will be computed on period of (2002-2020)

## Slide 28
MSL NTDE Differences: (83-01 vs. 60-78)

## Slide 29
MHW NTDE Differences: (83-01 vs. 60-78)

## Slide 30
MLLW NTDE Differences: (83-01 vs. 60-78)

## Slide 31
Implementing new ellipsoidal to orthometric roadmap NGS develops
Development of Next Generation TSS
Modernizing of Tidal Datum Fields for NTDE update
Changes in VDatum

## Slide 32
Assistance collecting GPS on
tidal benchmarks
Problems (Software or Models)
Enhancements
What we need from you:

## Slide 33
HTDP
NADCON5
IGLD85 Improvements
Spatially Varying Uncertainty
Other Enhancements
Uncertainty in one standard derivation (m)

## Slide 34
VDatum: Contact Us

## Slide 35
Rip Current
Waves
Waves

## Slide 36
Thank You!
Contact Information:
Email: vdatum.info@noaa.gov
Website: http://vdatum.noaa.gov
Stephen White
Email: stephen.a.white@noaa.gov
Phone: (301) 713-1428 x167