## Slide 1
Modernizing the National Spatial Reference System:
A 2017 update
Steve Hilla (GRD Chief)
Dru Smith (NSRS Modernization Manager)
Kevin Choi (CORS Branch Chief)
NOAA’s National Geodetic Survey

## Slide 2: “Modernizing the NSRS” means…
Replacing NAD 83
Replacing NAVD 88
Re-inventing Bluebooking
Improving the Geodetic Toolkit
Better Surveying Methodologies
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 3: So…what’s new in 6 months?
NAMES!!

## Slide 4: NSRS Modernization
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CTRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PTRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MTRF2022)

## Slide 5: NSRS Modernization
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 6: So…what’s new in 6 months?
NAMES!!
Mathematical Decisions!!

## Slide 7: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Remove long-standing non-geocentricity of NAD 83 frames
All four : identical to IGSxx at a TBD epoch
  2020.00?
All four : differ from IGSxx by plate rotation only
  Updated Euler Pole determination for rigid plate only

## Slide 8: NAD 83’s non-geocentricity
~2.2 m
NAD 83 origin
IGSxx origin
Earth’s Surface
hNAD83
hIGSxx
fNAD83 – fIGSxx
lNAD83 – lIGSxx
hNAD83 – hIGSxx
all vary
smoothly by latitude
and longitude
same
GRS-80
ellipsoid

## Slide 9: Plate-(pseudo)fixed frames
NAD 83(NSRS2007)
Epoch 2002.0
NAD 83(2011)
Epoch 2010.0
If NAD 83 were truly “plate
fixed” then an 8 year
epoch change would not
yield the systematic
plate rotation seen here.
(*)TRF2022 will determine
a new Euler Pole rotation
for each of 4 plates.
(*)=NA, C, T or P
NAD 83(2011) minus NAD 83(NSRS2007)

## Slide 10
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.

## Slide 11: Fixed-Epoch Transformation NAD 83 to “2022”

## Slide 12: NATRF2022 frame is rigid and fixed to rigid part of the N.A. plate
Non-rigid part of the N.A. plate
(deformation)
area

## Slide 13
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 14
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 15
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 16
Point on rigid part of plate
Point on deforming part of plate
l
l
t
t
NATRF2022 coordinates over time (Remember: The NATRF2022 frame is rigid)

## Slide 17: So if not HTDP, then what?
NATRF2022 would account for most horizontal velocity over time
Remaining signal typically modeled by HTDP (now)
In future, a TBD velocity model would be applied to account for that and vertical
The simplest solution is gridded CORS velocities

## Slide 18: Horizontal velocities after Repro1
Note scale difference between West (10 mm/yr) and east (2 mm/yr)

## Slide 19: CORS Implied Vertical Velocities - Control
Courtesy Galen Scott

## Slide 20: CORS Implied Vertical Velocities – Heat Map
Courtesy Galen Scott

## Slide 21: How to use this information?
Assuming CORS spacing is sufficient – grid
  Yields horizontal (NEV & GIA) plus vertical signal
Vertical important for orthometric heights:
  Ht = (ht0 + (t-t0)*dh/dt) - (Nt0 + (t-t0)*dN/dt)
    Where Ht is orthometric height at desired time
    ht0 is ellipsoidal height at epoch (maybe 2020.0)
    Nt0 is geoid height at epoch
    dh/dt is change in ellipsoid height over time
    dN/dt is change in geoid height over time

## Slide 22: What if this isn’t enough?
Will investigate sufficiency of gridded CORS
Concern is dynamic areas: horizontal & vertical
Will look at other models to evaluate
Cost versus benefit
  What we can easily do in-house and support
  increased complexity from outside models
Alternatively, users can model their own …

## Slide 23: Replacing NAVD 88 (et al.)

## Slide 24: Names
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 25: NAPGD2022
Begins with a 3-D global geopotential model
Then, derivative products are built
  GEOID2022
  DEFLEC2022*
  NGRAV2022*
* Names not yet finalized

## Slide 26: NAPGD2022: Pre-decisional items
NGS will acknowledge that the geoid is definitionally tied to global mean sea level
  This means that orthometric heights should, by definition, decrease as GMSL rises
  But NGS will not force users to adopt this particular change, but rather will offer it up as an optional correction to their orthometric heights

## Slide 27
NGS will basically offer users
of OPUS the option to “turn on”
the impact seen in Scenario 1.
If they turn it “off”, they get
orthometric heights as per
Scenario 2.

## Slide 28: NAPGD2022: Pre-decisional items
GEOID2022 (et al.) over the North America/Pacific/Caribbean/Central America/Greenland region will range from
0 to 90 latitude and from 170 to 350 longitude.
GEOID2022 (et al) over Guam/CNMI:
11-22, 143-148
GEOID2022 (et al) over American Samoa:
-16 to -10, 186-193

## Slide 29: NAPGD2022: Pre-decisional items
Three types of geoid change will be tracked
  Size, Shape, Change to W0
Time/Space span evaluated for cost/benefit ratio
Examples:
Issue | Type of Change | Temporal Period | Temporal Duration of Geoid Change | Spatial Impact | Magnitude of geoid change | Decision
Accretion of Space Dust | Size | Secular | Permanent | Global | 4x10-7 mm / y | Ignore
Earthquakes | Shape | Episodic | Permanent-ish | Local | Can be as large as a few cm | Study further
GMSL rise | W0 value | Secular | Permanent | Global | 1.7 mm / y | Provide as optional correction

## Slide 30: Time Dependencies

## Slide 31: April 2017: How things stand
Point DI4044 has 3 different NAD 83 ellipsoid heights (plus one superseded),
each at an epoch that does not match the epoch of the occupations, yielding
an estimate of the subsidence uplift of the point of +2.8 mm/year.
What happens in NATRF2022, when actual survey epochs will be used?
The current realization in Louisiana at this time: NAD 83(2011)
Current best estimate of dh/dt: +2.8 mm / year
1
2
3
4
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 32: DI4044 – True Ellipsoid Height History

## Slide 33: NATRF2022 and actual survey epochs
Point DI4044 was surveyed with GPS in 2006, 2006 (again), 2010, 2012 (in 2 parts which will be treated separately) and 2016. Computing the “h” values at the actual dates of the survey (using OPUS-S, then OPUS-Projects, and letting OPUS choose our CORS values) yields the following graph. IGS 08 serves as a proxy for NATRF2022 heights for now. (Note the NAD 83 values are shown with a bias of 1.38 meters so as to fit near the IGS08 values)
NATRF2022 best estimate of dh/dt: -4.0 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 34: NATRF2022 and actual survey epochs
Further information can be added, such as gridding the surrounding
CORS velocities, for a coarse estimate of what is happening locally.
CORS best estimate of dh/dt: -2.2 mm / year
NATRF2022 best estimate of dh/dt: -4.2 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 35: IGS08 vs NATRF2022
IGS08 coordinates are dominated by the primary motion associated with the North American Plate rotation, as manifest at this lat/lon:
12.9 mm/y West
1.1 mm/y South
NATRF2022 coordinates will have the plate rotation removed, but still
exhibit their time-dependency, until
the Intra-frame velocity model is used to estimate a coordinate at an epoch of convenience.

## Slide 36
IFV implied by interpolating
from surrounding CORS:
Northward 0.4 mm / year:
Difference: 2.0mm/year
“Intra Frame Velocity”
“Intra Frame Velocity”
NA plate rotation:
South 1.1 mm/year
NA plate rotation:
West 12.9 mm/year
IFV implied by interpolating
from surrounding CORS:
Eastward 0.3 mm / year
Difference: 0.7 mm / year

## Slide 37: So…what’s new in 6 months?
NAMES!!
Mathematical Decisions!!
NADCON 5.0!!

## Slide 38: The new Geodetic Toolkit
https://beta.ngs.noaa.gov/gtkweb/

## Slide 39: The new Geodetic Toolkit with NADCON 5.0
https://dev.ngs.noaa.gov/gtkweb/

## Slide 40
X, Y, Z
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83
Notes:

## Slide 41
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 42: Thank you!

## Slide 43: Questions?