## Slide 1
Modernizing the National Spatial Reference System
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: “Modernizing the NSRS” means…
Replacing NAD 83
Replacing NAVD 88
Re-inventing Bluebooking
Improving the Geodetic Toolkit
Better Surveying Methodologies
Notes: There are actually 3 “NAD 83”s, NAD 83(2011), NAD 83(PA11) and NAD 83(MA11)
There are also many more vertical datums than NAVD 88 in the NSRS, each one for specific states or territories that have no line of sight to CONUS/Alaska

## Slide 3
Modernizing the NSRS
The “blueprint” documents: Your best source for information
Geometric:
May 2017
(minor update Sep 2017)
Geopotential:
Nov 2017
Using the new frames/datum:
Sep(?) 2018

## Slide 4
Latitude, Longitude
& Ellipsoid Heights

## Slide 5: Replacing the NAD 83’s
The Old:
NAD 83(2011)
NAD 83(PA11)
NAD 83(MA11)
The New:
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 6: Replacing the NAD 83’s
Three plate-(pseudo)fixed frames will be replaced with four plate-fixed reference frames
  N. Amer., Pacific, Mariana, Caribbean(new!)
Fixed: NAD 83 isn’t geocentric
Fixed: NAD 83 doesn’t rotate properly with its plates
Method: Define each of the 4 new frames equal to IGS14 @ 2020
  Define each frame’s movement by a plate rotation only
  Put another way: “The frame rotates so your coordinates don’t have to”

## Slide 7
Time “t ” when
all four TRFs and the
IGS are identical.
(maybe 2020.0?)
0
MATRF2022
MATRF2022
Rotation of Mariana Plate
t=t + Dt
(“the future”)
0
t=t - Dt
(“the past”)
0
CATRF2022
CATRF2022
NATRF2022
PATRF2022
NATRF2022
PATRF2022
Rotation of Caribbean Plate
IGS frame through time
IGS frame
IGS frame
Rotation of Pacific Plate
Rotation of North American Plate
The relation of five global reference
frames through time.
Rotations are not to scale

## Slide 8
What does it mean to provide time-dependent coordinates in 5 frames?

## Slide 9: BSMK (North Dakota)

## Slide 10: BSMK (North Dakota)
NATRF2022 Latitude is CONSTANT over time
Let’s set t to 2005.0 for now…
0

## Slide 11: BSMK (North Dakota)
NATRF2022 Longitude is constant over time

## Slide 12: BSMK (North Dakota)
No matter WHAT frame, the ellipsoid height is dropping over time

## Slide 13: PIN1 (S. California)

## Slide 14: PIN1 (S. California)
Latitude in NATRF2022 and PATRF2022 change over time

## Slide 15: PIN1 (S. California)
Longitude in NATRF2022 and PATRF2022 change over time

## Slide 16: PIN1 (S. California)
No matter WHAT frame, the ellipsoid height is rising over time

## Slide 17
Orthometric Heights
(“Sea Level Heights”) and other
gravity-related quantities

## Slide 18: Replacing NAVD 88
  The Old:
  NAVD 88
  PRVD 02
  VIVD09
  ASVD02
  NMVD03
  GUVD04
  IGLD 85
  IGSN71
  GEOID12B
  DEFLEC12B
  The New:
  The North American-Pacific Geopotential Datum of 2022 (NAPGD2022)
  - Will include GEOID2022
Orthometric
Heights
Normal
Orthometric
Heights
Dynamic
Heights
Gravity
Geoid
Undulations
Deflections of
the Vertical

## Slide 19: Geopotential Basics
Why isn’t this a vertical datum?
  Because it contains more than heights
    And therefore NGS wants to be accurate in its name

## Slide 20: Expected changes to orthometric heights

## Slide 21: Expected changes to orthometric heights

## Slide 22: Definitional Relationship
Time-dependent ellipsoid heights
come from time-dependent
CORS coordinates which serve as control for
your time-dependent GNSS survey.
They will be modeled in the IFVM
Time-dependent geoid undulations
are modeled in the dynamic component
of GEOID2022 (“DGEOID2022”), which
will come from the geoid monitoring
service, or GeMS.

## Slide 23: Geoid Monitoring Service
Goal: Track all changes to the geoid which would prevent 1 cm accuracy
Three major aspects:
  Secular Shape: Hudson Bay
  Episodic Shape: Massive Earthquakes
  Geoid relation to Sea level: Global Sea Level Change

## Slide 24: Secular Mass Movement
Notes: There are two manifestations of the growing mass in the deep mantle under Hudson Bay:
Geometric – a GPS receiver will see the crust uplifting as the increase in mantle mass pushes the crust up in a displacement.
Geopotential – a gravimeter on the surface will sense the growing mass as an increase in the acceleration of gravity, BUT this will be slightly tempered by a reduction in gravity as well (because the gravimeter on the surface is getting farther from the Earth’s center). Still, the gain (from mass increase) is larger than the loss (from geometric movement) for a net gain. Because the net gain in gravity is not caused purely by being at a new crustal height, this translates into an increase in geoid undulations, or a “swelling” of the geoid in this region.
This is different than a purely geometric change caused by a compression of the crust. In that case, no significant mass is entering or leaving the region so, while GPS might sense a subsidence and a surface gravimeter might sense a slight increase as it moves closer to the Earth’s center, the geoid would not actually change.

## Slide 25: High resolution products
GEOID2022
  Official converter of *TRF2022 ellipsoid heights into NAPGD2022 orthometric heights
DEFLEC2022
  Surface deflections of the vertical in N/S and E/W
GRAV2022
  Surface acceleration of gravity
DEM2022
  Official DEM used in creation of all above products
All will be 1 x 1 arcminute grids
All will cover three finite regions of the globe
All will have a static and dynamic component
  Dynamic surface gravity and DEM not expected to be ready by 2022

## Slide 26: The three gridded regions
“North American region”
¼ of the Earth
“Guam/CNMI region”
“American Samoa region”

## Slide 27
Converting NAD 83 and NAVD 88
geospatial data into
NATRF2022/PATRF2022/CATRF2022/MATRF2022
and NAPGD2022

## Slide 28: Two options: NCAT and VDatum
Currently semi-independent programs
Being merged behind the scenes when calling identical routines, such as “NADCON 5.0”
  NCAT will remain “purely geodetic”
  VDatum will be “NCAT plus tidal datums”
Both will get “VERTCON 3.0” in late 2018
Both will run in 3 modes:
  Web services, Browser interactive, Downloadable

## Slide 29: NGS Coordinate Conversion and Transformation Tool (NCAT)
Now with
NADCON 5!
beta.ngs.noaa.gov/NCAT/

## Slide 30: VDatum
vdatum.noaa.gov

## Slide 31: Thank you!

## Slide 32: Questions?

## Slide 33: Extra Slides

## Slide 34: So much more…
OPUS-Projects being expanded to replace Bluebooking
  Leveling, RTK, Gravity
An entire new database being built
All historic GPS data back to 1997 being reprocessed into the TRFs
A new leveling manual to work in a GPS/geoid “vertical datum”

## Slide 35: So much more…
VERTCON 3 under construction
More GIS friendly products, services and tools being built
Replacement for NGS 58 (“GPS derived ellipsoid heights”) manual nearly complete

## Slide 36
X, Y, Z
NAD 83 (2011)
Allowable Regions:
CONUS
Alaska
Hawaii
PR/VI
AS
Guam/CNMI
St. Paul
St. George
St. Lawrence
USNG
UTM
SPC
f, l, h
xyz2plh
plh2xyz
a,f (GRS 80)
UTMS
a,f (GRS 80)
SPC83
NAD 83
USNG
NAD 83
USNG
NAD 83
Notes:

## Slide 37
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
USNG
UTM
SPC
f, l, h
X, Y, Z
UTM
f, l, h
Region: CONUS
NADCON 5 connections in RED
X, Y, Z
USNG
UTM
SPC
f, l, h
USSD
NAD 27
NAD 83 (1986)
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
NAD 83 (HARN)
2022

## Slide 38: Intra-frame velocity model
Note scale difference between West (10 mm/yr) and east (2 mm/yr)
Shown on this slide are CORS-implied velocities after removing the rotation of the
North American plate. NATRF2022 coordinates will change through time by these
amounts. These time-dependent changes will be captured in the IFVM.

## Slide 39: A simple IFVM model is applied…
The simplest IFVM is already available: Interpolation of 3-D velocities from CORS stations
Removing this simple IFVM resolves nearly all velocities seen in the previous slide
Eastern CONUS will largely be resolved
Western CONUS has some anomalies
NGS is engaged in research to provide the highest quality IFVM without our abilities, possibly enveloping:
  InSAR
  Geodynamic

## Slide 40: Episodic Mass Movement
M9.2 -> Geoid change of 1.5 cm
Notes: Rare, but worth monitoring, large earthquakes or volcanic eruptions can move enough mass locally to cause the geoid to make a permanent local shift.

## Slide 41: Choosing a new geoid as GMSL changes

## Slide 42: Plate-(pseudo)fixed frames
NAD 83(NSRS2007)
Epoch 2002.0
NAD 83(2011)
Epoch 2010.0
If NAD 83 were truly “plate
fixed” then an 8 year
epoch change would not
yield the systematic
plate rotation seen here.
(*)TRF2022 will determine
a new Euler Pole rotation
for each of 4 plates.
(*)=NA, C, T or P
NAD 83(2011) minus NAD 83(NSRS2007)

## Slide 43: NAD 83’s non-geocentricity
~2.2 m
NAD 83 origin
IGSxx origin
Earth’s Surface
hNAD83
hIGSxx
fNAD83 – fIGSxx
lNAD83 – lIGSxx
hNAD83 – hIGSxx
all vary
smoothly by latitude
and longitude
same
GRS-80
ellipsoid

## Slide 44: Fixed-Epoch Transformation NAD 83 to “2022”

## Slide 45: ICT2 (Kansas)

## Slide 46: ICT2 (Kansas)
Note the time-dependent movement of this Kansas point in latitude in NATRF2022! Such movement will be captured in the IFVM.

## Slide 47: ICT2 (Kansas)
However, in longitude, this CORS is fairly stable in NATRF2022! Still, any deviation from stability would be in the IFVM.

## Slide 48: ICT2 (Kansas)
All vertical motion is captured in the IFVM.

## Slide 49: PRMI (Puerto Rico)

## Slide 50: PRMI (Puerto Rico)

## Slide 51: PRMI (Puerto Rico)

## Slide 52: PRMI (Puerto Rico)

## Slide 53: BRW1 (N. Alaska)

## Slide 54: BRW1 (N. Alaska)

## Slide 55: BRW1 (N. Alaska)

## Slide 56: BRW1 (N. Alaska)

## Slide 57: KOD6 (S. Alaska)

## Slide 58: KOD6 (S. Alaska)

## Slide 59: KOD6 (S. Alaska)

## Slide 60: KOD6 (S. Alaska)

## Slide 61: KOK5 (Hawaii)

## Slide 62: KOK5 (Hawaii)

## Slide 63: KOK5 (Hawaii)

## Slide 64: KOK5 (Hawaii)

## Slide 65: ASPA (Am. Samoa)

## Slide 66: ASPA (Am. Samoa)

## Slide 67: ASPA (Am. Samoa)

## Slide 68: ASPA (Am. Samoa)

## Slide 69: ASPA (Am. Samoa)

## Slide 70: Mariana rotation
Snay (2003) used only one CORS (“GUAM”) to determine the Mariana rotation
  But 2 sites at a minimum are needed to uniquely determine a plate’s rotation
    “CNMI” (since decommissioned) was forced to equal “GUAM” to solve the problem
    Ill-posed, yet the values behave reasonably for GUAM.
    Less reasonable for newer CORS “CNMR”

## Slide 71: GUAM (Guam)

## Slide 72: GUAM (Guam)

## Slide 73: GUAM (Guam)

## Slide 74: GUAM (Guam)

## Slide 75: GUAM (Guam)

## Slide 76: CNMR (CNMI)

## Slide 77: CNMR (CNMI)

## Slide 78: CNMR (CNMI)

## Slide 79: CNMR (CNMI)

## Slide 80: CNMR (CNMI)

## Slide 81
Each frame will get 3 parameters
Euler Pole Latitude
Euler Pole Longitude
Rotation rate (radians / year)
This will be used to compute
time-dependent TRF2022
coordinates from time-dependent
IGS coordinates.

## Slide 82: Time-Dependencies as a service: NATRF2022 and actual survey epochs
CORS best estimate of dh/dt: -2.2 mm / year
NATRF2022 best estimate of dh/dt: -4.2 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
NAD 83 forcibly combined data spanning many years (using HTDP with no vertical modeling) to compute and find one height at one epoch.
NATRF2022 will compute coordinates at survey epoch to show actual motion.
Even gridding surrounding CORS yields better subsidence rates than you have today.
Notes: Potential outline and speaker assignments; can be adjusted as needed.

## Slide 83: Time Dependencies as a service: Intra-plate motions
Chart: Longitude (Easting) History of DI4044
| 2006.0237999999999 | 2010.7215000000001 | 2012.2249999999999 | 2016.7469000000001
ITRF | 802.7646 | 802.708 | 802.6744 | 802.6129
NATRF2022 | 802.7646 | 802.7672 | 802.7525 | 802.748

## Slide 84: So…what is “Geopotential”
Geo: Earth
Potential: Gravity Potential Energy
Geopotential: Gravity Potential Energy Field that surrounds the Earth.

## Slide 85: Surely you remember this page from your high school physics textbook?
For example: Choosing
which “W ” value is “the geoid”
0

## Slide 86: Gravity vs Gravitation
Q: But you said “Gravity” potential energy, yet that textbook said “Gravitational” potential energy…
A: Very observant!
  Gravitation: Masses attracting each other
  Gravity: Gravitation plus Centrifugal
    Gravity is what we actually feel on a rotating planet
Warning: Getting in the weeds…