## Slide 1
NGS Geoids, OPUS, NCAT, etc.
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
WVSPS Annual Convention
February 2022

## Slide 2: My Background
Licensed Surveyor in OH, PA, and WV (PS)
Certified GIS Professional (GISP)
Certified Floodplain Surveyor (CFS)
BS in Surveying & Mapping, Univ. of Akron
Came to NGS from USACE Pittsburgh District
  primary experience is engineering surveys, including structural deformation, hydrographic/bathymetric, terrestrial lidar, GNSS control, local/legacy datum resolution
Notes: -joined the NGS almost 2 years ago now
-Spent 9 years prior with USACE on topo, geodetic control, layout, boundary, deformation, lidar, GIS implementation, hydrographic/bathymetric, and contracting aerial acquisitions
-previously survey intern (private sector & BLM), GIS tech., warehouse picker/packer, busboy…
-I like Honda motorcycles, have owned a Honda Shadow, a Victory Vegas, but my favorite bike was a Honda ST1100 that I sold after my frist kid was born

## Slide 3: So much more to NSRS Modernization!
New version of PAGES
  Multi-Constellation  GPS, Galileo, GLONASS, Beidou, QZSS, etc.
  Target: 15 minute occupations
OPUS expansion plan
  RTK/RTN: 2020 rollout, already mentioned
  Leveling, Classical (Total Station), Gravity: 2020-2025
  Fully integrated (GPS projects with leveling and gravity? No problem!)
  Ease of submission to NGS for inclusion in the NSRS
New Mark Recovery Tool
  mentioned earlier, search: “NGS mark recovery” and go to Beta
Fully integrated toolkit
  NCAT and VDatum

## Slide 4: Using the modernized NSRS
OPUS
  Guidance (such as pre-selected CORSs and assistance in locating marks in project areas)
  Users will decide what control to hold fixed and what epochs they wish to set for the adjustment
    “Preliminary coordinates”
  If submitted to NGS (aka “Shared”), we will harvest your raw GNSS data and use it to compute Final Discrete coordinates
Notes: it all starts and ends with OPUS

## Slide 5: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
Notes: NGS develops and maintains the National Spatial Reference System, a national coordinate system that provides the foundation for transportation, navigation, land record systems, mapping and charting efforts, and a multitude of scientific and engineering applications.
But there are many ancillary programs and products we will also discuss.

## Slide 6: Not just new datums…
  NSRS Modernization
-OPUS enhancements/additions
-new types of coordinates
-new methods for establishing control
-streamlined Bluebooking
-retire the US Survey Foot
Notes: -so you’ve probably seen that phrase that I have front and center here, NSRS Modernization
-that’s the blanket term we use to refer to not just the new datums but other updates
-another phrase I want to mention are these “Blueprints for 2022”
-just about everything I cover today is mentioned in one of the Blueprints
-the Geodetic Toolkit, what’s that? another term that just refers to all those softwares NGS provides, like PAGES, ADJUST, etc.
-better methods – updating manuals like NGS-58 and 59 for example

## Slide 7: What can you do?
Help spread the word
  Engage your
    Surveyors
    Engineers
    GIS Professionals
Reach out to NGS for support
Follow best metadata practices
Educate others
  Share our links and info
Notes: Coordinate -Spread the word and tell others about NSRS Modernization
 Ask the agencies, surveyors, and engineers you work with about the preparations they are taking to learn about the upcoming changes
Educate
-Review materials and ask for support from NGS
Prepare
-Lead by example and use the best metadata practices

## Slide 8: Preparing for New Datums
  Know the epoch of your data/datasets
    consider how you will track this
      full to-the-second timestamp on every feature?
        GNSS makes this easily possible…
      labeling a year for each dataset?
      something in-between that works for your needs?

## Slide 9: Preparing for New Datums
  Transforming your data
    NCAT - NGS Coordinate Conversion and Transformation Tool
      available now: ASCII upload, Web Services, GitHub
      ask your software provider(s) about integration
        we envision this as most popular method of access
        Industry Workshop held May 2021
          Esri, Trimble, Blue Marble, etc… all the well known names attended
Notes: Transforming your data
NCAT - NGS Coordinate Conversion and Transformation Tool
available now: ASCII upload and Web Services
ask your software providers about integration
we envision this as most popular method of access
Industry Workshop held this year – esri, trimble, bluemarble, all the major well known names were represented
labeling a year for each dataset?
something in-between that works for your needs

## Slide 10: Preparing for New Datums
  Reprocessing your data
    in a perfect world, everyone would reprocess
      what does this mean?
        consider an ALTA w/topo
          start over with the onsite GNSS-based control
          reorient all your shots/ties (hopefully linked)
          recreate all the drainage features in new datum
      unrealistic! … and unnecessary for majority users
Notes:   Reprocessing your data
    in a perfect world, everyone would reprocess data
        consider a final product like you use everyday - a hydro-enforced DEM
          starting fresh with the raw GNSS/IMU processing
          generate new ellipsoid height point clouds
          recreate all the drainage features in new datum
    this is totally unrealistic  both from a financial and programmatic perspective

## Slide 11: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 12: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 13: Ecosystem and Climate Operations
Notes: -An NGS Program that adapts geodetic survey technologies, instrumentation, and procedures in support of coastal community resilience and ecological integrity, especially in responding to climate change.
-The five orange dots on this map are Sentinel Sites, or coastal sites at which various geospatial infrastructure is co-located.
*-you’re going to hear me say that again later, “co-located”
-anyway…
CLICK

## Slide 14: Ecosystem and Climate Operations
Notes: -Here’s a decent diagram illustrating a hypothetical Sentinel Site, with BMs, tide gage, and other wetland monitoring instruments that have been leveled as a network and tied via GNSS
**-well, the image isn’t super because there’s no tie b/w GNSS and BM!
-that’s why I called it decent! LOL
-an important NGS, and NOAA overall, mission but with low visibility especially in an inland region
**-guess I tend to forget, PA being such a large state, there is the Delware River which is tidal over a 100 miles upstream, well past Philly
-anyone do any hydro work over there? show of hands?

## Slide 15: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 16: Aeronautical Survey Program
Interagency Program: FAA and NGS
  Primary Airport Control Station (PACS) and Secondary Airport Control Stations (SACS)
  Airports GIS (AGIS)
  Airport Obstruction Charts (AOC)
Primary function of NGS is to serve as QA and subject-matter expert for ASP surveys that are contracted by airports
Notes: PACS are occupied with GNSS and tied to the NSRS via simultaneous observations to one CORS, one CBN Station, and two 1st order BMs.
SACS are then tied to the PACS with simultaneous observations.

## Slide 17: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 18: NOAA VDatum - online

## Slide 19: NOAA VDatum - download

## Slide 20: NOAA VDatum - download
Notes: -cool thing about vdatum is that it incorporates the HTDP (Horzontal Time Dependent Positioning) software
-might not be something most surveyors, in this region anyway, are paying a whole lot of attention to
-but don’t those decimal year things look familiar?
-if you look at any of your OPUS Solution Reports, you’re going to see an epoch date, in the same format, on the right hand side next to the ITRF or IGS coordinates

## Slide 21
Notes: -cool thing about vdatum is that it incorporates the HTDP (Horzontal Time Dependent Positioning) software
-might not be something most surveyors, in this region anyway, are paying a whole lot of attention to
-but don’t those decimal year things look familiar?
-if you look at any of your OPUS Solution Reports, you’re going to see an epoch date, in the same format, on the right hand side next to the ITRF or IGS coordinates

## Slide 22
Notes: -cool thing about vdatum is that it incorporates the HTDP (Horzontal Time Dependent Positioning) software
-might not be something most surveyors, in this region anyway, are paying a whole lot of attention to
-but don’t those decimal year things look familiar?
-if you look at any of your OPUS Solution Reports, you’re going to see an epoch date, in the same format, on the right hand side next to the ITRF or IGS coordinates

## Slide 23
Notes: -cool thing about vdatum is that it incorporates the HTDP (Horzontal Time Dependent Positioning) software
-might not be something most surveyors, in this region anyway, are paying a whole lot of attention to
-but don’t those decimal year things look familiar?
-if you look at any of your OPUS Solution Reports, you’re going to see an epoch date, in the same format, on the right hand side next to the ITRF or IGS coordinates

## Slide 24: NOAA VDatum Website
vdatum.noaa.gov

## Slide 25: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 26: GPS Orbit Data aka Ephemerides
NGS orbit analysis and computation is performed together with, and as a component of, the International GNSS Service (IGS)
  IGS coordinates the collection of satellite tracking data
  these orbits are what give us post-processed accuracy
Designated with this responsibility by the Civil GPS Service Interface Committee (CGSIC)
If you’re using OPUS, it’s all behind-the-curtain!
Notes: The CGSIC is an entity of the US Dept of Transportation.
Ephemeris is a table that lists the coordinates/positions of celestial objects (natural/anthro) during a given time period.
The ephemerides (plural term) are the backbone of GNSS-based positioning; precise ephemerides lead to accurate positions.
*but if you get an OPUS error message about orbit availability, this is your issue that you’ve got satellite data but nothing to process it against.

## Slide 27
Link to NGS GPS Calendar
.sp3 file
Notes: -this is an example .sp3 file
-There’s our GPS Week near the top, number 2038.
-See the SV numbers? Just like a RINEX file you’ll see G## for GPS sats.
-R## for Russian, and whatever else I can’t recall.
-On down you can see this is a Rapid Orbit file, satisfactory for most work.
-Then there’s the date/time stamp followed by the positional records.
-There’s a set of those positions logged every 15 minutes, as opposed to every 15 seconds of land-based receiver logging.

## Slide 28: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 29: National Shoreline
The official shoreline for the Nation, in support of NOAA’s nautical charting mission
Available for download as shapefile in Mean High Water and Mean Lower Low Water datum
Organized by “Project Area” – the blue boxes
hyperlink to the National Shoreline homepage
Notes: -This is an NGS product, highlights the origins of NGS as the Survey of the Coast, Coast & Geodetic Survey.
CLICK
-a sample screenshot of the Great Lakes area, note the Project Areas
CLICK
-And there you can see the dataset is generated up the Delaware past Philly

## Slide 30: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 31
https://www.ngs.noaa.gov/ADVISORS/
Notes: -14 Regional Advisors, we’ve transitioned from a State-based to a Regional Program
-our advisors homepage up there at the top, also easy to find us by querying any major search engine for “ngs advisors”
-if you know Ross Mackay, he is our Chief Advisor, I report to him…
**ya know, I don’t know why they don’t make him put his photo up here
-we do have one vacant advisor position, that was recently advertised and John up there in Wisconsin is officially retired in oh… 18 days

## Slide 32: Regional Geodetic Advisor Program
www.ngs.noaa.gov/ADVISORS/
query any major search engine: “ngs advisors”
Notes: Transitioned from a State to a Regional program in 2016. States no longer provide funding if they desire to have an Advisor, but NGS reorganized the personnel to support regions rather than single States.
Kentucky has appointed a State Geodetic Coordinator

## Slide 33: State Geodetic Coordinators
Not an NGS employee, rather:
  State/Commonwealth government
    RTN (aka “VRS”) Manager
    DOT survey lead
    Geospatial Information Officer
  Academia
    Professor or Program Director
  Professional society representative
Serves as a liaison between the State’s geospatial community and the NGS
Notes: -The State Geodetic Coordinator is not employed by NGS and is typically assigned by a state government agency or university.
-West Virginia has not requested a State Geodetic Coordinator

## Slide 34: State Geodetic Coordinators
Not an NGS employee
Serves as a liaison between the State’s geospatial community and the NGS
Erik Baldwin over at Bluefield State College

## Slide 35: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 36: Emergency Response Imagery
Mission of our Remote Sensing Division
Pre-Storm and Post-Storm photos are taken mostly along the coastal CONUS, and some other disasters natural or human
Supports Dept. of Homeland Security (DHS) and other emergency management organizations (FEMA, State, local, etc.)
Notes: -Pre and Post photos are taken when possible
-mostly natural disasters, hurricanes
-but have also supported Midwestern Flooding and tornadic events
-notably also responded in NYC and DC on September 11, 2001

## Slide 37: Emergency Response Imagery
Notes: -Just a quick sample of ERI, over in Kentucky.
-dataset from 2015 flooding along the Mississippi River.
-Screenshot here is over by the Kentucky Bend, New Madrid Bend, whatever you want to call it.

## Slide 38: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 39: Phase Center Offset - conceptual
Orange dot = mean point of signal reception
Blue dot = Antenna Reference Point (ARP)
Red line = Phase Center Offset (PCO)
Notes: -the ENU values of that red line, which is 3 dimensional, is different per antenna model
-this diagram is an oversimplification of the

## Slide 40: Phase Center Offset
The PCO is one reason it is important to select the correct antenna for OPUS upload!
choose
carefully!
if you have questions… drop me a line
Notes: -this why it is important to select the correct antenna when using OPUS
-there is another part of the Antenna Calibration, the Phase Center Variation… but that’s a whole other discussion so let’s move on to a video!

## Slide 41: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 42: NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 43
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 44: Coordinate Transformation Tool
X, Y, Z
USN G
UTM
SP C
X, Y, Z
USN G
UTM
SP C
X, Y,
Z
USN
G
UTM
SP
C
, , h
(NCAT / NADCON 5.0)
USSD
NAD 27
NAD 83 (1986)
Relating coordinates: then & now
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
, , h
NAD 83 (HARN)
, , h
2022
Notes: Flow diagram of NCAT at work.
All your input gets converted to ECEF coordinates, then transformed and/or converted, and then gets spit back out in your requested datum/coordinates.

## Slide 45: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 46: Continually Updated Shoreline Product
Just as the name says… it’s dynamic
Available for download as shapefiles
Developed by image interpretation and/or vertical modeling using water level stations (tide or lake gages)
Referenced to a computed Mean High Water
hyperlink to the CUSP homepage
Notes: -”continually updated” equals… dynamic!
CLICK
-In typical NGS fashion, there are various ways to navigate to and locate the data, but there’s a screenshot of the NSDE, the NOAA Shoreline Data Explorer
CLICK
-and there’s a quick screenshot of the Delaware River region

## Slide 48: Federal Register Notice summarized
NGS needs to start computing coordinates for the 2020.00 Reference Epoch in January 2022
Marks that you would like to have published in NATRF/NAPGD 2022 need “fresh” data
Why?
  Older data is of lower quality (constellation & orbits)
  Periodic re-surveys are better than decades old data
  Lower accuracy as we move further back in time
hyperlink to FRN: https://www.federalregister.gov/d/2020-16084
Notes: -at NGS we need to start computing coordinates for the 2020.00 Reference Epoch in January 2022
-What’s this ‘age-limiting’ phrasing? Well, second bullet there, meaning that some GPS data is now considered too old to have meaningful worthiness for inclusion

## Slide 49: Federal Register Notice summarized
No decision has been made as to a cutoff date
  FRN says it is unlikely to be <10 years
  Discussions of regional/state-based cutoff dates have been had.
What does this mean as of now?
  Observations prior to 01 January 2010 would not get new coordinates in NATRF/NAPGD2022
What does this look like on a map?
Notes: -NOTE that this is a decision that has NOT yet been made
-What does this mean to you?
-Observations prior to 01 January 2010 would not get new coordinates
-Let’s take a look at a couple maps…

## Slide 50
Notes: -You can see a few areas out west that are very sparse
-Midwest and northeast are pretty well covered

## Slide 51
Notes: -Fayette County looking good, result of the recently collected & published LFUCG (Lexington-Fayette Urban County Government)
-Pikeville area, way over east, has decent coverage
-Based on a cutoff date of 01 January 2010, that leaves 65 counties (of 120 total) with no published passive control in NATRF/NAPGD

## Slide 52
Notes: -Lucas and Brown Counties are peppered with OPUS Share solutions
-While Highland and Muskingum Counties have recently submitted projects published to the IDB, and both have a few OPUS Shares

## Slide 53
Notes: -Lucas and Brown Counties are peppered with OPUS Share solutions
-While Highland and Muskingum Counties have recently submitted projects published to the IDB, and both have a few OPUS Shares

## Slide 54
Notes: -Lucas and Brown Counties are peppered with OPUS Share solutions
-While Highland and Muskingum Counties have recently submitted projects published to the IDB, and both have a few OPUS Shares

## Slide 55: How can you improve your area?
What can you do to ensure your control will get coordinates in the new datums on rollout?
Re-observe and submit the data to NGS
  must be submitted by 31 December 2022
Options to submit your GNSS data:
  OPUS Share  4+ hrs static data; 2 photos; mark ties
    rinse & repeat … as we need redundancy
  OPUS Projects  2+ hrs data; photos; descriptions
  traditional “bluebook” submittal
Notes: -OPUS Share requires 4+ hrs static data; 2 photos; and a brief description of reference ties (not a full IDB “from the post office”)
 NOTE THAT OPUS SHARE OPTION REQUIRES 2 OBSERVATIONS
 WHY? WE REQUIRE REDUNDANCY FOR ANY OBS THAT GO INTO OUR DATABASE
-OPUS Projects  2+ hrs data; photos; full IDB style descriptions via WinDesc (*MUST USE WINDESC*)

## Slide 56: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 57
Geoids and Gravity
Notes: -they go hand-in-hand, like peas and carrots
-the word geoid has different definitions and dates back to the 1820s, including:
--Geometric surface of the Earth which intersects the direction of gravity at right angles and from which the surface of the world ocean is a part.

## Slide 58
Geoids and Gravity
or
“Ramblings on the geoid”
Notes: -they go hand-in-hand, like peas and carrots
-the word geoid has different definitions and dates back to the 1820s, including:
--Geometric surface of the Earth which intersects the direction of gravity at right angles and from which the surface of the world ocean is a part.

## Slide 59
A geoid model is your bridge from…
geoid
Ellipsoidal
Raw GPS Observations
Raw Hydrographic Surveys
Raw Lidar Data
NAD83
Orthometric
USGS
Topography
FEMA NFIP Data & Maps
Engineering and Construction Surveys
NAVD88
NGVD29
Notes: This slide illustrates the 3 categories of vertical datums and examples of where each is directly used They are project and application dependent.
First, we have ellipsoidal datums. Examples include WGS84 and NAD83 (North American Datum of 1983). You will encounter these datums frequently in hydrographic surveys that are vertically referenced with RTK-GPS; any native GPS measurements; and even raw lidar datasets.
Next, we have orthometric datums. These datums are very important because height differences referenced to orthometric datums will allow us to know the direction water will flow, because they have been “gravity-corrected”. The North American Vertical Datum of 1988 (or NAVD 88) is an orthometric datum, which you will see on USGS topographic maps, engineering and development site surveys, and FEMA Flood Insurance Rate Maps.
Finally, we have Tidal Datums, which are derived from water level measurements. They have extremely important applications including daily and extreme water levels; NOAA nautical charts, and shoreline mapping or boundaries along the coast.
*NOAA provides tools (like NCAT and Vdatum) to transform between these different height systems.
The Bridge

## Slide 60
“The true size and physical shape of the Earth” --social media, etc.
Nope
Geoid – an incorrect definition

## Slide 61
“Equipotential surface of the Earth’s gravity field that approximates Mean Sea Level more closely.”
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 314.
equi-huh?
More closely than what?
One textbook geoid definition
Notes: This is what I was introduced to in school. My point is not to say that this isn’t a solid explanation/definition here, rather to break it apart in an attempt to clarify it. This works, Jan’s book is great, and is updated regularly; I would highly recommend it to any educators or practitioners.

## Slide 62
“The equipotential surface of the Earth's gravity field which best fits, in a least squares sense, global Mean Sea Level.”
-website of the National Geodetic Survey
A surface of constant geopotential.
-some lecture notes of mine…
Two more geoid definitions
Notes: Top one is the definition adopted by NGS.
That explanation of being a least-squares best-fit to MSL helps a lot.

## Slide 63
  “The geoid is the equipotential surface that most closely coincides with the undisturbed mean sea level (and its continuation through the continents).”
    - Sjöberg, L. E., & Bagherbandi, M. (2017). Gravity Inversion and Integration, Theory and Applications in Geodesy and Geophysics. Springer.
  equipotential – equal potential
  potential – as in energy… or gravitational pull
My favorite verbage
Notes: -potential = “currently unrealized ability”

## Slide 64
It is not uniform, both strength and direction vary.
Can be defined by a vector
-distance (from ellipsoid) and direction
Gravitational Pull
Notes: -the fact that gravity varies is the reason we need to build a geoid model to calculate ortho heights from GNSS data
-if gravity didn’t vary then we could all just use ellipsoid heights

## Slide 65
A modeled surface to represent the location of equal gravitational force.
It’s an undulating surface, hence the phrase “geoid undulation” often used.
Gravity is acting perpendicular to every point on this surface.
Equipotential Surface
Notes: -undulating is a good word, because there are no “cliffs” in a geoid model, the smallest “feature” one will find in one of our geoid models is about 50km (30mi)
**much like the rolling hills of West Virginia
-Picture this surface like a DEM, but it’s cell values represent the height above or below the ellipsoid in which gravitational pull is equal.
-if that works for you, then think of a geoid model as a DGM, a Digital Gravity Model

## Slide 66
… coincides with the undisturbed mean sea level…
Equipotential Surface

## Slide 67
There are an infinite number of equipotential surfaces.
We use the term geoid to refer to one of those surfaces that aligns to a best-known global mean sea level.
Equipotential Surface
Notes: -the thing to keep in mind in this concept is that there are an infinite number of such surfaces of equal gravitational pull, depending on what the strength of that pull is
-let’s visualize that

## Slide 68
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 180. (slightly edited)
Equipotential Surface
NAPGD2022 defined by a specific strength of gravity  W0
Notes: Recall our ol’ buddy W sub-naught (W0)

## Slide 69
Geopotential
Notes: -The lines in different shades of blue represent different equipotential surfaces, or different strengths/levels of geopotential.
-The brown line represents the topographic surface, land.
-And there’s a puddle of water there in the middle, the blue drop.
-Imagine pouring water onto a dry lake bed. If the topographic surface is flat, as it is here, the water will simply pool up.
-The water “wants” to get to the lower potential lines, but there’s that dang lake bed in the way.

## Slide 70
Geopotential
Notes: -Now we’ve tilted the lakebed, like a hill. The water has a path to move towards lower potential, so it does.
-The water appears to flow because of a difference in height.

## Slide 71
Geopotential
Notes: -Ok, so here’s our water droplet again, and back on a flat lakebed.
--But now we have this dark red circle over here, which represents a mass anomaly, perhaps an large mineral deposit of some sort.
-This resulting geopotential difference, due to the anomaly, causes water to flow towards lower potential again. This time the water appears to flow because of gravity.
-See how the blue lines, our geopotential lines, bow around the anomaly? The mineral mass increases the pull of gravity so the lines must be drawn that way if they’re drawn to represent equipotential surfaces.

## Slide 72
In all scenarios, the water only flows when it has a path to lower geopotential – this is always a combination of gravity and height.
Geopotential
(-∫g dH)
Notes: Just a reminder that the example used is just that, an example. Water is not going to “flow uphill” due to some huge mineral deposit.

## Slide 73
Notes: Nice graphic, couldn’t leave this out. Note that CONUS is all blue, thus negative geoid height values on any datasheet you look at.
Minimum undulation, the lowest point is -106m, in India
Maximum undulation, the highest point is +85m in Iceland

## Slide 74
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 180. (slightly edited)
Orthometric Heights
Notes: REPEAT GRAPHIC HERE

## Slide 75
Notes: -So there’s a classic diagram from NGS that helps illustrate the geoid and other equipotential surfaces.
-But what about reality, where we don’t know that distance, P-sub-zero to P?
-In that case, we’ll probably know some other info, so we can use a simple algebraic formula.

## Slide 76
H = h + N
Orthometric Heights
Notes: -Well, if we know lower case h, our height above ellipsoid, and we know capital N, our geoid height or separation value (the difference b/w ellipsoid and geoid surface) then we can calculate our orthometric height.
-We have to do that because we position our gravity readings relative to the NAD83 ellipsoid, typically with GPS-based methods.
-For example, the gravity readings taken during the GRAV-D flights I mentioned earlier, those are positioned with post-processed GPS data.

## Slide 77
H = h + N
Orthometric Heights
Notes: Let’s take a look at a different diagram.

## Slide 78
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 180. (slightly edited)
H = h + N
Deflection of the Vertical
DoV (symbolized ε)
ε
ε
Orthometric Heights
Notes: -That angle there, the DoV or Deflection of the Vertical, that’s the difference between a line perpendicular to the ellipsoid and a line perpendicular to gravity.
--Picture your plumb bob suspended from an instrument… never mind, nobody uses a plumb bob anymore.--
-Anyway, the plumb bob is pointing down perpendicular to the geoid (gravity at work there), but your GNSS receiver is measuring height perpendicular to the … ellipsoid.
-So we need that DoV value to get accurate GNSS-based orthometric heights.
We know that angle because we know the reciprocal angle epsilon down below, that angle between the plumb line (perpendicular to the geoid) and the line perpendicular to the ellipsoid (our ellipsoid height).

## Slide 79
Notes: -Deflections are used to relate the orientation of a leveled instrument, such as a GNSS receiver or total station, to the horizontal reference frame NAD83.
-Important uses are corrections to zenith distance (vertical angle) measurements, and the conversion between astronomic and ellipsoidal azimuths (the Laplace correction).
-DoV values are maintained in a raster format mush like the geoid models.
-You can find the Laplace correction on a datasheet, below other items like the geoid height and ECEF XYZ coordinates.

## Slide 80
Notes: The DoV is a 2D measurement, so as you can see the modelers build a layer for each direction then they’re merged into one.

## Slide 81
NAVD88 geoids
versus
NAPGD2022 geoids

## Slide 82
  Gravimetric
  Hybrid
Two types of geoid models
Notes: -believe it or not there’s more than 2 types, but the 2 types you’ll see NGS publish are…

## Slide 83
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid then best fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 84
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 85: Gravimetric vs. Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 86: NAVD88 uses a Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 87: NAPGD2022 uses a Gravimetric Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
  Datum zero surface aligned to Global Mean Sea Level (GMSL)
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 88
NAD83(2011) 
NAD83(2007) 
NAD83(HARN/FBN)
NAD83(CORS96)
GEOID18
GEOID12B
GEOID09
GEOID06 (AK only)
GEOID03
GEOID99
GEOID96
Which NAD83 with which geoid?
Notes: I’ve gotten this question more than once.
-Does it matter which geoid model I use with which realization of NAD83?
-NGS Answer = yes
-Project-specific answer = maybe note
-I spoke at length with a gentlemen from the Virginia DOT about this, and he did a bunch of comparisons, saw a barely discernable difference… but still the NGS answer is going to be that for a given realization of NAD83, you should use only the corresponding geoid models for your work
-remember NGS is chasing the millimeter… but maybe you aren’t

## Slide 89: EGM08
GRACE
GOCE
USGG2012 GEOID12A/B
2012
2008
2014
2015
2016
xGeoid14B
xGeoid15B
xGeoid16B
+
GRAV-D
GOCO03s GOCO05S
Evolution of recent NGS geoid models

## Slide 91: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach
Notes: This is not an exhaustive list of NGS programs

## Slide 92: Online Positioning User Service
  OPUS Rapid Static (OPUS-RS)
      dual frequency receiver data
      static sessions only
      30 seconds epoch rate (aka recording interval)
      15 minutes to 2 hours of GPS data
  OPUS Static (OPUS-S)
      same requirements as above
      2 to 48 hours of GPS data
  OPUS Projects (OP)  also Beta OPUS Projects
      adds session processing and network adjustment
      training by NGS required; typically 12 hours
      upload to OPUS with a “Project ID” keyed in Options
Notes: Currently 4 types of OPUS.
*OPUS only supports GPS constellation data, last I talked to the OPUS developer the plan for incorporation of other constellations is Jan 2021.
Rapid Static – files uploaded that are 15 minutes to 2 hours in duration are processed using an NGS software called “RSGPS”
Static - files that are 2 to 48 hours in duration are processed using an NGS software called PAGES Your coordinates are the average of three independent, single-baseline solutions,
OP and Beta OP - these are not a different processing software, just a way to tie multiple OPUS-Static solutions together and use least squares methods to adjust them all as a coherent network
**the Beta serves as a testing bed for the developers to roll out new features or improvements and get feedback from users

## Slide 93: 30 seconds epoch rate

## Slide 94: OPUS-RS – 15 min to 2 hours
Rapid-static: OPUS first creates an atmospheric delay model from surrounding CORS data.
  -Atmospheric model
  -Delivered 179,000 solutions in 2021
Notes: OPUS-RS or Rapid Static performs two calculations.
1st - creates an atmospheric delay model from surrounding CORS data (white circle)
2nd - Your position is determined via a differential GPS static solution

## Slide 95: How does OPUS-RS work?
Selects three to nine “best” CORS based upon:
    Having common satellite visibility with the user data.
    50 < distance <250 km from the user's mark.
    Orientation relative to the user's mark.
The star represents the user’s mark; the triangles are CORS.
No CORS farther than 250 km from the user's mark will be included.
A minimum of three, and no more than nine CORS are used.
s
250km
>250km
Notes: Base stations are chosen by quadrant.

## Slide 96: How does OPUS-RS work?
In addition, user's mark must be no more than 50 km from the (convex) polygon created by the selected CORS.
If the user’s mark is more than 50 km outside this polygon, alternate CORS will be considered.
If none can be found, the processing will abort.
Notes: -Graphic shows five CORS and their resulting polygon
-If rover outside polygon from < 50 km, a warning will be placed at the top of the solution. Check Quality indicators and RMS to ensure a good solution.
-If rover outside polygon >50 km, and there’s no other CORS witin 250km, user will receive Convex Hull error and will not receive solution.

## Slide 97: OPUS-S – 2 to 48 hours
  -Best 3 of 5 baselines
  -Delivered 1,268,000 solutions in 2021
  206,000 solutions in 2011
baseline 1
baseline 3
baseline 4
baseline 2
baseline 5
Notes: -OPUS Static takes the best 3 of 5 baselines and provides you their peak-to-peak average
  -1.2 million solutions delivered in 2021, compared to in 2011 when we first broke the 200,000 solutions milestone
  CLICK FOR SECOND NUMBER

## Slide 98
“peak to peak” error ranges, explained:
LAT: 59 42 33.45847 0.003(m)
W LON: 151 27 27.92482 0.007(m)
EL HGT: 503.684(m) 0.032(m)
ORTHO HGT: 494.346(m) 0.055(m)
LAT range
baseline 3
LON range
CORS baseline 1
=
JGE, 2015
2 outermost baselines are ignored
baseline 4
baseline 2
baseline 5
position: averaged from the 3 most coherent baselines
ORTHO HGT range
ranges: a bounding box enclosing 3 most coherent baselines
for ORTHO HGT, geoid model uncertainty is added
EL HGT range
Notes: As explained earlier, an OPUS solution is actually an average of three independent, single-baseline solutions, each computed by double-differenced, carrier-phase measurements from one of three nearby CORS. While they are “independent” meaning they are run separately, they could all suffer from any single-point-of-failure buried within your data file, metadata, or orbit/tropo/other models or tools.
OPUS attempts 5 solutions, chooses the 3 which form the smallest “peak-to-peak” box and discards the other two.  explain, is this smallest in a 3D sense, or is horizontal only?
To provide orthometric height accuracy, we add to the ellipsoid height range a slop factor from the geoid model.

## Slide 99: Static vs. Rapid Static
 | Static | Rapid Static
Input | 2-48 hours | 15 minutes-2 hours
Output | normal, extended, XML Shared, Projects | normal, extended, XML
Accuracy (95%confidence) | 1-2 cm horizontal 3-6 cm ellipsoidal height | 1-2 cm horizontal 4-8 cm ellipsoidal height
Network Geometry | 3 CORS, preferably within 1000 km of rover | 3-9 CORS, surrounding & within 250 km of rover
Availability | global | 90% of CONUS (subject to geometry, above)

## Slide 100: RMSE of Horizontal Results
Notes: -what’s the takeaway on RS?
-if you get a warning, you may want to reconsider

## Slide 101: RMSE of Vertical Results
Notes: -what’s the takeaway on RS?
-if you get a warning, you may want to reconsider

## Slide 102: OPUS Share – 4 to 48 hours
baseline 1
baseline 3
baseline 5
  Based on OPUS-S
  2 photos
  Brief description
?
Shared Solution ≠ Datasheet

## Slide 103: OPUS Projects – 2 to 48 hours
  Based on OPUS-S
  Control network
    Solutions tied together
Notes:   Ties your observations together via multi-baseline processing and least squares adjustment

## Slide 104: OPUS Projects
Web-based access, nothing to download
Visualize/map your OPUS Solutions
Manage multiple Projects at once
Processing for multiple marks and multiple occupations, or repeat occupations of single mark
Advantages include:
Data uploading through OPUS
Process using PAGES… without learning PAGES (GUI)
Graphic visualization versus text Solution Reports
Support for Bluebooking!

## Slide 105: OPUS Projects – enter a Project ID
Project ID
for OP
Notes: -orange box highlights on the OPUS upload where the user keys in a “project id”

## Slide 106: Why complicate OPUS?
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: OPUS solutions are independent of each other, but they may be indirectly related …
Marks might “share” their environment (similar atmosphere over both).
Data might “share” the same GNSS constellation geometry.
OPUS solutions may “share” some or all of the same CORS.
Etc.
These correlations can increase with project size.

## Slide 107: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: Combining your data logically can improve results:
Neutral atmosphere (tropo) corrections can be improved which, in turn, can help with other things like phase ambiguity resolution.
Common mode effects, like baselines connecting the same CORS common to different marks, can be de-correlated.
OPUS Projects tries to logically group data together:
Data from the same mark are associated with that mark.
Marks simultaneously occupied are grouped into sessions. Session processing improve consistency and accuracy.
-Session processing is NGS jargon meaning the processing of two or more GPS data files whose contents were collected approximately simultaneously to estimate the coordinates of the marks at which the data were collected with respect to one or more marks chosen to act as reference stations

## Slide 108: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: These concepts can be extended to other marks and other sessions.

## Slide 109: Why complicate OPUS?
network adjustment
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: Ultimately, combining session solutions into an adjustment can improve accuracy for the entire network.

## Slide 110: Typical OP Network Diagram
"Hub” design recommended
Hub CORS to marks ≤ ~100 km
Use multiple CORS
Add one very long baseline from Hub to CORS, to improve tropospheric modeling
OPUS-Projects does session baseline processing
Hub
CORS
CORS
CORS
CORS
24hr
24hr
24hr
>2hr
>2hr

## Slide 111: What’s in it for you?
OPUS solutions = pretty good… but each treated as independent and assumes “perfect” CORS
Sessions = simultaneously-observed marks processed together in sessions increases consistency
Adjustments = interlinking sessions through least squares increases accuracy

## Slide 112
OPUS-Projects can’t work magic.
  does not make a project plan obsolete.
  does not make field logs obsolete.
  does not make mark descriptions obsolete.
  does not make mark photos obsolete.
  does not make remove sky obstructions.
  does not make bad data good.
  does not make processing decisions as well as you.
  does not quality control processing results as well as you, the Professional Surveyor
Notes: We can’t “spin straw into gold”.
-but if that’s what everyone wanted then I bet Mark could program us all right out of existence

## Slide 113
GPS survey
data files
photos
descriptions
etc.
Process data using vendor software or PAGE-NT.
Construct bluebook files using software and editor.
Run ADJUST.
geodesy.noaa.gov/ project_tracking/
review and publish to IDB
Bluebooking a Project now

## Slide 114
review and publish to IDB
Upload to OPUS-Projects
Process in OPUS-Projects
GPS survey
data files
photos
descriptions
etc.
Process data using vendor software or PAGE-NT.
Construct bluebook files using software and editor.
Run ADJUST.
geodesy.noaa.gov/ project_tracking/
Bluebooking with OPUS Projects in the future
Available now!
(with certain caveats)

## Slide 115
But wait… there’s more!
Coming soon…

## Slide 116: Hybrid Control Networks = Static + RTK/RTN
OPUS for RTK/RTN-GNSS
Notes: OPUS-RTK/RTN … it’s coming, planned release date of Jan 2020. I’ve seen the Development/Alpha version
1 - Download RTN data from a data collector to software.
2 - Then, identify which base stations were chosen by the RTN as references during the survey.
3 - Go download the static data logged at the RTN base stations on the day(s) of the RTN survey.
4 - Upload this static data, preferably as 24-h files, to OPUS-Projects.

## Slide 117: “What’s the benefit?” they say…
OPUS for RTK/RTN-GNSS
Run least squares adjustment(s) of the combined Static and RTN vectors
Hold NCN CORS (and possibly other published coordinates) in adjustments
Check quality of results
Submit survey project to NGS for review and publication in national database
…you’ll be able to Bluebook RTK/RTN data!
Notes: -planned rollout date of Jan 2020.
-I said RTN vectors a lot there, so really important to keep in mind that to do any of this, you will need to be logging your vectors!
-if you’re using the ODOT network, or the KYCORS, and all you’re doing id

## Slide 118
GNSS Vector EXchange (GVX)
Website: https://www.ngs.noaa.gov/data/formats/GVX/index.shtml
Detailed documentation, Schema, and Example File available
any major search engine: “ngs gvx file format”
…think of GVX as RINEX for RTK/RTN data
Collect RTK, RTN, or PPK, data with your GNSS receiver and field software
  Data must be logged and stored as vectors, not points!
Use your office (or field) software to export vectors to a .gvx file
Upload .gvx to OP5.0
Sidebar: What is this GVX thing?

## Slide 119: What happened to GPSonBM?
The program continues!
All submittals up until 31 Dec 2022 will be incorporated into the NAVD88NAPGD2022 Transformation Tool
How do I get a mark included?
  collect/submit 2+ OPUS Shared Solutions
Tracking map (AGOL)
  NGS committed to biweekly updates
Notes: -This is the last chance for the community to increase the accuracy of this transformation

## Slide 120: Mark Recovery – mobile browser compatible
use your smartphone to submit recovery
Any major search engine:
  “NGS survey mark recovery”
beta.ngs.noaa.gov/cgi-bin/recvy_entry_www.prl
Try it out! Give us feedback!
NGS.Feedback@noaa.gov
Notes: -INCLUDES A DIRECT PHOTO UPLOAD
--CURRENTLY HAVE A FEATURE TO SEARCH YOUR CURRENT AREA

## Slide 121: Mark Recovery – mobile browser compatible

## Slide 122: additional Resources
Notes: This presentation is intended to raise awareness about the upcoming changes and what they mean for floodplain mapping, but you probably have lots of remaining questions and we have a lot of resources online at our website
Please spread the word, and
make an effort to keep yourself and your colleagues informed.
Tell us what content is missing or how we can make it better!

## Slide 123
https://www.ngs.noaa.gov/ADVISORS/
Notes: -14 Regional Advisors, we’ve transitioned from a State-based to a Regional Program
-our advisors homepage up there at the top, also easy to find us by querying any major search engine for “ngs advisors”
-if you know Ross Mackay, he is our Chief Advisor, I report to him…
**ya know, I don’t know why they don’t make him put his photo up here
-we do have one vacant advisor position, that was recently advertised and John up there in Wisconsin is officially retired in oh… 18 days

## Slide 124: Regional Geodetic Advisor Program
geodesy.noaa.gov/ADVISORS/
query any major search engine: “ngs advisors”
Notes: Transitioned from a State to a Regional program in 2016. States no longer provide funding if they desire to have an Advisor, but NGS reorganized the personnel to support regions rather than single States.
Kentucky has appointed a State Geodetic Coordinator

## Slide 125: State Geodetic Coordinators
Not an NGS employee
Serves as a liaison between the State’s geospatial community and the NGS
Erik Baldwin over at Bluefield State College
Notes: -The State Geodetic Coordinator is not employed by NGS and is typically assigned by a state government agency or university.
-Wes Virginia we’ve got Eric over at Bluefield --- contact info.

## Slide 126
Geometric
Sep 2017; Rev. Apr 2021
NOAA TR NOS NGS 62
Geopotential
Nov 2017; Rev. Feb 2021
NOAA TR NOS NGS 64
Working in the modernized NSRS
Apr 2019; Rev. Feb 2021
NOAA TR NOS NGS 67
All three were revised in 2021
Blueprints for the Modernized NSRS
…your best source for information on modernization
Notes: Here’s the front cover of the three blueprint documents, and know that for each given topic these are your best source for information on modernization.
They’ve been written by teams, reviewed, re-written, re-reviewed, and ...
CLICK
…all three will have been re-released, with new titles, in 2021. The revisions were to solidify some items originally called out as To Be Determined, and the rename was to make it clear that 2022 would no longer be the target date.
*Blueprint Part 1 re-release may nor may not have been published by the time of this webinar, but it will be soon. I’ll show you how to find these at the end of today’s webinar.

## Slide 127
Educational Videos
<5 minutes
Online Lesson
(via MetEd/COMET)
~1 hour
Resources at geodesy.noaa.gov
Notes: Educational videos and online tutorials –
Our library of lessons and videos are great resources, and will reinforce a lot of information we covered today.
The videos are just 3-5 minutes long.
the lesson is a deeper dive but still only takes an hour.

## Slide 128
Educational Videos
<5 minutes
Online Lesson
(via MetEd/COMET)
~1 hour
NGS homepage: geodesy.noaa.gov
Notes: Educational videos and online tutorials –
Our library of lessons and videos are great resources, and will reinforce a lot of information we covered today.
The videos are just 3-5 minutes long.
the lesson is a deeper dive but still only takes an hour.

## Slide 129
Click this icon on homepage
Email Subscriptions
*Only 1-2 messages per month*
NGS News
  Includes quarterly NSRS Modernization newsletter
Webinar Series
Training
GPS on Benchmarks
Notes: Stay abreast of any new information coming from us via Email Subscription –
Sign up for notifications about News, webinars, and training opportunities with NGS.
We also use our News subscription list to send out our quarterly NSRS Modernization Newsletter.

## Slide 130
https://www.ngs.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 131
www.ngs.noaa.gov
beta.ngs.noaa.gov