## Slide 1
Vertical Datums of the NSRS
Past, Present, Future
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
WVAGP Conference
May 2022
Notes: -hi my name’s Jeff!
-so who am I?
-I’m a surveyor, NGS calls me a geodesist, and my background is in all types of surveying both land and hydrographic. I’ve been with NGS for about 2 years, came here from the USACE (Pittsburgh District), and have also worked for the Bureau of Land Management and various State & local government. Spent almost my entire career with government, and got my start surveying in the military. It’s taken me around the world, but originally I’m from SE Ohio, I’m a university of Akron graduate, and I have an older sister who lives just north up in Flint.

## Slide 2
Why does the NSRS matter to me?
+
+
FIRMs require data from disconnected sources.
Dates and datums must be consistently aligned.
Ellipsoidal Datum
Water Level Datum (and Flow Rates)
Orthometric Datum
Terrestrial Survey/Cross-Sections
Aerial LiDAR/Mapping
Historic Water Levels and Flow Rates
Notes: Example of why we need consistent coordinates (illustrated):
Just in the making of a single FIRM, data collected at different points in time using different methods:
-aerial lidar
-x-section and structure data via survey
-streamflow data/hydrographs
All of these must be reliably aligned and combined with historical data, in both the horizontal and vertical components, to produce a final product in which all of this information is available in one place, to assist professionals like yourselves in appropriate flood mitigation.
Therefore, Reliable Flood Rate Insurance products rely on the NSRS
In a perfect world…
datums would be parallel and smooth
Surface of Earth would not move

## Slide 3
Positional Components of
the NSRS
Geometric
aka “Horizontal”
Latitude, Longitude, Ellipsoid Height
Geopotential
aka Orthometric Height
aka “Elevation”
NAD83
NAVD88
Notes: -geometric component is latitude, longitude, and ellipsoid height
-geopotential component is combined with the geometric components to calculate an ortho height or capital H

## Slide 4
Three types of heights in NSRS
Water Level or Tidal
NOAA and USACE Hydrography
Daily and Extreme Water Levels (Gage)
Shoreline Mapping and Regulatory Boundaries at the Coast
geoid
Ellipsoidal
Raw GPS Observations
Raw Hydrographic Surveys
Raw Lidar Data
NAD83
Orthometric
USGS
Topography
FEMA NFIP Data & Maps
Engineering and Construction Surveys
NAVD88
NGVD29
Notes: This slide illustrates the 3 categories of vertical datums and examples of where each is directly used They are project and application dependent.
First, we have ellipsoidal datums. Examples include WGS84 and NAD83 (North American Datum of 1983). You will encounter these datums frequently in hydrographic surveys that are vertically referenced with RTK-GPS; any native GPS measurements; and even raw lidar datasets.
Next, we have orthometric datums. These datums are very important because height differences referenced to orthometric datums will allow us to know the direction water will flow, because they have been “gravity-corrected”. The North American Vertical Datum of 1988 (or NAVD 88) is an orthometric datum, which you will see on USGS topographic maps, engineering and development site surveys, and FEMA Flood Insurance Rate Maps.
Finally, we have Tidal Datums, which are derived from water level measurements. They have extremely important applications including daily and extreme water levels; NOAA nautical charts, and shoreline mapping or boundaries along the coast.
*NOAA provides tools (like NCAT and Vdatum) to transform between these different height systems.
The Bridge

## Slide 5
Orthometric
Notes: This slide illustrates the 3 categories of vertical datums and examples of where each is directly used They are project and application dependent.
First, we have ellipsoidal datums. Examples include WGS84 and NAD83 (North American Datum of 1983). You will encounter these datums frequently in hydrographic surveys that are vertically referenced with RTK-GPS; any native GPS measurements; and even raw lidar datasets.
Next, we have orthometric datums. These datums are very important because height differences referenced to orthometric datums will allow us to know the direction water will flow, because they have been “gravity-corrected”. The North American Vertical Datum of 1988 (or NAVD 88) is an orthometric datum, which you will see on USGS topographic maps, engineering and development site surveys, and FEMA Flood Insurance Rate Maps.
Finally, we have Tidal Datums, which are derived from water level measurements. They have extremely important applications including daily and extreme water levels; NOAA nautical charts, and shoreline mapping or boundaries along the coast.
*NOAA provides tools (like NCAT and Vdatum) to transform between these different height systems.

## Slide 6
National Geodetic Vertical Datum
of 1929
NGVD29
was replaced by

## Slide 7
North American Vertical Datum
of 1988
NAVD88
will be replaced by

## Slide 8
North American-Pacific Geopotential Datum of 2022
NAPGD2022
(pronounced: nap-jee-dee)

## Slide 9
A very brief history of (the most prevalent) U.S. vertical datums

## Slide 10
Referenced to 26 tide gauges in the US and Canada
Notes: It turns out that MSL is a close approximation to another surface, defined by gravity, called the geoid, which is the true zero surface for measuring elevations. Because we cannot directly see the geoid surface, we cannot actually measure the heights above or below the geoid surface. We must infer where this surface is by making gravity measurements and by modeling it mathematically. For practical purposes, we assume that at the coastline the geoid and the MSL surfaces are essentially the same. Nevertheless, as we move inland we measure heights relative to the zero height at the coast, which in effect means relative to MSL.
Definition: NGVD29 – The National Geodetic Vertical Datum of 1929…
The Sea Level Datum of 1929 was the vertical control datum established for vertical control surveying in the United States of America by the General Adjustment of 1929. The datum was used to measure elevation or altitude above, and depression or depth below, mean sea level (MSL).
Mean sea level was measured at 26 tide gauges: 21 in the United States and 5 in Canada. The datum was defined by the observed heights of mean sea level at the 26 tide gauges and by the set of elevations of all bench marks resulting from the adjustment. The adjustment required a total of 66,315 miles (106,724 km) of leveling with 246 closed circuits and 25 circuits at sea level.
Since the Sea Level Datum of 1929 was a hybrid model, it was not a pure model of mean sea level, the geoid, or any other equipotential surface. Therefore, it was renamed the National Geodetic Vertical Datum of 1929 (NGVD 29) in 1973. The NGVD 29 was subsequently replaced by the North American Vertical Datum of 1988 (NAVD 88) based upon the General Adjustment of the North American Datum of 1988.

## Slide 11: NGVD29 – based on 26 tide gauges
Concept
topographic surface
datum zero
surface
  Local Mean Sea Level differs at tide stations due to prevailing winds, ocean current, salinity, seabed topography, etc.

## Slide 12
Why one site this time?
removed local sea level variation problem of NGVD29
Referenced to one tidal bench mark in Canada
Notes: Definition: The surface of equal gravity potential to which orthometric heights shall refer in North America
One height held fixed [at 6.271 meters along the plumb line below the geodetic mark] at “Father Point” (Rimouski, Canada).
By fixing the geopotential value at the origin point, it was possible to ensure that the origins of IGLD 85 and NAVD 88 aligned.
**But perhaps more importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)
Use of one fixed height removed local sea level variation problem of NGVD 29
*It should be pointed out that while the datum was defined in such a way as to be usable on the North American continent, it was never actually adopted in Canada. It can be used there, but it’s not their official civilian datum.
Note that the designation of the vertical control point at Father Point is “1250 G=NAVD 88 DATUM POINT” for PID# TY5255 and is not available from the publicly accessible NGSIDB.

## Slide 13: NAVD88 – based on single benchmark
Concept
topographic surface
datum zero
surface
Notes: -

## Slide 14
Approximate Error in NAVD88 zero surface
Map is the H=0 surface differenced from satellite gravity data
Notes: Map highlights the tilt/bias to the zero reference surface, that’s another item that was discovered later on with the advent and proliferation of satellite positioning and remote sensing technology.
How was the map created, that is the NAVD88 zero surface (H=0) overlaid onto a satellite based geoid model, then color shaded by vertical difference

## Slide 15: NAVD88 – based on single benchmark
Concept
  Most, if not all, of this error in alignment was intentional.
  Huh?! It was chosen to minimize the change to contours in USGS quadrangles.
topographic surface
datum zero
surface
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 16
NAD83(2011) 
NAD83(2007) 
NAD83(HARN/FBN)
NAD83(CORS96)
GEOID18
GEOID12B
GEOID09
GEOID03
GEOID99
GEOID96
Which NAD83 with which geoid?
Notes: I’ve gotten this question more than once.
-Does it matter which geoid model I use with which realization of NAD83?
-NGS Answer = yes
-Project-specific answer = maybe note
-I spoke at length with a gentlemen from the Virginia DOT about this, and he did a bunch of comparisons, saw a barely discernable difference… but still the NGS answer is going to be that for a given realization of NAD83, you should use only the corresponding geoid models for your work
-remember NGS is chasing the millimeter… but maybe you aren’t

## Slide 17: NAPGD2022
Geopotential
  gravity based
  no leveling used to define it (none!)
GNSS is your “access point”
  collect data & submit it to OPUS
  no leveling necessary
Global Mean Sea Level (GMSL) based
  geoid change when sea level threshold crossed

## Slide 18
You’ve all used a DEM.
(Digital Elevation Model)
Picture a geoid model as a DGM.
(Digital Gravity Model)
-both raster cells of height values
but represent different things
Gravity  Geoid

## Slide 19
Seen this on the internet?

## Slide 20
“The true size and physical shape of the Earth” --social media, etc.
Nope
Geoid – an incorrect definition

## Slide 21
  “The geoid is the equipotential surface that most closely coincides with the undisturbed mean sea level (and its continuation through the continents).”
    - Sjöberg, L. E., & Bagherbandi, M. (2017). Gravity Inversion and Integration, Theory and Applications in Geodesy and Geophysics. Springer.
  equipotential  equal potential
  potential  as in energy… or gravitational pull
Geoid - my favorite definition

## Slide 22
-GPS for Land Surveyors, by Jan Van Sickle, 4th ed., CRC Press, Taylor & Francis Group, 2015, p. 180. (slightly edited)
Equipotential Surface
Geoids are defined by a specific strength of gravity  W0
Notes: Recall our ol’ buddy W sub-naught (W0)

## Slide 23
  airborne observations of relative gravity
  collected in as short of a timespan as is realistic
  full coverage
  on-the-ground observations of absolute gravity
  periodic or episodic; repeat every ___ years
  large spacing, a few per state
How do we measure gravity?
Notes: Two major campaigns within GRAV-D
High-resolution snapshot of gravity
  airborne observations of relative gravity
  collected in as short of a timespan as is realistic
  full coverage
Low-resolution “movie” of gravity changes
  on-the-ground observations of absolute gravity
  periodic or episodic; repeat every ___ years
  large spacing, a few per state

## Slide 24: Gravity for the Redefinition of the American Vertical Datum
as of April 2022:
93% complete
10 km data lines
70 km cross lines
20,000 ft altitude
230 kt flight speed
Green = Complete
Blue = In Processing
Yellow = Underway
White = Planned

## Slide 25
NAVD88 geoids
versus
NAPGD2022 geoids

## Slide 26
  Gravimetric
  Hybrid
Two types of geoid models
Notes: -believe it or not there’s more than 2 types, but the 2 types you’ll see NGS publish are…

## Slide 27
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid then best fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 28
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 29: Gravimetric vs. Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 30: NAVD88 uses a Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 31: NAPGD2022 uses a Gravimetric Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
  Datum zero surface aligned to Global Mean Sea Level (GMSL)
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 32: Comparing Heights
or …“digging for datums”

## Slide 33
A reference surface that can be used to measure heights in a uniform way.
Sally
Jane
How much taller is Sally than Jane?
Could measure directly from top of head to top of head.
Or, from floor up to tops of heads and then subtract!
X= ?
That’s a relative height, or height difference.
That’s a difference in heights above a datum.
Datum
Vertical Datum Visualized
X = (h Sally) – (h Jane)
Notes: A vertical reference system is a reference surface that can be used to measure heights in a uniform way.
So, how much taller is Sally?

## Slide 34
Datum Difference Visualized
Sally
Jane
X= ?
How much taller is Sally than Jane?
Need to know what they’re standing on!
We cannot compare heights that are measured from different reference surfaces.
X ≠ (h Sally) – (h Jane)
Datum 1
Datum 2
Can still calculate X with a relative height… but it is not accurate, as our reference surface is not the same.
NGVD29
NAVD88
Notes: -Well, we need to know how tall, or the slope of the hill.
-You cannot compare heights that are measured from different planes of reference.
*If we replace Sally and Jane with an example more related to floodplains:
What if we want to compare a BFE height in 1990 and a BFE height 2010
what if the land has subsided under that base flood elevation over time?
…hold that thought.

## Slide 35: Ok Jeff, how do I do that?
…we call that a datum transformation
Notes: -note that’s the proper technical term, but I’m not going to hound someone who says “conversion”… I slip sometimes too

## Slide 36
Conversion
    change the type of coordinate
    e.g. NAD83(2011) latitude & longitude  NAD83(2011) SPCS
  Transformation
    change the datum of coordinate
    e.g. NGVD29 height in feet  NAVD88 height in feet
    e.g. NAD 27 latitude & longitude  NAD 83(2011) latitude & longitude
Propagation
    change the epoch of coordinate
    e.g. NAPGD2022 epoch 2020.00 to NAPGD2022 epoch 2087.2570
    e.g. NATRF2022 epoch 2020.00 to NATRF2022 epoch 2023.243
Terminology - Changing Coordinates
Notes: Historically NGS has been inconsistent with these top two words.
Going forward, we will use them as:
  Conversion: Meaning to change the type of coordinate without changing the datum or frame
  e.g. change NAD 83(1986) latitude and longitude to NAD 83(1986) State Plane Coordinates
  Transformation: Meaning to change the datum or frame, without changing the type of coordinate
  e.g. changing an NAD 27 latitude & longitude to an NAD 83(1986) latitude & longitude
So, “NADCON” which transforms coordinates between datums could have been called “NADTRAN.” C’est la vie.

## Slide 37: What if time is a factor? What if things move?
Notes: -by “things” we mean the objects we’re measuring
-if earth is moving, we need o account for that

## Slide 38
Epoch Difference Visualized
2020
Sally
2027
Jane
X= ?
How much taller is Sally than Jane?
Need to know the epoch of our measurements!
We should not compare heights that are measured at significantly different times.
X ≠ (h2020.00 Sally) – (h2027.59 Jane)
Can calculate X… but it is not accurate, as the thing to be measured is not the same.
NAPGD2022
What if Sally and Jane are growing?
Notes: -Well, we need to know how tall, or the slope of the hill.
-You cannot compare heights that are measured from different planes of reference.
*If we replace Sally and Jane with an example more related to floodplains:
What if we want to compare a BFE height in 1990 and a BFE height 2010
what if the land has subsided under that base flood elevation over time?
…hold that thought.

## Slide 39
Estimated change in orthometric heights from NAVD88 to NAPGD2022
(NAPGD2022 approximated using xGEOID16B)

## Slide 40: Preparing for NAPGD2022
  Inventory heights in your data/datasets
    Have you mix & matched geoid models?
      Are you tracking levees or other flood control?
      Are you managing subsurface utilities?
        Access covers, junction boxes, cleanouts, etc.
      Maybe geoid differences aren’t even significant.
    Know your goals, know your data.

## Slide 41: Preparing for NAPGD2022
  Know the epoch of your data/datasets
    consider how you will track this
      full to-the-second timestamp on every feature?
      labeling a year for each dataset?
      something in-between that works for your needs

## Slide 42: Preparing for NAPGD2022
  Transforming your data
    NCAT - NGS Coordinate Conversion and Transformation Tool
      available now: ASCII upload, Web Services, GitHub
      ask your software provider(s) about integration
        we envision this as most popular method of access
        Industry Workshop held May 2021
          Esri, Trimble, Blue Marble, etc… all the well known names attended
Notes: Transforming your data
NCAT - NGS Coordinate Conversion and Transformation Tool
available now: ASCII upload and Web Services
ask your software providers about integration
we envision this as most popular method of access
Industry Workshop held last week – esri, trimble, bluemarble, all the major well known names were represented
labeling a year for each dataset?
something in-between that works for your needs

## Slide 43: additional Resources
Notes: This presentation is intended to raise awareness about the upcoming changes and what they mean for floodplain mapping, but you probably have lots of remaining questions and we have a lot of resources online at our website
Please spread the word, and
make an effort to keep yourself and your colleagues informed.
Tell us what content is missing or how we can make it better!

## Slide 44
https://www.ngs.noaa.gov/ADVISORS/
Notes: -14 Regional Advisors, we’ve transitioned from a State-based to a Regional Program
-our advisors homepage up there at the top, also easy to find us by querying any major search engine for “ngs advisors”
-if you know Ross Mackay, he is our Chief Advisor, I report to him…
**ya know, I don’t know why they don’t make him put his photo up here
-we do have one vacant advisor position, that was recently advertised and John up there in Wisconsin is officially retired in oh… 18 days

## Slide 45: State Geodetic Coordinators
Not an NGS employee
Serves as a liaison between the State’s geospatial community and the NGS
Erik Baldwin at Bluefield State College
Notes: -The State Geodetic Coordinator is not employed by NGS and is typically assigned by a state government agency or university.
-Wes Virginia we’ve got Eric over at Bluefield --- contact info.

## Slide 46
Educational Videos
<5 minutes
Online Lesson
(via MetEd/COMET)
~1 hour
Resources at geodesy.noaa.gov
Notes: Educational videos and online tutorials –
Our library of lessons and videos are great resources, and will reinforce a lot of information we covered today.
The videos are just 3-5 minutes long.
the lesson is a deeper dive but still only takes an hour.

## Slide 47
Click this icon on homepage
Email Subscriptions
*Only 1-2 messages per month*
NGS News
  Includes quarterly NSRS Modernization newsletter
Webinar Series
Training
  Primarily surveyor focused
GPS on Benchmarks
Notes: Stay abreast of any new information coming from us via Email Subscription –
Sign up for notifications about News, webinars, and training opportunities with NGS.
We also use our News subscription list to send out our quarterly NSRS Modernization Newsletter.

## Slide 48
https://www.ngs.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486