## Slide 1: NSRS Modernization An Update from NGS
CEC Geospatial Summit
March 2024
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 2
Any references to any commercially available hardware or software do not constitute an endorsement or a disapproval of any manufacturers, developers, dealers, or suppliers.
Thanks.

## Slide 3: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
Notes: -We are the Federal Government’s oldest scientific agency.
-part of the Executive Branch
-I know it can seem kind of strange that NGS is part of the NOS, but the origins of NGS lie with the C&GS.
-we are a “Program Office” of the NOS
Survey of the Coast – 1807
Coast Survey – 1836  in 1871 the agency was tasked by Congress with responsibility to carry geodetic control inland (>150 years)
Coast and Geodetic Survey – 1878
NGS since 1970

## Slide 4: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
≠
We’re not USGS, we’re NGS

## Slide 5: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
NSRS
Notes: NGS develops and maintains the National Spatial Reference System, a national coordinate system that provides the foundation for transportation, navigation, land record systems, mapping and charting efforts, and a multitude of scientific and engineering applications
CLICK
You’ve all seen this or some similar graphic I’m sure. That bottom layer… that’s our baby, the NSRS.

## Slide 6: NGS Mission
access… ? = traditionally  marks/disks/objects
= modern and future  NOAA CORS Network (NCN)
via OPUS
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
Notes: Follow up thought
-like it or not, we know that the vast majority of our users are obtaining NSRS coordinates via OPUS
-while that is our plan for the future of primary access, modernized NSRS, as of now the official form of access (specifically to NAVD88) truly is to “touch brass” as they say  meaning occupy a benchmark

## Slide 7: NOAA CORS Network (NCN)
Notes: -I would like to point out we have a new, official name for the network you see represented on this map,
-The NOAA CORS Network, or NCN
CLICK
-this is neat little graphic with some stats on teh NCN you can find on our website
-below the gaphic youll find a search bar with more information

## Slide 8: NOAA CORS Network (NCN) in PA
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 9: KeyNetGPS CORS Network
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 10: NOAA CORS Network (NCN) in PA
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 11: KeyNetGPS CORS Network
non-NCN CORS
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 12: Online Positioning User Service
      dual frequency receiver
      static observations (via RINEX  ABCD123x.24o)
      30 seconds epoch/logging rate aka recording interval
  OPUS Rapid Static (OPUS-RS)
      15 minutes to 2 hours of GPS data
  OPUS Static (OPUS-S)
      same requirements as above
      2 to 48 hours of GPS data
  OPUS Projects (OP)
      adds session processing and network adjustment
      training by NGS currently required (~12 hours)
Also Beta OPUS-S
Multi-constellation
More CORS checking

## Slide 13: NGS Products and Services
Not just OPUS
All exist in three environments:
  Development (DEV) - internal testing and development
    same as when you hear a company talk about an “Alpha” product
  Beta - continued internal testing, open for public testing
    key features have already been vetted/tested
  Production - final product, open to public use
    this is what you see first when navigating our website
Notes: I’ll be talking about OPUS today, but I need to clarify one of our processes for this to all be clear. I will also mention that this is a new-ish workflow for NGS, began in the past 8 or so years.
So all NGS Products & Services go thru this process as they are created, tested internally, open for testing by you our constituents, and then rolled out as final products.
CLICK
There’s three environments that products will exist in, listed here in the order they occur
First, a tool will be created on the “DEV” servers for internal NGS-only development, testing, and otherwise “working the bugs out”
this is the same phase as when you hear a software company or video game maker talk about their alpha products
CLICK
Next, after some level of confidence in the product is gained, it will be migrated to the Beta servers, thereby open to the public for their own testing
it’s important to note that when a product is available via our Beta page, when you use it you are indeed now a “beta tester”
key features will have already been tested in the Development environment, but it is still a beta, so as a beta tester please let us know if you have issues/complications/struggles or the like
CLICK
At some point, when all I’s are dotted and T’s crossed, the thing will be moved to the Production environment.
 by then, the tool is integrated into others, has been vetted with 2 testing phases and functions as expected, but may still continue to receive version updates by repeating this process

## Slide 14
www.ngs.noaa.gov
beta.ngs.noaa.gov
Remember, you won’t see the DEV environment…
Notes: So here we have 3 screenshots, first here showing the Production OPUS Projects gateway page
CLICK
Second is the Beta page, with the text here showing the URL for our Beta homepage
-How do you find that beta page? substitute “beta” for “www”
-or most tools that have a beta will have a link to that beta platform
CLICK
Last is the Development or DEV example, which again you will not see unless via a demo from NGS personnel

## Slide 15: Wait… how do I get to the NGS Beta site?

## Slide 16
www.ngs.noaa.gov
beta.ngs.noaa.gov

## Slide 17: OPUS only processes every 30s
You can upload 5s interval data
  But OPUS will trim/decimate to 30s interval
  And this may result in error messages
You can even upload 1s interval data
  But only shorter files, or OPUS will abort
For static, 30s yields good results
  If using your commercial software, 15s can be advantageous
Notes: Even if you’re running RTK…
  You can setup your base to only log @ 30s rate
  Know your equipment

## Slide 18: OPUS processes every 30s
20s decimates to 60s

## Slide 19
 | OPUS Shared | OPUS Projects (RINEX) | OPUS Projects (GVX)
Minimum Occupations | 4 hours At least 1, maybe 2* | 2 hours At least 2 | 5 minutes At least 3
Processing | OPUS-S (sequential) | PAGES (simultaneous) | Real Time (RTN/NRTK)
Adjustment | None | Least Squares Network | Least Squares Network
Metadata | 2 photos Brief Description | 3 photos, WinDesc files, Logs, & Report | 3 photos, WinDesc files, Logs, & Report
*Need 2 or more GPS datasets in our database, existing data holdings count toward that.
OPUS Shared vs. OPUS Projects

## Slide 20: Passive Control
All marks are passive—they sit there and hold a point
Geodetic Control – Terminology
Notes: All marks are passive!—in that they sit there doing nothing in and of themselves besides holding a point
This includes the fixed antenna mount that is a part of a CORS.
But, some marks have permanently installed equipment that enable nearly continuous observations and these are called “active” stations.

## Slide 21
Passive Control

## Slide 22: Active Control
Some marks have permanently installed equipment that enables nearly continuous observations
Geodetic Control – Terminology
(they still sit there and hold a point)
Notes: All marks are passive!—in that they sit there doing nothing in and of themselves besides holding a point
This includes the fixed antenna mount that is a part of a CORS.
But, some marks have permanently installed equipment that enable nearly continuous observations and these are called “active” stations.

## Slide 23
Active Control

## Slide 24: Active vs. Passive Control
Passive – setting up your RTK Base on existing geodetic control (e.g. Datasheet) while collecting with RTK Rover
Active – setting up your RTK Base to log data while collecting with RTK Rover then processing Base data via OPUS; or collecting with RTN/NRTK Rover
Geodetic Control – Terminology
My point: surveying is still surveying
Notes: Often the term active geodetic control has been used to mean some equipment is continuously or at least frequently collecting observations at or near a point
Yet those observations are often used to compute coordinates (often time-dependent) at a point on a mark, which, by its nature is passive

## Slide 25: Yes, we are delayed.
  NSRS Modernization
Notes: So remember, today’s presentation is not JUST about new datums, it is about modernizing the NSRS as a whole.
You don’t know what the NSRS is? Stay tuned, we’ll get there as we go along.

## Slide 26: Delayed Release of the Modernized NSRS
How long will the delay be?
  Our website or newsletter is best source of projected timeframe, current estimate is middle of 2025.
Will the names stay the same?
  Yes, terms containing “2022” such as “NATRF2022” and “NAPGD2022” will remain the same.
Will all previously proposed products be released along with the new datums?
  No, they will not. Check out our June 2022 webinar.
hyperlink to the Track Our Progress homepage
hyperlink to the full FAQ
June 2022 webinar

## Slide 27: Modernizing the NSRS
Updating all NSRS coordinates
  Replace existing datums with new datums
  Replacing existing SPCS83 with new SPCS2022
  Accounting for coordinates changing with time
Improving NGS products and services
Simplifying customer contributions
Making the NSRS:
  More accurate
  More accessible
  More efficient
Rollout in
2025
begins

## Slide 28
Positional Components of
the NSRS
Geometric
aka “Horizontal”
Latitude, Longitude, Ellipsoid Height
Geopotential
aka Orthometric Height
aka “Elevation”
NAD83
NAVD88
Notes: -geometric component is latitude, longitude, and ellipsoid height
-geopotential component is combined with the geometric components to calculate an ortho height or capital H

## Slide 29
NATRF2022
North American Terrestrial Reference Frame of 2022
will replace
NAD83
North American Datum of 1983
Technically, not just NATRF2022 but also its 3 sister TRFs…

## Slide 30: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 31
Existing, accepted terminology
  International TRF
  first realization of the ITRF was 1992
  NATRF2022 will be based on ITRF2020
“Horizontal Datum” - misnomer for NAD83
  Really is a Geometric Reference Frame
Terrestrial Reference Frame?
Notes: -Where do you see an Epoch right now in NGS data?
CLICK
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 32
International Terrestrial Reference Frame
(ITRF)
Is native coordinate system for NCN.
Is what OPUS uses.
Is what most of world uses.
Is what NGA aligns WGS-84 to.
Notes: So what is that acronym, ITRF?
-it is a global reference frame, the most widely adopted one, or the “gold standard” or the “Cadillac” or what-have-you
-ITRF is the internationally recognized standard
-who realizes the ITRF? well, NGS contributes to the realization but
CLICK
-The IERS is in responsible charge of defining, realizing and promoting the ITRF
-and the ITRF was formally adopted by the…yes, more acronyms
CLICK
IUGG some years ago

## Slide 33
Watch the grid!
ITRF concept
Epoch:
Notes: Ok, now ITRF mentioned a couple slides ago.
Most simplistic way to explain ITRF is to watch this animation.
This is a very loose representation/visualization of what the ITRF is, a characterization only.

## Slide 34: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 35: Plate Rotation visualized
Drift…
Notes: -these are ground-level horizontal velocities
-the arrows illustrate the positions and velocities of CORS plotted in ITRF2014
-our scale is on the left there, with that arrow representing 20mm of motion per year
-so right thru Ohio it’s a little cluttered but we’re seeing arrows about that length so about 2cm/20mm per yr
-what do we notice about the direction of these arrows?
-they look rotational, don’t they?
CLICK HERE
-Note the arrows in California do not conform to the rotation… those are CORS on a different PLATE which is moving in a different direction
CLICK HERE
-so when you look at those arrows you can see the rotation, but the point of rotation is obviously off the map, way down below the screen right?
-that point is what’s known as an Euler Pole

## Slide 36: Plate-Fixed NSRS TRFs
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)
Notes: We say “NATRF2022” is “fixed” to the N.A. Plate, making it a “plate fixed” frame
-the frame is constant to itself, but rotating within ITRF, and moving in a different direction than the other 3 frames

## Slide 37
ITRF – constant frame, rotating plate

## Slide 38: Plate-Fixed
NATRF – rotating frame, constant with plate

## Slide 39
ITRF or NATRF – your choice if you know epoch
if you know epoch

## Slide 40: Decades of continuously logged GPS data from the NOAA CORS Network (NCN).
  But how?

## Slide 41
NOAA CORS Network (NCN)

## Slide 42: Plate-Fixed
NATRF – rotating frame, constant with plate
= CORS

## Slide 43: Plate-Fixed
ITRF or NATRF
= CORS
Notes: ITRF is independent of any plates, tied to the layer below,
-”plate-agnostic” if we want to sound all silicon valley ish
-the plates go down about 200 km (125 mi) deep below our feet right now, as we’re on a continental plate
--(oceanic plates are roughly half the thickness, like 100 km)
- but thickness of the tectonic plates varies greatly, from down to 15 km up over the 200 km I mentioned earlier

## Slide 44
Epoch
eh-puck? ee-pock? … to-may-to, to-mah-to
an instant of time; a moment in time
astronomy & geodesy use a decimal date
  2021.4762 = 23 June 2021 @ 19:16:00
  using epochs is important, not your format
    start preparing to assign epochs to your data
Terminology – Time/4D
Notes: -Where do you see an Epoch right now in NGS data?
CLICK
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 45
Notes: -Where do you see an Epoch right now in NGS data?
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 46
Reference Epoch
Survey Epoch
Notes: -Where do you see an Epoch right now in NGS data?
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 47: What is a Reference Epoch?
First let’s look at complete nomenclature…
If you use NAD83 you’re already using one, but perhaps unaware.

## Slide 48: Complete NAD83 Nomenclature
NAD83(2011) epoch 2010.00
Geometric
Datum
Realization
(aka Datum Tag)
Epoch
(in the case of NAD83, a Reference Epoch)
NAD83(1986) epoch 1984.00
NAD83(HARN) epoch 1993.62
NAD83(CORS96) epoch 2002.00
NAD83(2007) epoch 2007.00
Other NAD83 Reference Epochs
NAD83(1986) epoch 1984.00
NAD83(HARN) epoch 1993.62
NAD83(CORS96) epoch 2002.00
NAD83(2007) epoch 2007.00
NAD83(2011) epoch 2010.00
ITRF2014 epoch 2019.9185
IGS08 epoch 2005.00
NATRF2022 epoch 2020.00

## Slide 49
eh-puck? ee-pock? … to-may-to, to-mah-to
an instant of time, or a date selected as a point of reference
Epoch
Reference Epoch
Survey Epoch
Notes: -Some communities/countries will refer to the Survey Epoch as the Continuous Epoch or the Dynamic Epoch
*****for 2022, everywhere I use the term ITRF2014 may end up being ITRF2020*****
-we’re aligning to 2020.000 because the goal is to finalize the datum for 2022, and it takes time to process the data and run the calculations, hence aligned to the 2020.000 epoch

## Slide 50: What is a Survey Epoch?
If you use OPUS you’re already using one, but perhaps unaware.

## Slide 51: Complete ITRF Nomenclature
ITRF2014 (epoch 2021.0276)
Geometric
Datum
Epoch
(in the above example, a Survey Epoch)
ITRF92 epoch 1988.0
ITRF2000 epoch 1997.0
ITRF2005 epoch 2000.0
ITRF2008 epoch 2005.0
ITRF2014 epoch 2010.0
ITRF Reference Epochs
NAD83(1986) epoch 1984.00
NAD83(HARN) epoch 1993.62
NAD83(CORS96) epoch 2002.00
NAD83(2007) epoch 2007.00
NAD83(2011) epoch 2010.00
ITRF2014 epoch 2019.9185
IGS08 epoch 2005.00
NATRF2022 epoch 2020.00
ITRF2008 epoch 2012.2011
IGS08 epoch 2006.7572
ITRF2014 epoch 2017.4457
ITRF2014 epoch 2019.9185
ITRF2014 epoch 2021.0276
Examples of ITRF Survey Epoch

## Slide 52: Epochs in Current NSRS
Reference Epoch (RE)
Position after propagated back in time from SE to RE
Seen on OPUS Solution
Used in NAD 83
Ground movement will be hidden
Survey Epoch (SE)
Position at the moment of survey data collection
Seen on OPUS Solution
Necessary for ITRF
Ground movement will be illustrated

## Slide 53: Epochs in Modernized NSRS
Reference Epoch (RE)
Position after propagated back in time from SE to RE
Used in NATRF2022
REC = RE Coordinate
Ground movement will be hidden
Survey Epoch (SE)
Position at the moment of survey data collection
Used in NATRF2022
SEC = SE Coordinate
Ground movement will be illustrated

## Slide 54: 4D alignment – Epochs
One epoch in which ITRF2020 will be equal to NATRF2022…
At 00:00 on January 01, 2020 any given coordinates in
ITRF2020 (epoch 2020.0) = NATRF2022 (epoch 2020.0)
Notes: After that, they diverge and continue to do so, we’ll visualize that soon

## Slide 55
Conversion
    change the type of coordinate
    NAD83(2011) latitude & longitude  NAD83(2011) SPCS
  Transformation
    change the datum of coordinate
    NGVD29 height  NAVD88 height
    NAD 27 latitude & longitude  NAD 83(2011) latitude & longitude
Propagation
    change the epoch of coordinate
    NATRF2022 epoch 2020.00 to NATRF2022 epoch 2023.243
Terminology - Changing Coordinates
Notes: Historically NGS has been inconsistent with these top two words.
Going forward, we will use them as:
  Conversion: Meaning to change the type of coordinate without changing the datum or frame
  Transformation: Meaning to change the datum or frame, without changing the type of coordinate

## Slide 56: NCAT
  How will you do that?
Epochs/Time/4D
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: -so you’ve probably seen that phrase that I have front and center here, NSRS Modernization
-that’s the blanket term we use to refer to not just the new datums but other updates

## Slide 57: NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 58
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 59
NCAT is available via web services

## Slide 60
NCAT is available via web services
Note that each operation is a separate service
Struggling?
Contact us.
We can help!

## Slide 61
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 62
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 63: NCAT source code is on GitHub

## Slide 67: What’s the difference?
NCAT
NSRS Datums
  NAD 27
  NAD 83
  NGVD 29
  NAVD 88
  PRVD 02
  ASVD 02
  NMVD 03
  GUVD 04
  VIVD 09
VDatum
NSRS Datums
Geoid Models
  Add/Subtract from Ellipsoid
Tidal Datums
  MHW, MLLW, MTL
Great Lakes Datum
  IGLD85
ITRF#### ≈ WGS84
Local Tidal (LT)

## Slide 68
Estimated Geometric Change - Horizontal
NAD83 (2011)  NATRF2022
3.6 ft
4.3 ft
3.9 ft
Direction of Shift
4.6 ft
3.0 ft
Notes: What’s the magnitude of the horizontal datum shift across Pennsylvania?
Minimum Shift ~3.75 feet
Maximum Shift ~3.97
Remember this is just an estimation, don’t hold me to the numbers please

## Slide 70: New Lat/Long = New XY
With a new horizontal datum…
There comes a new set of SPCS zones

## Slide 72
State Plane Coordinate System of 1983
SPCS83
North and South Zones as they exist now
Notes: We start with the SPCS83 zones as a frame of reference
NOTE that the color shading of these zones is matched to that of the Preliminary SPCS2022 Zones that follow

## Slide 74
State Plane Coordinate System of 2022
SPCS2022
NGS designed a Single Statewide Zone for every State

## Slide 77
State Plane Coordinate System of 2022
SPCS2022
Ohio stakeholders designed 88 zones
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 80: SPCS2022 Zone Layers in Ohio
Both Single Statewide and Multi-Zone Layers will coexist
Think about your data, your goals, your customers
  Remember that geographic coordinates are your friend!
Smaller zones not “the best” … it all depends on usage & goals

## Slide 81: SPCS2022 Zone Layers and LDPs
Each state may have max of 3 zone “layers”
  One layer must be statewide zone
    Single Statewide Zone
  Other layers have two or more zones
    Multi-Zone
  A third layer can exist, but must be discontinuous coverage
    Left open for possibilities in many states
Notes: (Cleveland Regional Geodetic Survey)

## Slide 82: Which is best?
Each has strengths and each has weaknesses.

## Slide 83
Do you really need to…?
Notes: Reminder that you don’t have to cutoff data at any SPCS zone extent  just need to understand that they’re designed with certain extents in mind

## Slide 84
State Plane Coordinate System of 2022
SPCS2022
Not just Ohio
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 85: Number of SPCS2022 zones (preliminary)
CONUS, Alaska, and Hawaii
Three island zones not shown:
Puerto Rico and U.S. Virgins Islands
American Samoa
Guam and the Commonwealth of the Northern Mariana Islands

## Slide 86: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 87
The Survey Foot is dead!
Long live the Survey Foot!
US Survey Foot was deprecated 31 December 2022… now what?!?
Notes: We start with the SPCS83 zones as a frame of reference
NOTE that the color shading of these zones is matched to that of the Preliminary SPCS2022 Zones that follow

## Slide 88
Deprecated 31 December 2022
Which begs the question
  What should you be doing now?
What happened to the US Survey Foot?

## Slide 89: What should you be doing now?
Ask the right questions
  Does state law specify US Foot for SPCS83?
    40 states do that we know of
  Does it specify US Foot for boundary surveys? (Does that matter?)
    We’re not tracking that, it’s not NSRS-related
Prepare for this along with new datums
  GeoBoard Geodetic Working Group
    Anyone always welcome to any meeting/discussion
    Update Monday evening is that it will likely be un-opposed

## Slide 90: What should you be doing now?
Prepare for this along with new datums
Understand the difference between sft and ift
  2 parts per million
Understand this is not enforced
  Neither NIST or NGS are a regulatory agency
  We support education/outreach of course
  But OPUS, NCAT, etc. will not have US Survey Foot options for output in SPCS2022 zones

## Slide 91
1,000,000.00 sft = 999,998.00 ift
10,000,000.00 sft = 9,999,980.00 ift
1,000.00 sft = 999.998 ift (can you measure that?)
International  1 ft = .3048 m
US  1 ft = .30480061 m (approx.)
2 parts per million (ppm)?

## Slide 93
The Survey Foot is dead!
Long live the Survey Foot!
US Survey Foot was deprecated 31 December 2022…
But it will always be available in NGS tools for NAD83 and NAD27 coordinates

## Slide 94
Positional Components of
the NSRS
Geometric
aka “Horizontal”
Latitude, Longitude, Ellipsoid Height
Geopotential
aka Orthometric Height
aka “Elevation”
NAD83
NAVD88
Notes: -geometric component is latitude, longitude, and ellipsoid height
-geopotential component is combined with the geometric components to calculate an ortho height or capital H

## Slide 95
Three types of heights in NSRS
Water Level or Tidal
NOAA and USACE Hydrography
Daily and Extreme Water Levels (Gage)
Shoreline Mapping and Regulatory Boundaries at the Coast
geoid
Ellipsoidal
Raw GPS Observations
Raw Hydrographic Surveys
Raw Lidar Data
NAD83
Orthometric
USGS
Topography
FEMA NFIP Data & Maps
Engineering and Construction Surveys
NAVD88
NGVD29
Notes: This slide illustrates the 3 categories of vertical datums and examples of where each is directly used They are project and application dependent.
First, we have ellipsoidal datums. Examples include WGS84 and NAD83 (North American Datum of 1983). You will encounter these datums frequently in hydrographic surveys that are vertically referenced with RTK-GPS; any native GPS measurements; and even raw lidar datasets.
Next, we have orthometric datums. These datums are very important because height differences referenced to orthometric datums will allow us to know the direction water will flow, because they have been “gravity-corrected”. The North American Vertical Datum of 1988 (or NAVD 88) is an orthometric datum, which you will see on USGS topographic maps, engineering and development site surveys, and FEMA Flood Insurance Rate Maps.
Finally, we have Tidal Datums, which are derived from water level measurements. They have extremely important applications including daily and extreme water levels; NOAA nautical charts, and shoreline mapping or boundaries along the coast.
*NOAA provides tools (like NCAT and Vdatum) to transform between these different height systems.
The Bridge

## Slide 96
Orthometric
Notes: This slide illustrates the 3 categories of vertical datums and examples of where each is directly used They are project and application dependent.
First, we have ellipsoidal datums. Examples include WGS84 and NAD83 (North American Datum of 1983). You will encounter these datums frequently in hydrographic surveys that are vertically referenced with RTK-GPS; any native GPS measurements; and even raw lidar datasets.
Next, we have orthometric datums. These datums are very important because height differences referenced to orthometric datums will allow us to know the direction water will flow, because they have been “gravity-corrected”. The North American Vertical Datum of 1988 (or NAVD 88) is an orthometric datum, which you will see on USGS topographic maps, engineering and development site surveys, and FEMA Flood Insurance Rate Maps.
Finally, we have Tidal Datums, which are derived from water level measurements. They have extremely important applications including daily and extreme water levels; NOAA nautical charts, and shoreline mapping or boundaries along the coast.
*NOAA provides tools (like NCAT and Vdatum) to transform between these different height systems.

## Slide 97
North American Vertical Datum
of 1988
NAVD88
will be replaced by

## Slide 98
North American-Pacific Geopotential Datum of 2022
NAPGD2022
(pronounced: nap-jee-dee)

## Slide 99
NAVD88 geoids
versus
NAPGD2022 geoids

## Slide 100
  Gravimetric
  Hybrid
Two types of geoid models
Notes: -believe it or not there’s more than 2 types, but the 2 types you’ll see NGS publish are…

## Slide 101
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid then best fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 102
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
Notes: So… all the geoids you’re using to get elevations from your GNSS data

## Slide 103: Gravimetric vs. Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 104: NAVD88 uses a Hybrid Geoid
Concept
topographic surface
datum zero
surface
gravimetric geoid
hybrid
geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 105: NAPGD2022 uses a Gravimetric Geoid
  Datum zero surface aligned to Global Mean Sea Level (GMSL)
Concept
topographic surface
datum zero
surface
gravimetric geoid
Notes: -importantly, the height chosen was to minimize 2988 differences on USGS topo maps in the eastern U.S. … thus, the “zero height surface” of NAVD 88 was NOT chosen for its closeness to the geoid (but it was close…few decimeters)

## Slide 106: Sea Level Change and the Geoid
GMSL
Geoid
Threshold Level
H2020.000
H2085.000
-Threshold Level is published as 20 cm
-Process is repeated as GMSL changes
Notes: The illustrated strategy will be adopted at NGS. An animated characterization of this approach
What this means is that NGS will decouple the geoid from GMSL, until they have diverged by some threshold amount, currently defined as 20cm.
When that threshold is reached a new geoid will be defined and held fixed until reaching next threshold. In this way, the impact of the change of GMSL is accounted for in the heights of the NSRS, while the appearance of stability is maintained for “decades at a time” (BP2 Section 14).
If we calculate how long that might be based on existing rates of sea level rise of 3ish mm/yr then we’re talking over 50 years

## Slide 107
equipotential surfaces
(equal gravity)
ground surface
Why leveling is not part of NAPGD2022
…but will still be important for you.
Geoid at Site Scale

## Slide 108
Why leveling is not part of NAPGD2022
…but will still be important for you.
ground surface
equipotential surfaces
(equal gravity)
Geoid at Continental Scale

## Slide 109
Estimated change in orthometric heights from NAVD88 to NAPGD2022
(NAPGD2022 approximated using xGEOID16B)

## Slide 110
Estimated change in orthometric heights from NAVD88 to NAPGD2022
OPUS Extended Solution Report

## Slide 111
OPUS Extended Solution Report
  Scroll all the way to the bottom…
Estimated change in orthometric heights from NAVD88 to NAPGD2022

## Slide 112: Preparing
Inventory heights in your data/datasets
  Have you mix & matched geoid models?
    Are you tracking levees or other flood control?
    Are you managing subsurface utilities?
      Access covers, junction boxes, cleanouts, etc.
    Maybe geoid differences aren’t even significant?
      VADOT story…
  Know your goals, know your data.

## Slide 113: Preparing
Know the epoch of your data/datasets
  consider how you will track this
    full to-the-second timestamp on every feature?
      Modern survey equipment makes this possible
    labeling a year for each dataset?
      Easy to add to workflows, datasets/databases, folders
    something in-between that works for your needs?
2023.1957
2023:27
20230127
Epoch nomenclature is your choice

## Slide 114: Preparing
Reprocessing your data
  perfect world = everyone reprocesses everything
    what does this mean?
      consider an ALTA w/topo
        start over with the onsite GNSS-based control
        reorient all your shots/ties (hopefully linked)
        recreate all the drainage features in new datum
    unrealistic! … and unnecessary for majority users
Notes:   Reprocessing your data
    in a perfect world, everyone would reprocess data
        consider a final product like you use everyday - a hydro-enforced DEM
          starting fresh with the raw GNSS/IMU processing
          generate new ellipsoid height point clouds
          recreate all the drainage features in new datum
    this is totally unrealistic  both from a financial and programmatic perspective

## Slide 115: Preparing
  Transforming your data
    NCAT - NGS Coordinate Conversion and Transformation Tool
      ASCII up/download, Web Services, Download, GitHub
      ask your software provider(s) about integration
        we envision COTS integrations as most popular method of access
        Industry Workshops - May 2021 and August 2022
          Esri, Trimble, Blue Marble, etc… all the well known names attended
        Geospatial Software Developers’ Summit – Nov/Dec
          International & Virtual  US NGS and NRCan CGS
Notes: Transforming your data
NCAT - NGS Coordinate Conversion and Transformation Tool
available now: ASCII upload and Web Services
ask your software providers about integration
we envision this as most popular method of access
Industry Workshop held this year – esri, trimble, bluemarble, all the major well known names were represented
labeling a year for each dataset?
something in-between that works for your needs

## Slide 116: Preparing
What can you do to ensure your control will get coordinates in the new datums on rollout?
Re-observe and submit the data to NGS
  must be submitted by 29 February 2024
Options to submit your data:
  OPUS Share  4+ hrs static data; 2 photos; mark ties
    rinse & repeat … as we need redundancy
  OPUS Projects  2+ hrs static GPS data
   5+ minutes RTN-GNSS data, 3x per mark
  Also: photos, field logs, descriptions, survey report
Notes: -OPUS Share requires 4+ hrs static data; 2 photos; and a brief description of reference ties (not a full IDB “from the post office”)
 NOTE THAT OPUS SHARE OPTION REQUIRES 2 OBSERVATIONS
 WHY? WE REQUIRE REDUNDANCY FOR ANY OBS THAT GO INTO OUR DATABASE
-OPUS Projects  2+ hrs data; photos; full IDB style descriptions via WinDesc (*MUST USE WINDESC*)

## Slide 117: Remember…
  What’s the goal of NATRF2022?
    Give you the stability in positions that you expect
  That’s the point of Reference Epochs (REs)
    Akin to the different realizations of NAD83
    REs will be published every 5 or 10 years
      you choose when you update
      in a perfect world, everyone would stay current
aka versions
Notes: What’s the goal of the way NATRF2022 was designed, by including EPP2022 and IFVM2022
Does a database of manholes in PA need cm-level coordinate updates on an annual basis? Probably not.

## Slide 118: Additional Resources

## Slide 119
geodesy.noaa.gov/ADVISORS/
Regional Geodetic Advisor Program
14 RGAs across country
We are here to support:
  You
  Your constituents
  Our Federal Partners
Questions about
NSRS Modernization?
  Reach out now
  Be prepared

## Slide 120
Educational Videos
<5 minutes
Online Lesson
(via MetEd/COMET)
~1 hour
NGS homepage: geodesy.noaa.gov
Notes: Educational videos and online tutorials –
Our library of lessons and videos are great resources, and will reinforce a lot of information we covered today.
The videos are just 3-5 minutes long.
the lesson is a deeper dive but still only takes an hour.

## Slide 121
Click this icon on homepage
Email Subscriptions
*Only 1-2 messages per month*
NGS News
  Includes quarterly NSRS Modernization newsletter
Webinar Series
Training
GPS on Benchmarks

## Slide 122
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
https://geodesy.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”

## Slide 123
Scan to save my contact info on your phone